## Slide 1: Bode-Fano Evasion for Broadband Axion Receivers
Andrew Kunwoo Yi
SLAC National Accelerator Laboratory
October 9th, 2025
DMRadio Collaboration Meeting

## Slide 2: Building a wideband receiver for axion experiments
Axion parameter space is very wide (almost 20 orders of magnitude)
Resonant searches have narrow bandwidth
  1 GHz axion, 50 kHz cavity bandwidth
  We want an axion search with a wide receiver bandwidth, but this is difficult due to the Bode-Fano limit
from https://cajohare.github.io/AxionLimits/

## Slide 3: Bode-Fano Limits
Bode-Fano limit: A complex load having energy storage elements limits the bandwidth of the match achieved by a matching network
Criteria (assumptions): Passivity, Linearity, Time Invariance
Removing some of these assumptions could bypass the Bode-Fano limits

## Slide 4: The resonant receiver
Resonant when
Axion as an AC source
Zero impedance here

## Slide 5: The Bode-Fano evading receiver
Removes the “passive” assumption from Bode-Fano criteria
Zero impedance across all frequencies
Negative inductance needs energy fed into it

## Slide 6: RLC circuit model of a haloscope
A negative inductor can cancel out the haloscope’s inductance
Axion as an AC source
Resonant only when
Use negative inductance instead of capacitance
Reactive impedance cancelled at all frequencies  broadband with good sensitivity

## Slide 7: How to achieve negative inductance?
Negative Impedance Converters (NICs)
  Works at room temperature conditions, but noisy
Cryogenic solution: Josephson junction inductance is a function of the phase across the junction
Irwin group design example
The Josephson junction can be “biased” to a certain phase by changing the current flowing across it (= active device)
Superconductor
Superconductor
Insulator
: critical current

## Slide 8: What we are trying to achieve
Build a circuit where geometric inductance () is cancelled out with the Josephson inductance () while maintaining stability
Generalization: Build a circuit where the inclusion of the Josephson junction reduces the total inductance
Find a promising design, simulate the circuit, and fabricate it to test it out in the lab
Josephson junction will have negative inductance when its phase is between

## Slide 9: Is stabilizing negative inductance possible?
Yes, and it has been observed before
Josephson junction inductance as part of a circuit
R. Rifkin and B.S. Deaver, Jr., Phys. Rev. B 13, 3894 (1976)
Radiofrequency quantum upconverters (RQUs) with a three-junction loop with specific conditions
Negative Josephson junction inductance
from https://irwinlab.stanford.edu/quantum-sensing
Left half:
Negative Josephson junction inductance
Right half:
Positive Josephson junction inductance

## Slide 10: Is stabilizing negative inductance possible?
The total inductance in general is higher when the Josephson inductance is negative
Total inductance of the circuit increases when the Josephson inductance is negative (phase around )
The red region is where one Josephson junction’s phase is (negative Josephson inductance)
Using parameters from the Rifkin and Deaver paper
RQU simulation

## Slide 11: Instability of negative inductance
There is instability when Josephson junctions are biased such that it also reduces the total inductance of the circuit
Example circuit
Example circuit total inductance as a function of Josephson junction phase
Bias Current (A)
JJ Phase (rad)
We never reach that region
Phase as a function of time when trying to bias the junction into the “low inductance region”

## Slide 12: Stabilizing negative inductance Josephson junctions
Loop equation: In a loop (left) with geometric inductance , the Josephson junction settles at a phase (when its initial phase is )
can be negative with select parameter values of , , (shaded red region)
Initial phase

## Slide 13: Preserving negative inductance
From the voltage source’s point of view, the “total inductance” is
From junction’s point of view, its phase is determined by the value of
Initial phase
Initial phase
Phase is still determined by the value of
Voltage source point of view “total inductance” is

## Slide 14: Inductance cancelling with Josephson junctions
DC current biases junction to phase
Voltage source
Inductance cancelling device
Inductance to cancel
Inductance seen by the voltage source
Inductance seen by the junction
WRSPICE simulation
Inductance is cancelled below the red shaded region and is lowest when the junction is initially biased to

## Slide 15: Inductance cancelling with Josephson junctions
Inductance is not cancelled
Current lags behind voltage
Inductance is cancelled
Voltage is opposite sign for negative inductance
Current leads voltage
Voltage check
Compare amplitudes (and signs) of the voltages across and
Current check
Compare phase difference between voltage source voltage and current in left loop
WRSPICE simulation results

## Slide 16: Adding an output
Modeling the axion as a voltage source, and coupling out a 50 ohm output resistor
Power drawn from voltage source and transfer to output resistor can be calculated
Voltage source
Inductance(s) to cancel
DC current biases junction to phase
Inductance cancelling device
Output read here

## Slide 17: Power transfer comparison
Comparison between capacitor (resonant), short (no Bode-Fano Evasion), and (Bode- Fano Evasion)
Voltage source
Inductance(s) to cancel
Output read here
Matching network
Matching network can be:
Capacitor
(resonant)
Short
(non-resonant, no Bode-Fano)
Expectation
(Analytic)
Simulation
(WRSPICE)
Inductance cancelling
(Bode-Fano Evasion)

## Slide 18: Phase considerations
Voltage source
Inductance(s) to cancel
Current source
Inductance(s) to cancel
small
“Stiff” voltage source
Phase oscillates (and stays there)
“Equivalent” voltage source
Phase drifts away from
Long term behavior:
is no longer negative
Long term behavior:
stays negative
Does resistance in main loop prevent the junction from staying at intended phase?

## Slide 19: Fabrication considerations
Fasthenry simulations for two-loop circuit with input and output
No capacitive/resistive effects considered
5-parameter search for potential dimensions
To input
To output
Josephson junction
DC bias for junction
⑤
①
②
③
④

## Slide 20: Fabrication considerations
Initial inductance simulations show that there are combinations where is possible
  If the junction phase stays at intended phase without drifting away due to resistance
Negative is consistently possible for designs within ±0.5 um trace precision
Future plans: make design to fabricate and test @ Chelsea’s new fridge at SLAC!

## Slide 21: Summary
Even the most sensitive axion searches to date (resonant experiments) take a long time. Can we make broadband axion receivers?
The Bode-Fano limits dictates the sensitivity and bandwidth of a resonant search if components are passive, linear, and time invariant
Josephson junctions could bypass the Bode-Fano limits as an active component that behaves like a negative inductor depending on its phase
Some designs with junctions and specific parameter choices show that inductance can be cancelled at the simulation level
Currently trying to understand the circuit in terms of power transfer
(ratio between output and input power)
Plans on fabricating an actual device to test in our group’s new fridge @ SLAC

## Slide 22: Axion signal conversion power
The axion signal conversion power depends on various factors
: Total energy of a specific mode
: Axion to photon coupling
(value varies depending on model)
: Axion density in galaxy halos
: Axion mass
: Cavity coupling parameter ()
: Cavity resonant frequency
: Average external magnetic field
: Cavity volume
*Uses natural units and assumes cavity is resonant to axion frequency
: Form factor, depends on internal electric field of mode and external magnetic field
: Loaded quality factor, including losses of cavity () and receiver ()
For an empty cylindrical cavity inside an external B-field in the -direction, the TM010 mode has the highest form factor at 0.69
*Assumes