## Slide 1: Machine Detector Interface MDI
John T. Seeman
SLAC National Accelerator Laboratory
September 8, 2026
4th Annual Higgs Factory-Future Circular Collider Workshop at SLAC

## Slide 2: Machine Detector Interface (MDI) Tutorial
John Seeman (SLAC)
September 8, 2026
The Interaction Region IR in a high-current high-luminosity e+e- collider is compact and complex, combining many of the most difficult aspects of the accelerator and detector. MDI helps coordinate plans for the highly interconnected interface between detector and accelerator to facilitate that both are successful even at the highest luminosities, often at several center-of-mass energies, for example from the Z pole to the t-tbar threshold. The accelerator and detector layouts integrate accelerator components such as lightweight and actively cooled beampipes, superconducting IR-magnets, bellows, and remote vacuum connections with detector components of inner detectors, vertex chamber, diagnostics, luminosity detectors, and utilities (cables, cooling, power, supports). This tutorial will cover more than thirty interface topics (from SC magnets, shielding solenoids, vacuum chamber masks, and inner detector elements to IR beam physics, beam loss sources, various beam backgrounds, and irradiation protection shielding). Examples from past and present colliders (KEKB, PEP-II, SuperKEKB) and future colliders under design (FCCee, ILC) will be used. Attendee interactions are encouraged.

## Slide 3: MDI inputs from these people and others.
T. Raubenheimer, S. Gessner, T. Montagne, C. Niebuhr, K. Suguitan, G. Kerr, L. Pollastrini

## Slide 4: MDI Tutorial Topics
1) General overview and IR layouts for various colliders
2) Main IR parameters
3) IR Comparison of various colliders
4) IP beta function versus L*
5) Detector requirements
6) Detector sub-components
7) IR accelerator requirements
8) Accelerator sub-components
9) Detector-Accelerator Interferences
Main collider goal
MDI compromises
Detector end cap withdrawal
10) Luminosity measurement
Lumi-Cal at 1.076 m
-11) Vacuum Chambers
IR chamber design +/-0.5 m
Y chamber 0.5-2 m
Y chamber HOM issues and reduction
Lumi-Cal at 1.8 m
Remote flanges (e.g. CESR, SuperKEKB, SMA)
12) Magnet cryostat 2.4 to 7 m
Cryostat cryogen feed
lines and splice box
Q1 magnet in 3 pieces
Q2 magnet in 2 pieces
Compensating and screening solenoids
Correction magnet coils
13) Component assembly
14) Installation
15) Vibration control
16) Polarization
17) Background sources
Beam background types
Beam gas, Touschek, synchrotron radiation, non-Gaussian tails, luminosity,

## Slide 5: FCCee Rings and IR beam lines

## Slide 6: Main Parameters for FCC at Jan 26 Lattice Review: LCC chosen.

## Slide 7: General Detector-Collider Overviews (M. Boscolo)
FCC Detector Concepts (IR accelerator inside detector)
New: ALFA + two more!

## Slide 8: Integrated Physics
Integrated physics is (simplified)

## Slide 9: Practical Integrated Physics
Integrated Physics is
Det-fiducial-volume x (~Beam lifetime)
Laverage = Lpeak x (1-Ldecay)-beam real-time lattice/coupling variations
Accel colliding time = colliding time – running down times - maintenance stops
(Maintenance time: PEP-II = 1 month/yr, CERN =3 months/yr (YETS)
Detector collection= (1 - recording deadtime) (1-injection deadtime)
Detector fiducial volume = ~0.99
To go to 0.995  need to squeeze final quads out (L* x 2 distance) and will,
thus, lower peak Lumi by ~1/2. Caution: a push for +5% could lose -50% in
physics.
Beam lifetime ~ 10 min. Injection detector time veto is a few msec per injection.

## Slide 10: SuperKEKB and Belle-II
A new record of peak luminosity of 5.32x10^34 was achieved
(Belle II HV off) and the integrated luminosity reached 914 /fb .

## Slide 11: Example: SuperKEKB Operations (June 8, 2026) (courtesy KEK)
HER one
beam trip
LER unstable current + one beam trip
Belle-II data
collection
is about 80%
Top-up injection
for both beams.
Lifetimes =
HER ~ 39 min
LER ~ 20 min
Luminosity lifetime ~13 min

## Slide 12: SuperKEKB Parameters

## Slide 13: Overall SuperKEKB IR Layout

## Slide 14: SuperKEKB IR Cryostats

## Slide 15: Belle-II Center View

## Slide 16: CEPC Overview (~2023)

## Slide 17: CEPC Parameters

## Slide 18: CEPC IR magnets and cryostats (Dec 2023)

## Slide 19: ILC layout

## Slide 20: ILC Detector Concept (Accelerator IR Quads Magnets Outside)

## Slide 21: FCC tunnel cavern possibilities
(J. Szaga)

## Slide 22: Lowering LHC Detector Components

## Slide 23: IR Layout

## Slide 24: Comparisons of IR (features for FCCee, CEPC, ILC, SuperKEKB)
Machine |  | FCCee | CEPC | ILC | SuperKEKB
Crossing-angle | mrad | 30 | 33 | 14 | 83
L* | m | 2.2 | 1.9 | 3.5 | 0.935
L* x Cross-angle | mm | 66 | 63 | 49 | 78
Vertical by* at IP | mm | 0.7-1.6 | 0.9-2.7 | 0.4 | 0.3
Detector soln field | T | 2/3 | 3 | 3.5/5 | 1.5
Detector stay clear | mrad | 100 | 118/141 | 90 | 350/436
He temperature | K | 1.9 | 4.2 | 4.5 | 4.5
QC1s side-by-side |  | Yes | Yes | No | No

## Slide 25: IR Final Focus Optics 1984 (SLC at SLAC)
Vertical plane
Horizontal plane

## Slide 26: Beta functions grow quadratically away from the IR
(Matt Sands)
~s2/b*
Beam size grows linearly from IP.
FF Quad size is limited by beam sizes/backgrounds.
Quad aperture limits lowest by* .

## Slide 27: IR accelerator optics for various colliders

## Slide 28: IP off energy corrections and crab waist

## Slide 29: Accelerator Knobs for IP Tuning

## Slide 30: FCCee Machine Detector Interface (M. Boscolo)

## Slide 31: Luminosity Equations

## Slide 32: Crab Waist Collision Scheme

## Slide 33: Lattice and Beam Issues that affect the luminosity

## Slide 34: Tracking times for different effects

## Slide 35: Crab waist strength and luminosity (for SuperKEKB)

## Slide 36: IP beam size and errors (SuperKEKB, Funakoshi)

## Slide 37: Luminosity Tuning

## Slide 38: FCCee IR Optics for FCCee (L* study) (K. Oide March 2025)
Study effects of L* on Luminosity In FCCee

## Slide 39: Beam–beam resonances in FCCee with different symmetries

## Slide 40: SuperKEKB Vertical tune and Vertical Emittance
Bunch core particles are at a different tune than the bunch tail particles.

## Slide 41: Tracking and errors tolerances for Luminosity

## Slide 42: SuperKEKB Beam-Beam Measurements (Funakoshi)

## Slide 43: SuperKEKB Specific Luminosity

## Slide 44: Future: AI and Machine Learning for Luminosity Tuning

## Slide 45: Near Detector IDEA with L* of 2.4 m to front of QC1A.

## Slide 46: FCCee ALFA Detector near the FCCee IP
L* = 2.4 m
IP
Face of QC1A

## Slide 47: Remote Flange disconnect (IDEA detector + Accelerator Cryostat

## Slide 48: IR accelerator Components Inside the Detector

## Slide 49: Central Beam Pipe, Vertex and Lumi-Cal Integration

## Slide 50: Luminosity Monitors
Robert Kieffer
None
Each of the four experimental IPs will be equipped with a pair of Beamstrahlung extraction lines and associated dump.
Each of these extraction lines will be equipped with the same instrumentation systems (8 lines total).
Monitoring of the Beamstrahlung signal and the Bhabha scattering events will allow precise IP tuning for increased luminosity.
Positron Beam
Electron Beam
Beamsstrahlung photons
Beamsstrahlung photons

## Slide 51: FCCee Accelerator IR Vacuum Chamber (Mock-up)
M. Boscolo et al)

## Slide 52: IR Mechanical Design

## Slide 53: FCCee Interaction Pont Mock-up at INFN-Frascati
Manuela Boscolo et al + …

## Slide 54: KEKB IR Layout and Cryo-plant Overview

## Slide 55: SuperKEKB SC magnet cryostat and feedlines

## Slide 56: For comparison: SuperKEKB IR SC Magnet System
Norihito Ohuchi (2013): “IR SC magnet system
is the most important and complicated
hardware in SuperKEKB.”
SuperKEKB IR SC magnets:
8 quadrupoles, 4 solenoids, 43 correctors

## Slide 57: SuperKEKB SC magnet cryostat and slice box

## Slide 58: First look at IR accelerator 1.9 deg cryo-plant (P. Borges de Sousa…)

## Slide 59: Remote Vacuum Connection Details (KEK and DESY)

## Slide 60: Remote Vacuum Flange (SuperKEKB, Ohuchi)

## Slide 61: New concept: Remote connection option : SMA
F. Niccoli,
F. Fransesini
…

## Slide 62: FCCee Detector End-caps Open Longitudinally
J. Szaga,
O. Beltramello …

## Slide 63: Magnets: Beam trajectories in FCCee IR

## Slide 64: IR MAGNETS: longitudinal locations, lengths, and strengths (K. Oide)
K. Oide is available to discussion any needed changes. P. Raimondi’s lattice
has more space from QC1 to QC2.

## Slide 65: FCCee some cryo-stat dimensions
Cross section
views
M. Koratzinos, M. Boscolo

## Slide 66: IR Magnet Cross Section View (front and end of each magnet) Showing separated heat shield and vacuum vessel.
Magnet coils
Beam vacuum walls
Cryostat vacuum walls
Cryostat He walls
And heat shield walls
Beam centroids
J. Seeman November 2023
.
Cryostat outer
support

## Slide 67: IR cryostat component dimensions

## Slide 68
IR QC1 and QC2 in different cryostats but one integrated raft (not to scale)
Need to make space for cryogens, leads, and cantilever supports.
3.36 m
QC1-1
QC1-2
QC1-3
QC2-1
QC2-2
2.58 m
~1.5 m
2.2 m to IP
FCCee IR Cryostat (preferred option):

## Slide 69: Needed functions for the space between QC1 and QC2
Beam pipes (cold vs warm)
e+ and e- BPMs (radial space)
Cantilevered supports (many forces)
Detector shielding near beam pipe (backgrounds and magnet quenches)
Vibration mitigation and control (orbit control)
Two cryostat end caps, cryogenic ports, disconnects (cryogen flow, heat load)
Magnet leads (warm to cold)
Alignment (internal positioning, remote)
Instrumentation (what to measure and how)
Remote operation flange controls and access (design, safe operation)
Vacuum disconnects (locations)
Assembly strategy (order of installation)
Cool down radial differential movements (Dr/r ~3x10^-3, 0.5 mm movements)
Cables (routes, numbers)

## Slide 70: CEPC IR 6.8 m cryostat (Dec 2023)

## Slide 71: ILC IR magnet locations (2013)

## Slide 72: ILC IR magnets (2013)

## Slide 73: Canted Cosine Theta quadrupoles and direct wind (BNL)

## Slide 74: SC CCT QC1 quadrupole field measurements (M. Koratzinos …)

## Slide 75: Detector and accelerator solenoid magnetic fields

## Slide 76: IR Accelerator Optics – Solenoid Compensation

## Slide 77: Alternative IR Solenoid Compensation Scheme

## Slide 78: Solenoid Compensation Scheme (B. Parker, V. Teotia, BNL)

## Slide 79: PEP-II IR BaBar detector field measurements

## Slide 80: PEP-II IR rafts near BaBar detector

## Slide 81: Cables: Example BaBar Vertex Chamber
Assembly instructions has >100 pages!

## Slide 82: PEP-II IR Vacuum Chamber with 3D structures

## Slide 83: FCCee Center Accelerator Vacuum Chamber (Fransesini)

## Slide 84: IP Vacuum Chamber Design (Fransesini)

## Slide 85: Vacuum and Cryogenic Failure Modes: Inner He vessel in cryostat may crush if quench or vacuum loss
Water pump pulled ~1 Bar pressure on water tank at SLAC causing it to crush.
Example at SLAC of thin-walled water chamber:

## Slide 86: Accelerator and Detector Survey and Alignment

## Slide 87: HOM calculations of IP vacuum Chambers (A. Novokhatski)

## Slide 88: IR Trapped HOM Mode at Y chamber (Novokhatski)
Trapped mode is part vertical, horizontal, and longitudinal: Hybrid mode.

## Slide 89: FCCee IR bellows has HOM Losses
Central chamber has 1.5 Amp x 2 beams = 3 Amps of short length bunches!

## Slide 90: HOM Modes in IR bellows design

## Slide 91: SuperKEKB beam impedance to study beam instabilities

## Slide 92: Polarization and Energy Calibration

## Slide 93: Beam polarization measurement near the IP

## Slide 94: FCC background studies

## Slide 95: Comprehensive collimation systems

## Slide 96: Radiative Bhabha’s in SuperKEKB IR

## Slide 97: BELLE-II and SuperKEKB backgrounds

## Slide 98: PEP-II Synchrotron Radiation Fans

## Slide 99: SR scattering from FCCee Mask Tips (M. Sullivan)

## Slide 100: Background sources

## Slide 101: FCC IR Background Simulations

## Slide 102: Inputs for IP local background simulations

## Slide 103: Direct observation of background spectra
The Beamstrahlung spectra should reach down to optical wavelengths.
Another possibility is to use glassy carbon screens (super light weight) to monitor Beamstrahlung photons in the optical range.
To be evaluated: the quantity of visible photons generated by Beamstrahlung.
And the BS to SR radiation levels with IP shielding against SR.

## Slide 104: Large tails on beam shape due to Beamstrahlung

## Slide 105: Beamstrahlung Radiation Spectrum

## Slide 106: Beam Synchrotron Radiation in FCCee IR

## Slide 107
Optical line to monitor a scintillating screen on the extraction line.
Robert Kieffer
None
Could be inserted at low intensity for IP tuning procedures
Heat deposition study: Monte Carlo simulation of particle matter interaction.
Cooling system for the screen?
The study will define the accessible range of bunch-charge (Beamstrahlung at the IP / heating the screen)
Positioning: Be as far as possible from IP (dilution) and not to close from the dump (radiation background).
Mirror
Actuated
Insertable screen
Viewport
Beamsstrhalung photons
Camera in shielding
From IP
To Dump
None
Zero degree: Straight Ahead Detector

## Slide 108: Beam gas scattering

## Slide 109: Secondary scatters

## Slide 110: Radiative Bhabha Impact on IR Accelerator Quadrupoles
(May not be up to date)

## Slide 111: Thank you for your participation!
Many FCCee topics to study!
FIN
Questions?