## Slide 1
Phonon Collection Modeling in G4CMP with Finite Surface Losses
Toward Direct Absorber Phonon Sensor Design
Selby Q Dang / SLAC + Stanford
June 15, 2026 | RISQ 2026 G4CMP Workshop
Notes: I will be presenting on studies of phonon loss and its effects on phonon collection modeling and implications toward sensor design.

## Slide 2: Overview
Benchmarking effects of phonon loss is relevant for modeling diverse phonon sensors in G4CMP.
Selby Q Dang | RISQ 2026
https://journals.aps.org/prb/pdf/10.1103/PhysRevB.110.024519
I. Benchmarking phonon loss
II. Impact of phonon loss on forward modeling
Evidence for phonon thermalization in cryogenic crystals is not fully modeled by anharmonic decay or loss to device clamps
sensor
"dead metal"
mounts
incident particle
?
Position-dependent phonon responsivity gives insight into loss mechanisms
Using one possible loss model, we can optimize sensor layout for efficiency
Notes: The takeaway from this talk is that phonon loss is a relevant consideration for modeling various kinds of phonon sensors. What do we mean by loss? There has been experimental evidence for phonons thermalizing in cryogenic crystal volumes, which are not fully explained by models of anharmonic decay or loss to device clamps. The plots on the right from Eric’s 2024 paper shows that phonon loss to the side walls in his qubit chips were necessary in reconstructing the QP response. Today we will talk about benchmarking possible models of phonon loss with a MEMS study and how we can use this insight into optimizing sensor layout.

## Slide 3
Benchmarking Phonon Loss
Part I

## Slide 4: MEMS Measurement
We probed our detector response to LED pulses at different XY positions using the MEMS.
Image credit: Leonid Sajkov
polished faces
side walls
Nb feedline
Cu housing
Al resonator
Our KIPM detector:
MKID as phonon sensor
Direct absorber: no trapping
Small sensor (<0.1% coverage on Si substrate)
Thin film (30 nm Al)
Single resonator
https://custom.cvent.com/B6DBF01384AB4E1CB4B0C6F97B77BDB2/files/event/22930724c2e84b3b93f62c7170746141/47687c07935646a0acea1924d0112ab4.pdf
Image credit: Zoë Smith
MEMS + KIPM paper in prep!
Selby Q Dang | RISQ 2026
I. Benchmarking phonon loss
Notes: We performed an optical calibration of a KIPM detector using the MEMS, which gives us a proxy to the peak-normalized phonon collection efficiency. We won’t have time to talk about how a KIPM detector works, but please ask me after this talk if you’re interested. What you do need to know about our KIPM detector is that it uses MKIDs as phonon sensors, and it is a direct absorber, which means it can tell us when and where phonon energy arrives but doesn’t do quasiparticle trapping. The sensor is small, the film is thin, and there is only one sensor on this chip. We have some exciting data of peak-normalized signal amplitude as a function of position and time, which we will be comparing our sims to.

## Slide 5: Direct Absorber Architecture
In our detector, phonons are directly absorbed into the MKID inductor, which generates the signal.
I. Benchmarking phonon loss
Direct absorber (e.g. KIPM):
Quasiparticle trapping (e.g. QET, SQUAT):
Cooper Pair
Quasiparticle
Incident Particle
Athermal Phonon
Crystalline Substrate
Sensitive Volume
Collector Volume
Selby Q Dang | RISQ 2026
Analysis of Event Position Dependence in HVeV Detectors with G4CMP and MEMS
Caitlyn Stone-Whitehead
6/15, 10:20 am
SQUATs: Qubit-Based Sensors for Dark Matter
Hannah Magoon
6/18, 10:00 am
Notes: Just to hammer in this point: our sensor is a direct absorber, meaning that phonons go straight into the sensor that generates the signal. We don’t have a collection volume that traps quasiparticles like in QETs or SQUATs, but my colleagues have very interesting talks about these other detectors.

## Slide 6: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0
pabs, Cu | 0
pabs, polished surfaces | 0
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: So we have this data on our detector’s relative phonon collection efficiency, epsilon, which displays a particular position dependence. In particular, we notice that epsilon drops off steeply when we’re close to the sensor, and then it levels out when we’re farther away. We implemented a few models of phonon loss to study their effects on this position dependence. First, if we just have a sensor and a chunk of silicon without any loss, there isn’t any position dependence.

## Slide 7: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0.745
pabs, Cu | 0.736
pabs, polished surfaces | 0
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: And then if we add in all the metal and superconducting volumes at nominal values of loss, we overshoot this position dependence metric.

## Slide 8: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0.745
pabs, Cu | 0
pabs, polished surfaces | 0
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: Adding just the dead metal at a nominal value was still too much, and it shows a bigger discrepancy between the horizontal and vertical regions.

## Slide 9: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0
pabs, Cu | 0.736
pabs, polished surfaces | 0
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: Adding just the mounts was even worse.

## Slide 10: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0
pabs, Cu | 0
pabs, polished surfaces | 0
pabs, side walls | 0.025
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: Things start to get better when we use Eric’s model of the side walls.

## Slide 11: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0
pabs, Cu | 0
pabs, polished surfaces | 0.0025
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: They still look nice when we consider loss to the polished surfaces, and there’s a flat position dependence away from the sensor, which we like.

## Slide 12: From Phonon Loss to Position Dependence
Loss mechanisms differently affect position dependence in phonon collection efficiency.
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0.1
pabs, Cu | 0
pabs, polished surfaces | 0.002
pabs, side walls | 0
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
I. Benchmarking phonon loss
Notes: If we add back in a little bit of loss to the dead metal, we can even recreate the slight discrepancy between the horizontal and vertical regions.
So are we saying surfaces are THE loss model? No. But we are saying that the loss mechanism we’re seeing seems fairly isotropic and not localized to any detector feature.

## Slide 13: Parameter Space for Low Coverage
Assuming isotropic phonon loss, position dependence is a good indicator for loss probability.
Increased surface loss
Faster absorption
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
pabs,∞: absorption probability at interface × area coverage fraction
I. Benchmarking phonon loss
polished faces
side walls
Nb feedline
Cu housing
Al resonator
Notes: Now if we assume an isotropic loss to surfaces, we can zoom out a bit into the parameter space for this thin film, low-coverage single sensor. And we find these trends in their collection efficiency and position dependence. We notice that changing the loss probability changes both metrics dramatically, whereas changing absorption probability only changes the absolute collection efficiency. So we can use position dependence to pinpoint a loss probability. We think our KIPM detector lives around the lower left corner on this grid, corresponding to about a 0.2% surface loss probability.

## Slide 14
Impact of Phonon Loss on Forward Modeling
Part II

## Slide 15: Varying Sensor Area
Assuming isotropic phonon loss, we can map out how different phonon sensor layouts perform.
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
η: average η(x,y) above 2σ ε:
average η(x,y) below 2σ
average η(x,y) above 2σ

## Slide 16: Varying Number of Sensors
Assuming isotropic phonon loss, we can map out how different phonon sensor layouts perform.
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
η: average η(x,y) above 2σ ε:
average η(x,y) below 2σ
average η(x,y) above 2σ
Notes: log scale all the x axes
log log
good efficiency, low position dependence, overall area high
thickness vs number of sensors
look at this space! it's super nonlinear!
for qubits thickness affects delta Delta

## Slide 17: Varying Sensor Film Thickness
Assuming isotropic phonon loss, we can map out how different phonon sensor layouts perform.
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
η: average η(x,y) above 2σ ε:
average η(x,y) below 2σ
average η(x,y) above 2σ

## Slide 18: Parameter Space Beyond Low Coverage
From our assumptions of phonon loss, we can create a "lookup table" for the optimization space relevant to different sensor layouts.
KIPM
low-coverage QET (Berkeley)
high-coverage QET (HVeV)
Selby Q Dang | RISQ 2026
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
η: average η(x,y) above 2σ ε:
average η(x,y) below 2σ
average η(x,y) above 2σ
arxiv.org/2505.16092v1
arxiv.org/2601.16307

## Slide 19: Direct Absorber Volume Optimization
We explore the volume optimization for direct absorber phonon sensors as a trade off between collection efficiency and sensor resolution.
Selby Q Dang | RISQ 2026
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
our KIPM
η: absolute phonon energy collection efficiency
η: average η(x,y) above 2σ
The ideal calorimeter, without any trapping enhancement, will have resolution scale as the square root of absorber volume.

## Slide 20: Conclusion
Benchmarking effects of phonon loss is relevant for modeling diverse phonon sensors in G4CMP.
Our MEMS measurement of position-dependent phonon responsivity provides a benchmark for phonon loss, which we think is isotropic & potentially at crystal surfaces
Assuming this isotropic loss, we can project efficiency for different sensor layouts
Next steps: given models of sensor resolution, we can make sensitivity projections for different sensor layouts and architectures
Selby Q Dang | RISQ 2026
I. Benchmarking phonon loss
II. Impact of phonon loss on forward modeling

## Slide 21: Thank you!

## Slide 22
Backup

## Slide 23: Microwave Kinetic Inductance Detectors
Quasiparticles from broken Cooper pairs shift kinetic inductance in a superconducting resonator.
https://doi.org/10.7907/GZ72-V784
Selby Q Dang | RISQ 2026
I. Benchmarking phonon loss

## Slide 24: Kinetic Inductance Phonon-Mediated Detectors
Our KIPM (OW230427)
1mm x 2cm x 2cm Si chip
30 nm Al resonator, 70 nm Nb feedline
0.09% sensor surface area coverage
<13,695.6 μm3 active inductor volume
Fabricated at JPL by Osmond Wen and Bruce Bumble
Use cases: low-threshold rare event searches, co-sensors for qubits
Overall detector resolution is limited by low phonon collection efficiency
resolution on energy deposited in the substrate
(hundreds of eV)
phonon collection efficiency (<1%)
resolution on energy absorbed by the sensor (few eV)
number of resonators
feedline
inductor
capacitor
Selby Q Dang | RISQ 2026
σEdep [eV] | 380 | 320 | 850
σEabs [eV] | 5.9 ± 0.9 | 2.1 ± 0.1 | 23
η [%] | 7.0 ± 1.1 | 0.78 ± 0.07 | 1.1 ± 0.2
I. Benchmarking phonon loss

## Slide 25: Note on Parameters for Part I
I. Benchmarking phonon loss
Studies in Part I do not model quasiparticles using either KaplanQP or TrackedFilmResponse
  Any above-gap phonons that are absorbed according to the phonon absorption probability are counted toward energy depositions
Other relevant parameters:
  For slides 6-12, electron-hole pairs are generated in a uniform (x,y) distribution across the L-scan region & an exponential z distribution consistent with the attenuation of a 625-nm optical photon in Si
  For slide 13, electron-hole pairs are generated at the center of the inductor for the "on-sensor" (x,y) position and (-9.3 mm, 8.52 mm) for the "off-sensor" (x,y) position; the z position is still sampled from the exponential distribution
  Electron-hole pairs each have a 0.814-eV kinetic energy partitioned in an "all-to-one" scheme to electron or hole
  Charge trapping is off
  Maximum phonon bounces = 100000
Selby Q Dang | RISQ 2026

## Slide 26: η(r) in Part I
polished faces
side walls
Nb feedline
Cu housing
Al resonator
pabs, inductor | 0.103
pabs, capacitor | 0
pabs, Nb | 0.1
pabs, Cu | 0
pabs, polished surfaces | 0.002
pabs, side walls | 0
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
Selby Q Dang | RISQ 2026
I. Benchmarking phonon loss

## Slide 27: Note on Parameters for Part II
Studies in Part II model quasiparticles in 0D using KaplanQP
  Phonon transmission probability: ptrans, Si → Al = 0.795*
  Pairbreaking probability: pbreak = 1 - exp(-4d/λpb)
    d = sensor film thickness, λpb= pairbreaking length ≈ 866 nm*
  filmAbsorption: pabs = ptrans × pbreak
Other relevant parameters:
  For slides 15-17, electron-hole pairs are generated in a uniform (x,y) distribution and an exponential z distribution consistent with the attenuation of a 625-nm optical photon in Si
  For slides 18-19, electron-hole pairs are generated in a diagonal (x,y) distribution from (0 mm, 0 mm) to (11 mm, 11 mm) and an exponential z distribution
  Electron-hole pairs each have a 0.814-eV kinetic energy partitioned in an "all-to-one" scheme to electron or hole
  Charge trapping is off
  Maximum phonon bounces = 100000
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
Selby Q Dang | RISQ 2026
*https://journals.aps.org/prb/pdf/10.1103/PhysRevB.110.024519

## Slide 28: More Sensor Layout Studies
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
ε: relative phonon energy collection efficiency; ε(x,y) = η(x,y) / ηmax
η: average η(x,y) above 2σ ε:
average η(x,y) below 2σ
average η(x,y) above 2σ

## Slide 29: More Sensor Layout Studies
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
Selby Q Dang | RISQ 2026
η: absolute phonon energy collection efficiency
η: average η(x,y) above 2σ

## Slide 30: Volume Scaling of an Ideal Calorimeter
Selby Q Dang | RISQ 2026
II. Impact of phonon loss on forward modeling
I. Benchmarking phonon loss
Linearize first term & assume film thermalizes in steady state, we get
Solution with initial ΔT=E/C:
Temperature evolution, in the limit of mapping sensor response to equilibrium temperature state:
→ pulse amplitude ∝ energy deposited
Power signal from fluctuation-dissipation theorem:
Noise in Fourier space:
Energy resolution:
In the limit that , where CVT is the volumetric specific heat: