## Slide 1: SRF R&D needs for PIP-II, the Fermilab complex, and a muon collider
Sergey Belomestnykh
Fermilab
February 5, 2026

## Slide 2: Outline
PIP-II SRF R&D needs
SRF R&D for Fermilab Accelerator Complex evolution
SRF R&D for muon Collider
Summary

## Slide 3: SRF R&D for PIP-II
1

## Slide 4: PIP-II at Fermilab
Proton Improvement Plan II (PIP-II) is an upgrade of the Fermilab accelerator complex to enable the world’s most intense beam of neutrinos to LBNF/DUNE
FNAL Booster
800 MeV SRF Linac
CW RF Operations
25 kW Dump
Dump
Main Ring Tunnel
Beam Transfer Line
Space reserved for two CMs (1 GeV)
and beam separator
Space for Mu2e-II
Beam line
Front End
HWR, 8 Cavities, 162.5 MHz
SSR1, 2 CM x 8 Cav, 325 MHz
SSR2, 7 CM x 5 Cav, 325 MHz
LB650, 9 CM x 4 Cav, 650 MHz
HB650, 4(+2) CM x 6 Cav, 650 MHz
PIP-II Scope
800 MeV, 2mA H− SRF linac
CW RF Operations
Linac-to-Booster transfer line
Accelerator Complex Upgrades
  Booster
  Recycler
  Main Injector (MI)
Conventional Facilities
PIP-II Beam Power
1.2 MW MI proton beam on target
Upgradable to multi-MW

## Slide 5: PIP-II SRF cavities
QL |  |  |  |  | 
kLFD | 1.5 Hz/(MV/m)2 | 4.4 Hz/(MV/m)2 | 4.5 Hz/(MV/m)2 | 2.2 Hz/(MV/m)2 | 1.0 Hz/(MV/m)2
LFD at | 140 Hz | 440 Hz | 592 Hz | 617 Hz | 349 Hz
LFD/HBW | 4.0 | 8.1 | 18.4 | 19.7 | 10.6
QL |  |  |  |  | 
kLFD | 1.5 Hz/(MV/m)2 | 4.4 Hz/(MV/m)2 | 4.5 Hz/(MV/m)2 | 2.2 Hz/(MV/m)2 | 1.0 Hz/(MV/m)2
 | 140 Hz | 440 Hz | 592 Hz | 617 Hz | 349 Hz
LFD/HBW | 4.0 | 8.1 | 18.4 | 19.7 | 10.6

## Slide 6: R&D to improve SRF linac performance
PIP-II is in production mode. No on-project R&D is planned at this stage.
However, there are two important general R&D topics that can help improving the SRF linac performance (benefiting both the project and operations):
  Prevention and mitigation of field emission (FE), which still rears its ugly head from time to time
  Resonance control (RC)
R&D on FE prevention and mitigation includes
  Careful optimization of HPR for each cavity shape
  Robot-assisted cleanroom assembly of cavity strings (see Genfa Wu’s presentation)
  In situ processing of FE (see Bianca Giaccone’s presentation)

## Slide 7: R&D on resonance control
Why resonance control?
  Initial operation of PIP-II will be with pulsed beam (0.54 ms) at 20 Hz repletion rate but with CW RF operation. Pulsed RF is not in the PIP-II scope.
  Operating SRF cavities in pulsed mode would reduce the annual cost of operation by a factor of ~10.
Challenge: cavities have narrow half-bandwidths (HBW in the range 30-50 Hz), while the expected detuning due to Lorentz force is up to ~20 times larger than HBW.
In addition, there will be microphonics noise on top of LFD.
Need to develop a robust AI/ML RC.
There are opportunities to experiment with RC during upcoming PIP-II cryomodule tests in the next ~3 years

## Slide 8: Prior results (~10 years ago)
Testing was done on SSR1 cavities (30 Hz HBW) at the STC at 2 K.
RF was driven open loop, no phase and amplitude feedback, only piezo controls for detuning. A combination of feedback loop and gradient square and adaptive feed-forward LFD compensation was studied under following conditions:
  >12.5 MV/m (spec); 25 Hz rep rate (20 Hz spec); 7.5 ms fill; 7.5 ms flattop (0.54 ms spec).
Longer flattop to help diagnose performance.
0.55 ms PIP-II
Adaptive ON
Adaptive OFF
Without the other two compensation methods, the cavity readily fell off resonance.
Achieved ~7.4 Hz rms detuning on the flattop.
Specification for peak detuning is 20 Hz, so further improvement in rms of approximately factor of 2 is needed.
Without adaptive compensation the detuning was almost an order of magnitude worse.

## Slide 9: SRF for Fermilab Accelerator Complex evolution
2

## Slide 10: Fermilab Accelerator Complex
National User Facility
Multiple interconnected machines for staged acceleration and delivery of protons ( pulses per year)
Several experimental areas operating concurrently
800 MeV PIP-II SRF linac will replace the existing 400 MeV copper linac
PIP-II will deliver upgrades of critical components in other machines to reach 1.2 MW of proton beam power on target for LBNF/DUNE

## Slide 11: ACE-MIRT – the next step
ACE-MIRT = Accelerator Complex Evolution - Main Injector Ramp and Targetry
Further beam power on target increase (at 120 GeV) can be achieved through higher beam intensity or faster cycling of MI.
The former option requires replacing Booster/Recycler with a new machine (several options are under consideration).
The latter option would utilize the excess beam from PIP-II/Boster (also a risk mitigation strategy if intensity ramp up of PIP-II/Booster is slower than expected).
Reducing the MI 120 GeV cycle time from present 1.07 s to 0.65 s would require installation of 17 normal conducting cavities in addition to 20 existing ones.
A tunable (~1%) 53 MHz SRF cavity may be an attractive option to replace 37 NC cavities with 6 SRF cavities, see Kellen McGee’s presentation.

## Slide 12: ACE-BR?
ACE-BR = Accelerator Complex Evolution – Booster Replacement
Further upgrades of Fermilab Accelerator Complex are nebulous at present.
At some point we will need to replace Booster and eliminate Recycler Ring to remove intensity limitations due to these accelerators.
There are several options including an 8-GeV SRF linac, a Rapid Cycling Synchrotron (RCS) or a combination of the two. An accumulator ring may be required.
The final choice would depend on what is the next big project at Fermilab. A muon collider demonstrator perhaps? Upgrading PIP-II SRF linac energy for other applications?
In any scenario, there will be a need for SRF technology. So, any new advances in making SRF more efficient will be beneficial.

## Slide 13: SRF R&D for muon collider
3

## Slide 14: Muon Collider layout and RF technologies
NC RF for capture and cooling
High-gradient cavities in high magnetic field
High charge, Huge beam size, Important beam losses
Peak RF power
Little synergy with other projects
SRF for acceleration
High charge, short bunch
High efficiency at high gradient
Maintain beam quality
Longitudinal and transverse stability

## Slide 15: Muon Collider layout and RF technologies
NC RF for capture and cooling
High-gradient cavities in high magnetic field
High charge, Huge beam size, Important beam losses
Peak RF power
Little synergy with other projects
SRF for acceleration
High charge, short bunch
High efficiency at high gradient
Maintain beam quality
Longitudinal and transverse stability

## Slide 16: SRF for accelerators (10 TeV c.m. MC)
SC LINAC (88 MHz and 264 MHz) and RLA1 are not included, no design yet
SRF technology:
Bulk Nb or Nb/Cu for 352 MHz
Bulk Nb (TESLA cavities) for 1.3 GHz and 1.06 GHz

## Slide 17: MC challenges for SRF systems
There are significant challenges that need to be addressed. Among these challenges are:
Very high muon bunch intensity ( muons in the RCS chain) would favor larger cavity apertures and hence lower RF frequencies;
Beam loading in RCS chain will not be the same in all cavities, as the cavities will be distributed around the rings in several stations and the time between passages of counter-rotating and bunches will be different – need further studies;
Relatively small aperture of 1300 MHz cavity might require switching to lower frequency;
High gradient operation of multi-cell lower frequency cavities must be demonstrated;
The lower frequency SRF cavities of 352 MHz most likely will utilize Nb/Cu SRF technology – requires significant R&D efforts;
Stray magnetic fields from high-field magnets may significantly degrade performance of SRF cavities – there is a need to developing efficient magnetic shielding and/or develop SRF cavities based on alternative superconductors;
Effect of high-intensity radiation from muon decays on the performance of SRF cavities is unknown and must be studied;
High peak RF power per cavity, especially in the RLA, requires R&D on fundamental power couplers.

## Slide 18: State of the art: bulk Nb
1300 MHz TESLA cavity
1300 MHz TESLA SRF technology was developed for a future linear collider. Parameters are consistent with the MC requirements.
ILC250 will need about 8,000 cavities.
European XFEL has been built with this technology (831 cavities).
While the cavity usable gradient specification is 23.6 MV/m (26 MV/m in vertical test), many cavities exceeded this gradient.
Recently, an accelerating gradient of >50 MV/m was achieved on two single cell 650 MHz cavities (PIP-II geometry, cold EP + bake).
Sample of best XFEL cavity results
53.3 MV/m was reached on B9AS-AES-003 650 MHz cavity at Fermilab

## Slide 19: Sensitivity to residual magnetic field
Ideally, if the external magnetic fields is less than , the DC flux will be expelled due to Meissner effect. However, because of lattice defects and other inhomogeneities, the flux lines may be “pinned” and trapped during cooldown.
For high purity (RRR = 300) Nb prepared by chemical etching the rough estimate is
Earth’s field is G, which if trapped would produce residual resistivity of ~150 nOhm at 1 GHz and
Hence one needs good magnetic shielding around the cavity to reach the quality factors in the 1010 range.
Typically, 1.3 GHz cryomodules have residual magnetic field of less than mG at the cavity surface. The magnetic shielding requirement is relaxed at lower frequencies.
Cavities subjected to nitrogen doping or advanced baking treatments have even higher sensitivity (~3 times for 1.3 GHz) to trapped magnetic field.
Proximity of SRF cavities to high-filed magnets in RCSs necessitates a need to develop efficient magnetic shielding.
Ohm for elliptical cavities is the geometry factor,
Is the surface resistance

## Slide 20: Nb/Cu SRF technology
352 MHz LEP2 cavity (Nb/Cu)
Number of cavities in LEP and available voltage
Why Nb/Cu? – Save on Nb (material cost + large sheets may be difficult to come by).
LEP2 is the only example of a large-scale deployment of Nb/Cu SRF cavities (352 MHz), operated at 4.5 K.
Used magnetron sputtering technology.
Performance does not meet Muon Collider requirements (average gradient was up to 7.5 MV/m at the end of LEP2 run), need x2 improvement in gradient.
There was a CERN-Cornell collaboration on a 200 MHz SRF cavity for an earlier version of MC. The cavity was coaled using CERN Nb/Cu technology, tested at Cornell. The cavity reached 10 MV/m with of (circa 2003).
Need performance improvement!
LEP2 SRF cavity
200 MHz SRF cavity
200 MHz test results

## Slide 21: Nb/Cu state of the art
Comes FCC-ee: The collider (for Z, WW, and ZH energies) will use 2-cell 400 MHz Nb/Cu SRF cavities (x264).
FCC-ee requirements: 10.6 MV/m, at 4.5 K very close to LEP2 performance but need to cure slope & extend field reach. For bare cavity vertical test: 13.2 MV/m,
CERN has an active R&D on improving Nb/Cu using High Power Impulse Magnetron Sputtering (HiPIMS) coating. Results are encouraging (improved slope, somewhat higher gradient), but nowhere near MC requirements yet.
Plans: optimize bipolar HiPIMS, thicker layer of Nb (6 mm vs. current 1.5 mm), improving Cu substrate (electropolishing, seamless)
vs. at 4.2 K for 1.3 GHz Nb/Cu cavities. Blue star indicated FCC-ee requirements scaled from 400 MHz.
400 MHz Nb/Cu results (2023)
400 MHz 2-cell FCC-ee cavity

## Slide 22: State of the art: Nb3Sn
The most progress to date has been made with the vapor diffusion process of forming Nb3Sn layer on Nb.
The process takes place in a high vacuum furnace, which is heated to about .
The tin source is heated to or even higher temperature. The tin vapor coats the cavity inner surface and alloys with Nb.
There was progress over the years, but:
  Accelerating gradient is still relatively low
  Reproducibility from coating to coating is not good
  Material is brittle (especially at room temperature), and cavities require very gentle handling
If a robust procedure is developed, Nb3Sn cavities might be a good option as they are more tolerant to trapped magnetic flux.
  More on Nb3Sn in later presentations

## Slide 23: R&D plan for the next 5 years
The following plan was presented to ESPPU:
The final choice of RF frequencies, should be based on the beam dynamics requirements. However, the RF power requirements and cryomodule integration issues might play a significant role.
Based on the beam dynamics requirements, perform optimization and concept designs of SRF cavities for low energy acceleration in the SC linac and RLAs and high energy acceleration in RCSs. Select one or two most challenging designs for prototyping.
Develop an optimal cavity treatment recipe for high gradient operation and low sensitivity to residual magnetic field. Demonstrate the cavity performance in vertical testing. Utilize synergies as much as possible.
Develop HOM damping schemes as well as HOM coupler and FPC (Fundamental Power Coupler) designs per requirements based on the collective effects and beam dynamic studies.
Investigate cavity tuner technologies capable of providing the necessary tuning speeds and ranges with the required precision.
The designed cavities need to be integrated into a conceptual cryomodule design.

## Slide 24: R&D plan for the second 5 years
The following plan was presented to ESPPU:
Based on the concepts develop during the first 5 years, the full conceptual design of the RF systems for the linac and RCSs will be developed at this stage. This will include
  The designs of cryomodules for the cavities operating at different frequencies.
  RF power and cryogenic distribution, tunnel layout, etc.
Prototypes of the cavities and possibly cryomodules will be built and tested to verify the design concepts.
While the current baseline assumes an accelerating gradient of 30 MV/m, possible improvements in the SRF technology over the previous 5 years could enhance this value significantly.
  Consequently, the number of required cavities could be reduced, decreasing the complexity of the integration as well as the size of the cryogenic plant.
  Additionally, the overall power consumption of the RF system could possibly be reduced.
  Thus, an iteration on the overall SRF system design where appropriate might be necessary.

## Slide 25: Summary: R&D needs
Short-term R&D (PIP-II)
  FE prevention and mitigation (improving HPR, robot-assisted cleanroom assembly of cavity strings, in situ processing)
  AI/ML Resonance Control for narrowband SRF cavities
Medium-term R&D (ACE-MIRT, MC R&D)
  Low frequency tunable SRF cavities for proton synchrotrons
  Frequency tuners for such cavities
  Novel HOM damping schemes
  High-power (MW range) fundamental power couplers
  New, non-elliptical, SRF structures (88 MHz and 264 MHz) for the MC SC linac
  Further improvement of and
Long-term R&D (ACE-BR, MC Demonstrator)
  Developing alternative materials to bulk Nb, e.g., Nb/Cu, Nb3Sn
  More efficient magnetic shielding