## Slide 1
Conduction Cooled SRF Photogun for MeV Time-Resolved Electron Microscopy and Spectroscopy
Apply MeV beam to Ultrafast ED/EM/STEM/EELS can greatly reduce the challenges of the sample preparation, also suppresses the space charge effect at higher bunch charges
Stringent requirements on energy spread:
  UED: dE/E~10-4, σt~10s’ fs, < 106 electrons
  UEM: dE/E~10-6, σt ~ps-ns, >106 electrons (single shot or stroboscopic)
  USTEM: 100pm level focused beam size
  UEELS: <100meV level of energy spread
Current UED facilities are based on NC guns:
  Large facility + high power RF needed (expensive)
  Timing jitter 10~100fs
  Repetition is <1000 pps
Conduction cooled Nb3Sn SRF photo-gun:
  2W cryocooler is required ($80K, affordable)
  CW operation (high throughput)
  Smaller footprint, 10W RF power only

## Slide 2
Ultimate Goal
2
https://arxiv.org/pdf/2601.02597
CC-SRF enabling MeV HT-HB

## Slide 3
10 Year Roadmap
3
CC-SRF-MeV-UED
CC-SRF photogun with beam parameters qualified for UED applications.
Time jitter to the 10fs level
Pulse compressor working with CW beam
User beamline demonstrator
CC-SRF-MeV-UEM
Superconducting Objective Lens or PMQ Lens
Beamline optics with chromatic corrections.
User beamline demonstrating the beam parameters to achieve sub-nm spatial resolution and 100fs temporal resolution (STR< 10-23)
CC-SRF-MeV-STEM
Fast beam scanning
fs or sub fs Synchronization
MHz MeV Direct Electron Detector
User beamline demonstrating the beam parameters to achieve 100pm spatial resolution.
CC-SRF-MeV-EELS
MeV energy monochromator
User beamline demonstrating the beam parameters to achieve 100meV energy resolution.