## Slide 1
Proposals for Future Development of Technology for SRF Accelerators for
Scientivic and Industrial Applications.
Vyacheslav Yakovlev, Fermilab
February 5, 2026

## Slide 2
Proposals for Future Development of Technology for SRF Accelerators
Development of new concepts for accelerator components to expand the application area and parameter range of SRF cavities
a. New types of SRF cavities for emerging application areas
  Tunable SRF cavities for proton synchrotrons providing tuning range of up to 1% and strong HOM damping
  New compact SRF crab cavities (QMIR) for colliders and light sources.
b. New concepts for high-power couplers with low cryogenic load
  Improved “electromagnetic shielding” for cryo-loss reduction.
  New materials for high-power RF windows:
    Conductive ceramics to prevent electric charge accumulation and breakdown in ceramics. Such materials already exist and tested; however, optimization of their brazing technology is required.
    Investigation of new materials with thermal expansion coefficients close to those of ceramics and high thermal conductivity, such as Mo–Cu and W–Cu composites.
    Development of brazing-free RF windows, which would eliminate many technological challenges. These windows are currently used in the RFQ of PIP-II but require further development for application in SRF cavities.
c. New types of fast tuners for SRF cavities with a large tuning range
d. New HOM dampers for SRF cavities
Compact on-axis circular waveguide HOM dampers

## Slide 3
Development of new robotic technologies for SRF cavity and cryomodule (CM) assembly and processing
Establish a collaborative robotic (cobotic) platform for high-pressure rinsing and SRF cavity assembly.
Enable a future-proof, shape- and frequency-independent infrastructure adaptable to new SRF cavity concepts.
Continue develop a custom machine-vision system designed from scratch by SRF experts for cleanroom operation.
Embed SRF knowledge into system perception and control to support programmable, scalable workflows.
Accelerate transition from R&D to production and position Fermilab for next-generation SRF development.
Diagnostics of Field Emission in SRF Cryomodules
Detailed measurement of FE radiation field properties (spatial and energy distributions) as a mean to locate field emitters inside cryomodule' SRF cavities
Use Geant4 toolkit for Monte-Carlo simulation of propagation of radiation through materials of cryomodule components and accelerator enclosure
Use simulation data to optimize radiation detectors performance and placement
Train AI model to locate field emitters based on radiation measurement

## Slide 4
Artificial Intelligence (AI)/Machine Learning (ML) resonance-control (RC) algorithm
Goal: Create a new AI/ML resonance‑control (RC) algorithm to enable pulse‑RF operation of SRF linacs with low beam loading (PIP II).
Benefit: Operating in pulsed mode (low duty factor) cuts RF and cryogenic costs by millions of dollars per year.
Technical challenge: If SRF cavities have short pulses and narrow bandwidth, their resonance frequency is perturbed by stochastic vibrations and the Lorentz‑force detuning during each RF pulse, making fast, accurate control difficult.
Proposed solution: Develop an autonomous, Fast Adaptive Neural‑Control (FANC‑RC) system that uses neural‑network‑based control algorithms. Operates in real‑time on an FPGA platform. Learns continuously from streaming data and adapts to changing environmental conditions.