## Slide 1
GARD HEP RF Roadmap
RF Sources Subtopic
3 & 4 March 2026
Galen Aymar
John Moss
Ali Nassiri

## Slide 2: Key Motivations
What is the RF Source Subgroup trying to do?
1. Summarize existing rf sources
2. Highlight key technologies
3. Find approaches to higher-performing sources (efficiency, compactness, cost effectiveness, etc.)
4. Encourage collaboration and participation (accelerator facilities, industries, universities)
5. Identify key areas that require sustained R&D (priority-based)

## Slide 3: Summary of Subtopic Meeting
The RF Source subtopic agenda and speakers
Large Science Projects – Fulvia Pilat, ORNL
  Covered existing and future facilities to provide context
High Efficiency RF Sources – Chiara Marelli, CERN and Mohamed Othman, SLAC
  Discussed the status and future developments of HE vacuum electronic devices
Solid State Amplifiers – Doug Horan, ANL and John Lyles, LANL
  Described the latest developments in high power RF transistor technology – LDMOS and GaN
Modeling – Alexander Vlasov (NRL), Cho-Kuen Ng (SLAC)
  Described the latest effort in vacuum tube code development
Advanced Manufacturing – Julian Merrick, SLAC, Amy Elliot, ORNL and Paul Pritchard, ORNL
  Discussed the latest in advanced manufacturing techniques and their application to RF devices
Community Contributions:
  High Efficiency RF Source development at CCR – Lawrence Ives
  Needs for RF Sources at SACLA and SPring-8 – Takahiro Inagaki
  RF R&D at JLAB – Robert Rimmer
  ALBA RF Source Needs – Pol Solans Rossell
  Recent HPRF Efforts at FRIB – Shen ZHao

## Slide 5: Key Highlights from Subtopic Meeting
HE RF Sources
Vacuum electron devices dominate
  CERN recently redesigned the TH2167 klystron for higher efficiency (60 -> 70%)
  SLAC working on retrofit of 5045 to increase efficiency (45 -> 55%) and a retrofit of the 75XP4 using PPM to increase efficiency by 6%
  Work on new sources:
    Parallel efforts on 1.2 MW MB IOTs with efficiency of 70%
    1MW MBK with efficiency of 80%
    400kW MB Tristron – hybrid between a klystron and IOT with predicted efficiency > 80%
    100kW HE-IOT with efficiency > 80%
  Next step is 90%!
Tristron (A.D. Sushkov et. al. 1967)
HE-IOT
C. Marelli (CERN) and M. Othman (SLAC). Presented at the GARD RF Sources Subtopic Virtual Workshop 2026.

## Slide 6: Key Highlights from Subtopic Meeting
Solid State Amplifiers
Two primary transistor types – LDMOS and GaN
  LDMOS dominates installation < 500MHz
    Efficiency greater than 60%
    Low phase variation (~5 degrees from 10 – 90% of output power)
  GaN making inroads at higher frequencies – example is the 805MHz, 1.2MW SSA at LANL
    3.6kW peak on transistor test pallet
    5kWp chips are in test now
  Challenges
    Floor space – Comparable VEDs take up less real estate
    Heat dissipation/power density – making progress with new technologies like GaN on SiC (225 deg C)
    "Other" electronic components
    Power combining
    Workforce
GaN on SiC transistor under test – 3.6kWp
D. Horan (ANL) and J. Lyles (LANL). Presented at the GARD RF Sources Subtopic Virtual Workshop 2026.
160kW CW SSA at ANL

## Slide 7: Key Highlights from Subtopic Meeting
Modeling
Model codes are constantly updated to meet the latest goals in source development (HE, higher power, more compact, etc)
  Primary code types
    PIC (Neptune, MICHELLE)
    Hybrid/Parametric (CHRISTINE, TESLA, MAGY, ACE3P)
  Key Challenges
    Time scales, complex device geometry, complex beam dynamics
    Extending cooperation between DOE, DOW, US Industry
    Workforce
  Developments
    Parameterized optimization of RF source design
    Unstructured mesh, parallel simulation (multi-GPU, HPC) for PIC codes
    Multi-frequency, non-symmetric beam, beam tunnel variation, complex geometries for Hybrid codes
    Incorporation of AI
A. Vlasov (NRL) and C. Ng (SLAC). Presented at the GARD RF Sources Subtopic Virtual Workshop 2026.
NEPTUNE simulation of an MBK
75XP4 Klsytron Start-to-End Simulation in ACE3P

## Slide 8: Key Highlights from Subtopic Meeting
Manufacturing
Use of advanced manufacturing (AM) holds the potential to drastically reduce cost and time of RF source production
  Can be applied wholistically – think all RF system components, not just source
  Can pass to industry at MRL/TRL 5 – 6
  Can apply techniques to both SSA and VEDs
  Good for complex geometries
  Challenges
    "Vacuum facing" components – RF surfaces, porosity
    Thermal conductivity
    Field emission
    Inaccessible surfaces
J. Merrick (SLAC), A. Elliot (ORNL), and P. Pritchard (ORNL). Presented at the GARD RF Sources Subtopic Virtual Workshop 2026.
AI-designed, multi-material component fab'd with AM
Risk evaluation for AM applied to Klystron Fab

## Slide 9: Key Highlights from Subtopic Meeting
Community Contributions
The community is driving many of the advancements we see today on a variety of sources. Members are actively seeking collaborators to help meet their individual challenges.
L. Ives (CCR), T. Inagako (SPring8), R. Rimmer (JLab), P. Rossell (ALBA), S. Zhao (FRIB) Presented at the GARD RF Sources Subtopic Virtual Workshop 2026.
Multibeam Triode in development at CCR – estimated cost of $0.50/watt!
RF source developments at SPring-8 – seeking collaborators!
Magnetron work at JLab shows promise for ADS!
ALBA II: 4th Generation is on the way in Barcelona.
A variety of new RF sources in use/design at FRIB!

## Slide 10: Challenge Areas – Part 1
Here are the high-level points from the RF Source workshop:
Increasing RF source efficiency (VED and SSA)
  Critical for future facilities – EIC, FCC
  Create new (or revisit old) VED topology
  Continue to iterate transistor design for higher power density - don’t forget ancillary electronic components!
Develop common (suite of) RF sources
  Systematic tracking of new source developments versus needs, with a centralized database
  Combiner schemes to allow lowest common source to be scaled up for various uses
Reducing cost
  AM holds much potential, especially for VED fabrication
  Common RF sources between facilities
Keeping industry involved ( Active collaboration and participation)
  Pass technology along to industry at TRL > 5 – keep them actively involved from onset
  Include industry in technical workshops

## Slide 11: Challenge Areas – Part 2
A few more:
Funding necessary R&D developing/enhancing rf sources through separate channels
  Common "developments" (sources, manufacturing techniques, etc.) - the more facilities that benefit, the higher probability of funding?
Workforce
  "Centralized" training program – USPAS? CERN Accelerator School? - for both engineering and technical craft students
  Universities roles?
  Mentoring – is a "centralized" mentorship program viable?

## Slide 12: Milestones
Short term (1-3 years)
  Determine performance requirements for common RF sources (global)
    Form working groups with industry aligned along VED and SSA technology
    Include modeling and analysis
  Start "centralized" workforce development program
    Common curricula – CERN AS, USPAS? Universities?- for engineer/scientists and technicians
    Open to public and private participants
  "Proof of Concept" prototyping of high impact (expensive, long lead) RF components using AM
Medium term (3 – 5 years)
  Prototype VED with AM
  "Graduate" first class from workforce development program
  Prototype first common RF source from multiple manufacturers
Long term (> 5 years)
  Routine use of AM in RF components
  Routine fabrication of common RF sources
  Graduate 20 or more technical professionals from workforce development program per year

## Slide 13: Questions For Discussion
Let's start back at slide 10 and discuss the Challenge Areas and Milestones
Let's take the challenges one at a time. Is there more (or less) detail that needs to be captured?
Are there other challenges not captured that you believe are important?
Same for the milestones – are they adequate? What else might be a good addition (or subtraction)?