## Slide 1: DOE RF Roadmap Update
SRF Overview and Discussion
03/03/2026
Anne-Marie Valente-Feliciano & Matthias Liepe
Notes: Tip: Keep titles under 60 characters for readability
To change the photo: Right-click on photo and select change photo

## Slide 2: Outline
Introduction: The last decade for High Q/High G
Towards the Future: Virtual talks summaries
Challenge areas for the next decade
  SRF Foundation: Fundamental SRF Research
  The Last Mile: Advanced Processing for Pushing Bulk Nb to the Theoretical Max
  The Next SRF Materials Frontier: Beyond bulk Nb
  Fast-Tracking the Frontier: AI/ML for SRF
  SRF Technology & System Integration
Discussion

## Slide 3: INTRODUCTION: THE LAST DECADE

## Slide 4: DOE GARD RF Roadmap - circa 2017
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 5: Decadal roadmap and milestones for the high Q SRF frontier
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 6: Decadal roadmap and milestones for the high Gradient SRF frontier
Notes: Guidelines: 6-8 bullets per slide; Use sentence fragments for bullets

## Slide 7: TOWARDS THE FUTURE SRF Virtual Talks Summaries

## Slide 8: Virtual GARD SRF Roadmap Meeting: February 5
21 Invited Talks + 5 Community Contribution Talks
Facilities: SRF needs for the next decade
Niobium
SRF thin films
AI/ML for SRF R&D and Operations
SRF Technology
Community Talks

## Slide 9: Facilities: SRF R&D needs for PIP-II, FNAL complex, and a muon collider Speaker: Sergey Belomestnykh, FNAL
Key points / Summary:
PIP-II is in production mode. No on-project R&D is planned at this stage but 2 important general R&D topics to improve SRF linac performance (project & operations):
  Prevention & mitigation of field emission (FE) - Careful optimization of HPR for each cavity shape, robot assisted cleanroom assembly, in situ FE processing
  Resonance control (RC)
Fermilab Accelerator Complex
Accelerator Complex Evolution (ACE) - Main Injector Ramp and Targetry (MIRT) & Booster Replacement (BR)
Muon Collider
Presents many challenges :
Very high muon bunch intensity favoring larger cavity apertures thus lower RF frequencies;
Studies required for Beam loading in RCS chain due to cavities will distributed around the rings in several stations
High gradient operation of multi-cell lower frequency cavities must be demonstrated;
352 MHz frequency dictates Nb/Cu SRF technology – requires significant R&D efforts;
Mitigate Stray magnetic fields from high-field magnets to maintain SRF cavitis performance: develop efficient magnetic shielding and/or develop SRF cavities based on alternative superconductors;
Effect of high-intensity radiation from muon decays on the performance of SRF cavities is unknown
High peak RF power per cavity,mandates R&D on fundamental power couplers.

## Slide 10: Facilities: SRF R&D needs for PIP-II, FNAL complex, and a muon collider Speaker: Sergey Belomestnykh, FNAL
Recommendations:
Short-term R&D (PIP-II)
  FE prevention and mitigation (improving HPR, robot-assisted cleanroom assembly of cavity strings, in situ processing)
  AI/ML Resonance Control for narrowband SRF cavities
Medium-term R&D (ACE-MIRT, MC R&D)
  Low frequency tunable SRF cavities for proton synchrotrons
  Frequency tuners for such cavities
  Novel HOM damping schemes
  High-power (MW range) fundamental power couplers
  New, non-elliptical, SRF structures (88 MHz and 264 MHz) for the MC SC linac
  Further improvement of and
Long-term R&D (ACE-BR, MC Demonstrator)
  Developing alternative materials to bulk Nb, e.g., Nb/Cu, Nb3Sn
  More efficient magnetic shielding

## Slide 11: Facilities: EIC-ee SRF R&D needs Speaker: Zack Conway, JLab
Key points / Summary:
High Luminosity
Deliver 800 kW of power via 2-4.5 K SRF cavities
Beamline components strongly interacting with the beams
  RF shielded bellows
  Broadband absorbers
Crab cavity designs : fit limited space of EIC
Recommendations:
  Cavities
  FPCs
  Solid State Amplifiers
  LLRF
Low-loss, low-R/Q, heavily damped systems
Clean Assembly
High RF power generation: efficiency, and fidelity
New SRF materials and designs if they can operate at high power and fields
Broadband HOM damping
  New materials :Controllable/predictable properties ,commercial availability
  Alternative methods
Crab cavity design
LLRF systems capable of operating with beyond state-of-the-art amplitude and phase noise across many MHz of bandwidth.
Project R&D is limited. Requires great foresight in R&D.
Stable high power RF sources
LLRF techniques for ultra-low noise systems
Cavity structures
  Crab cavities
  Alternative materials enabling high power with low RF losses
  Coupler outer conductors

## Slide 12: Facilities: SRF R&D for ion accelerators Speaker: Mike Kelly, ANL
Key points / Summary:
New technology for cost effectiveion linacs applications (ATLAS upgrades…)
  Nb3Sn
Proton and heavy-ion facilities for science: ATLAS, (PIP-II, FRIB, EIC?)
  Our 10-year strategic plan for a high intensity ATLAS upgrade using all modern SRF structures probably only possible with cost reductions enabled by Nb3Sn
Accelerator Driven Systems (ADS): 600 MeV to 1 GeV proton accelerators for waste transmutation, neutrons for nuclear engineering studies, energy production Cost based on Nb >$2B, drastic reduction with Nb3Sn?…
Isotopes for medicine : Dedicated dual 40 MV electron and light-ion SRF linacs
Low intensity heavy-ion linacs: post accelerator for RIB’s, Single Event Effect facility :Candidates for higher frequency (small aperture) SRF structures
Recommendations:
Study degradation in SRF cavities from ion beams exposure (Nb samples or cavities )
2 years New diagnostics supporting Nb3Sn coating / e.g. “coating monitor concept (FNAL)” could be used broadly to study and compare coatings on different cavities and from different facilities
2-3 years : Lattice/beam physics/cavity EM design/preliminary layout studies for future ‘green field’ proton and heavy-ion linacs that make best use of Nb3Sn , include higher frequencies and potentially different β ranges than existing structures (Examples with cross cutting interest: a 10 MeV/u heavy-ion linac; a 1 GeV proton linac)
3-5 years :Development and demonstration of new Nb3Sn SRF structures for ions -Protons and heavy ion linacs from Nb3Sn will likely use similar cavities even if the overall linac designs differ

## Slide 13: Facilities: FCC-ee SRF R&D needs Speaker: Frank Gerigk, CERN
Key points / Summary:
400 MHz 2-cell cavities Nb/Cu & 800 MHz 6-cell bulk Nb cavities
400 MHz & 800 MHz
    RF power & HOM couplers
    prototype CM
    High-efficiency power source
      Z-power sources: ~500 kW for 400 MHz, and ~50 kW for 800 MHz.
      Ttbar power sources: ~90 kW for 400 MHz, ~250 kW for 800 MHz.
    High-power infrastructure for coupler and system test
66 400 MHz CMs for the start of the Z.
28 800 MHz CNs for Z, + 84 CM for ttbar.
Recommendations:
400 MHz – Push Nb/Cu technology: Nb HiPIMS film deposition, seamless substrate, electropolishing
800 MHz- Define recipe to reach ultra-high quality factor Q0 with the FCC design shape.
      New materials like Nb3Sn
Priorities :
High-Q at moderate gradients
High-efficiency RF sources (+resonant rings), and the needed development for couplers and cryomodules towards TRL6 level.

## Slide 14: Facilities: SRF accelerators for industrial application , Speaker: Sergey Kutsaev SRF R&D needs for lithography and US manufacturing ecosystem development, Speaker: Bruce Duhnam
Key points / Summary:
xLight
Emerging applications requiring cost-efficient high-power electron accelerators:
⎼ Environmental applications. 5-10 MeV 100-1000 kW beams can used to kill pathogens or destroy chemicals in food, water, flu gases etc.
⎼ Accelerator Driven Systems. 50-150 MeV 1MW beams can be used to generate neutron flux in
modular sub-critical reactors or radioisotope production.
⎼ EUV lithography. GeV electron beams can be used to generate nm-wave EUV light for chip fabrication.
⎼ Ultrafast Electron Microscopy. SRF guns can generate c.w. high-brightness MeV beams for high-
resolution imaging.
Technological (& commercial) challenges
⎼ New materials (Nb3Sn) reduce the losses by an order of magnitude
⎼ Compact Liquid-He-free cryocoolers with high power capacity (2-10 W)
⎼ Low-loss cryomodules based on conduction cooling
⎼ RF power sources (magnetrons, solid-state) with high efficiency (>50%) and low cost per Watt (<$3-7/W)
⎼ Reliability and serviceability
⎼ Fabrication
⎼ Beam loss management
Very few Nb cavity vendors, long lead time
Nb3Sn coating is a very complex and delicate process
Vendor hesitation to step into SRF business
(high initial investments, unstable demand, unflexible infrastructure)
Recommendations:
Mandatory
- Demonstration of high-power operation, reliability, robustness and real costs
⎼ Beam injection / extraction systems development
Wish list
⎼ Higher-efficiency / lower-price cryocoolers to enable lower power applications
⎼ Solid-state RF amplifiers with 70% <$3/W costs, or magnetron combination to MW level
Future
⎼ Technology transfer and mass-production of SRF cavities

## Slide 15: Niobium: Nb treatments for high performance : Potential and future R&D Speaker: Daniel Bafia, FNAL
Key points / Summary:
Near-surface engineering is a major performance knob
  Impurities, and interfaces clearly govern Q0 and gradient in Nb SRF cavities
Coupling RF measurements with materials science transformed the field
Thermal diffusion has delivered major gains
  Easily accessible, but constrained by diffusion lengths and imperfect interface control
Recommendations:
The next decade is not about finding the next new bake; it’s about deterministic engineering over the surface => opens a new design space
Fundamental research with materials science needed to develop a holistic understanding of all loss mechanisms
Explore new engineering controls: CVD/ALD enables encapsulation, multilayers, high-k superconductors, and new doping schemes
Co-doping with different impurities is a promising path forward for standard thermal diffusion

## Slide 16
Area | 5 Year Milestone | 10 Year Milestone
Materials Characterization | Demonstrate controlled co-doping using impurity-dependent diffusion lengths without CVD/ALD Explore feasibility of multilayer material growth | Establish predictive link between impurity profiles, microstructure, and RF loss mechanisms
Mechanistic understanding | Identify dominant RF loss mechanisms and relevant timescales | Establish a full, quantitative loss budget for RF losses in various SRF systems
Cavity Demonstration | Demonstrate Q = 4 x 1010 at 45 MV/m using co-doping and/or encapsulation | Demonstrate Q₀ ≈ 5×10¹⁰ at ~50 MV/m via encapsulation + impurity co-doping / tailoring Demonstrate predictive treatment design (“ask-and-receive”) based on materials-informed RF models
Together, these milestones transition SRF development from empirical optimization to predictive, materials-informed design.

## Slide 17: Niobium: Engineered Nb surfaces: Potential and future R&D directions Speaker: Marc Wenskat, DESY
Key points / Summary:
Surface passivation / encapsulation:
  Native oxide impacts RF performance
Superconducting thin films (d ≈ λL)
  Several RF/DC measurements on samples show that individual pieces of the puzzle are correct
  Proof-of-principle with an SRF cavity still pending
Recommendations:
For SRF the interplay between oxide properties and consequences of removing it should be studied => “Optimal” material for encapsulation? Oxides? Which one?
Theory development needed: (SI)N S , roughness/transition …
Show that it works!

## Slide 18: Niobium: Reducing residual resistance at operating fields Speaker: Pashupati Dhakal, TJNAF
Key points / Summary:
High Q0 cavities are very sensitive to trapped magnetic flux during cooldown, often mask the benefit of high Q0
Main source of residual surface resistance at operating field is due to residual flux trapping during cool down
Recommendations:
Develop new mitigation strategies

## Slide 19: Nb3Sn & Thin Films: Nb3Sn by vapor diffusion Speaker: Uttar Pudasaini, JLab
Key points / Summary:
Improve Performance through Process Optimization
Post-processing Technique development
Q-slope and quench due to material imperfections or surface defects
identify, understand, and eliminate defects towards a reproducible process

## Slide 20: Nb3Sn & Thin Films: Nb3Sn by vapor diffusion Speaker: Uttar Pudasaini, JLab
Recommendations:
Elucidate Nb₃Sn growth mechanisms in vapor diffusion coatings as a function of process parameters
  Given the large parameter space, AI-assisted optimization could be attractive
Correlate material properties with RF performance to optimize coating parameters
Develop a feedback-driven coating growth model adaptable to arbitrary cavity geometries
Develop post-processing techniques for surface topography management
Study grain boundary structures and composition
Broadened, coordinated R&D efforts and resources to fullfill Nb3Sn potential

## Slide 21: Nb3Sn & Thin Films: Alternative SRF materials Speaker: Nathan Sitaraman, Cornell University
Key points / Summary:
Several candidate materials beyond Nb3Sn: Nb-Zr Alloy, NbTiN, A15 compounds (Nb3Al…), MgB2…
Each have their own set of advantages and drawbacks, none is ideal. Fundamental R&D is still necessary to really assess their potential
    High Tc: Easy
    High Q at low fields: Easy(ish)
    Minimizing defect concentration: Hard
      Took decades of R&D for Nb, Nb3Sn to perfect this and minimize residual resistance
    Complete elimination of defects: Impossible!
      On cavity scale, there will *always* be a nonzero number of nanoscale (~10nm+) defects
    R&D efforts very productive toward minimizing defect concentration
Recommendations:
Focus on systems with potential to tolerate some defects at high fields
      Thin layers necessary!
      Low-loss interface with Nb substrate (and/or barrier layer) necessary!
Evaluate the potential in pulsed conditions also

## Slide 22: Nb3Sn & Thin Films: Thin-film growth of SRF materials Speaker: Cristian Pira, INFN
Key points / Summary:
Thin Film approach enables a broad portfolio of solutions, no one-size-fits-all solution,
  Cavity cost reduction (Nb on Cu)
  High Q / High T operation (Nb3Sn)
  High Gradient (SIS)
TProcesses needs to be tailored to the final goals,
Film(s)-substrate system dictates thermal budget, growth technique choice (Hybrid approach)
Substrate quality & preparation are paramount
Nb on Cu by PVD is a mature technology for cost reduction approach, especially for low frequencies  Emergetic Condnsation with HiPIMS seems to be the right way to increase the usable gradient
Nb3Sn is by far the most promising material beyond Nb  Various technologies are being developed for 4K operations with Nb substrates  PVD approach looks very promising for Nb3Sn on Cu. 1st results on elliptical cavities expected soon
Recommendations:
Developments of thin iflm based SRF at different levels of maturity, technologies mor complex than bulk Nb, require significant investments (fundamental developments, coating systems, characterization….)
Tailor development to the film/substrate system and to fit the goals Cleanroom assembly and handling are a must
Engaging industries early in the developments to industrialize the thin-film process
Functionalization of the materials
The beginning of a technological revolution for SRF!

## Slide 23: Nb3Sn & Thin Films: Practical implications of new materials Speaker: Grigory Eremeev, FNAL
Key points / Summary:
Nb3Sn technology has advanced from R&D to practical accelerator applications with several coating facilities world-wide producing Nb3Sn with performance level suitable for accelerator applications
Further understanding via careful designs and use of analytical tools is key to realizing Nb3Sn high field potential
Current developments to improve performance and enable practical implementations :post-processing, mechanical strength, contamination (ex. Ti, Si), tuning sensitivity, handling for CM assembly,
Recommendations:
Tailor developments to the materials taking into account the bi-metallic nature of the system (Nb3Sn/Nb)
Near-term (5yrs) First Nb3Sn user facility First Nb3Sn industrial demonstrators | Mid-term (10 yrs) Nb3Sn as the technology of choice for SRF accelerators Large scale operation of Nb3Sn industrial accelerators

## Slide 24: Nb3Sn & Thin Films: SRF theory: Ideal surfaces and future R&D directions Speaker: Alexander Gurevich, ODU
Key points / Summary:
Switch from the MB model to the Eliashberg theory which describes realistic superconductors with strong e-p pairing (Nb, Nb3Sn, NbN etc)
Enigma of quasiparticle subgap states which define the ultimate Q limit at T<<Tc (SRF cavities and qubits). Many possible mechanisms (TLS, correlated impurities, strong e-p coupling, etc).
Field dependent Q(H) at high rf fields: Pandora box of nonequilibrium superconductivity and complex kinetics of superconductors under strong RF fields. e-p and e-e relaxation times and their strong dependencies on T and rf field
Extended Q(H) rise, the effect of nonequilibrium kinetics of quasiparticles or two-level states
Ultimate breakdown of superconductivity - the physics of dynamic superheating field at GHz frequencies at low T
Extreme dynamics of superfast tips of trapped vortices at the SRF depairing limit. Effect of trapped flux on the high-field Q slope
The exact SRF performance limits are currently unknown
Recommendations:
SRF performance both at low and high RF fields can be improved by impurity management and surface nanostructuring, even if we do not know what the limits are.
Filling the knowledge gaps requires developing the Eliashberg + nonequilibrium theories of SRF limits in conjunction with advanced computational modeling.
Enable understanding for
Mechanisms of residual resistance, subgap states, TLS
Theoretical Q and H limits for key SRF players (Nb and Nb3Sn)
Theory of nonequilibrium superconductivity which describes Q(H) at high rf fields
Extreme dynamics of trapped vortices driven by rf fields in SRF cavities

## Slide 25: AI/ML for SRF: Frameworks for material development using AI/ML Speaker: Richard Hennig, U. of Florida
Key points / Summary:
Accelerate the discovery & design of
SRF materials
  Generative AI — new superconductors
  Property ML — screening + design
  ML potentials — synthesis + defects
Recommendations:
AI/ML to make SRF materials development predictive, not empirical, and couple it to validated performance.
Near-Term (1-2 yrs)
Build the framework with open SRF-relevant datasets, benchmarks with SRF metrics, build a “materials model card” standard(domain of validity + uncertainty reporting), use validation loop (synthesize + characterize with small, diverse test set)
Mid-Term (5 yrs)
Build tools for Inverse design, multiscale “digital twin” to push limits of materials and predict defects influence on performance, improve Nb3Sn processes
Transfer to new coatings / multilayers as SRF materials mature

## Slide 26: AI/ML for SRF: Future directions for SRF accelerator operation Speaker: Christopher Tennant, TJNAF
Key points / Summary:
AI/ML already demonstrates its value for SRF operations – fault classification, prediction, optimization, anomaly detection …-successful proof-of-concept projects
Today’s Genesis Mission = inflection point
  within MOAT, collaboration on a single project across accelerator user facilities from multiple offices of the Office of Science– across– remarkable progress in ~3 months
  Agentic AI is a game changer, shifting from AI-assisted to AI-augmented
Recommendations:
AI-assisted (now): humans drive; AI accelerates analysis, suggests actions, and reduces “time-to-answer”  anomaly detection, offline optimization
AI-augmented (next): AI executes multi-step workflows under explicit oversight (plan-first, approvals, safe write boundaries)  Osprey-style agents
AI-autonomous (future): AI can run routine operations end-to-end, but only inside strict safety, interlock, and policy boundaries  “autopilot”

## Slide 27: SRF Technology: In-situ processing of SRF cavities in cryomodules Speaker: Bianca Giaccone, FNAL
Key points / Summary:
Field emission has been observed to degrade over time in SRF machines
In-situ techniques can allow to mitigate FE and MP without requiring CM disassembly
In-situ techniques are not (yet?) effective on all types of contamination
Plasma processing, helium RF processing, and ozone processing have been applied successfully
Recommendations:
Develop clear understanding of complementarity and applicability of the three in-situ techniques
Short Term R&D:
  Optimize recipes and demonstrate, when needed, applicability to full sized CMs
Mid/Long Term R&D:
  Gain better fundamental understanding of the physical phenomena and diagnostic techniques
  Deploy ozone treatment as a safe and simple technique to address hydrocarbon-induced FE and MP in CMs
  Extend plasma processing applicability beyond hydrocarbon contamination
Long Term Goal:
  Techniques that can be deployed on CMs in-situ as needed to recover performance affected by FE and/or MP

## Slide 28: SRF Technology: New cavity shapes and types Speaker: Kellen McGee, FNAL
Key points / Summary:
Nb structure optimizations can deliver immediate performance benefit to next generation machines
Novel SRF structures are enabling technologies for:
  High gradient devices: linear higgs factories, compact devices
  Next-generation SRF for RCS to reduce beam impedance/instabilities
Improved facility efficiency and flexibility is a key component of accelerator stewardship, expanding experimental reach
Recommendations:
Consistent R&D to ensure these options are well developed for adoption by future projects
Tunable cavity proof-of-principle must be demonstrated in a timely manner to become a viable candidate for ACE-MIRT
Tunable SRF cavity for RCSs
Travelling wave cavity
QMiR Cavity for EIC

## Slide 29: SRF Technology: Cavity fabrication, cost reduction, vendor development Speaker: Gigi Ciovati, JLab
Key points / Summary:
Whereas innovations in material and fabrication methods have been successfully demonstrated, the ~40-year-old conventional methods are still the standard ones used for SRF cavity productions.
Recent developments focus on additive manufacturing.
Recent start-up of private companies aiming at producing large-scale SRF linacs provide a unique opportunity to drive innovation and foster a closer collaboration between public and private sector.
Recommendations:
Strategic investments and programmatic decisions by the public sector are needed to realize the potential of this opportunity.
Establish a “National SRF Consortium” with members from Labs and Universities with SRF expertise.
An industrial “third space” should be created where national laboratories and industry can effectively and efficiently collaborate on SRF R&D projects.

## Slide 30: SRF Technology: Clean cavity preparation and assembly Speaker: Ganfa Wu, FNAL
Key points / Summary:
Robotic-assisted clean assembly: Reduced potential cavity contamination risk, improved assembly ergonomics, and improved efficiency
Cavity string design needs optimization (paradigm shift) for the AI Robotic future for cryomodule gradients >40 MV/m
Recommendations:
If sufficiently supported, the future could be very “clean and FE-free”.
  In 5 years, a robotic assembly with many improvements to the current cryomodule design
  In 10-15 years, a new type of cryomodule design that is robotically compatible and achieves high yield, high performance

## Slide 31: SRF Technology: SRF ecosystem: Cavity fabrication, preparation, and test facility needs for the US Speaker: Martina Martinello, SLAC
Key points / Summary:
The U.S. SRF ecosystem is technically strong but structurally capacity-limited => SRF technology readiness is no longer the limiting factor
High Impact R&D actively reshape facility needs
There is no single U.S. company that provides end-to-end cavity production
Future SRF programs will be infrastructure-limited unless facility capacity and workforce pipelines evolve now.
Recommendations:
Transition from project-driven infrastructure → programmatic national capacity
Expand processing and cold-test throughput with redundancy
Strengthen domestic industry integration
Integrate workforce pipelines across labs, universities, and industry

## Slide 33: Community Contributions
Key points / Summary:
Ferroelectric Fast Reactive Tuners can provide ultra-fast frequency adjustment without mechanical motion
High Temp Superconductors (HTS) present the possibility of lower loss cavities at LN temperatures for some applications
Conduction cooled Nb3Sn SRF photo-gun prototype recently tested
Q₀ improvement directly reduces cryocooler count and system cost for conduction cooled Nb₃Sn-coated SRF cryomodules
Other SRF technology needs include new concepts for high-power couplers with low cryogenic load, new types of fast tuners for SRF cavities with a large tuning range, new HOM dampers for SRF cavities, diagnostics of field emission in SRF cryomodules, and AI/ML cavity resonance-control algorithm

## Slide 34: CHALLENGE AREAS FOR THE NEXT DECADE

## Slide 35: SRF Foundation: Fundamental SRF Research ​
Area definition: Advance fundamental SRF science using theory and experiment, aiming at a holistic understanding of RF dissipation, loss mechanisms, and ultimate limits to Q0 and gradients.
Motivation: SRF materials research is evolving from an empirical optimization to predictive, materials and knowledge informed design. Continuing this paradigm-shift will enable SRF materials by design, opening new design spaces for highest-performance surfaces.
Synergies: Fundamental SRF knowledge is the foundation for materials development for any future SRF driven accelerator for science and industry as well as for quantum and digital logic materials.

## Slide 36: SRF Foundation: Fundamental SRF Research ​
Milestones
  Short to medium term
    Develop the Eliashberg + nonequilibrium theories of SRF limits in conjunction with advanced computational modeling
    Probe RF field limits in long and ultra-short pulse operation on samples with bulk and layered (nanostructured) surfaces
    Identify dominant RF loss mechanisms and relevant timescales
    Explore new engineering growth controls including CVD/ALD, enabling encapsulation, multilayers, high-kappa superconductors, and new doping schemes
  Medium to long term
    Understand mechanisms of residual resistance, subgap states, TLS losses
    Advance theory of nonequilibrium superconductivity: Q(H) at high RF fields
    Predict theoretical Q and H limits for key SRF players (Nb and Nb3Sn)
    Establish predictive link between impurity profiles, microstructure, and RF loss mechanisms
    Define & demonstrate full growth control for engineering surfaces – functionalization of materials

## Slide 37: The Last Mile: Advanced Processing for Pushing Bulk Nb to the Theoretical Max ​
Area definition: Guided by fundamental SRF knowledge, and using new engineering controls for materials growth, develop optimized Nb-based surfaces that enhance performance, approaching theoretical limits (currently unknown).
Motivation: Bulk Nb is one of the baseline material for the next SRF-based frontier collider (e.g., FCC-ee). Feasibility (cost and energy consumption) of such a machine requires significantly increased Q0 at medium to high fields (25 – 50 MV/m).
Synergies: SRF-driven accelerators for science and industry mostly will remain Nb-based short to medium term. Any advances in Nb SRF performance will have broad and enabling benefits to these applications of SRF technology.

## Slide 38: The Last Mile: Advanced Processing for Pushing Bulk Nb to the Theoretical Max ​
Milestones
  Short to medium term
    Reduce residual resistance at medium to high operating field by developing techniques and materials that minimize flux trapping and reducing sensitivity to trapped magnetic flux.
    Develop optimized oxide passivation / capping layers
    Demonstrate controlled co-doping with multiple impurities via heat treatments
    Goal: Demonstrate Q = 4 x 1010 at 40 MV/m (2K, 1.3 GHz)
  Medium to long term
    Develop optimized capping / multi layers on Nb and demonstrate enhanced performance (Q0 and/or gradient)
    Develop controlled growth methods for tailored impurity concentrations for engineered Nb-based surfaces
    Demonstrate predictive “surface/treatment by design”, leading to tailed performance
    Goal: Demonstrate Q > 5 x 1010 at 50 MV/m (2K, 1.3 GHz)

## Slide 39: The next SRF materials frontier: Beyond bulk Nb
Area definition: Develop thin-film based SRF technologies tailored (film-substrate system, growth techniques…) to specific goals
        Advance the efficiency frontier: Focus on Nb3Sn, but also evaluate other higher-Tc materials
        Advance the gradient frontier: Surfaces by design
        Develop the copper backbone: High-performance thin-films on cost-effective substrates
Motivation: Nb/Cu is fundamental for the next SRF-based frontier collider (e.g., FCC-ee, Muon Collider). Feasibility (cost and energy consumption) of such a machine requires significantly increased Q0 at medium to high fields. Feasibility of Nb3Sn/Cu would be a paradigm shift for large instruments and industrial machines.
Synergies: Strong synergies, film-based SRF technology is the envisioned enabler of the future for accelerators for science and industry as well as for quantum and digital logic materials.

## Slide 40: The next SRF materials frontier: Beyond bulk Nb
Milestones
  Short to medium term
    Establish Nb film baseline @ 1.3 GHz (2 K) & @ 800- 400MHz (4.2 K)
    Demonstrate Q Nb/Cu= 4 x 1010 at 30 MV/m (2 K, 1.3 GHz) and Q Nb/Cu > 2x109 at 15 MV/m (4.5 K, 400-800 MHz)
    Further develop Nb3Sn/Nb and Nb3Sn/Cu technology and establish baseline performance
    Demonstrate Eacc Nb3Sn> 15 MV/m with Q0 > 4x1010 at 0.8 - 1.3 GHz, 4.5 K
    Demonstrate Eacc Nb3Sn> 25 MV/m with Q0 > 2x1010 at 0.8 - 1.3 GHz, 4.5 K
    Demonstrate cavity operation in short pulse mode with Eacc > 50 MV/m
    Nb3Sn studies for cryomodule operation
    Turn-key Nb3Sn cryomodule technology (Industry transfer)
    Evaluate potential of alternative film materials and SIS structures first on samples, then on cavities (depending on development maturity) – Develop tailored growth techniques (PVD/EC, CVD, ALD, electrodeposition, hybrid…)
    Reduce sensitivity to magnetic flux for new materials
    Develop adequate Cu substrate and processes for reproducible and reliable film deposition

## Slide 41: The next SRF materials frontier: Beyond bulk Nb
Milestones
  Medium to long term
    Develop Nb /Cu multi-cell cavities at low frequencies
    Deploy SIS structures on Nb & Nb/Cu with 30–50% Eacc increase and a factor of two in Q0
    Deploy Nb3Sn/Nb and Nb3Sn/Cu technology to multi-cell cavities and integrate in cryomodules
    Demonstrate EaccNb3Sn > 20 MV/m with Q0 > 3x1010 at 800 MHz, 4.5 K
    Integrate Nb, Nb3Sn, other materials, SIS in common deposition
    Potential for Eacc > 20 MV/m with Q0 > 6x1010 at 800 MHz, 4.5 K
    Potential for Eacc = 50 MV/m to 100 MV/m operation

## Slide 42: Fast-Tracking the SRF Frontier: AI/ML for SRF
Area definition: Develop frameworks for predictive SRF materials coupled to validated performance and for “autonomous” optimized accelerator systems .
Motivation: Fast-track SRF material developments and provide a framework for machine operation with reliable and stable operation; AI-autonomous industrial accelerator system to steer away from expert-operation.
Synergies: AI/ML has a role to play in every aspects of SRF technology from material developments (bulk Nb, SRF films, defects…) to machine operation.

## Slide 43: Fast-Tracking the SRF Frontier: AI/ML for SRF
Milestones
  Short to medium term
    Build the framework with open SRF-relevant datasets, benchmarks with SRF metrics, build a “materials model card” standard (domain of validity + uncertainty reporting), use validation loop (synthesize + characterize with small, diverse test set)
    Develop AI executed multi-step workflows under explicit oversight (plan-first, approvals, safe write boundaries)
    Establish a foundation for AI policy boundaries
  Medium to long term
    Build tools for Inverse design, multiscale “digital twin” to push limits of materials and predict defects influence on performance, improve Nb3Sn processes
    Transfer to new coatings / multilayers as SRF materials mature
    Build AI-autonomous platform where AI can run routine operations end-to-end in autopilot, inside strict safety, interlock, and policy boundaries

## Slide 44: SRF Technology & System Integration
Area definition: Develop cavity designs, auxiliary systems, technologies, and processes needed for reducing cost and for achieving, maintaining, and recovering high SRF cavity performance in HEP accelerators.
Motivation: Future SRF-driven accelerators for HEP require SRF cavity and auxiliary systems (e.g., RF couplers, HOM dampers, frequency control) performance well above the current state of the art, reliably and at a reduced cost.
Synergies: Strong synergies with SRF technology needs for future high-current accelerators (e.g., EIC), future high Q0 / high QL SRF accelerators (e.g., SRF linac based light sources, industrial SRF linacs), SRF for synchrotrons etc.

## Slide 45: SRF Technology & System Integration
Milestones
  Short to medium term
    Integrated workforce development across universities, labs, and industry
    Fast, large tuning-range SRF cavity for RCS (>5 MHz/s tuning rate)
    AI/ML cavity resonance-control for high QL cavity operation (pulsed and CW)
    Robotic assisted clean assembly of SRF beam lines
    Continue exploration of alternative, lower cost SRF cavity fabrication techniques
    Low cost, high-power RF couplers and HOM dampers for high-power, high current operation
    Launch of SRF facility strategy
  Medium to long term
    Integrated workforce development across universities, labs, and industry
    Techniques that can be deployed in-situ to recover performance affected by FE or MP
    Expanded shared SRF facilities with strengthen domestic industry integration.
    Continued development of novel SRF cavity concepts and geometries
    Cryomodule designs that are optimized to be robotically compatible and achieve high yield