## Slide 1: PixESL at MAPS 2026
Francesco E. Brambilla
SLAC, Stanford, USA
27-4 Jul-Aug 2026
francesco.enrico.brambilla@cern.ch

## Slide 2: Introduction
Overview
ESL design
Electronic design flow
PixESL in simulation flow

## Slide 3: Overview
CERN
  The world’s largest laboratory in particle physics
  LHC is a 27km-long circular particle accelerator in Geneva, Switzerland.
  4 main experiments to investigate particles produced by collisions in the accelerator.
  Site of the discovery of the Higgs boson particle in 2012
  Pioneered the World Wide Web in 1989
Notes: Add DVCON paper link?

## Slide 4: Overview – Pixel detectors
Pixel detectors measure the position and charge of the particle interactions
Various types:
  Charge-coupled devices: charge is collected on pixels and then shifted to the periphery.
  Monolithic Active Pixel Sensors: per-pixel amplification and measurement.
  Hybrid detectors: sensing substrate bonded to readout chip.
MAPS
CCD
Hybrid

## Slide 5: Overview – Detector Specifications & Prototyping
The latest generations of pixel detectors push towards higher performance in:
  Pixel pitch and count, sustainable particle rate, charge and timestamping resolution…
The performance targets are defined by the physics applications:
  How can we draw a set of specifications matching that performance?
  How do we validate those specifications against the application?
Electronic System-Level (ESL) modeling can guide us to write an abstract model of the detector to prototype and study its performance in the early design phase.

## Slide 6: Overview - PixESL
Project
  PixESL: Pixel detector virtual Electronic System-Level prototyping framework
  GitLab repositories: PixESL core & PixESL4school
Context
  EP R&D Programme on Technologies for Future Experiments: IC Technology Work-Package (WP5)
  Used to prototype MAPS and hybrids detectors at CERN.
Publications
  [2024] Paper: Virtual Prototyping Framework for Pixel Detector Electronics in High Energy Physics
  [2024] Paper: SystemC framework for architecture modelling of electronic systems in future particle detectors
Notes: Add DVCON paper link?

## Slide 7: Electronic System Level – ESL design
ESL is a methodology for modelling and simulating complex electronic systems.
Key points:
Abstraction
System-level perspective
Simulation and analysis
Design space exploration
Validation
PixESL
Pixel detectors virtual Electronic System-Level prototyping framework
Notes: We want to build a framework called PixESL to introduce the Electronic System Level design for the first time in the High Energy Physics environment.
ESL is a design methodology which proposes a higher level of abstraction to see the design from a system-system perspective through models. And this allows faster design analysis and design space exploration.
The idea is to include all these key point in a single framework.

## Slide 8: Electronics design flow
guidelines
limitations
Time-consuming
(~years)
NO structured feedback
Physics simulation
Specifications
Hardware design
Verification
Time-consuming
(~years)
Notes: Why are we introducing this problem? Because across time we noticed that going from specs to hardware design takes a lot of time and there is no structured feedback… and you have to do it through meetings/presentations between physicists and engineers.

## Slide 9: Electronics design flow with ESL prototype
guidelines
limitations
ref. model
ASIC limits
guidelines
limitations
Reference model
Specifications
Physics simulation
Hardware design
Verification
PixESL framework
Virtual prototype
Notes: So, with the PixESL framework we are proposing to add the ESL design as an additional step.
PixESL is a framework where you design the virtual prototype to describe an electronic system, and it allows for both validation and verification
In this way the flow is split into two phases: the validation of the specifications with a faster turn around time;
And a verification part which profits from the virtual prototype using it as a reference model, and also this one shows a faster turn around time.

## Slide 10: Electronics design flow with ESL prototype - Validation
guidelines
limitations
ref. model
Physics simulation
Hardware design
Verification
PixESL framework
Virtual prototype
ASIC limits
guidelines
limitations
Fast (~months)
Reference model
for physical simulation
Validation
Specifications
Physics simulation
PixESL framework
Virtual prototype
Notes: So, with the PixESL framework we are proposing to add the ESL design as an additional step.
PixESL is a framework where you design the virtual prototype to describe an electronic system, and it allows for both validation and verification
In this way the flow is split into two phases: the validation of the specifications with a faster turn around time;
And a verification part which profits from the virtual prototype using it as a reference model, and also this one shows a faster turn around time.

## Slide 11: Electronics design flow with ESL prototype - Verification
guidelines
limitations
ref. model
Reference model
for verification
Verification
Physics simulation
Hardware design
Verification
PixESL framework
Virtual prototype
ASIC limits
guidelines
limitations
Specifications
Physics simulation
PixESL framework
Virtual prototype
Notes: So, with the PixESL framework we are proposing to add the ESL design as an additional step.
PixESL is a framework where you design the virtual prototype to describe an electronic system, and it allows for both validation and verification
In this way the flow is split into two phases: the validation of the specifications with a faster turn around time;
And a verification part which profits from the virtual prototype using it as a reference model, and also this one shows a faster turn around time.

## Slide 12: PixESL in simulation flow
TCAD focuses on simulating the detailed structure and fabrication of semiconductor sensor devices
Allpix² focuses on simulating the physical processes in silicon detectors
PixESL focuses on modelling the behaviour of pixel detector circuits
Simulation flow
Particle-sensor interaction
Chip output
Sensor
design
Charge deposition + collection (+ digitization)
Front-end architecture +
Readout architecture +
Post-processing
PixESL

## Slide 13: PixESL framework
Virtual Prototyping
Modeling Methodology
Front-End model
Readout model
PixESL in a nutshell

## Slide 14: PixESL – Virtual Prototyping
PixESL applies the Electronic System Level concepts to pixel detectors design flow for a cycle-accurate simulation from analog front-end to chip/system readout.
faster runtime (~70k transactions/s)
compared to RTL simulation (x50)
Charge, ToA, position, …
Digital packets
Pixel matrix | 4x4
Pixel node | 2x2
Readout node | 2x2
Periphery node | 2x1
Data aggregator | 1x1
Notes: PixESL is a framework where you design the virtual prototype to describe an electronic system.
Having the complete view of the electronics design allows to see limitations/bottlenecks at each step.
You have the FULL description of the system from input data to the output.
Mentions: latency, readout efficiency, losses, etc…
[Here, the slide is agnostic to the language used]

## Slide 15: PixESL – Virtual Prototyping
PixESL applies the Electronic System Level concepts to pixel detectors design flow for a cycle-accurate simulation from analog front-end to chip/system readout.
faster runtime (~70k transactions/s)
compared to RTL simulation (x50)
Charge, ToA, position, …
Digital packets
Pixel matrix | 4x4
Pixel node | 4x4
Readout node | 2x2
Periphery node | 2x1
Data aggregator | 1x1
Notes: The tool will generate the virtual prototype based on the architecture configuration given as input.

## Slide 16: PixESL – Virtual Prototyping
PixESL applies the Electronic System Level concepts to pixel detectors design flow for a cycle-accurate simulation from analog front-end to chip/system readout.
Detector Simulation e.g. AllPix2, Geant4,...,
provides pixel hit input data with charge and time of injection
ROC Virtual Prototype in PixESL provides a C++-based high-level simulation platform to study the entire electronics system chain at an early stage of development.
Readout Chip output data
with performance metrics

## Slide 17: PixESL – Modeling Methodology
Detector Simulation e.g. AllPix2, Geant4,...,
provides pixel hit input data with charge and time of injection
ROC Virtual Prototype in PixESL provides a C++-based high-level simulation platform to study the entire electronics system chain at an early stage of development.
Readout Chip output data
with performance metrics
Pixel [C++/SystemC]
  Analog Front-End
  Digital Front-End
Readout & Periphery [SystemC TLM 2.0]
  Readout network
  Output link
Data processing [SystemC TLM 2.0]
  Ex: Event aggregator
Notes: Mention that this is an example of the architecture configuration, e.g., 2x2 pixel
When there is a readout network, you can explore new features like data processing, e.g. An Event Sorter at the periphery

## Slide 18: PixESL – Front-End model
AFE wrapper
AFE wrapper
AFE wrapper
Modular design approach: each module can be easily changed to model different functionality.
Modeled with C++ and SystemC specialized classes:
Analog Front-End core [C++] analytical model of the analog circuits
AFE Wrapper [C++  SystemC] translates the AFE outputs into SystemC events
TDC model [SystemC] formats the pixel packet and routes it outside the node
AFE core
AFE core
AFE core
AFE core
TDC model
AFE wrapper
Front-End node

## Slide 19: PixESL – Readout model
Modeled with SystemC Transaction Level Modeling 2.0 (TLM 2.0):
Each node contains:
  Initiator: Selects a target and transmits packets to other nodes
  Target: arbitrates incoming packets
  Memory: buffers packets between init. and target
Packet transfer protocol implemented with TLM 2.0 library
Nodes can be connected arbitrarily and their functionality customized

## Slide 20: PixESL in a nutshell
Open-source
The model is based on C++ and [link]
Performance analysis is based on Python
User-friendly
Reconfigurable architectures and network
User and developer roles are separated
Reusable
Generalized layers and standardized packet transport
A library of useful layers and components
Validation of the specifications and verification of the hardware design
Notes: From AFE to chip readout –so we want to model the whole system
We still want to keep the accuracy of the system at a cycle level
Python based analyzer to make it accessible
We want to build a library of reusable components and not just specific cases.
And we want it to be integrated in our verification framework.

## Slide 21: Applications at CERN
LHCb VeLo Upgrade II (hybrid data-driven detector)
ALMIRA Alice3 Upgrade (Monolithic tracker)

## Slide 22: PixESL for LHCb VELO Upgrade II
The Readout Chip for the LHCb tracker upgrade II is the prototype of Velopix2:
Data-driven readout architecture
Pixel hit rate 3.5 GHz/cm2
28 nm CMOS technology
Design derived from Velopix and Timepix4
Time resolution 25 ps, 50 μm pixel pitch
PixESL model:
The pixel emulates the Analog Front-End model
Super-Pixel, region and EoC node are digital readout stages
The simulation is based on physical events
The geometry of the architecture is user-configurable
Velopix

## Slide 23: PixESL for LHCb VELO Upgrade II - Results
 | Velopix | Proposed
Pixel | 256x256 | 256x256
SP | 128x128 | 128x128
Regions | 64x8 | 128x8 *
EoC | 64 (8 ch.) | 128 (16 ch.)
Readout eff. | 90 % | 99 %
Avg. latency | ~100 cy. | ~30 cy.
*By doubling the transactions per cycle
Arbitration | Round-robin | Back-pressure
Notes: Study of the network

## Slide 24: PixESL for LHCb VELO Upgrade II - Results
PixESL allows to perform design space exploration to:
analyze bottlenecks
separate bugs from system inefficiencies
Notes: Study of the front-end
You can classify efficiency – analog pile-up, …
You can measure what you lose at the level of the front-end, at the level of the network, etc…
How long it takes to the packet to get out of the chip.
It is important for the Back-End
Either on-chip or off-chip, someone must do sorting.
Analyzes at the level of the pixel matrix.
This is the high level view.
With a very low max. latency of the readout system, you are dominated by the network. While, if you increase it, the limitation becomes the Front-End. And this is the condition we want.
Because it means the Network does not impact the efficiency of the system.

## Slide 25: PixESL for LHCb VELO Upgrade II - Results
Velopix
Notes: Study of the network

## Slide 26: PixESL for LHCb VELO Upgrade II Co-simulation for chip verification
PixESL usage in testbench to:
Model the Analog FE to drive the DUT
Predict the output packets from pixels
Reuse of AFE and Pixel models from Validation phase.
PixESL shows a faster runtime (~70k transactions/s) compared to RTL simulation (x50)
SV Shell
LHCb VELO Upgrade II Virtual
Prototype
DUT
Scoreboard
Predictions
SystemVerilog Testbench
Packets
Stimuli
Notes: It was a

## Slide 27: PixESL for ALICE3 Tracker Upgrade
ALMIRA project is developing the next generation of vertex and tracking detectors for ALICE:
Monolithic stitched sensor for wafer-sized detector chips.
Pixel hit rate 100 MHz/cm2 and 70mW/cm2 power target.
Pixel pitch of 10 μm with 100ns time-of-arrival resolution.
TPSCo 65nm CMOS technology.
First readout stage is asynchronous non-zero-suppressed in an 8x8 pixel area.
Synchronous data and control busses for global data transmission.
PixESL model:
Analog FE model derived from analog simulation:
  LUTs map the input charge(s) to ToT and ToA.
Asynch. model of the Pixel Macro (PM)
Pixel Group and EoC node are synch. readout stages
The simulation is based on physical events
Thanks to the ALMIRA project for these slides

## Slide 28: ALICE3 Tracker Upgrade Analog Front-end Studies
The analog FE is accurately modeled through automated scripts that map the AFE circuitry behaviour in the analog Spectre simulation to a LUT-based PixESL Analog FE. It models:
ToT and ToA as a function of charge and set threshold
Deadtime between two hits as function of their charges
Random Threshold Mismatch
Charge Noise

## Slide 29: ALICE3 Tracker Upgrade - Grouping Efficiency in the Pixel Macro
Each pixel macro collects hits/tracks for a configurable integration time.
The longer the integration, the more tracks show up in a single packet, thus reducing bandwidth.
For an excessively long integration time, multiple tracks per packet can occur in the same location, thus increasing the chance of losing hits due to pileup.
Integration time: 175 ns
Integration time: 315 ns
10351 packets
7769 packets
More pileup
More packets

## Slide 30: Conclusions
PixESL is a valid tool for high-level modelling and architectural analysis
The project is part of the ECFA DRD7 collaboration funded by
Q2 2023
Q3 2023
Q4 2023
Q1 2024
Q2 2024
Q3 2024
Q4 2024
…
Q4 2025
Q1 2026
Q2 2026
PixESL kick-off
First Velopix model
Front-End modelling
Verification integration
Architecture configurability
Open Source
PixESL release
VeLo Upgrade II
Picopix model
Contacts
PixESL Maintainers:
PixESL-maintainers@cern.ch
PixESL Project
Repo: https://gitlab.cern.ch/iod/pixesl-group/core
Docs: https://cern.ch/pixesl
Accessible upon request
ALICE3 Tracker Upgrade
Notes: The PixESL framework proposes a rapid and efficient prototyping approach for system-level development, 50 times faster compared to RTL simulations, using well-established open-source languages like SystemC and Python.
In the first phase we

## Slide 31
Thank you!