## Slide 1: Beam Synchronous ML for E300
Sheldon Rego
E300 collaboration meeting
2/2/26

## Slide 2
Sextupole magnet field lines.
Credit: Andy Wolski, U. of Liverpool, Linear dynamics, Lecture 3
Sextupole optimization
Sextupole magnets tune higher order momentum dispersion and handle precise shaping of the particle beam.
PWFA performance is very sensitive to sextupole settings
4 sextupoles at FACET-II x [X, Y]→ 8 degrees of freedom
Enormous parameter space to search by hand….ML!
However, the ML optimizer needs to ignore bad shots caused by shot-to-shot machine jitter rather than sub-optimal sextupole settings.
Bad shot filtering is done by filtering on S14 BLEN.
Thus, we need a program that beam synchronously matches scalar diagnostics with the spectrometer cameras in real time to provide inputs to the optimizer.

## Slide 3
Objectives
Project goal: Build PWFA spectrometer tool that interfaces with:
ML optimizer
Live display GUI
Main challenge: Acquisition needs to be beam synchronous (BSA)
Notes: PWFA?

## Slide 4
Optimization goals
Sextupoles
S14 BLEN
IP TORO
SYAG
Energy
CHER

## Slide 5
BSA ML optimizer workflow
SYAG
TORO
BLEN
Cameras
Scalars
Collect measurements
PWFA Spec. calculation
Eloss: Total energy lost by drive bunch (below 10 GeV)
Egain: Total energy gained by trailing bunch (above 10 GeV)
Qaccel: Total charge accelerated above 10 GeV
Eta_tot: Total drive to trailing energy transfer efficiency
Machine
Learning Optimizer
CHER
Try new sextupole position
BLEN within range?
Yes
No
Notes: Speed through 5, 6, 7

## Slide 6
BSA acquisition: Single bunch configuration
Controls system
CHER PID PV
SYAG PID PV
acquisition.py
Read CHER Image Array and CHER Pulse ID PV, write to buffer, tell matching.py to start matching
Read SYAG Image Array and SYAG Pulse ID PV, write to buffer
buffer.dat
Buffer name | Stored data |  |  | 
CHER Image Array | .. | .. | .. | …
CHER Pulse ID | .. | .. | .. | …
SYAG Image Array | .. | .. | .. | …
SYAG Pulse ID | .. | .. | .. | …
10 Hz Scalar Buffer
Buffer name | Stored data |  |  | 
Scalar Pulse ID | .. | .. | .. | …
BLEN | .. | .. | .. | …
TORO | .. | .. | .. | …
matching.py
Search for SYAG and Scalar PID match for given CHER PID
Calculate Eloss
w+
w+
r
Calc. PVs
caget/caput with EPICS PV
read/write to np.memmap
PySide6 signal/slot
ML optimizer
Current status:
Full process takes ~0.3s
→ 1/3rd of all shots are acquired, matched and calculated at 10 Hz beam repetition rate

## Slide 7
BSA acquisition: Final design
Controls system
CHER PID PV
SYAG PID PV
acquisition.py
Read CHER Image Array and CHER Pulse ID, write to buffer, tell matching.py to start matching
Read SYAG Image Array and SYAG Pulse ID, write to buffer
buffer.dat
Buffer name | Stored data |  |  | 
CHER Image Array | .. | .. | .. | …
CHER Pulse ID | .. | .. | .. | …
SYAG Image Array | .. | .. | .. | …
SYAG Pulse ID | .. | .. | .. | …
10 Hz Scalar Buffer
Buffer name | Stored data |  |  | 
BLEN | .. | .. | .. | …
TORO | .. | .. | .. | …
matching.py
main.py
Front end GUI
Search for Pulse ID match across buffers
Calculate everything
w+
w+
r
GUI push buttons and edit fields
Update front end graphics
Calc. PVs
caget/caput with EPICS PV
read/write to np.memmap
GUI front
end update
PySide6 signal/slot
ML optimizer
Notes: Show overlay of what is needed for xopt and Live Spectrometer (not the same) [ also shut off waterfall when xopt is running to save computation]

## Slide 8
ML optimization workflow
Controls system
CHER PID PV
SYAG PID PV
acquisition.py
Read CHER Image Array and CHER Pulse ID, write to buffer, tell matching.py to start matching
Read SYAG Image Array and SYAG Pulse ID, write to buffer
buffer.dat
Buffer name | Stored data |  |  | 
CHER Image Array | .. | .. | .. | …
CHER Pulse ID | .. | .. | .. | …
SYAG Image Array | .. | .. | .. | …
SYAG Pulse ID | .. | .. | .. | …
10 Hz Scalar Buffer
Buffer name | Stored data |  |  | 
BLEN | .. | .. | .. | …
TORO | .. | .. | .. | …
matching.py
main.py
Front end GUI
Search for Pulse ID match across buffers
Calculate everything
w+
w+
r
GUI push buttons and edit fields
Update front end graphics
Calc. PVs
caget/caput with EPICS PV
read/write to np.memmap
GUI front
end update
PySide6 signal/slot
ML optimizer
Notes: Show overlay of what is needed for xopt and Live Spectrometer (not the same) [ also shut off waterfall when xopt is running to save computation]

## Slide 9
PWFA spectrometer GUI workflow
Controls system
CHER PID PV
SYAG PID PV
acquisition.py
Read CHER Image Array and CHER Pulse ID, write to buffer, tell matching.py to start matching
Read SYAG Image Array and SYAG Pulse ID, write to buffer
buffer.dat
Buffer name | Stored data |  |  | 
CHER Image Array | .. | .. | .. | …
CHER Pulse ID | .. | .. | .. | …
SYAG Image Array | .. | .. | .. | …
SYAG Pulse ID | .. | .. | .. | …
10 Hz Scalar Buffer
Buffer name | Stored data |  |  | 
BLEN | .. | .. | .. | …
TORO | .. | .. | .. | …
matching.py
main.py
Front end GUI
Search for Pulse ID match across buffers
Calculate everything
w+
w+
r
GUI push buttons and edit fields
Update front end graphics
Calc. PVs
caget/caput with EPICS PV
read/write to np.memmap
GUI front
end update
PySide6 signal/slot
ML optimizer
Notes: Show overlay of what is needed for xopt and Live Spectrometer (not the same) [ also shut off waterfall when xopt is running to save computation]

## Slide 10
User interface: old design (Matlab)

## Slide 11
User interface: Qt Creator
Electron Spectrum waterfall plot display window [charge density vs shot number]
2 independent Spectrometer Display windows
Spectrometer diagnostics for most recent shot
Set configuration and global calculation variables
Start/stop

## Slide 12
User interface
Electron Spectrum waterfall plot display window [charge density vs shot number]
2 independent Spectrometer Display windows
Spectrometer diagnostics for most recent shot
Set configuration and global calculation variables
Start/stop
Graphics plotting does not work right now…goal for upcoming E300 run

## Slide 13
Summary of E300 25/11-26/11 shift
Tested BSA acquisition script over 2 shifts in late November
Day 2
Day 1

## Slide 14
Summary of E300 25/11-26/11 shift
Initial energy loss = 3.26 J
Initial drive to wake transfer efficiency ~18%
Final energy loss = 3.89 J
Final drive to wake transfer efficiency ~24.3%
Sextupole tuning
Energy loss - Before
Energy loss - After

## Slide 15
Slice Dispersion
Slice Dispersion Plots - Before
Slice Dispersion Plots – After xOpt
Sextupole tuning significantly improved the shaping of the electron beam – smaller x and y size and angular dispersion after ML optimization!
Sextupole tuning
Credit: Doug Storey
~100 μm
~100 μrad
~180 μm
~125 μrad
~40 μm
~20 μrad
~50 μrad
~40 μm

## Slide 16
ML optimizer
(*) set optimizer to TURBO mode at step 45, ie. force converge in narrow region around best point till step 45
(*)
Set acceptable BLEN range to accept shot
For each sextupole configuration, Eloss was the average of 20 good shots
(*)
Bayesian optimizer surrogate function: “how sensitive is the optimum w.r.t. sextupole moves?”
Credit: Doug Storey

## Slide 17
Beam Synchronous Acquisition…. or is it?
Current program assumes that if we acquire a sensor/camera and its Pulse ID on the next line of code, then they are synchronized
Small chance that the Pulse ID update (at 10 Hz) occurs between these two lines ⟶ we occasionally have a misaligned shot
Not a dealbreaker (optimizer still improves PWFA performance), but not the optimal solution
Most rigorous method is to synchronize with the timestamp metadata sent by the server
Works for some cameras but not others

## Slide 18
Progress Summary
Completed:
Designed backend for acquisition, matching and calculation program for single bunch configuration
Prepared preliminary framework for full program
ML optimizer successfully improves drive bunch energy loss, dispersion and dispersion’
To prepare for upcoming run:
Complete and commission all tools (acquisition, matching, calculation, GUI) for single and two bunch configuration
Test ML optimization with various figures of merit
Implement timestamp based BSA matching
Impact for E300:
Need >30% drive to wake transfer efficiency to achieve total efficiency goals of FACET-II – rigorous ML optimization needed
Improvements in slice dispersion measurements are promising

## Slide 19: Thank you
Questions?