## Slide 1
2/2/2026
E300 Collaboration Meeting
E300 FY26 Plans
Doug Storey | AARD

## Slide 2: What did we do in FY25
Laser preionization of Li oven
Longitudinal characterization and optimization
  Increased XTCAV resolution
  Use of notch/jaw  optimization of beam loading
Transverse tuning tools
  BPM slice dispersion tool
  First attempts at matching  cm, 1 Torr Li
  ML optimization of Eloss/Egain
Resulted in repeatable, high-quality acceleration of witness bunches with high efficiency
High-quality acceleration of witness bunches

## Slide 3: Progress on PWFA in FACET-II so far
Parameter |  | FY24 Results | FY25 Results | 2016 AAC Goal
Emittance | µm | >200 | ~200* | 10
Energy Spread | % | 4 | < 1 | < 5
Energy Gain | GeV | 1.5 | 4 | 10
Charge Accelerated | pC | ~100 | ~200 | ~100
Total Efficiency | % | 4 | ~6 | > 10
Overall state:
  Energy gain and energy spread is ok with this oven length
  Efficiency and charge capture needs improvement
  Lots of work towards emittance preservation

## Slide 4: PWFA goals for FY26
Parameter |  | FY24 Results | FY25 Results | 2016 AAC Goal
Emittance | µm | >200 | ~200 | 10
Energy Spread | % | 4 | < 1 | < 5
Energy Gain | GeV | 1.5 | 4 | 10
Charge Accelerated | pC | ~100 | ~200 | ~100
Total Efficiency | % | 4 | ~6 | > 10
How do we do better? Better longitudinal and transverse control
  Stable longitudinal working point  Fine tuning of drive/witness current profile and notch/jaw to optimize charge capture, beam loading
  Matching into the plasma  emittance preservation, improved charge capture, efficiency
FY26 Goals
~10’s
< 1
~5
>100 pC (100%)
10

## Slide 5: Guidance from simulation studies
Simulation setup:
  Drive current profile from XTCAV data
  Witness current profile from ML reconstruction
  Transverse properties from quad scan data:
    Drive: µm, cm
    Witness: µm, cm
Results:
  Excellent agreement to energy spectrum of drive and witness
  Emittance grows to ~130 µm
  Beam spot <10 µm, so fully contained in bubble
Witness evolution through the plasma
Energy Spectrum
Simulations by T. Dalichaouch

## Slide 6: Path to higher energy transfer efficiency
Optimization of bunch separation alone will not get us from ~5%  10%
Charge capture/transport:
  Starting to study transverse offsets in simulation
  We think there is an additional aperture in the beamline that is limiting charge transport
    Solutions: 1) smaller outgoing divergence, 2) improve aperture
Need to better optimize:
  Drive current profile
  Drive participating charge
  Witness “charge participation” / charge transport
  Matching/witness offset
Simulations by T. Dalichaouch

## Slide 7: 1) Improve Drive-to-Wake energy transfer
Need to extract at least 30% energy from the drive bunch
  Need a minimum of 20 µm bunch length x 20 µm spot size
FY25
FY26
FY25
FY26
Simulations by C. Zhang
FY25 Results -

## Slide 8: 2) Improved transverse performance
Matching
  Need to focus to cm
  With energy slices focused at the same plane
Dispersion/dispersion’ tuning
  Offset witness can lead to increased emittance growth, transverse instabilities, charge loss
  Optimized through linac tuning and sextupoles
    Simulation studies to quantify the requirement are underway (Thamine)
    New optimization tools under development
      Sheldon/Brendan – xOpt/Badger tuning
      Yiheng – ML optimization of dispersion/dispersion’
Plots by C. Zhang
Drive
Witness
Plasma
Drive
Witness
Drive
Witness
Witness
Plasma
Drive

## Slide 9: Shift plan/ideas for Jan. to July 2026
Get the S20 beam back to “nominal” state
  Beam matched going into the Final Focus
  Sextupoles de-scrambled, or understood why they are acting different than last run
    Metric: Nominal beam should have spot size of ~20um, waist locations within /2 of setpoint
Tool development
  TCAV GUI (Peter) – improved analysis and DAQ integration
  Slice BPM tool (Yiheng) – More user friendly, extend to ML tuning of dispersion/dispersion’
Single bunch PWFA studies (~2-3 shifts)
  Finish commissioning ML optimization tools, aim for >40% drive to wake energy transfer
    xOpt sextupole optimization (Sheldon)
    Metric: Aiming for >30% energy transfer, prefer >40%

## Slide 10: Shift plan/ideas for Jan. to July 2026, continued
Two bunch studies – No plasma studies (few shifts)
  Longitudinal setup – with more XTCAV power
    No-plasma shifts dedicated to Virtual TCAV (Jinseo), SYAG charge reconstruction
    Metric: Can use virtual TCAV/SYAG to predict shot-by-shot longitudinal profiles & charges
  Transverse setup (Yiheng) – tuning directly on dispersion/dispersion
  Low beta function commissioning
    Metric: Measure spot sizes commensurate with emittance and beta down to cm
Two bunch - With plasma (~3 shifts, every two weeks, starting in mid-Feb/Mar)
  Improved “PWFA Live” analysis tools (Sheldon) – Integration with ML
  More of the same:
    Linac longitudinal optimization, notch/jaw beam loading optimization
    Transverse tuning – sextupoles, ML, dispersion tuning, etc
    Starting at lower density (~1 Torr), then increasing when we think we are doing it right
  Transverse instability studies (Daniel)

## Slide 11: Person requirements for FY26 E300
Last spring we ran E300 for 30 days in total (25 with the oven on)
How should we do it this year?
  Li oven operators: oven startup/shutdown, on shift heat management, on-call for issues
    Ivan, Kelly, Daniel, Yiheng, ??
  Laser operators: Laser startup, EOS setup/monitoring, Laser alignment and on-shift management
    Alex, Junzhi, Claire, Sheldon (Mar-May), ???
  2 bunch specialists: Assist with daytime beam setup/tuning, understanding of machine setup
    Zack, New-Nathan??
  On-shift specialists, data analyzers, visitors, well-wishers, distant relations, very old friends

## Slide 12: Summary
What do we need to do to do better?
Get the S20 beam back to “nominal” state
Be better at both longitudinal and transverse tuning, at the same time, every time (or at least 10% of the time)

## Slide 14: Characterizing the nominal working point
Two-bunch from cathode, with collimators
  Driver: ~1.2 nC, 6-8 kA
  Witness: 150-250 pC incoming charge
  Plasma: 40cm long lithium plasma, 4e16 cm-3
Sorted by figure of merit:
Full dataset (laser pre-ionized)
14 GeV bunch:
GeV
pC
16 GeV bunch:
GeV
pC

## Slide 15: Can we predict what shots are going to be higher quality?
Brendan’s analysis: linear regression coupled with feature importance permutation
- Finds a list PV’s with high correlation with FOM
Filter data by PVs
BPM 333 X
BPM 511 X
BPM 801 X
BPM 2445 X
BPM 3156 X
BC11 BLEN
BC14 BLEN
Further analysis to determine optimal range of these PV’s that minimizes FOM
Only shots with similar incoming PV’s
Energy gain, | (4.1 ± 0.3) GeV
Gradient, | (10 ± 1.0) GeV/m
Field uniformity, | (2.0 ± 0.2) %
Witness charge capture, | (62 ± 4) %
Instantaneous efficiency, | ~20-30 %
Total efficiency, | (4.9 ± 0.5) %
 | (4.1 ± 0.3) GeV
 | (10 ± 1.0) GeV/m
 | (2.0 ± 0.2) %
 | (62 ± 4) %
 | ~20-30 %
 | (4.9 ± 0.5) %

## Slide 16: FY26 fall run - xOpt Optimization of Drive-to-Wake Transfer Efficiency
Challenges:
  Ensuring BSA acquisition of camera and scalar data
  xOpt setup (Thanks Ryan Roussel)
Optimum found with ~25% drive-to-wake efficiency
  Comparable to best performance
    (43% efficiency, but with a much longer oven)
Minimum energy particles down to <4 GeV

## Slide 17: FY26 fall run - Post-optimization characterization
Slice dispersion and dispersion’ much improved by optimization
Offset in x and y waist positions persists after optimization
Slice Dispersion Plots - Before
Slice Dispersion Plots – After xOpt
Quad scans after xOpt

## Slide 18: Additional thoughts
Witness transport: Is there an aperture that is limiting witness transport
Data – save more data!
  Do the CMOS IOCs allow for smaller images to be saved??

## Slide 19: Main results from FY24 run
Single bunch
  Long oven
Two bunch
  Short (damaged) Li oven
  ~1.5-2 GeV energy gain,
  Energy spread <4%
  Emittance > 200 µm

## Slide 20: Progress this past fall – Single E300 oven run
Shift goals:
  Use xOpt with BSA-acquisition to optimize PWFA
    Goal: Maximum drive-to-wake energy transfer
    Actuator: 8 sextupole mover positions
  Compare optimization performance to Nelder-Mead optimizer
  Use the new slice dispersion measurement GUI and quad scans to measure the beam
  Support E324