## Slide 1: Quantum information for high-energy and nuclear particle physics
Konrad W. Lehnert
SLAC Summer institute 2026
Palo Alto, California
The Haloscope At Yale Sensitive To Axion CDM
Notes: Well hello, my name is Dan Palken; I work for Konrad, and I’ll be giving my Comps III talk on how I plan to enhance the primary figure of merit – the scan rate – of a dark matter detector called an axion haloscope.
I’ll be achieving this scan rate enhancement with two distinct innovations: quantum squeezing, which will rid our system of much of its vacuum noise, and then a statistical analysis that takes a leap forward from what has been being done in this field for the past 30 years.

## Slide 2: What can Quantum info do for high-energy and nuclear particle physics?
many things, but I will discuss the example I know best
quantum enhanced sensing of classical fields
hypothetical ultralight dark matter, especially the QCD axion (this lecture)
gravitational wave detection

## Slide 3: Summary
quantum enhanced sensing: engineering design choice, not magic
useful if easier to lower noise than to increase signal
reduces time or money needed to detect a signal
primary benefit is an increase in sensor bandwidth
https://doi.org/10.48550/arXiv.2110.04912

## Slide 4: Outline
theory of quantum squeezing to enhance classical field sensing
squeezing deployed in a search for axionic dark matter
strategies for more quantum enhancement

## Slide 5: Classical fields: large amplitude but weak coupling to a sensor
high-Q
resonator
decoherence
hypothetical field
null hypothesis
field hypothesis
distinguish evolution under
possible sensor
resonant circuit (DM Radio)
microwave cavity (ADMX/HAYSTAC)
spin ensemble (CASPER)
mechanical resonator (Windchime)
Notes: Points to make here. Work as hard as you can to make coupling rate strong, it’s always weaker than decoherence rate. At tiny fraction of the energy stored in the field may enter the sensor to be detected but there is essentially no hope to detecting the energy in the cavity decaying into the field.

## Slide 6: If signal is an oscillatory “force” of unknown frequency
amplifiers measure cavity quadratures X1 and X2
null hypothesis
dark matter hypothesis
rotating frame removes simple harmonic evolution
quadrature variables
Notes: key point to make: on resonance defined by how long you’re willing to wait.

## Slide 7: Quantum noise pollutes inference of classical force
ground state
displaced ground state
amplifiers measure cavity quadratures X1 and X2
coherent state limit (CSL) also “SQL”
prepare in ground state, measure X or Y
null hypothesis
field hypothesis

## Slide 8: Squeezed states approximate quadrature eigenstates
phase space volume conserved
commutator preserved
no added noise

## Slide 9: Squeezing and noiseless measurement circumvent quantum limit
squeezed state
displaced squeezed state
amplifiers measure cavity quadratures X1 and X2
‘beat’ the CSL:
prepare in X squeezed state, measure X noiselessly
null hypothesis
field hypothesis

## Slide 10: Quantum state preparation and measurement access quantum metrology
amplifiers measure cavity quadratures X1 and X2
prepare
evolve
measure
optimize estimation of parameters over:
initial state preparation
measured quantity
classical statistics

## Slide 11: Frequently asked questions
Does the quantum advantage disappear when considering decoherence?
Do you need to know the phase of the signal to benefit from squeezing?
Can you measure both quadratures of the signal better than the CSL?

## Slide 12: Impact of loss and decoherence on squeezing and signal
time evolution with decoherence from loss
in a characteristic decoherence time
squeezing is lost
displacement reaches steady-state value

## Slide 13: Squeezing improves sensor bandwidth
measure after decoherence time
squeeze and measure fast
preserve SNR when detuned

## Slide 14: Measuring both quadratures doubles the signal and noise power
measure only
measure and
Wigner function
marginal of Wigner function
Huisimi – Q function

## Slide 15: Two-mode squeezing operation is unitary
resonator 1
resonator 2
correlations reveal entanglement

## Slide 16: Quantum enhanced measurement of both quadratures
evolve
unentangle
resonator coupled to hypothetical field
ancillary resonator
two-mode squeezed & entangled state
Notes: These ultralight dark matter searches are laboratory scale experiments. As such they complement facility scale searches that use accelerators or large underground detectors, to search for much more massive particles. They test a different class of models and by using entangled quantum sensors even small experiments can have large reach.
Because the dark-matter field is highly occupied but weakly coupled it creates a tiny but classical signal on the laboratory detector apparatus, which is usually some kind of tunable high-quality harmonic oscillator. The oscillator can be an ensemble of atomic or molecular spins , an inductor-capacitor resonant circuit, or a microwave cavity.
Whatever the nature of the oscillator, represented in a phase space picture
[animate], an experiment proceeds by preparing the oscillator in its ground state and measuring, about one coherence time later, where it ended up, thus resolving the presence of a dark matter force.
If one is technically perfect, only the zero-point motion of the oscillator
[animate] limits how precisely it can be prepared and only the non-commutation of the phase space variables limit how precisely it can be measured.
This point of technical perfection defines a quantum limited search rate for a particular apparatus.

## Slide 17: Squeezing in an axion dark matter search

## Slide 18: Ultralight dark matter must be bosonic
dark matter (LCDM)
“cold:” gravitationally bound to us
mean density: ~ 0.4 GeV/cm3
weakly interacting
implications for particles with rest mass
quantum degenerate Bose gas
more “field-like” than “particle-like”
persistent, large amplitude, weakly coupled field

## Slide 19: Hypothetical QCD axion: a light particle that is cold and dense enough to contribute to dark matter
mechanism to resolve strong-CP problem (Peccei and Quinn)
associated particle (axion) is dark matter candidate
mass range
as a frequency
*post-inflation scenario

## Slide 20: Axion field couples (weakly) to electromagnetism
modified QCD Lagrangian
A
linearize coupling around static -field
dark matter axions create microwave photons
g
g
g
A

## Slide 21: Scan narrowband cavity to search for resonant axion to photon conversion: haloscope (Sikivie 1983)
tunable cavity
solenoid
amp
spectrum analyzer
axion field more coherent than cavity
Johnson-Nyquist and amplifier noise
tune → wait and integrate → tune
resolve variance with 10-3 precision
106 realizations of random process

## Slide 22: Cool cavity and measure with noiseless amplifier to reach CSL
tunable cavity
solenoid
1 L volume
Q = 104
Josephson parametric amplifier (JPA)
measure noiselessly
haloscope near the CSL (HAYSTAC 2017)

## Slide 23: Low noise amplification with Josephson parametric amplifiers
coil
port 2:
pump
flux line
SQUID array
port 1:
signal
capacitor
100 mm
tunable over 1.5 GHz gain > 30 dB
coil
tuned

## Slide 24: Phase sensitive amplifier measures one quadrature noiselessly
JPA
in
out
pump
cavity band
phase sensitive mode:
half-pump resonant with cavity

## Slide 25: JPA noiselessly transforms ground state into squeezed state
JPA
pump
squeezed quadrature: quantum noise suppressed
/2
use JPA to prepare cavity in squeezed state

## Slide 26: Demonstration of squeezing and determination of loss: second JPA analyzes squeezed state created by first
phase chooses measured quadrature relative to squeezed quadrature
pump
JPA
JPA
squeeze
measure
SQ
AMP
var(X) (dB)
CSL
loss h:

## Slide 27: Squeezing achieves best sensitivity over a wider bandwidth
suppress measurement port noise
resonant signal and critically coupled
overcoupled cavity with squeezing
axion field
measurement
loss
pump

## Slide 28: Scan rate enhancement, perfect efficiency
scan rate enhancement
Sensitivity
no squeezing
squeezing
slight reduction in sensitivity
much larger bandwidth

## Slide 29: Effect of propagation losses on the scan rate
loss:
scan rate enhancement
Is doubling the search rate meaningful?
saves 10,000 years or 600 M$
dramatic improvement with reduced loss
transmission loss diminishes benefit

## Slide 30: Quantum enhanced sensing is now routine in HAYSTAC
double the quantum limited scan rate
A quantum enhanced search for dark matter axions
K.M. Backes, D.A. Palken, et al., Nature 590, 238–242 (2021).
M. J. Jewell et al. (HAYSTAC Collaboration) Phys. Rev. D 107, 072007 (2023).
X. Bai et al. (HAYSTAC Collaboration)
Phys. Rev. Lett. 134, 151006 (2025).

## Slide 31: The coherent state limit is hard to beat in a search for fundamental fields
hard to beat CSL
coupling to fundamental fields: big objects
quantum control and measurement: small systems
near technical perfection required
5 mm

## Slide 32: strategy for more quantum enhancement

## Slide 33: Amplify signal before encountering measurement port noise
standard quantum limit
cavity entanglement
“CEASEFIRE” Demo
vacuum
squeezing
HAYSTAC apparatus
Y. Jiang, E.P. Ruddy, K.O. Quinlan, M. Malnou, N.E. Frattini, KWL, PRX Quantum 4, 020302 (2023)
K. Wurtz, Benjamin Brubaker, Y. Jiang, E. Ruddy, Daniel Palken, KWL, PRX Quantum 2, 040350 (2021)
(dB)
Notes: So far we have introduced what’s the quantum limited searches, and squeezing the measurement noise enables 2 times SRE. In the last topic of this talk, I will spend my time in telling you an alternative method, by amplifying the cavity noise and axion signal together but keep measurement noise unamplified, an alternative way to increase the sensitivity bw, we are able to search 6 times faster by the balanced interactions. And by slightly imbalance the interaction rates using the same method, we can accelerate the searches by 8 times compared to quantum-limited case.

## Slide 34: Dynamically couple axion cavity and readout mode by 3-wave mixing
3WM
A
B
P
auxiliary readout mode
axion-sensitive cavity

## Slide 35: State swapping (C) interaction swaps states between two modes
3WM
A
B
P
auxiliary readout mode
axion-sensitive cavity
state-swapping
Notes: The first interaction we want to build is the state swapping interaction between two modes, by pump C mode at the diff frequency of A,B mode, we can continuously swap the states of two modes at rate g_C, as represented by the beam splitter Hamiltonian here.

## Slide 36: Two-mode squeezing (G) induces amplification and entanglement
3WM
A
B
P
auxiliary readout mode
axion-sensitive cavity
two-mode squeezing
Notes: The 2nd type of interaction is the two-mode squeezing interaction, by pumping at the sum frequency of the A, B mode, each mode contains the amplified cavity noise and signal from A mode and amplified meas noise from mode B, as represented by the amplified purple bulb here. Two-mode squeezing interaction allows amplification at rate g_G as shown in Hamiltonian, it also builds up the quadrature correlations between two modes.

## Slide 37: Two-mode squeezing (G) induces amplification and entanglement
3WM
A
B
P
auxiliary readout mode
axion-sensitive cavity
two-mode squeezing
Notes: The 2nd type of interaction is the two-mode squeezing interaction, by pumping at the sum frequency of the A, B mode, each mode contains the amplified cavity noise and signal from A mode and amplified meas noise from mode B, as represented by the amplified purple bulb here. Two-mode squeezing interaction allows amplification at rate g_G as shown in Hamiltonian, it also builds up the quadrature correlations between two modes.

## Slide 38: Quantum non-demolition interaction yields bandwidth increase
increase
c.c.
QND
amplification
readout
3WM
A
B
P
Chien, T-C., et al. Physical Review A 101.4 (2020): 042336.
Metelmann, A. and Clerk, A.A., Physical Review X 5.2 (2015): 021025.
Notes: When these two interactions are applied simultaneously, and at equal interaction rates, this manifests as QND Hamiltonian. We can write down the Hamiltonian in quadrature basis as shown here, where quadrature variables X_A,B are the linear combination of annihilation and creation operators A and B. This Hamiltonian is a quantum non-demolition Hamiltonian as revealed in the Heisenberg equations of motion. EoMs tell that the signal and cavity noise contained in XA will be amplified at YB, while leaving the original quadrature unchanged, representing the QND. As shown in the phase space picture.
Now if we readout along the amplified quadrature, we get amplified signal and cavity noise, and unity measurement noise. Through this amplification, we realize the sensitivity bandwidth increase, therefore increase the search rate.

## Slide 39: Imbalanced GC operation for further scan rate enhancement
10 MHz
6 MHz
Y Jiang, et, al., PRX Quantum 4 (2), 020302. (2023)
SNR2 norm.
Notes: In real experiment, one of the practical limitation comes from the balanced state swapping and two-mode squeezing interaction is the stability. If there are some ambient flux noise that shifts the mode frequency, the imbalanced interaction rates, especially if the TMS rate is larger than state swapping rate, that would lead the system to be unstable, which limits the ultimate achievable interaction rates. To overcome this challenge, we make the slightly imbalance of the GC interaction, causing swap rate to be larger than two-mode squeezing rate, this operation would solve the instability problem, and moreover, this imbalanced operation itself would also widen the visibility bandwidth. In this experiment, the main benefit from this operation is that is allows the increased interaction rates from 7.6 MHz to 12 MHz, which results in a SRE of 8 times.
As a summary for the 2nd type of quantum-enhanced sensing technique, plotted here is the SNR^2 over the detuning wrt axion mode freq, for quantum limited case in orange, balanced GC/QND interaction in purple, and slightly imbalanced GC interaction in teal. The area under the curve from the purple and teal wrt to the quantum limited case gives the SRE of 5.6 and 8.2, respectively. So we increase the SRE by increasing the bandwidth that the detector is sensitive to axion signal. Moreover, another benefit comes from the increase of peak visibility, which is because of the GC interaction causes amplification before any lossy element which adds a fixed amount of noise, this amplification reduce the relative size from the pollution of the noise from the lossy element, therefore giving a higher peak visibility than the quantum-limited case, where part of our scan rate enhancement is benefit from the peak visibility increase.
Just to mention, in the first type of receiver, preparing a squeezed state, then transport it through a lossy circulator to the cavity, the SRE is ultimately limited by the added noise from the lossy element. In the 2nd method, we amplify the signal before sending it to the lossy circulator, which allows this method to have robust reaction to the added noise from the circulator, even further benefit from the peak visibility increase than the quantum limited case.

## Slide 40: Acknowledgements for CEASEFIRE data
Kyle
Liz
Konrad
Joyce
fall 2021
Max
Yale/JILA
Liz Ruddy
Yue (Joyce) Jiang
Kyle Quinlan
Nick Frattini
Konrad Lehnert
NIST Maxime Malnou
HAYSTAC collaborators
Yale
Berkeley
Johns Hopkins
The Haloscope At Yale Sensitive To Axion CDM