## Slide 1
Optomechanical sensors for fundamental physics
David Moore, Yale
SLAC Summer Institute
August 11, 2026

## Slide 2
Optomechanics primer
An optomechanical system is a mass whose motion is controlled and read out through light
The canonical system is an optical cavity where one mirror is free to move:
Two coupled harmonic oscillators (light and mechanical motion)
  Each photon exerts a tiny force on the mirror, and mirror’s motion imprints phase on light
As we’ll see in a minute, many other systems that at first appear very different in geometry have this same basic quantum description
D. Moore, Yale
100 THz
kHz – GHz
~ Hz-kHz (coupling per )
Photon number (optical cavity)
Energy per photon
Phonon number (mechanical resonator)
Energy per phonon
Mirror displacement
Optomechanical coupling

## Slide 3
How well can you measure a mass this way?
The phase of the light leaving the cavity encodes the mirror’s position
If we get rid of all sources of noise other than the measurement itself (thermal noise, noisy electronics, …), we are still limited by quantum noise:
D. Moore, Yale
Noise added by measurement at SQL:
Cartoon of imprecision and backaction:
  Imprecision: Uncertainty in mirror position due to shot noise fluctuations in measured phase
  Backaction: Fluctuations in mirror position due to shot noise in radiation pressure
Imprecision
Backaction

## Slide 4
Beyond the SQL
The SQL is not a fundamental limit, but represents a constraint on a weak, continuous measurement of both the position and momentum
  E.g., a strong, projective measurement can localize much smaller in (at the cost of a large uncertainty in , which can interfere with subsequent measurements)
  More generally, we can squeeze light (or possibly mechanical DOFs) to achieve measurements beyond SQL
D. Moore, Yale
x
x
Cartoon of squeezed position measurement:
Unsqueezed
Squeezed
Always obey but push noise into quadrature we’re not interested in

## Slide 5
Squeezing in LIGO
Gravitational wave detectors have pioneered many of these techniques, and are now using squeezing to enhance sensitivity
  Notably, first exhausted “classical” sensitivity improvements at high frequency (e.g. more laser power)
D. Moore, Yale
~6dB squeezing ~(2x lower amplitude noise)
8x larger observing volume
LIGO Livingston strain spectrum (ASD):
LIGO O4 Collaboration, PRX 13, 041021 (2023)

## Slide 6
Other optomechanical systems
A wide variety of optomechanical systems are revolutionizing how we measure tiny forces
Many types of systems are reaching quantum regime following pioneering work by the gravitational wave community
These sensors are can detect extremely tiny forces or accelerations
  In the large mass range, excellent accelerometers (e.g. gravity, dark matter, …)
  In the sub-ng range, reaching sensitivity to the forces imparted by single sub-atomic particles
D. Moore, Yale
For more details see, e.g.:
  “Snowmass 2021: Quantum Sensors for HEP Science,” arXiv:2203.07250.
  "Mechanical Quantum Sensing in the Search for Dark Matter,” Quant. Sci. Tech. 6 024002 (2021), arXiv:2008.06074
  “Searching for new physics using optically levitated sensors,” Quant. Sci. Tech. 6 014008 (2021), arXiv:2008.13197
  “Quantum sensing for particle physics,” Nature Reviews Physics 6, 329 (2024)
  …
Aspelmeyer et al., Rev. Mod. Phys. 86, 1391 (2014)
LIGO, VIRGO, KAGRA

## Slide 7
Photographs of trapped nano/micro particles at Yale:
Levitated optomechanics
D. Moore, Yale
Nano- to micro-sized dielectric masses can be optically trapped with ~100 mW of laser power
Levitated masses are isolated both electrically and thermally
  Ultra-low decoherence allows quantum control of motional degrees of freedom
  Force sensitivities at the zN level, with acceleration sensitivities near a nano-g
Highly focused tweezers (~0.1 – 1𝜇m):
Levitation trap
(~1 – 30 𝜇m):
~1 fg – 1 pg
~1 pg – 30 ng
Particle mass
fg
pg
ng
Force sensitivity [N/]
Accel. sensitivity [g/]
10-21
10-19
10-18
10-8
10-7
10-6
Force and acceleration sensitivity vs particle mass:
Moore and Geraci, Quantum Sci. Technol. 6 014008 (2021)
10-20
10-5

## Slide 8
Step 3: Stabilize spin
p0
Monteiro et al., PRA 97, 051802(R), arXiv:1803.04297 (2018)
Optically spin to >MHz frequency
Experimental sequence (>ng spheres)
Monteiro et al., PRA 101, 053835, arXiv:2001.10931(2020)
Monteiro et al., PRA 96, 063841, arXiv:1711.04675 (2017)
Out-of-loop sensor
K
Step 4: Cool center-of-mass mode
Active feedback cooling to K temperatures
Pump to 10-7 mbar
E ~ 1 V/mm
qinit >104 e-
Monteiro et al., PRA 101, 053835, arXiv:2001.10931(2020)
Step 2: Electrically neutralize
~1-10 mm
25 mm
Step 5: Orient electric dipole moment
Apply electric field (if desired)
Afek et al., PRA 104, 053512, arXiv:2108.04406 (2021)
Step 1: Trap sphere (~1 mbar)
Piezo stack
Monteiro et al., PRA 101, 053835, arXiv:2001.10931(2020)

## Slide 9
Also upgraded our system with high power laser (100 W) to demonstrate first microparticle arrays up to ~10 x 10 in vacuum
Similar technology to tweezer arrays for neutral atom quantum computing
  Additionally require closed loop feedback on trap positions
Microsphere arrays (Yale)
D. Moore, Yale
7x7 array of spheres in vacuum:
~500 m
Simplified schematic:
Siegel et al. PRA 111, 033514 (2025)
Played at 8x speed
25 spheres = 1015 atoms!
9

## Slide 10
Optomechanical sensors for the “invisible” Universe
D. Moore, Yale
https://www.symmetrymagazine.org/article/the-hidden-neutrino
Neutrinos
Are there heavy, right-handed neutrinos that haven’t been observed?
What are the masses of the light neutrinos?
Dark matter
https://www.symmetrymagazine.org/article/december-2013/four-things-you-might-not-know-about-dark-matter
What is the nature of dark matter?
Can we detect forces imparted by dark matter interactions in the lab?
These questions remain unanswered largely due to the extremely weak interactions of interest
  Quantum measurement/control of much larger masses than single atoms/ions may allow new tools to prove these phenomena
Optomechanical systems are ideal for searching for new interactions that couple to massive objects (compare e.g. to sensors for couplings to E&M fields [talk by D. Speller])
Gravity
What is the gravitational field sourced by a massive, delocalized particle?
Are there BSM sources of high frequency gravitational waves?

## Slide 11
Dark matter
D. Moore, Yale
https://www.symmetrymagazine.org/article/december-2013/four-things-you-might-not-know-about-dark-matter

## Slide 12
Ultralight dark matter
D. Moore, Yale
Dark matter with mass 1 eV would have a number density per cubic wavelength 1
  Leads to “wave-like” dark matter, which can impart classical forces (see talk by Y. Kahn)
In both cases, signal oscillates at and is coherent over ~106 cycles (see talk by K. Lehnert):
  Aim to detect oscillating length change or force above thermal and measurement noise
  Typically need resonant enhancement, require tuning over many masses
Scalar (search for oscillating constants):
Can use clocks, optical cavites, etc. (see talk by V. Xu)
Vector (search for oscillating force on mass):
E.g., coupling to B-L pushes on neutrons:
a ≲ 10-11 m/s2 at 10 kHz [i.e., 10-20 N on a μg mass]
Carney et al., New J. Phys. 23 023041 (2021)

## Slide 13
Current and projected sensitivity:
Ultralight dark matter (Optical cavities)
D. Moore, Yale
Several experiments are now pursuing these models
  Optical cavity comparisons (Northwestern):
Comparison of two cryogenic cavities:
Deshpande et al., PRL 135, 261001 (2025)

## Slide 14
Ultralight dark matter (POLONAISE)
D. Moore, Yale
  POLONAISE:
Magnetically levitated 400 ug mass:
Amaral et al., PRL 134, 251001 (2025)
Current and projected sensitivity:
2025 result

## Slide 15
Ultralight dark matter (Trampoline oscillators)
D. Moore, Yale
Membrane oscillators (U Arizona/NIST):
Chowdhury et al, PRD 113, L121303 (2026)
Current and projected sensitivity:
Tethered trampoline membrane oscillator:

## Slide 16
Kinematic detection of (particle) dark matter
D. Moore, Yale
For masses eV, DM interacts as “particles,” i.e. discrete collisions (see talk by T. Lin)
Mechanical sensors could be sensitive to dark matter models that primarily interact coherently with entire objects, rather than single nuclei or electrons
Rate NT A2
~104
q-1 ~ 10 fm
Ton-scale WIMP detectors (e.g. LZ, XENONnT,…):
Coherence only over a single nucleus:
1023
fg-ng scale trapped objects:
q-1 ~ 10 nm
Rate (NT)2
~ (109)2 to (1014)2
Coherence over an entire nano- or micro-sized object:
Can rival Avogadro’s number!
Long range force:
Low momentum transfer:
Monteiro et al., PRL 125, 181102 (2020), arXiv:2007.12067
Afek et al., PRL 128, 101301 (2022), arXiv:2111.03597
Xe (A~100)

## Slide 17
Impulses with nanospheres (Yale)
D. Moore, Yale
Recently demonstrated impulse sensing within 3x of the SQL for ~100 nm diameter (~fg mass) spheres
  Performed most sensitive search to date for certain classes of dark matter that primarily interact with the entire nanosphere
  Resolution 50 keV/c sufficient to detect with momentum of 1 MeV/c with SNR ~ 20
Schematic of impulse measurement:
PRX Quantum 6, 040367 (2025), arXiv:2508.00815
Measured force noise, 5 fg particle:
keV/c
keV/c
Backaction
Imprecision

## Slide 18
Dark matter search (nanospheres)
D. Moore, Yale
Performed search for dark matter with two nanospheres (total exposure ~5 fg x month)
  Tail of events above Gaussian noise background observed
  Conservatively set new limits on dark matter-neutron coupling, assuming events could either be dark matter or unidentified backgrounds
PRX Quantum 6, 040367 (2025), arXiv:2508.00815
Measured recoil spectrum:
Limits on dark matter/neutron coupling:
Sphere 2
Sphere 1
Natural directionality  any detection would be definitive!
Event rate vs sidereal time:

## Slide 19
Neutrinos
D. Moore, Yale
https://www.symmetrymagazine.org/article/the-hidden-neutrino

## Slide 20
Nuclear decays in mechanical sensors
D. Moore, Yale
Auger e-
x-rays
EC decay
decay
10 m sphere
10 MeV/c = 5x10-21Ns
100 nm sphere
10 keV/c = 5x10-24 Ns
D. Carney, K. Leach, and DCM, “Searches for massive neutrinos with mechanical quantum sensors,” PRX Quantum 4, 010315 (2023) arXiv:2207.05883
J. Wang et al., “Mechanical detection of nuclear decays,” Phys. Rev. Lett. 133, 023602 (2024), arXiv:2402.13257
Phase space trajectory:
Magrini et al., Nature 595, 373 (2021)
Tebbenjohanns et al., Nature 595, 378 (2021)
See, e.g.:
Levitated sensors are now reaching sufficient sensitivity to detect the miniscule forces imparted by single sub-atomic particles
  For weak decays, allows the momentum of each neutrino to be reconstructed on an event-by-event basis
Example force measurements for nuclear decay:

## Slide 21
Nuclear decays in mechanical sensors
D. Moore, Yale
Levitated sensors are now reaching sufficient sensitivity to detect the miniscule forces imparted by single sub-atomic particles
  For weak decays, allows the momentum of each neutrino to be reconstructed on an event-by-event basis
Phase space trajectory:
Magrini et al., Nature 595, 373 (2021)
Tebbenjohanns et al., Nature 595, 378 (2021)
See, e.g.:
Auger e-
x-rays
EC decay
decay
10 m sphere
10 MeV/c = 5x10-21Ns
100 nm sphere
10 keV/c = 5x10-24 Ns
D. Carney, K. Leach, and DCM, “Searches for massive neutrinos with mechanical quantum sensors,” PRX Quantum 4, 010315 (2023) arXiv:2207.05883
J. Wang et al., “Mechanical detection of nuclear decays,” Phys. Rev. Lett. 133, 023602 (2024), arXiv:2402.13257
Example force measurements for nuclear decay:

## Slide 22
Example measured gas collision:
Proof-of-principle (gas collisions)
D. Moore, Yale
Sensitivity needed to see single room temperature gas molecules collide with the particle similar to 𝜈
  Injected trace levels of heavy gases (Kr, Xe, SF6) and reconstructed the momentum transfers from individual collisions
arXiv:2604.18371
Collision spectrum vs. pressure:
Increasing p

## Slide 23
Radioisotope loading ( decays)
D. Moore, Yale
As a proof-of-principle, we have detected single 𝛼 decays with >m sized spheres
  Momentum is ~200 MeV/c (compared to 0.1-1 MeV/c for typical )
Have demonstrated loading of small quantities of 212Pb into trapped microspheres
Rn-220 decay chain:
Schematic of loading scheme:
220Rn
216Po+
Drift in E-field
212Pb
~100 nm
T1/2 = 56 s
T1/2 = 0.14 s
T1/2 = 10.6 h
3 m diameter SiO2 sphere
PRL133, 023602 (2024), arXiv:2402.13257

## Slide 24
Detection of single nuclear decays (charge)
Can detect single nuclear decays through the change in net charge of the particle
Example of measured charge changes vs. time:
decays
Auto-discharge
PRL133, 023602 (2024), arXiv:2402.13257

## Slide 25
Detection of single nuclear decays (recoil)
Reconstruct recoil of the entire particle correlated with the decay time
Recoil coincident with charge change:
Signal to noise = 13
PRL133, 023602 (2024), arXiv:2402.13257
Zoom to decay time:

## Slide 26
Gravity
D. Moore, Yale

## Slide 27
High frequency gravitational waves
D. Moore, Yale
By incorporating levitated particle in Michelson interferometer, can use high Qs to potentially resonantly enhance high frequency GW signals (10s - 100s of kHz)
Currently under development by Levitated Sensor Detector (LSD) collaboration
Aggarwal et al., PRL 128, 111101 (2022)
LSD Concept:
Projected sensitivity:

## Slide 28
Is gravity “quantum”?
D. Moore, Yale
Can we experimentally probe fundamental questions about gravity with micron-scale particles:
What is the gravitational field sourced by a spatial superposition?
Gravitational field sourced by classical mass:
Spatial superposition:
?
Figures from A. Markowitz
See also talk by D. Carney

## Slide 29
Is gravity “quantum”?
D. Moore, Yale
Figures from A. Markowitz
Semiclassical View:
Quantum View:
No entanglement, classical potential
Potential depends on wavefunction, masses entangled
Weak field gravity quantized by Bronstein (1936):
Physikalische Zeitschrift der Sowjetunion, 9, 2–3, p140–157 (1936)
Semiclassical gravity review: Miki et al., PRD 111, 104084 (2025)
Can we experimentally probe fundamental questions about gravity with micron-scale particles:
See also talk by D. Carney

## Slide 30
Canonical thought experiment
D. Moore, Yale
As more and more massive systems allow us to control them in quantum states, can we imagine testing this?
  Long history of considering these sorts of questions, going back at least to the 1957 Chapel Hill Conference
Feynman’s thought experiment:
Decoherence! (and backgrounds)

## Slide 31
Key figures of merit
D. Moore, Yale
Massive objects in quantum states
Small decoherence
Small electromagnetic interactions
Gravitational
potential
Tidal coupling
Gravitational entanglement rate
Slide from A. Markowitz

## Slide 32
Which massive system should we use?
D. Moore, Yale
Slide from A. Markowitz
Whittle, C… Zweizig, J. Science (2021)
mass
Pedalino, S., … Gerlich, S. Nature 649, 866–870 (2026).
atoms
macromolecules,
metallic clusters
levitated nanoparticles
Solid state acoustics
10 kg
delocalization
1e-19 m
2.8e-22 kg
1e-7 m
1e-11
9e-26 kg
0.5 m
1e-12
1e-18
2e-8 kg
Bild, M., … Yang, Y. Science 380, 274-278 (2023)
1e-18 m
1e-19
T. Kovachy e.a. Nature 528, 530-533 (2015)
Gravitational Wave Observatories
1.2e-10 m
Fig of merit
1e-18 kg
1e-22
Rossi, M., …, Novotny, L. PRL 135, 083601 (2025)

## Slide 33
Microdiamond concept
D. Moore, Yale
Several recent proposals to realize this type of concept, typically with levitated objects*
Bose et al. https://journals.aps.org/prl/abstract/10.1103/PhysRevLett.119.240401 (2017)
Marletto and Vedral, https://journals.aps.org/prl/abstract/10.1103/PhysRevLett.119.240402 (2017)
Anupam Mazumdar, University of Groningen
Gravitational interaction of two superpositions:
(Macroscopic Superpositions Towards Witnessing the Quantum nature of Gravity)
MAST-QG:
*Also some proposals with tethered ~mm sized masses (MIT, ISTA Austria)
Initial concept:
Stern-Gerlach interferometer using single nitrogen-vacancy center in a nanodiamond
Non-gravitational interactions shielded by conducting sheet
Conceptual experimental parameters:
  Particle mass 10 pg (m diameter)
  Superposition size 50 m
  Particle separation 30 m
NV spin:

## Slide 34
Summary
D. Moore, Yale
Optomechanical systems are revolutionizing how we measure tiny forces and accelerations acting on masses in the lab
Many weakly interacting phenomena of interest in fundamental physics may produce such forces
A wide variety of new systems are currently under development, with applications to weakly interacting phenomena such as dark matter, neutrinos, and gravity

## Slide 35
Have developed hybrid magnetic/optical trap for nano- and micro-diamonds based on design by Brian D’Urso’s group (MSU)
Diamagnetic trapping with optical readout and control, allowing multiple diamonds to be co-trapped
Photo of trapping chamber:
1 mm
Front view:
Side view:
N
S
N
S
Zoom to trap:
Trap design based on: Sci Rep 6, 30125 (2016), [B. D’Urso group]
35
Diamagnetic trap for microdiamonds
Plots and figures from A. Markowitz
D. Moore, Yale
~44 Hz, x-resonance
Increasing feedback damping
Cooling center of mass
Reinjecting sensing noise
Feedback cooling to sub-K temperatures:

## Slide 36
Sterile 𝜈
D. Moore, Yale
Search for keV-MeV steriles by reconstructing recoil momentum in weak decays
If sterile mixes with , would observe “wrong momentum” in fraction of decays
Surround array of spheres with position sensitive detectors to reconstruct momentum
Bolton et al., JHEP 2020, 170 (2020), arXiv:1912.03058
Masses:
m1
m2
m3
m4
Experimental limits on sterile 𝜈 mixing with 𝜈e:
Mixing with ,
Sterile mass, [GeV]
“Minimal” DM candidate?
Nanospheres
Detector concept:
Nanosphere array
Scintillator + SiPM arrays

## Slide 37
Projected sensitivity versus livetime:
Example electron capture decay (37Ar):
Projected sensitivity
D. Moore, Yale
If a keV – MeV mass sterile 𝜈 mixes with the light 𝜈, then expect small fraction of decays to emit a heavy 𝜈
Possibility to probe many orders of magnitude beyond best existing experiments with mechanical sensors
= 750 keV
1 sphere month
10 sphere years
1000 sphere years
100 nm sphere
1 month
PRX Q 4, 010315 (2023) arXiv:2207.05883