## Slide 1
Experience with a
Digital Twin Deployment on the CLARA Facility
Making a brighter future through advanced accelerators
Matthew King
On behalf of: Alexander Brynes, Nasiq Ziyan, James Jones, Mark Johnson, David Dunning
Contact: matthew.king@stfc.ac.uk

## Slide 2: Contents
Introduction to AI and Digital Twins at CLARA and other UK facilities
Digital Twin framework
  Framework overview
  Lattice description
  Digital Twin cookbook
  Deployment example
Lessons learnt
The need for an AI test facility

## Slide 3: AI and Digital Twins at CLARA and other UK facilities
Long-standing software development towards AI and digital twins for accelerators at STFC Daresbury Laboratory’s CLARA accelerator since ~2015
CLARA is a 250 MeV electron accelerator test facility
Rutherford Appleton Lab/Harwell Campus
Since 2022, there has been close collaboration between CLARA and ISIS neutron and muon source (both working with SLAC) to develop cross-facility AI and DT tools
This work is extending with support from the Ada Lovelace Centre + Scientific Computing department
Parallels to MOAT
Daresbury Lab/Campus
CLARA

## Slide 4: Software Packages @ ASTeC
LAURA (Lattice Architecture for Unified Representation of Accelerators)
  YAML-based lattice definition
  Standardized, extensible schemas
  arXiv, Github, RTD
CATAP (Controls Abstraction Towards Accelerator Physics)
  Templated Middle Layer for high-level control
  Generated based on LAURA definitions
  arXiv, Github
SARABI (Soft Architecture for Rendering Automated Backend IOCs)
  Templated CA/PVA IOCs
  Generated base on LAURA definitions
  arXiv, Github
SIMBA (Simulations for Integrated Modeling of Beams in Accelerators)
  Unified simulation framework for particle tracking using LAURA definitions
  Supports:
    ASTRA, GPT, ELEGANT, Ocelot, CSR-Track, Cheetah, Wake-T, Xsuite
    Beam-based surrogate models
  arXiv, Github, RTD
JANUS (Joint Accelerator Network for Unified Simulation)
  Digital Twin framework generated from LAURA definitions
  SIMBA handles tracking
  CATAP handles control system interactions
  arXiv, Github

## Slide 5: JANUS Overview
LAURA
[Lattice Definition]
CATAP
[Control system middle layer]
SIMBA
[Simulation framework]
SARABI
[CA/PVA IOC generator]
GENERATES
GENERATES
INGESTS
JANUS
A Digital Twin Framework
DTs generated from LAURA Lattice Definitions
Papers:
CATAP: arXiv:2509.19794
SIMBA/LAURA: arXiv:2604.19103
JANUS: arXiv:2604.19101
A generalizable Digital Twin framework for particle accelerators:
Virtual prototyping | Online/Offline optimisation | Integrated training environment
COMBINE

## Slide 6
Lattice Description
How do you describe an accelerator lattice?
It depends who you ask!
Physicist:
Components that use EM fields to direct, steer and focus beams of particles.
Description format:
Simulation code lattice files
Controls Engineer:
Elements that can be used to change or monitor the beam using setpoints, currents and voltages
Description format:
Control system configuration files (i.e. EPICS database)
RF / Magnet / Diagnostics expert:
In-depth knowledge of the physics and design of specific components.
Description format:
Models of components and their fields; direct control of hardware
Mechanical Engineer:
Elements physically connected, aligned and placed on girders.
Description format:
CAD models and drawings
Can there be an all-encompassing description of a lattice that will satisfy everyone?
(Perhaps not, but for a digital twin/shadow we at least need to unify the control system and simulation descriptions.)

## Slide 7: History of Lattice Descriptions @ CLARA
Pre-2017 lattice definitions:
  Simulation: Mathematica/MATLAB projects
  Control System: PVs for control defined in applications (hard-coded)
  Engineering: Centralized server for diagrams etc.
2017-2019 lattice definitions:
  Simulation: YAML definitions with package-specific schema
  Control System: Middle-layer specific format with bespoke parser
  Engineering: Centralized server for diagrams etc.
2019 – 2025 lattice definitions:
  Simulation: YAML definitions with package-specific schema
  Control System: YAML definitions with middle-layer specific schema
  Engineering: Centralized server for diagrams etc.
2025 – Current lattice definitions:
  Simulation: LAURA lattice definitions
  Control System: LAURA lattice definitions
  Engineering: Centralized server for diagrams etc. (linkable in LAURA lattice)
  Concurrent with PALS efforts in US

## Slide 8: How to Design a Digital Twin (A recipe of trial and error..)

## Slide 9: Digital Twin Cookbook
Recipe:
Digital Twin Loop à la Accelerator
Serves
Continuous optimization and analysis of one accelerator system
Preparation Time
A few months of integration
Cooking Time
Forever (or until someone switches the machine off)
Ingredients
Machine
1 functioning accelerator
Network access to the control system
A list of machine parameters
Method for publishing results back to operators
Knowledge of:
  What can be changed through the control system
  What can be measured through the control system
Simulation
1 functioning simulation model
A method for interrogating simulation results
Knowledge of:
  Machine-Simulation mappings
  Unit conversions
  Lookup tables
  Calibration curves

## Slide 10: Digital Twin Cookbook
Step 1: Harvest Fresh Machine Settings…
Collect the latest settings from the accelerator*:
*Chef's Suggestion:
A control system middle layer, such as CATAP can make it easier to grab machine parameters
Step 2: Prepare the Simulation Inputs
Translate machine settings into simulation parameters*.
*Chef's Suggestion:
Keeping your conversions and mappings in a LAURA lattice can quicken this process!
Control System
EPICS to Lattice
Lattice API
Lattice DB
Lattice API
Lattice to SIMBA
SIMBA API
Notes: Magnet currents
RF cavity settings
Laser parameters
Any other relevant deviceconfiguration
Decide whether to use:
Setpoints (what you asked for)
Readbacks (what you actually got)

## Slide 11: Digital Twin Cookbook
Step 3: Start the Tracking*
*Chef's Suggestion:
The SIMBA software package can ingest a LAURA lattice for tracking
Step 4: Wait Until Tender
Monitor simulation progress using one of the following techniques:
Traditional slow-cooker method
  Poll the simulation status periodically
Modern smart-kitchen method
  Subscribe to a message broker, kafka for example.
  Receive a notification when the simulation is finished
Traditional tracking can be slow!
  SIMBA is able to use AI-guided culinary automation (surrogate models)
SIMBA Instance
SIMBA API [SIMBA instance + kafka]

## Slide 12: Digital Twin Cookbook
Step 5: Retrieve the Results
Extract the simulation outputs
Store settings and results in database
  Beam distributions can be challenging for large macroparticle numbers
Step 6: Plate and Serve
Publish the simulation results
Step 7: Repeat
Return to Step 1 and continue indefinitely…
Thanks to the database, preparation times reduce with use!
SIMBA API
SIMBA to Lattice
Lattice API
Lattice DB
Lattice API
Lattice DB
Lattice to EPICS
Control System

## Slide 13: Digital Twin Cookbook
Chef's Notes
The secret to a successful Digital Twin is maintaining strict consistency of parameter mappings and units.
Most failed recipes result from bad conversions between machine and simulation parameters.
Once you can verify your simulation pairs well with the machine, you can begin to investigate advanced "twinning"
- See future recipes…
NEW!
JANUS
A Digital Twin Framework
DTs generated from LAURA Lattice Definitions
From the creators of: SIMBA, CATAP, and LAURA

## Slide 14: JANUS Framework
Accelerator Lattice
The ground source of truth about the accelerator, containing:
  Element definitions
  Control system information
Based on LAURA format
Virtual Control System
Generated procedurally based on the lattice
Sends signals to update simulation model when changes are made
Can be swapped for physical controls
Simulation Model
Can use particle tracking codes or AI models
Chain tracking together for multiple machine sections defined in LAURA
Based on SIMBA package
Lattice Database
Each run is associated with a UUID and saved to a database
Settings and Results are stored in SQL
To be used for surrogate model training
Accessible using GraphQL interface via Lattice API
JANUS Server
Lattice DB
Lattice API
Lattice to SIMBA
SIMBA to Lattice
SIMBA API
Tracking Codes
ML Models
JANUS Client
EPICS to Lattice
Lattice to EPICS
Control System
Web Frontend
User Application
Deployment Modes
Basic Twin mode – trigger simulations based on physical control system values, results sent back
Dev mode – trigger simulations based on virtual control system values
Advanced Twin mode – Bi-directional, autonomous feedback between physical control system and JANUS

## Slide 15
JANUS Framework - Control Room Deployment
Comparison between measured and simulated bunch lengths after final linac (compression scan) -- both set up only using the control system.
Web-based interface to JANUS:
PVs can be monitored and specific PVs used to trigger simulations.
Real-machine version of JANUS can be accessed from any control room PC.
Same Framework, accessing Physical IOCs
Virtual diagnostics (6D phase spaces, Twiss) are available for all entries in the database, also available via PVAccess on physical machine.

## Slide 16: Lesson Learnt
During design/deployment of JANUS:
A consistent, structured, ontology that you can query is vital
  Reliable foundation to build software stack from
  Software can become more templated
  Rich-text descriptions can be useful for LLMs
Multiple access points provide flexibility:
  Run simulations via the web
  Access database via the web
  App prototyping with virtual control system with/without simulation data
Model Matching Lessons:
There are plenty of simulation parameters that aren't one-to-one with the machine
Machines are complicated and modelling every interaction is complex
Focusing on how information is exchanged between machine and simulation is worthwhile
  There are lots of "gotchas" hidden here
The measure of trust is not clear when the machine can drift, setups can change, and hardware can break!
  Context and intention of the data is not always captured

## Slide 17: Conclusions
None of the items in this talk would have been possible without CLARA acting as a test facility
To develop an advanced digital twin needs continued regular access to beamtime:
  Parasitic: Useful, but it can make data hard to contextualize
  Designated: needs preparation to get quality data
  Significant work is still required:
    Advancing DT: Model matching, Optimizations, Automated feedback etc.
    Extending DT: Connection to experiments, Robotics, Non-simulation parameters
Developing an advanced digital twin solution and an AI test facility in combination can have widespread benefits for all accelerators
Papers:
CATAP: arXiv:2509.19794
SIMBA/LAURA: arXiv:2604.19103
JANUS: arXiv:2604.19101

## Slide 18
Thank you
On behalf of: Alexander Brynes, Nasiq Ziyan, James Jones, Mark Johnson, David Dunning
Contact: matthew.king@stfc.ac.uk

## Slide 19
Appendix

## Slide 20: LAURA
Attempts to provide an "all-encompassing" definition for an accelerator
Element definitions can contain:
  physical, simulation, controls, electrical, manufacturer information
Elements are chained together into sections
Machines are created from an ordered chain of sections
LAURA API allows this to be done in either YAML or programmatically in python
Translator Module:
  Export the lattice to codes supported by SIMBA
  Import lattice in supported codes: ELEGANT

## Slide 21
SIMBA
SIMBA is a python package to enable simulations of (linear) particle accelerators.
The lattice is derived from the LAURA structure.
Abstract away the details of underlying tracking codes:
Consistent beam tracking across multiple beam physics modalities (i.e. RF gun, linac, FEL, plasma...).
Does not require expertise in multiple codes!
Can also call ML models of lattice sections.
SIMBA
Abstract input files away
Interact only with python methods
Code-agnostic input/output
Convert input/output data to standard formats
Learn new “abstract” code
SIMBA repo
Data flow in SIMBA
Start-to-end CLARA simulation

## Slide 22
CATAP
Controlling LCLS magnets using CATAP middle layer, arXiv.2509:19794
Control Room Application
Control Room Script
CATAP Python Modules
Channel Access
Controls Network
IOC
IOC
IOC
IOC
IOC
IOC
A middle layer is an abstraction layer between the control system and the control room that simplifies the ways in which operators interact with the machine programmatically.
Since the LAURA structure defines the control
system variables for an element, we can:
Create virtual accelerator elements from the same source of truth as the simulation model.
Programmatically construct an entire virtual accelerator.
Programmatically construct accelerator-specific middle layer with a uniform architecture.
Controlling LCLS magnets using CATAP middle layer, arXiv.2509:19794
PV Access

## Slide 23: Model Matching with JANUS
Task
Try to find a set of tractable problems to:
  Determine how close the model is to machine settings;
  Find out where the discrepancies are;
  Figure out whether (a) the model and/or (b) the machine need to be adjusted.
Initial Plans
Match photoinjector model to machine
Using single screen, perform an N-dimensional parameter scan, varying as many things as possible (within reasonable limits).
Monitor beam distribution on screen.
Simulate these setups in JANUS
CATAP can load settings onto virtual control system
Next Steps
Extend these scans to post-linac and spectrometer
Incorporate Twiss measurements.
Find discrepancies between the model and the data.
Use this large dataset to learn how to do more advanced filtering / inference

## Slide 24: CLARA FEBE Layout
Example Technical System | CLARA Front End (35 MeV) | CLARA (250 MeV) | CLARA FEBE (250 MeV)
RF Structures | 2 | 7 | 7
Magnets | 22 | 77 | 126
Diagnostic Systems | 13 | 65 | 94
Vacuum Gauges and Pumps | 57 | 109 | 155
First experiments in the Full Energy Beam Exploitation (FEBE) user area took place in early 2026

## Slide 25: Established AI/ML and digital twin expertise within ASTeC
ML-based laser/electron bunch temporal shaping:
https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.27.041602
Electron bunch phase space tomography:
https://iopscience.iop.org/article/10.1088/1748-0221/19/07/P07013
Long-standing community building since ~2018
AI-based beam optimisation and diagnostics
Auto-Generating Digital Twins for Particle Accelerators
Closing the Loop: Deploying Auto-Generating Digital Twins for Particle Accelerators
https://arxiv.org/pdf/2604.19101