## Slide 1: Outlook for AI/ML tools for the SNS accelerator
July 15, 2026
A. Zhukov, K. Ruisard
On behalf of SNS accelerator ML team: ORNL, JLab, PNNL and others

## Slide 2: Spallation Neutron Source
Use-cases for AI/ML
  Anomaly detection
  Loss optimization
  Errant beam prevention
  Human interface with LLM/RAG
Notes: H- accelerating to 1.3GeV
Charge exchange at the foil is the biggest issue

## Slide 3: The SNS Linac is currently operating at 2.0 MW
(as of April 23, 2026)
The Proton Power Upgrade increased SNS beam power on target from 1.4 MW to 2.0 MW, mainly through 30% increase in beam energy (1 GeV  1.3 GeV)
1.4 MW baseline design
2 MW
Completed PPU installation
Cost of improved performance is tighter constraints on activation, unplanned downtime, maintenance schedules
Even a 20-year-old, relatively stable machine has a shifting “machine state”
2.8 MW 10Hz equivalent
Notes: Ee don’t understand our machine model very well. However, the SNS Linac is running really well
2 decades of operational experience
Smooth commissioning due to empirical understanding
-----------------------------
Beam loss outlook: we’re coming up on 2 years (and 3 shutdowns) of PPU beam
How did losses change? Activation levels went up…then down again. Losses are currently in-line with expectations.
ring activation is higher than expected (very localized spot ~1700 mrem/hr at a foot!)
PPU facts:
Commissioned in about 4 weeks in June/July 2024
Over 1 ms, 1000 pulses of negative hydrogen ions, each 700 ns long are accelerated to 1.3 GeV or 0.91c
Accumulated 700 ns long pulse of 1.5 E14 protons is extracted to target 60 times a second – roughly 32 kJ per pulse

## Slide 4: Challenges to SNS operations
(1) Maintenance! Our goal is to reduce activation and reduce failures
Predicting hardware failures on both long and short time scales gives us…
More lead-time to schedule maintenance or intervene
Fewer instances of spilled beam loss
(2) Beam physics in linac does not operate as designed; empirical intervention has been more successful than model-based interventions
SNS Systems downtime: interruptions in Neutron Production can lead to rescheduling of experiments
Notes: Main causes for downtime Target and RF systems

## Slide 5: Pulse structure and timing
Time scale for use cases
  Anomaly detection in Target support loops (min/hr/days)
  Optimization of beam losses (sec/min/hr)
  Errant beam prevention (ms)
  Human interface with LLM/RAG (s)
AP physics model works with one bunch doesn’t have halo details
Macro-pulses 60Hz
16.67mS
RF bunches 402.5MHz
Empty RF only pulse
The only way we can affect current macro-pulse is MPS trip!
Mini-pulses (turns) 1MHz
The fastest optics change can be applied at ~ 2Hz

## Slide 6: Target Anomaly Detection
Flag anomalies using reconstruction (autoencoders, PCA) and tree-based (Isolation Forest) ML
STAR system (System Tracking And Reliability)
Automatically detect anomalies
> 30 interdependent systems
Target systems
Support personnel
24/7 and long-term improvement
Event tracking
STAR system
entry
Archiver
data
data
Archives relevant data
Learns from archived data
Observes new data
Generates reports
Learns from feedback
ML
data
anomaly report
report feedback
data
Credit D. Winder
A. Raj
Notes: ○ Most developed use case
○ person -in -the loop example; if anomaly is flagged, target operators should have a look.
○ Look at temperature, pressure in mercury loop; predict anomalies based on time series.

## Slide 7: Target Anomaly Detection
A. Raj, et al, “Automating Anomaly Detection for Target Systems at Spallation Neutron Source” NPIC June 2025 Chicago.
Anomalies (•) It shows anomalous high increase in the pump tank and vent line pressures while the beam power ramped.
Best model detected 13 previously unobserved anomalies with 11 being alert worthy
Physics model created for future physics informed ML
Running ML analysis only once a week, going to 10m: then we can prevent downtime
Results
Integration with STAR system
Credit D. Winder, A. Raj

## Slide 8: Errant Beam – beam is the best diagnostics tool?
MEBT
Linac
Target
2.5 MeV
186 MeV
Ring
H+
H-
1300 MeV
CCL
SRF, b=0.61
RFQ
HEBT01
CCL102
DTL
SRF, b=0.81
Phase waveforms
(~1MS/s)
Beam current waveforms (~100MS/s)
HEBT01- HEBT06
Prevention of errant beam pulses
Errant beam pulse beam losses can result in lower SRF cavity performance and activated beam lines. Initially use the differential current monitor
Use pulse before as abnormal
Source
Example errant beam
Beam lost
Notes: DCM direct comparison of upstream and downstream
120k point per pulse at 60Hz
Inspector tool to look into faults or normal pulses

## Slide 9: Errant Beam using phase data (from BPMs)
Phase data
Phase has a direct relationship with the acceleration
We have many Beam Position Monitors with phase data
Potentially immediately applicable to live machine
Time Range​ | Alarms Prevented​ | Pulses Aborted Per Day​
Nov. 13-20, 2025​ | 28​ | 2,429​
Nov. 20-27, 2025​ | 2​ | 2,128​
T. Robertson
History of
leads to
Notes: BPM provides phase – bunch time of arrival
24 hours ~ 5M pulses
10^-3 false positive allowed. 5M pulses per day. Keep charge on target fixed

## Slide 10: Beam Loss Optimization
Example of beamline activation due to losses
Measured beam losses lead to activation
X[mm]
x’[mrad]
1e-6 boundary
1e-2 level
5xRMS
1xRMS
Aleksandrov
Shishlo
Notes: We don’t have a model for losses
  Is it halo?
  We know IBSt affects us
  Large beam is bad, small beam is bad
We need to minimize losses to reduce activation
Operators perform a lot of time consuming manual loss tuning by changing
  Cavity phases (less amplitudes)
  Quad gradients
  Dipole correctors

## Slide 11: Beam Loss Optimization – RL or not RL ?
Problems
  Short pulse doesn’t work, BLMs too noisy
  1Hz too slow due to RF cavity learning
  Needs production at 60Hz to start experimenting
Virtual Accelerator
Optimization
Proxy server
Safeguard
Accelerator Network
Edge computer
Accelerator
Proxy
Necessary to limit action to stay within operating envelope
  Splits large steps into smaller safe steps
  Aborts stepping if constraint violated
  Can redirect optimization
Beam loss in SCL and HEBT, optimizing cavity phases
Losses in HEBT11a push back against lowering sum
Notes: Any change on production machine requires authorization and potentially a configuration control approval
Let’s approve proxy once and then be absolutely flexible in agents without EPICS access
Test everything on virac

## Slide 12: RL agents
Two main approaches
  Model-Based RL: The agent can predict the reward for some action
  before performing it thereby planning what it should do. Model-Free RL: The agent needs to carry out the action to see what happens and learn from it.
https://spinningup.openai.com/en/latest/spinningup/rl_intro2.html
SciOptControlToolkit
Control policy
Position along accelerator
Transverse displacement
physics model
DRL
Initial perturbed
Notes: Tried Deep Reinforcment learning trained on virac
No physics in the agent
Physics is inside virac
Worked on real machine for orbit correction
If we have a model do we need RL?

## Slide 13: LLM usage for human interface and eLog analysis
MPS trips and generates a log of related events
Small test batch pre-processed
Find pre-processed entry that’s most similar to fault
Displays
  Fault
  Cause
  Recovery guidance
  Personnel contacted
  Proposed elog entry
  Warnings and evidence
  Button to grab raw elog entries from event
G. Gallimore

## Slide 14: Specific needs of pulsed hadron machine
Harder:
, there is no such thing as independent control of linac cavities
  Unless you have a very precise model
Maintenance is difficult to schedule, due to high activation
Pulsed mode implies certain time and data transfer constraints
Easier:
Relaxed constraints on beam parameters - many knobs can be changed without affecting beam on target profile.
We never tune beam for users, fast optimization and flexibility is not a goal.

## Slide 15: Errant Beam infrastructure
1 PB
Storage
10 Gbps
GitLab Runners
Container(s)
artifacts
Mindmeld Nvidia GPU Server
Edge Server
DCM
BPM
Enterprise Network
Accelerator Network
ML Model
External Storage
user
Icarus
Predictions
Operator view
Data Tagging
A. Raj
Notes: Limitations of existing control network

## Slide 16
Weekly Anomaly Logging and Inference
STAR
A. Raj

## Slide 17: Data
MEBT
Linac
Target
2.5 MeV
186 MeV
Ring
H-
1300 MeV
CCL
SRF, b=0.61
RFQ
DTL
SRF, b=0.81
8xWaveforms 1MS/s (~1MB/s)
4xWaveforms 100MS/s (~100MB/s)
Streaming not typical for SNS Accelerator
Waveforms ~1ms long, repeated at 60 Hz
Scalars at 60 S/s
Source
Storage
(1 PB)
Phase
Beam current
Archiver
40xScalars at 1S/s
(~200 B/s)
Pressure, Temperature,
Flow, etc
Losses,
Magnet Settings
350xScalars at 60S/s
(~20 kB/s)
Each pulse
Each second

## Slide 18: Desired infrastructure
We implemented ML infrastructure on top of existing Controls network
Heavily rely on one GPU server behind firewall – obviously, single point of failure (research mode)
Lacking network speed to connect diagnostics to training – various workarounds
Potential challenges/decisions for future AI-friendly accelerators
Separate dedicated network?
Edge inference or not?
Real time no-FPGA turnaround for inference ~ 10mS scale
Distributed storage (another network?) and/or distributed training?
Virtual accelerator should be there from the design stage

## Slide 19: Dream capabilities
Multi-source anomaly detector – voting system?
Agentic operator - propose interventions depending on anomaly and based on historical experiences. Learn patterns from operators
Global optimization - slow optimization problem where large changes may be caused by variables outside controls problem
Continual learning
  When to re-train?
  How to forget irrelevant part while keeping important one
Robust digital twin infrastructure - where to put physics model?
  RL action
  Training only
Kishan’s talk

## Slide 20: Anticipated headwinds for SNS
Cyber security
  live inference should be local
  training potentially
Data management and size of data Over 1 year, errant beams project accrued 1 PByte from 6 Beam Position Monitors and 1 Differential Beam Current Monitor
Is RL an answer to 10+ dimensional optimization problems?
Conservative approach to operations
  How can you certify procedures that are not reproducible? Can they be benchmarked? Can we guarantee long-term stability?
  When something goes wrong with the agent, how do you track down the cause? How can you be sure you've fixed it?
  What expertise do you lose when outsourcing routine tasks to agent?

## Slide 21: Questions?