## Slide 1
S. Bettoni, A. Latina
WP1: A. Grudiev1, S. Bettoni2, P. Craievich2, S. Doebert1, A. Latina1, J.-Y. Raguin2, P. M. Reviriego1, R. Zennaro2
SLAC collaboration contact person: B. O’Shea3
1 CERN
2 Paul Scherrer Institute
3 SLAC
Injectors and Beam Physics for Future Accelerators, SLAC, 14th September 2026
FCC-ee linac design and synergies with FACET-II

## Slide 2: Outlook
FCCee injector: focus on the high energy linac
  Design strategy
  Results
Possible experiments at FACET-II:
  Done
  To be done
  Under investigation
Conclusions and outlook

## Slide 3: The FCCee injector layout: focus on the high energy linac
 | Initial (@ DR) | Final (@ TL to booster)
Normalized (ex,ey) (mm.mrad) | (10,1) | <(20,2)
Energy spread (%) | 0.7 | 0.70.1
Bunch length (mm) | ~5-7 | 4
Jitter amplification (final) | -- | <2
Jitter amplification (along linac) | -- | <1.5
Special requirement | Vary the bunch charge from “0” nC to 5 nC | 

## Slide 4
FODO sections

## Slide 5: Wakefields along the linac
Wakefield
Longitudinal
Static
Emittance growth due to components alignment
Static
Dynamics
Amplification of angle/orbit jitter
Transverse
Impact on the energy spread
Optimization/mitigation
Goals
Short range wakefield  single bunch effects
Long-range wakefield  multi-bunch effects
Optics along the linac: kind of lattice, phase advance/cell, distance among quadrupoles
Beam parameters: bunch length
Machine components parameters: RF structures operating phase and length
Steering algorithms: one-2-one, DFS, WFS
Minimize the projected emittance growth
Maintain orbit stability
Maximize transport efficiency
Considered wakefield sources: RF structure and resistive wall

## Slide 6
Static effects
Mitigation of the emittance growth

## Slide 7: Static effects: assumptions and procedures
One-to-one orbit correction
  Orbit xi with errors computed
  Response matrix computed
  Correctors strengths calculated (SVD) to steer the beam
Dispersion Free Steering (DFS)
  Orbit xi with errors computed
  Response matrix computed
  Off-energy beam (different RF phase) orbit xΔE,i computed
  Response matrix computed
  Correctors strengths calculated, minimizing 2 defined as:
Wakefield Free Steering (WFS)
  Orbit xi with errors computed
  Response matrix computed
  Off-charge beam (different bunch charge) orbit xΔE,i computed
  Response matrix computed
  Correctors strengths calculated, minimizing 2 defined similarly to before
Steering algorithms
  Taken emittance at 90% of the “good seeds”
BPM
Offset x, y = 30 mm rms
Resolution x, y = 10 mm
Gaussian distributions
Imperfections (expectations from SwissFEL)
RF cavities
Offset x, y = 100 mm rms
Gaussian distribution
Quadrupoles
Offset x, y = 100 mm rms
Gaussian distribution
Distribution of the final emittances (100 seeds)
Cumulative sum distribution of the final emittance

## Slide 8: Heritage from the different designs
Best beam quality for on-crest operation
Chirp for the bunch decompression necessary for the downstream sections
(Maximum energy gain)
Optimum splitting of the linac in sub-sections  better beam quality (avoid residual error propagation)
On-crest operation
Linac “binning”
Investigated several designs  learning from one to the other one

## Slide 9
Dynamic effects
Not amplify or even better damp any orbit jitter
Amplification
Damping
Stability

## Slide 10: “Painting” of the transverse phase space and jitter
Bunch
Jitter amplification computation:
  Single bunches distributed on a circle (in 10 degrees step size) injected to the line with different (x,x’) or (y,y’)
  Computed the area in the initial beam transverse phase space  A0
  Computed the area in the final beam transverse phase space  AF
  Jitter amplification, JA, is defined as the ratio of the square root areas 
Advantages of the use of this metric:
    JA is independent on the initial jitter
    JA considers the effect on the full transverse phase space, and not only in x OR x’ (y or y’)  it does not depend on the location where it is determined (beam waist or any other Twiss alpha)
    Given JA of a generic kth section, , the total jitter amplification is given by the product of all of them for single- and multi-bunch
    Given the initial jitter , the jitter at a given location is computed as:
x
x’
Approach already applied to the CLIC design

## Slide 11: Dynamic: example of dependences
SLC design: several quadrupoles spacing along the different sections
Save cost and simplify  less quadrupoles  more spacing among the quadrupoles
 weaker for Beam Break Up instability
Large quads separation lattice for FCCee HE linac
Closer quads lattice for FCCee HE linac
FACET lattice (former central sections of SLC)

## Slide 12: Dynamic: single-bunch
The HE linac is optimized to damp any incoming beam transverse jitter!
Amplification
Damping
page 12
Optimized parameters:
    “Kind” of lattice (number of quads/RF structure)
    Bunch length
    RF structure aperture and length
    Quadrupoles spacing
    Length of the RF structures
    Phase advance per cell
    Combination of the parameters
Essential to experimentally verify this effect

## Slide 13: Dynamic: multi-bunch effects
Considered three wakefield kick scenarios:
  Kick on the next bunch (simulates damping)
  Constant kick (pessimistic scenario)
  Exponentially decreasing kick (simulates detuning)
Detuning was chosen as a mitigation technique for the damping of HOMs and was found to be highly effective.
No multi-bunch limitation was found for bunch spacings of 25 ns with the baseline 3 GHz structure with iris aperture of a/λ = 0.12.
ECHO2D simulations show recoherence appearing at t ≥ 100 ns, which manifests as an increase in the jitter amplification for bunch spacings ≥ 30 ns.
Courtesy of A. Latina, A. Grudiev, A. Kurtulus

## Slide 14: The zoo of the effects: optimize what by what?
Overall design: single bunch effects
Multi- bunch effects
Static effects: Emittance growth
Dynamic effects: Jitter amplification
Aperture and length of the RF structure, lattice
Wake suppression
Main results are based on RF-Track with some benchmarks with other codes

## Slide 15: The winner configuration
  RF frequency: 2-6 GHz
  RF aperture: 10-25 mm
  RF structure length: 2.5-4 m
  Optics (phase advance per cell): 70-140o
  Kind of lattice: 1Q2RF and 2Q2RF
Investigated space parameters
Criteria for selection
  Beam dynamics  beam parameters
  RF efficiency  Reff
  Cost  number of elements and footprint
  1-to-1 and DFS
  1-to-1, DFS and WFS
  WFS not included here (De ~-0.1 to -0.15 mm.mrad)
Correction algorithms

## Slide 16
Compression, decompression and more

## Slide 17: From the DR to the HE linac beam preparation: BC
Bunch length (rms): 5 mm  0.8 mm
Chirp/dechirp in integer number of modules (1 module = 4 RF structures)  margin to compress differently, if necessary
Expected horizontal emittance growth~15% for the presently assumed bunch length coming from the damping ring
Bunch from the DR too long to travel through the HE linac (@ GHz frequency) due to the energy spread cumulated (RF curvature)

## Slide 18: BC: full 6D beam characterization
Noise on beam size measurement = 1%
Transport
Transverse phase space measurement
Longitudinal space measurement
Control of the optics along and downstream of the chicane
Full characterization of the bunch in the (6D) space before going to the HE linac of the FODO section

## Slide 19: Energy compressor (EC)
Goal: manipulate and stabilize the bunch longitudinal phase space
Bunch length (mm) | dp/p (%) | Dt (ps) | Dp/p (%)
4.02 | 0.11 |  | 
4.04 | 0.11 | 5.1 | -0.02
4.06 | 0.10 | 9.7 | -0.04
4.08 | 0.09 | 15.3 | -0.07
Achievements:
Target bunch length: 4 mm
Target single-bunch energy spread (extra margin factor 3): 0.1%
Bunch-to-bunch energy offset<0.1%
Energy offset  time offset tolerable (booster group specs)
Advantages of using the EC:
  EC allows operating the HE linac on-crest: optimal for the beam quality and energy efficiency
  We need to decompress in any case the bunch before sending it to the booster (4 mm too long to travel through HE linac)  energy chirp and (chicane) necessary
  Improved the robustness of the machine to the bunch charge variation from “0” to 5 nC, and the energy stability in the downstream transfer line (dispersive line)
  Bunch length and energy spread can be independently set
Advantages of the EC located at the end of HE linac:
  Energy stabilization  impactful along a dispersive section like the several km downstream transfer line
  Not possible to install it at the TL end, because of the large R56: out of the linear part of the RF and bunch-to-bunch time separation too large for the booster
  An intermediate location may be considered, but RF at 3 GHz must be brought underground  presently not the baseline, but possible from the BD point of view (see FCC week 2023)
page 19
D
Energy
(intra/inter
-
bunch)
D
Time
Target energy difference in the bunch (single bunch) and/or in between
the bunches (multi
-
bunch)
HE
LINAC
f1
RF EC
f2
RF
D
phase
R
56
DR
T
O
THE
BOOSTER
BC
The “golden pulse”

## Slide 20: From the BD design to the technical design
BC section
EC section
FODO section
 | Initial (@ DR) | Final (@TL to booster) | Design final (@ booster)/along
Normalized (ex,ey) (mm.mrad) | (10,1) | <(20,2) | (<15, 1.36)
Energy spread (%) | 0.7 | 0.70.1 | 0.1
Bunch length (mm) | ~5-7 | 4 | 4
Jitter amplification (final) | -- | <2 | 0.95
Jitter amplification (along linac) | -- | <1.5 | 1.20
All the requirements fulfilled with the present design (possible further improvements under considerations)

## Slide 21
Experimental tests at FACET-II
Experimentally verify what found in simulations

## Slide 22: FCCee – SLAC collaboration at FACET-II
FCCee/SLAC ongoing collaboration on several topics (financed by CHART/CERN/Beam4US grant). SLAC contact person: B. O’Shea.
page 22

## Slide 23: FCC-ee injector complex layout
Aspects proposed for experimental verification mainly for electrons (ongoing):
  Bunch generation for top-up injection: charge scan from “0” nC to 5 nC
  Emittance versus bunch compression at nC charge
  Transverse jitter amplification and damping
  Test of the energy compressor
  Other methods to ease the setup of the FCCee linac in the shadow of other activities: impact of the RF focusing on the optics, fast RF phasing, …
Aspects proposed for experimental verification mainly for electrons (ongoing):
  Bunch generation for top-up injection: charge scan from “0” nC to 5 nC  see S. Doebert’s presentation
  Emittance versus bunch compression at nC charge  next to come
  Transverse jitter amplification and damping  done (see in few slides)
  Test of the energy compressor  postponed
  Other methods to ease the setup of the FCCee linac in the shadow of other activities: impact of the RF focusing on the optics, fast RF phasing, …  under preparation

## Slide 24: FCC-ee injector complex layout
Aspects proposed for experimental verification mainly for electrons (ongoing):
  Bunch generation for top-up injection: charge scan from “0” nC to 5 nC
  Emittance versus bunch compression at nC charge
  Transverse jitter amplification and damping
  Test of the energy compressor
  Other methods to ease the setup of the FCCee linac: impact of the RF focusing on the optics, fast RF phasing, …

## Slide 25: Bunch compression and emittance growth: reality
page 25
Experimentally observed emittance growth for 200 pC bunch at moderate compression factor C/CF
More details in “S. Bettoni et al., PRAB, 19, 034402 (link)” and S. Bettoni et al., talk at the FEL conference 2015 (link)
SwissFEL Test Facility (PSI)

## Slide 26: Bunch compression and emittance growth: reality vs simulations
Elegant: no emittance growth (1D model)
CSRTrack 1D model  no emittance growth
CSRTrack “3D” model  qualitative but not quantitative agreement
page 26
Qualitative but not quantitative agreement between measurements and simulations found  a measurement campaign would be auspicable
More details in “S. Bettoni et al., PRAB, 19, 034402 (link)” and “S. Bettoni et al., talk at the FEL conference 2015 (link)”

## Slide 27: FCC-ee injector complex layout
Aspects proposed for experimental verification mainly for electrons (ongoing):
  Bunch generation for top-up injection: charge scan from “0” nC to 5 nC
  Emittance versus bunch compression at nC charge
  Transverse jitter amplification and damping
  Test of the energy compressor
  Other methods to ease the setup of the FCCee linac: impact of the RF focusing on the optics, fast RF phasing, …

## Slide 28: Beam transfer jitter damping: what is the mechanism?
Head
Tail
Principle: use the same mechanism of the BNS damping but operating the RF structures on-crest
Advantages: best beam quality, energy efficiency
Tuning knobs: bunch properties, optics, kind of lattice, RF structure length
More info in S. Bettoni, A. Latina, A. Grudiev, Phys. Rev. Accel. Beams 28, 061601 (2025): link
page 28
RF
WF

## Slide 29: Experimental demonstration at FACET-II
What we simulated
FACET-II L3 “configured” to represent the FCC-ee HE-linac dynamics Balance between enough JA, damping and not too large JA (i.e. 5 nC, bunch length~1 mm)
Tuning knob: bunch length along L3 via L2 phase+BC14  vary the energy spread along the bunch
Prediction: amplification → damping downstream of BC14
How we measured it
• Corrector scan (~90° phase advance)
• BPM trajectory measurements
• Normalized BPM-area observable
• Excellent signal-to-noise ratio for our purpose
First experimental evidence that RF curvature and longitudinal wakefields suppress beam transverse jitter.
Damping observed at 1.5 nC for longer bunch
For the same charge shorter bunch damping not observed
Damping begins downstream of BC14 (where the bunch is elongated-for wakefield it should amplify more)
What we observed
30 consecutive shots
At a BPMs pair
Along the linac
page 29
Thanks to Brendan, Zack, Ryan and the excellent operation crews for the superb support!
Experimental validation of the FCCee HE linac stabilization strategy

## Slide 30: Conclusions and outlook
    The FCCee injector design is in a good track:
      Beam parameters fulfill all the specifications with margin and flexibility for single- and multi-bunch effects
      Detailed design of the RF structures well advanced
      Definition of the specifications for the technical expert groups (diagnostics, magnets, …) to move from a BD to a real design
We look forward to continuing this fruitful collaboration and exploring many more topics together, helping to make the FCC-ee injector design as realistic and robust as possible.
    FCCee and FACET-II possible synergies:
      FACET-II being a multi-GeV multi-nC machine is the perfect accelerator to experimentally verify the findings of the simulations before building FCCe
      Ongoing collaboration topics and more hopefully to come

## Slide 31: Acknowledgments…
…to you for your time,
to the entire WP1, the SLAC team, and to CHART*
FCCIS: 'This project has received funding from the European Union's Horizon 2020 research and innovation programme under the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754.'
*This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration

## Slide 32: Conclusions and outlook
    The FCCee injector design is in a good track:
      Beam parameters fulfill all the specifications with margin and flexibility for single- and multi-bunch effects
      Detailed design of the RF structures well advanced
      Definition of the specifications for the technical expert groups (diagnostics, magnets, …) to move from a BD to a real design
We look forward to continuing this fruitful collaboration and exploring many more topics together, helping to make the FCC-ee injector design as realistic and robust as possible.
    FCCee and FACET-II possible synergies:
      FACET-II being a multi-GeV multi-nC machine is the perfect accelerator to experimentally verify the findings of the simulations before building FCCe
      Ongoing collaboration topics and more hopefully to come