## Slide 1
Plasma-based positron sources
for wakefield acceleration studies at EuPRAXIA
Gianluca Sarri
g.sarri@qub.ac.uk
School of Mathematics and Physics, The Queen’s University of Belfast
10 TeV collider working group, 29/06/2026
DISCLAIMER: not a final design, still very much work in progress…

## Slide 2
Introduction
Gianluca Sarri

## Slide 3
Novel collider designs
Gianluca Sarri
Several collider designs have been proposed, based on “conventional” RF technology, to approach, and potentially surpass, the TeV barrier
International linear collider (ILC)
GeV (extendable to 1 TeV)
Linac gradients ~ 15 – 30 MV/m
Overall length > 30 km
Luminosity > 1034 cm2 s-1
arXiv:1306.6327 (2013)
Compact Linear collider (CLIC)
GeV (extendable to 3 TeV)
Linac gradients ~ 70 – 100 MV/m
Overall length > 11 km
Luminosity > 1034 cm2 s-1
arXiv:1812.06018v3 (2013)

## Slide 4
Plasmas?
Gianluca Sarri
Plasma-based accelerating cavities can sustain much higher accelerating gradients (1 – 100 GV/m) than RF cavities (<100 MV/m). The parameters are challenging though!
C. Joshi et al., Nature Physics (2025)
High charge
Metre-scale plasmas
Staging
Beam delivery limits compactness
High rep-rate
These requirements are challenging for electrons but not fundamentally impossible. What about positrons though?

## Slide 5
HALHF
Gianluca Sarri
The “positron problem” is so difficult, that ingenious solutions have been proposed to circumvent the problem altogether
arXiv:2503.19880v2 (2025)
Asymmetric collisions (375 GeV for e- and 41.7 for e+ for the 250 GeV case)
The asymmetry must carry onto other beam parameters too
Staged plasma acceleration for electrons
RF linac technology for positrons

## Slide 6
Positron acceleration in a plasma
Gianluca Sarri
Typical non-linear wakes have only narrow regions suitable for plasma acceleration, with highly non-uniform longitudinal (energy spread growth) and transverse (emittance growth) fields.
Several more advanced schemes have been numerically proposed, but experimental progress has been limited, and it is currently hampered by a lack of suitable facilities.
G. J. Cao et al., PRAB (2024)

## Slide 7
Positron acceleration in a plasma
Gianluca Sarri
J. Vieira et al., PRL (2014)
Typical non-linear wakes have only narrow regions suitable for plasma acceleration, with highly non-uniform longitudinal (energy spread growth) and transverse (emittance growth) fields.
Several more advanced schemes have been numerically proposed, but experimental progress has been limited, and it is currently hampered by a lack of suitable facilities.
Efforts mainly focused on tailoring the distribution of the driver and/or the plasma
Doughnut-shaped drivers
X Efficiency-quality trade-off
X Potentially unstable propagation
Finite channels
S. Diederichs et al., PRAB (2019)
X Potentially low efficiency
Asymmetric drivers
X Efficiency-quality trade-off
X Complex
S. Zhou et al., PRL (2021)

## Slide 8
Laser-driven positron sources
Plasma-based positron acceleration
is a challenging task!
Most research has been carried out numerically
In preparation for the design of a plasma-based
(or plasma-assisted…) positron arm for a collider,
it is necessary to experimentally test
these accelerators, in order to identify the
best and most practical ways to accelerate
positrons in a plasma.
A first step would thus be to provide positron
beam facilities to the community
Gianluca Sarri
- short duration: sz ~ 10 mm
- narrow transverse size: sx,y 100 mm
- “reasonable charge”: Q ~ multi pC
- “reasonable energy”: E ~ 100s of MeV
- low energy spread: DE/E ~ few %
- fs-scale synchronization and mm-scale overlap
with driver beams
For meaningful experimental studies, it is necessary to provide witness beams with remarkably demanding characteristics:
A possible roadmap for the experimental development of high-quality positron beams could be:
SHORT TERM ( 5-10 years) Development of positron test beam facilities in Europe
      (e.g. EuPRAXIA, EPAC…)
MEDIUM TERM (10 – 20 years) - Converging onto specific acceleration schemes
- Experimental demonstration of 10s of GeV high-quality beams
LONG TERM (>20 years): - Demonstration of ~100 GeV high quality beams in a hybrid scheme
  (conventional injector + plasma accelerating modules)

## Slide 9
EuPRAXIA
Gianluca Sarri

## Slide 10
EuPRAXIA
Gianluca Sarri
EuPRAXIA is the first accelerator user facility based on plasma acceleration technology.
The first ESFRI plasma accelerator project and their first accelerator project since 2016.
EuPRAXIA Conceptual Design Report: R. Assman et al., Eur. Phys. J. Special Topics 229, SUPPL 1 (2020)

## Slide 11
EuPRAXIA
Gianluca Sarri
EuPRAXIA is the first accelerator user facility based on plasma acceleration
EuPRAXIA Conceptual Design Report: R. Assman et al., Eur. Phys. J. Special Topics 229, SUPPL 1 (2020)
Beam-driven site (LNF, Italy)
Laser-driven site (ELI-BL, Czechia)
TDR: https://www.openaccessrepository.it/doi/10.15161/oar.it/aye3c-2cx65

## Slide 12
A plasma-based positron source
Experimental proof-of-principle
Gianluca Sarri

## Slide 13
Experimental proof-of-principle
Gianluca Sarri
M. Streeter et al., Sci. Rep. (2025)
First proof-of-principle of laser-driven high-energy positrons obtained with the Astra-Gemini laser at CLF (100 TW)

## Slide 14
Experimental proof-of-principle
Gianluca Sarri
First proof-of-principle of laser-driven high-energy positrons obtained with the Astra-Gemini laser at CLF (100 TW)
M. Streeter et al., Sci. Rep. (2025)
G. Sarri et al., PPCF (2022)

## Slide 15
Experimental proof-of-principle
Gianluca Sarri
First proof-of-principle of laser-driven high-energy positrons obtained with the Astra-Gemini laser at CLF (100 TW)
M. Streeter et al., Sci. Rep. (2025)
Obtained positron beam properties
Energy: 500 MeV
Bandwidth: DE/E ~ 5%
Charge: 0.2 pC
Norm. Emit.: 18 mm
Duration: < 50 fs
Results obtained with ~1.4 nC electron beams with maximum energy of ~ 900 MeV
Extending these results to a PW-scale laser indicates already the possibility of achieving GeV positron beams with > 10 pC charge in a few percent bandwidth and small transverse and longitudinal size
G. Sarri et al., PPCF (2022)

## Slide 16
A plasma-based positron source
Numerical modelling
Gianluca Sarri

## Slide 17
Experimental proof-of-principle
Gianluca Sarri
We can do much better than that though: 1) Higher electron beam charge, 2) Better conversion, 3) Better transport/conditioning
T. Foster et al., to be submitted (2026)
plasma lens
FBPIC with Bayesian optimization
Different laser powers (0.2 – 1 PW)
FLUKA simulations
Beam transport simulations with
differential evolution algorithm
Plasma lens
simulations

## Slide 18
Experimental proof-of-principle
Gianluca Sarri
We assume 4 laser beam configurations
T. Foster et al., to be submitted (2026)
200 TW  FLAME at LNF
500 TW  FLAME at LNF (upgrade)
670 TW  EPAC at CLF (conservative)
1 PW  EPAC at CLF (optimum)
Simple ionization-injection setup
He gas with N2 dopant (1 – 5 %)
25 mm plateau (20 mm for 200 TW)
1 mm cosine-squared ramps on either side
This is because, for positron generation, we have no real requirement on electron beam quality (i.e., small emittance or narrowband spectra)

## Slide 19
Electron beam optimisation
Gianluca Sarri
T. Foster et al., to be submitted (2026)
Bayesian optimization (maximum charge above 500 MeV)

## Slide 20
Electron beam optimisation
Gianluca Sarri
T. Foster et al., to be submitted (2026)
Bayesian optimization (maximum charge above 500 MeV)
Laser Power (TW) | 200 | 500 | 670 | 1000
Charge (nC) | 1.02 | 3.11 | 3.78 | 5.04
Energy (GeV) | 0.6 | 0.9 | 1.2 | 1.7
Positron beam virtually insensitive to spectral shape and spatial quality of the electron beam
Electron beam duration (> 1 GeV, for 1 PW) ~ 30 fs

## Slide 21
Positron source
Gianluca Sarri
T. Foster et al., to be submitted (2026)
Trade-off between positron yield and emittance
~ 80 pC

## Slide 22
Positron source
Gianluca Sarri
T. Foster et al., to be submitted (2026)
Trade-off between positron yield and emittance
~ 80 pC
Charge = 80 pC
Divergence = 18 mrad
Source size = 40 mm
Energy = 500 ± 5% MeV
Norm. Emit. = 600 mm *
* Much better emittance obtainable for thin converters, but much lower charge…
102
100
10-2

## Slide 23
Positron transport
Gianluca Sarri
T. Foster et al., to be submitted (2026)
2 triplets and a chicane to separate positrons from electrons and photons
Differential evolution algorithm to optimise positron beam at focus
E = 482 MeV DE/E = 4%
Q = 5 mrad sx,y = 1 mm
C = 50 pC sz = 10 mm

## Slide 24
Plasma lens focussing
Gianluca Sarri
Start-to-end numerical modelling with Bayesian optimisation for 0.2 – 1 PW laser
Active plasma lens for final focussing
Courtesy of M. Galletti (LNF, INFN)
Example: 1PW laser
E ~ 500 MeV ± 4.4%
Tput ~ 80 %
Q ~ 1 - 40 pC
en ~ 80 - 800 mm
indicative values, energy- and setup-dependent!
T. Foster et al., to be submitted (2026)
low-charge mode
high-charge mode
pC-scale, high quality

## Slide 25
Implementation example
(LNF, 200 TW laser)
Gianluca Sarri

## Slide 26
Area and capability
EuAPS
SPARC
Gianluca Sarri

## Slide 27
SPARC
EuAPS
Gianluca Sarri
Area and capability

## Slide 28
~10 m
90:10 BS
F/40
Gasjet +
converter
Chicane + QMs
F/15
PM
Gascell
Diagnostics
Delay
line
Lens
STEP 1: Generation of broadband GeV electron beams with nC total charge
STEP 2: Generation and characterization of the positron beam
STEP 4: First demonstration of laser-driven positron wakefield acceleration
STEP 3: Transport and energy selection: demonstration of 500 MeV ±10% 3 pC charge e+
STEP 5: Coupling of the positron beam (witness) with SPARC (driver)?
Gianluca Sarri
Area and capability

## Slide 29
Conclusions
Gianluca Sarri

## Slide 30
Wakefield accelerators present promising characteristics to reduce cost, footprint, and environmental impact of the next generation of particle colliders.
For the electron arm, their implementation is challenging but not impossible!
The positron arm is far more complicated and, while numerical proposals exist, progress in this area is hampered by a global lack of suitable experimental facilities.
EuPRAXIA aims to deliver ultra-short (sz ~ 10 mm), high-energy (E ~ 500 ± 5% MeV), and high charge (10s of pC) positron beam to study positron-wakefield acceleration
First numerical modelling of a simple beamline demonstrate that this is achievable in a small setup. pC beams within 10x30x30 micron volumes, up to 40 pC in larger beams
A lot of work is still required!
1) Optimize the beamline
2) Increase charge
3) Ensure high rep-rate operations
4) Achieve a high level of stability
5) Couple it with suitable drivers
Gianluca Sarri
Conclusions

## Slide 31
Thanks for your attention!
Gianluca Sarri
g.sarri@qub.ac.uk