## Slide 1: Finding Muons in ATLAS
Nicoletta Garelli SLAC

## Slide 2: Outline
Introduction
  Run1, Long Shutdown 1 and beginning of Run 2
A new readout system for the Cathode Strip Chambers (CSC)
  Limitations of the previous system
  The RCE
  Commissioning and first results
Muon spectrometer run coordination
  Highlights of LS1 activities
  Recombine the 4 muon systems for Run 2
Conclusions

## Slide 3: LHC Run-1 in a Nutshell
30 Nov 2009: Collisions@2.36TeV
2009
30 March 2010: Collisions@7TeV
5 April 2012: Collisions@8TeV
14 Feb 2013: Start of LS1
Pb-Pb
Pb-Pb
p-Pb
2010
2011
2012
2013
ATLAS pile-up (interactions per bunch crossing) increasing O(2)  O(10)  O(25)
50 ns bunch spacing
The design value was O(20)

## Slide 4: ATLAS Run-1 Achievements

## Slide 5: Run-2 LHC Plans & Conditions
Long Shutdown 1 (LS1) = 2 years for upgrading the machine
Parameter | Run 1 | Run 2
Center of Mass Energy | 7 (8) TeV | 13 (14) TeV
Bunch spacing | 50 ns | 25 ns
Integrated Luminosity | ~ 30 fb-1 | ~100 – 150 fb-1
Peak Instantaneous luminosity | 7.5 1033 cm-2 s-1 | 1.3-1.5 1034 cm-2 s-1
# bunches | 1400 | 2550-2800
Pile-up | ~30 | ~40

## Slide 6: LHC Restart
Feb 2014: ATLAS shafts closed
Eastern April, 5th: First beams
Small Note: One big wheel of the muon trigger system could not operate reliably till few hours before the first beam splashes  mistake in the configuration settings of the Trigger, Timing and Control distribution
Little example to show how important the re-commissioning phase is

## Slide 7: LHC Schedule for 2015
We are here
Jul 16: ~100 pb-1 so far… a long way to go before stable LHC operation

## Slide 8: ATLAS Improvements and Additions during LS1 (best of)
Additional fourth pixel sensors layer installed (Insertable B-Layer)
New beam-pipe support with reduced material  reduced contribution to physics background
Equipped and commissioned double layer RPC trigger chambers in the barrel feet region
Repair broken front-end boards of LArg Calorimeter  back to 100% working detector
New readout system for small muon wheels (CSC)

## Slide 9: The ATLAS Muon Spectrometer
Muon Detection: charged particles emerging from calorimeters Muon Spectrometer: 4 sub-systems (different technologies) in air-core toroid magnet
  Trigger chambers: RPC (~600) and TGC (~3600)
  Precision chambers: CSC (32) and MDT (~1200)
Momentum resolution 2011

## Slide 10: Cathode Strip Chambers (CSC)
Located in the innermost layer of the EndCaps of the Muon spectrometer covering the region 2.0 ≤ Ƞ ≤ 2.7
Multiwire proportional chambers operated using Ar/C02 (80%:20%) at atmospheric pressure
The position is measured by the induced charge on the segmented cathode strips by the avalanche formed on the anode wire

## Slide 11: The CSC Detector
16 chambers per wheel; large and small alternating and partially overlapping
Each chamber:
  4 precision (η) layers with 192 channels each
  4 transverse (φ) layers with 48 channels each
On-detector electronics composed of 5 Amplifier-Shaper Modules (ASM) boards to amplify, shape, transmit events
  Bipolar pulse with 140 ns shaping time
  Pulse sampled every 50 ns, each sample digitized to 12 bits of data

## Slide 12: Big Data to Process
Despite being a small detector, CSC produces a large data volume of unsparsified data
ROD must perform the “feature extraction”: threshold cut, out-of-time rejection and cluster finding
  Nominally process 4 time-samples (50 ns blocks) per event
On-detector
readout
Off-detector
readout
Central DAQ and Trigger
1 event = 5760 B
Max bw = 200 MB/s
570 MB/s @ 100 kHz
Read-Out Driver (ROD)
time
ADC
ATLAS fragment

## Slide 13: The Off-Detector Electronics (Run I)
All ATLAS detectors use ROD boards plugged in a VME crate
Common:
  VMEbus communication
  Single Board Computer in each crate where common software controls and configures the system
  Rack infrastructure (cooling, monitoring)
Custom
  Firmware
  Interface with the central trigger and timing system. CSC used one Timing Interface Module (TIM) per crate
  Rear modules to connect the RODs to the DAQ and Trigger system
2 VME crates
1 crate = 1 SBC, 8 RODs, 1 TIM

## Slide 14: Run 1 CSC Readout System Performance
In 2008 CSC could not join the ATLAS data taking runs
  ROD could not cope fast enough with the data processing
SLAC team redesigned software and firmware to enable data taking in time for beam turn-on
  Maintaining the same hardware
CSC met design goals, but ROD limitations reached in 2012: ~2% deadtime with peak luminosity of ~ 4 1033 cm-2 s-1 and L1 rate of 70 kHz
Several methods introduced to improve the situation
  Data samples reduced from 4 to 2
  Higher thresholds applied [ADC count should be greater than the threshold, which is configurable]

## Slide 15: Run 1 ROD Limitations
Busy (dead-time) beyond 1% at 75 kHz, ok for Run 1, but not sustainable for Run 2
Run 1 – max performance
Run 2 expectations Old ROD: Deadtime > 10%
SLAC team engaged to deliver a new readout system within 2 years

## Slide 16: The RCE: the Implementation for the CSC
We decided to use the Reconfigurable Cluster Element (RCE), a generic DAQ R&D component developed at SLAC
  Based on Advanced TeleCommunication Architecture (ATCA)
We could have upgraded the VME-based hardware, but
  CSC project: perfect match for the new RCE-based DAQ
  LS1: the right moment for deploying a new system which can be used in the upgrade phases
  Very stimulating to commission a new architecture into a well established project (the ATLAS DAQ system)
NEW

## Slide 17: What is RCE?
RCE (Reconfigurable Cluster Element ): bundled set of hardware, firmware & software. Physically it is a System-On-Chip (Xilinx ZYNQ) + interfaces + memory
ZYNQ
  New generation of Xilinx programmable device
  Combine an FPGA with a processor, ARM dual-core @ 800 MHZ
  Processor-centric: processor boots at reset and then configure FPGA
  Software-centric development: user can use C/C++ for programming the processor

## Slide 18: DPM & DTM
RCEs housed in
  Data Processing Modules (DPM): main task ‘feature extraction’
  Data Transport Modules (DTM)
1 DPM per CSC chamber (each chamber read-out individually)
TIM functionality replaced in DTM/DPM instead of dedicated hardware
Software:
  RTEMS (Open Source Real-Time kernel) for DPM
  ArchLinux for DTM

## Slide 19: Cluster On Board (COB)
Rear Transition Module (RTM)

## Slide 20: New Hardware
1 ATCA shelf with 6 COBs +RTM
1 PC, the control processor
  24 core netbooted PC
1 Ethernet switch
ATCN SWITCH
COB
COB
COB
COB
CSC SWITCH
Control Processor
ATCN
CSC NETWORK
COB
COB
Uplink for DHCP traffic
Run Control
OLD
NEW

## Slide 21: The New Rack Infrastructure
Equipping the new rack in the service counting room was not easy
  Establish the rack cooling distribution: ATCA shelves require horizontal cooling; VME crates vertical cooling
  Design and install a patch panel for fast and safe interchange of readout systems (old and new) during the commissioning
The ATCA shelf is monitored and controlled via the ATLAS Detector Control System (DCS)
  Led to the development of a common interface between the ATCA and the DCS SCADA system

## Slide 22: The Control Processor
Connected ATLAS Technical Control Network (ATCN) and CSC network
RCE are embedded system not exposed to external world and vice-versa
On the control processor one Readout Application per chamber (for a total of 32) is started to initiate data taking
  Readout Application implements interface with ATLAS run control finite state machine and sends/receives data from RCEs via network
ATCN SWITCH
COB
COB
COB
COB
CSC SWITCH
Control Processor
ATCN
CSC NETWORK
COB
COB
Uplink for DHCP traffic
Run Control

## Slide 23: The RCE Middleware
Establish communication protocol between control processor and RCEs via Ethernet (CSC network)
First implementation: “VMEbus over TCP”
  We simply ported the old interface software to TCP calls
  System functionality proved
We evaluated different options compatible with the network stack of RTEMS (no IPV6 support/headers)
1980’s technology to the rescue: Open Network Computing (ONC) Remote Procedure Call (RPC)
  We just need to execute a function call over the network
  RTEMs includes a port of ONC/RPC
  External Data Representation for data serialization
  We use strings as argument and return values to RPC
  Payload is a string in JSON encoding
New middleware in production system since May 2015

## Slide 24: Automated Recoveries
During Run 1 ATLAS deployed automated procedures to minimize deadtime during data taking in case of a malfunctioning component
It is possible without stopping the run to:
  Restart a part of the detector readout
  Remove a component which is misbehaving
  Eventually recover it later
CSC had a poor implementation of the stop-less procedures in Run 1
NOW: robust and fast recoveries with the new readout system
  And we needed them in very few cases so far…

## Slide 25: Detector - Counting Room Connection
Data transferred from on-detector readout electronics via high-speed fiber optics (G-Links)
  Single optical fibers from chambers grouped in bundles of 12 fibers (MPO) connected to 2 patch panels on the calorimeter support structure
    Patch panel connections very dense and difficult to manipulate
    One broken connector after the opening/closure of end-cap during LS1
  From the patch panel, MPO fibers reach ROD system in counting room
  320 G-links for event data + 120 G-links for configuration data
    MPO fibers 7,8 not used

## Slide 26: The G-link Issue 1/2
At configure, the RCE firmware establish the G-link protocol
  All chambers must be ‘locked’ to transmit data
Some hardware problems
But also some firmware bugs promptly fixed
25.01.2015 G-link lock status

## Slide 27: The G-link Issue 2/2
Status in March and June 2015
Still one G-link misbehaves… investigations on-going
Some G-links become bad while running and recover few minutes later
Installed splitter + patch panel to recover a single broken fiber

## Slide 28: The Feature Extraction (FEX)
FPGA (firmware)
  Extract from the wave-form 4 (nominal), 8, 12 (new, useful for signal tail studies) 50 ns time samples
  Peak occurs in the second or third time sample
  Threshold comparison: second or third time sample is compared to the threshold: if time sample > threshold  strip accepted as well as nearest strips
  Handle also overlapping events, when an additional L1 trigger arrives within 200 ns of the previous L1
ARM (software)
  Receive time samples from the FEX firmware
  Convert bit map of accepted channels to a list of clusters
  DMA’s the data from the firmware
  Assembles time samples into events
  Formats the event, i.e. the assembled time samples
  Outputs the formatted event to the DAQ and Trigger system

## Slide 29: The Data Reduction
Each RCE is handling about 5Gbits/sec, or, with 6 active RCEs, 30Gbits/sec @ 100kHz event rate per COB
  This is well below RCE actual capabilities (by a factor of >10)
Future direction:
  33% inflation of the data volume from the FPGA data to the output
  ARM is adding control/meta information and performing a checksum
  A new design could reduce these 1096 bytes to just around 500 bytes
  (*) Data reduction varies with luminosity (from 1/60 to 1/6)
FPGA
ARM
5760 B/RCE/event
824 (*) B/RCE/event
1096 (*) B/RCE/event

## Slide 30: CSC Running at L1=100 kHz

## Slide 31: First Achievements with Cosmic Data
Combined cosmic data taking with muon triggers
Some events with all 8 layers hit
Event rate ~6Hz for events with more than 4 layers hit

## Slide 32: ATLAS Event Display of Cosmic Ray Event

## Slide 33: CSC Timing
Beam Splash data (left) showed the correct time difference between the two endcaps (50 ns)
Collision data (right) show the same peaking time for the two endcaps
C
A
C
A

## Slide 34: New CSC Readout: a Success
Within 2 years we put together a readout system from scratch which meets (exceeds) all the requirements
OLD ROD | NEW ROD
L1 max rate ~ 70 kHz | L1 max rate > 100 kHz
1 ROD treats 2 chambers | 1 RCE treats 1 chamber
Extra board for the TTC distribution | Directly embedded distributed TTC system
Usage of bulky HOLA card | S-link logic in RCE firmware
Usage of high power G-link HDMP chips | G-link logic in RCE firmware
Work in Progress to produce a plot showing the 100 kHz rate capability at Run 2 occupancy, next seminar

## Slide 35: Coordinating all Muon Systems
Since early 2014 I am Muon Run Coordinator  also take care of all other Muon subsystems
  Completion of LS1 activities
  Ensure smooth data taking
  Arrange special runs (e.g. alignment, timing)

## Slide 36: MDT
MDT = Monitored Drift Tube Chambers
Precision muon tracking detectors in both barrel and endcap
  Working chambers close to 100%
Endcap chambers doubled the readout rate in LS1, removing potential bottleneck

## Slide 37: MDT/RPC Elevator Chambers
Close coverage holes (0.9%) in sector 13
BME = sMDT + new-type 1mm-gap RPC
  RPC secondary readout enters MDT mezzanine boards (phase 2 studies)
BME
BOE
Service connections
  More complicated and time-consuming than expected
BME status
  sMDT & RPC secondary readout included in ATLAS run
  RPC chambers still to be commissioned

## Slide 38: MDT Actual Point of Attention
Regular noise bursts during physics runs
  Inner barrel A sectors 6-13 (HV from the same rack)
A month ago MDT reported noise bursts too, also seen by the electromagnetic calorimeter, which disappeared by itself
  Inner barrel C and the Larg C side
  All those chambers shared the HV line

## Slide 39: Resistive Plate Chambers (RPC)
Barrel trigger
Gas inlet repair work in LS1
  ~400 chambers with leaks, 100 of them found in 2014
RPC chambers in feet sectors
  Two layers of RPCs in BO feet sectors (12/14), to cover holes (2.8%)
  20 chambers installed since before Run 1 w/o readout/trigger electronics
  Commissioning to be finished

## Slide 40: TGC Additional Coincidence
Thin Gap Chambers (TGC)
TGC inner chambers (EI/FI) in small wheel added to coincidence logic with big wheel (1.0 < h < 1.9)
Not available in Run 1
New boards installed at the end of LS1
Trigger validation on-going
Tile-m coincidence using Tile calorimeter (D5, D6 layers) and TGC EIL4 chambers (1.0 < h < 1.3)
Commissioning on-going

## Slide 41: TGC Points of Attention
During Run 1 TGC system produced large fraction of deadtime caused by series of large size of data in a short time (Noise burst events)
  FIFO overflow
  Timing misalignment
Noise burst stopper for Run 2
  Firmware to veto noise burst events
  Still under commissioning
Storm of corrupted fragments during Run 2 causing deadtime
  Cause not understood
  Burst of events?

## Slide 42: Alignment & TGC Timing
To bring all regions to 50 mm resolution:
  A toroid-off cosmic run for the barrel
  A toroid-off collision run to collect 30M-50M muons for the endcap
    Start collecting data on Sat 4 July  LHC problems  ATLAS decided to postpone it
In the shade of the attempted endcap alignment: TGC time scan
1
2
We keep Run 1 settings

## Slide 43: Efficiency
TGC shows a very good data/MC agreement
RPC is ~10% less efficient in data
  3% feet /elev. chambers, 4% timing, 3% to be understood
Muon reconstruction efficiency measured using Z  m+m- decays

## Slide 44: First Run 2 Data
Dimuon invariant mass distribution for oppositely charged, muon pairs with pT > 4 GeV and η|< 2.5 GeV
J/Y
Y’
U
Z
J/Y mass. MC calibration done with Run 1 data  good agreement with data

## Slide 45: Conclusion
During LS1 the ATLAS experiment carried on many upgrade activities to face the challenge of Run 2
  Higher beam energy, higher trigger rates
The new readout system for the small muon wheels (CSC) was one of the critical update and it has been successfully developed, deployed and commissioned
  Work well and reliably at 100kHz L1 rate
All four muon systems had a dense program during LS1 and some items are still under final commissioning
  Work on going to consolidate the new additions
Muon Spectrometer getting ready to 25 ns LHC operations

## Slide 46: THANK YOU

## Slide 47: Backup

## Slide 48: Naming Convention
All MDT chamber names consist of 7 characters
Chambers with same station Index (and same side) form a projective tower = crossed by tracks from the IP. Losing eg 2 MLs in the same tower = hole in coverage/momentum rec.

## Slide 49: Link to Offline Processing
Each CSC chamber is now read out individually
  Additional flexibility for the system
The event format is close to the old CSC format
  Contains the data (RPU block) of one chamber instead of two due to the new doubled ROS links (16 fragments  32 fragments)
A new, disjoint set of source IDs (to distinguish from the old data)
  adapted ROD decoder and bytestream converter
All changes implemented downstream (HLT)
  Region selector, cabling map, geometry, etc.
All successfully tested at the end of 2014