## Slide 1: DM Radio 2nd Consortium Meeting Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
Primary modeling tool is ANSYS Maxwell 3D with the following Capabilities:
1) For static magnetic fields
Magnetic energy and forces
Inductance – Self and mutual
Ability to calculate combined field quantities
Stranded and solid conductors
Adaptive Meshing
Choice of convergence parameters
Geometry creation or CAD import

## Slide 2: Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
2) For Transient magnetic fields
Transient currents and forces—Useful for calculating radial crushing force on thin sheath during magnetic quench
Field and current diffusion– Useful for quench propagation and superconductor stability
Coupling to external circuits

## Slide 3: Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
The second modeling tool is ANSYS Mechanical and ANSYS Workbench
1) For ANSYS Mechanical
Stress
Vibration
Thermal, static and transient
2) For ANSYS Workbench to get Multiphysics Simulations
Couple Maxwell geometry and solutions (e.g. forces) into ANSYS Mechanical in both directions
Maxwell forces to get stress
ANSYS Mechanical vibrations to get Maxwell eddy currents

## Slide 4: Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
Pitfalls / Design Challenges
Sufficient cooling/thermal sinking/higher than expected heat loads – heat load budgets
For iron core magnets, supplemental LN2 precooling and cooldown time
Coil winding – How is it done, mandrel material, who does it.
Superconductor choice – Cu/NbTi ratio, type of conductor, peak field on conductor, thermal margin, quench propagation/current extraction, conductor stress, potted or not, adequate conduction cooling, incorporation of high purity aluminum for quench back, conductor insulation
Possible available conductor that can be used

## Slide 5: Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
Pitfalls / Design Challenges
5) External structural support of coil windings – All forces are outward with a net force towards the axis of symmetry. This could take substantial space
6) Internal structural support of the coil winding package – preloading of coil
7) Vertical support of the gravity load – Connection of supports through winding
8) High temperature current leads and SC splices
9) Stray fields on superconducting shields -- Choice of superconductor

## Slide 6: Engineering Pitfalls and Modeling Capability at SLAC Wes Craddock January 23, 2020
Pitfalls / Design Challenges
10) Vibrations from seismic and pulse tube refrigerators – relative motion of shields and pick up coil