## Slide 1
Details in Konstantin’s slides in Lorenzo Rota’s SiD CMOS meeting on Nov 11, 2021 https://indico.slac.stanford.edu/event/7000/

## Slide 2
Device thickness ~100 mm (determined by mechanical design)
Epi layer thickness te ~50 mm (to be optimised)
Depletion depth td ~10 mm (to be optimised)
Pixel size 50 mm square (nominal)
Vary t and t to find optimal centroid detrmination, for incident angles 0 to ~60o
Second phase will be to study tracking performance with the suggested layout of tracking and timing layers. How compact can it be made?
Pinned photodiode, full charge collection over pixel area

## Slide 3
Highly transparency tracking system (3% X0)
Featuring:
  Low mass tracking layers integrating through the bunch train
  Using timing information from the vertex detector and dedicated timing layers (pre-ECAL) for robust pattern recognition
The main challenge is to minimise power and hence material
Tracking layers:
  Air-cooled, power dissipation ~O(100 W)
  Sensors 100 μm thick, low mass support (0.6% X0 per layer)
  Pixel size around 50 μm × 50 μm
Outer timing layers:
3 closely spaced layers for redundancy
  Single bunch timing resolution (<554 ns)
  Material budget less critical
  Probably air-cooled, evaporative cooling if needed
  150 µm pixels
The vertex detector also provides single-bunch timing
Outer timing layers
Vertex detector
Track reconstruction proceeds from mini-vectors in the timing layers, and proceeds inwards one layer at a time.
Note that even low-pT tracks (curlers) deposit signals in the timing layers (endcaps), so permit clean reconstruction.
Products of long-lived decays (K0s and L0 ) may be tricky.
Main questions: Will it work?
If so, can it be more compact?