## Slide 1: C3, the Cryomodule
Martin Breidenbach, Emilio Nanni, Marco Oriunno, Sami Tantawi, Caterina Vernieri
January 2022

## Slide 2: Functionality
Provide stable support for accelerator sections and quadrupoles
Provide the “Cool” environment of ~80K
Provide alignment capability within and to adjacent cryomodules.
Provide feedthroughs for waveguides and other cables.
Provide the above safely and reliably
This is a discussion of the “Pre-Conceptual Design”
It is a search for showstoppers and problems
It is a search for manufacturability issues - 100’s are needed!

## Slide 3: First brazed C-Band module

## Slide 4: Stages
The basic mechanical building block is the “Raft”
  2 accelerator sections + permanent magnet quad & BPM per raft
4 rafts per cryomodule, ~10 m
10 cryomodules per Sector, ~100 m
10 Sectors per SuperSector, ~ 1 km
The cryomodule

## Slide 5: Comparison to ILC
~96 cm diameter

## Slide 6: Raft Components
Permanent magnet quad
Tunable cold (final version)
Mechanically integrated cavity BPM in quad

## Slide 7: Raft
Raft channel will become a very open truss structure.
Each accelerator section is aligned with 5 d.o.f., with Z pinned by a ball at te midpoint
One waveguide feeds both manifolds. No load as in a travelling wave structure.
Expect flange to be welded.

## Slide 8: Raft Support
Present scheme:
  Raft components statically aligned in raft (once)
  Raft suspended by piezo transducers, range ~ 200 𝜇m, bandwidth ~100 Hz (???). Beam based alignment and feedback.
  Transducer intermediate stage suspended by high resolution cryogenic motor jacks. Range ~2 mm, usage rare after initial alignment (earthquakes?). Motor unusual in that it can have short lifetime bearings and be dirty.

## Slide 9: The Cryomodule
Inner cryostat (probably) 304 Stainless
Outer cryostat can be mild steel
Only 4 ports for waveguides and a few other cables.
Plan (hope?) to have only welded joints in cryostat - no bolted flanges or other connectors. Weld preps designed for “can opener” removal.
Note that Cryomodule fits in standard 40’ ISO container for transport.

## Slide 10: Waveguide Installation Concept
Rafts inserted

## Slide 11: Transition waveguide assembly

## Slide 12: Connect (weld) waveguide flanges

## Slide 13: Bring up Cold Plate

## Slide 14: Weld Cold plate to seat and cold bellows flange.

## Slide 15: Bring up Warm Plate

## Slide 16: Weld Warm Plate

## Slide 17: Thermal Contraction
Integrated contraction from room temperature to 77K:
Cu -0.31% SS 304 -0.29%
So 𝜟L between 1 meter of Cu and 1 meter of SS 304 is ~200 𝜇m
  Accelerator is pinned in Z to raft at its midpoint
  Accelerator sections separate by 200 𝜇m
  𝜟L is taken by bellows
10 m SS inner cryostat contracts ~3 cm. Outer steel shell stays warm, so sliding support needed.
  SS inner cryostat pinned in Z to outer shell at midpoint.
  Cryomodules cold sections separate by 3 cm at ends.
  𝜟L is taken by bellows

## Slide 18: Thermal Loads
4 operational modes (so far!)
Gradient (Mev/m) | Power Dissipation (W) | RF Flat top pulse length (ns) | Pulse Compression | Comments | Power/Area W/cm2 | Delta T Cu-Bulk LN (K)
70 | 2500 | 700 | N | C3-250 | 0.393 | 2.3
120 | 2500 | 250 | N | C3-550 | 0.393 | 2.3
150 | 3900 | 250 | N | C3-550 in 7 km | 0.614 | 2.5
120 | 1650 | 250 | Y | C3-550 | 0.259 | 2.1

## Slide 19: Thermal Loads
Gradient (Mev/m) | Power Dissipation (W) | RF Flat top pulse length (ns) | Pulse Compression | Comments | Power/Area W/cm2 | Delta T Cu-Bulk LN (K)
70 | 2500 | 700 | N | C3-250 | 0.393 | 2.3
120 | 2500 | 250 | N | C3-550 | 0.393 | 2.3
150 | 3900 | 250 | N | C3-550 in 7 km | 0.614 | 2.5
120 | 1650 | 250 | Y | C3-550 | 0.259 | 2.1
Nucleate boiling regime

## Slide 21: Alignment
Raft = 2 accelerators + quad pre-aligned
Initial alignment by stretched wires
Dynamic Beam-Based alignment - lots of SLC experience
Wire alignment (Rather pre-conceptual):
Two wires in each cryomodule, alternately spanning two cryomodules (~20 m):
Taut wire Cryomodules

## Slide 22: Wires, continued
4 capacitive quadrupole sensors (used by LEP) per raft.
2 attached to first accelerator, 2 attached to quad
measure X,Y, roll, pitch, yaw - no direct Z measurement
except for cavity phase
Needs work!

## Slide 23: Vibrations
Initial study at SLAC with Cu slab ~accelerator size in open LN bath on pneumatically isolated table.
Fitted with cryogenic accelerometers for x, y, z, table y
Just beginning when COVID stopped everything.
First measurements with only 400 W internal heater.
Very important to continue this work, study bubble aggregation and related effects.
Consider contouring/coating exterior of accelerator to promote bubble migration