## Slide 1: C3 Diagnostics and Controls
Josef Frisch, SLAC Jan 18, 2022

## Slide 2: Approach: Demo and Collider
Demo ~2026?
Small system, expect engineering to dominate controls / instrumentation costs
Use existing designs when suitable in order to reduce engineering costs
Concentrate engineering on subsystems with new or beyond state of the art requirements.
Collider ~2040
Large system, expect production to dominate control / instrumentation costs
Technology advances rapidly, delay detailed designs to take advantage of best available technology to reduce production costs

## Slide 3: Instrumentation / controls underlying technologies
Radio frequency based:
  Low level RF
  Precision phase / timing distribution / arrival time monitors
  Beam position monitors (cavity and stripline)
Triggering system
Profile Monitoring
Computation and data
Magnet Controls
Conventional control
  Temperature monitoring
  Slow motion control
Safety and machine protection
Other
  Active mechanical feedback for structures
  Laser controls
  Bunch length spectrometers

## Slide 4: For DEMO: The ATCA Common Platform
Developed at SLAC for high performance distributed control systems
Based on the Advanced Telecommunications Computing Architecture (ATCA)
High density, backplane carries all global signals
ATCA Crate “shelf”
Standard hardware, SLAC application:
Available from 1 slot to 14 slot
Power supply with hot swap
Management
Networks
Cooling
Designed for high-reliability applications

## Slide 5: Common Platform
Carrier card: FPGA, memory, backplane connections
AMC cards: ADCs, DACs, high performance front end electronics
RTM: General purpose IO, extra networks, miscellaneous
1: Carrier Card
2: Crate
3: RTM
Each carrier supports 2 AMC application cards
SLAC hardware and software application on ATCA

## Slide 6: ATCA / common platform backplane
Ethernet for data / control (10Gbit, 10/40 uplink)
Timing data stream (3.7Gbit)
Machine protection / uplink (3.7Gbit)
Slot 1
switch
Slot 2
payload
payload
payload
payload
payload
payload
payload
10G / 40G data
IPMI
MPS
Timing
Single cards can be used with rear transition module networking
All carrier cards can also serve as slot 2 nodes
Crates available from 1 to 14 cards
IPMI management network
For most applications, all networks are carried on the backplane, minimal external connections

## Slide 7: Platform for C3?
Difficult to predict technology > 10 years out, so concepts based on 2022 systems may change substantially
Xilinx RFSoC shown in Pentek module
2.4” X 4”
16X 2.5Gs/s or 8X 5Gs/s high performance ADC
16X 9.85 Gs/s high performance DAC
FPGA fabric: 4270 DSP slices
Quad-core ARM processor 1.33GHz
Dual core ARM redundant processor
Memory management and 8GB DDR4
Network and connectivity
This is an entire Data acquisition and control subsystem on a card
Stand-alone or as VPX 3U card (From Abaco systems)
Backend for LLRF, BPMs, etc.
Existing devices not quite able to directly digitize C-band with high performance, but that may be developed soon

## Slide 8: C3 Parameters (for the purpose of instrumentation / controls)
System Length | Few Kilometers
Beam power | Few MW
Repetition rate | 120Hz
Bunch charge | 1nC
RF pulse length | <250ns
Bunch spacing | >2.5ns

## Slide 9: RF Systems: Low Level RF
Based on the SLAC “Mission Readiness” LLRF system – in production use on the Ultrafast Electron Diffraction experiment and demonstrated on the LCLS1 LINAC
S:AC “Common Platform” System
LCLS Implementation

## Slide 10: Performance
Receiver RF phase performance: 0.004 degrees RMS in 1MHz bandwidth at S-band
Receiver phase stability: 0.25 degrees S-band / degree C
Identical reference and
Transmitter performance: 0.015 degrees RMS in 1MHz bandwidth
Arbitrary RF waveform generation
  SLED, frequency chirps, Ideal loading for standing waves structures etc.
Modification from 2856MHz to 5712MHz
Design is frequency flexible – daughter card defines operating RF and clock frequencies: Tested at 2856, 2805, 1400, and 476MHz
Existing mixer (LTC5551 / LTC5521) limited to 3.5GHz can be replaced with LTC5548 which works to 14GHz
Expect <0.01 degrees RMS readback noise and < 0.03 degrees RMS drive
Capable of inter-pulse feedback with ~500ns latency, but no performance gain observed on LCLS stations. RFSoC based system could operate with 200ns latency feedback

## Slide 11: Low Level RF Sub-boosters
Typical RF drive to klystron ~1KW
Commercial rack-mount units available from various vendors
R&K –CA5712BW20-5959RP shown
800W peak at 5712MHz
<0.05deg RMS phase stability pulse to pulse
May be suitable for DEMO system
Compact GaN C-band pulse power amplifiers available that can be integrated into a ~1KW system
Wolfspeed CGHV59350 shown
Typical 470W output at 5712MHz
Suitable for C3 (possibly DEMO, depending on cost trade-off vs commercial rack-mount units)
Area of improving technology – expect better / cheaper in 2030

## Slide 12: Precision phase distribution
Requirements similar to X-ray FEL facilities: LCLS2 requires ~100fs (0.2 degrees C-band) stability over ~4km
Master Source: Commercial oscillators, Wenzel GMXO shown
Broadband phase noise corresponding to 0.006 degrees RMS at C-band in a 10MHz bandwidth
1/f noise significant only below 1KHz (generally not important for accelerators)
Can be frequency locked to GPS
Long distance phase distribution: Both commercial and in-house designs exist
Libera Sync unit (used a PSI XFEL and planned for SLAC LCLS2)
<10fs (.02 degree) jitter. <0.02 degree drift over 10 degrees C temperature. (500M fiber).
SLAC / LCLS developing multi-km link with I-tech
For short haul (<100M) RF cable reflectometers can provide good stability. (LCLS / LCLS2)

## Slide 13: Precision timing
Beam arrival Time monitors
Use RF cavities
LCLS sees ~15fs noise, <50fs drift over 100 hours demonstrated
Can be used to measure beam vs RF time anywhere in the accelerator
Based on same RF hardware as the LLRF system
Laser timing control
Laser photodiode and ringing filter
Phase detection with standard ATCA LLRF hardware
FPGA driven feedback to laser length control piezo
<50fs RMS jitter, < 100fs drift
S-band arrival time monitor.
C3 would use C-band

## Slide 14: Triggering System
Clock and data distributed on fiber network
  Telecom type fiber, ~few Gbit clock rate
All receivers count down from fiducial work to programmed delays
LCLS / LCLS2 system integrated with common platform hardware, firmware and software
  Trigger receiver firmware integrated into all common platform hardware
10ps trigger jitter
Good timing stability (<<100ps) available using digital reflectometer. (used for LCLS2)
SLAC timing RTM

## Slide 15: Precision Timing Overall
All systems phase locked to master source
RF phase reference provides ~10fs timing to precision devices
Trigger system provide <10ps triggers to all pulsed devices

## Slide 16: Timing layout for C3

## Slide 17: Beam Position Monitors
Stripline and Cavity BPMs both in common use on accelerators.
  Cavity BPMs provide better noise due to higher coupling to beam
  Cavity BPMs provide better offset stability due to operation near null
  Cavity BPMs recommended for most parts of DEMO and C3
Cavity BPMs have demonstrated 10 nanometer resolution for low beam offsets, 1nC
Regular production operation at 250nm for ~50X devices on LCLS at 100pC
Yoichi et al, ATF Japan
Andrew Young, LCLS
170nm resolution

## Slide 18: Beam position monitors and bunch spacing
Short bunch spacing (2.5ns) requires high bandwidth readout.
Note: Cavity decay time can be >> bunch spacing: it’s a linear problem to separate individual bunches.
SIMULATION
Glen White
Demonstrated with beam at ATF2 but not published
Design choice: BPM cavity resonant or off-frequency:
Resonant: Best overall train average position measurement
Off-frequency : Best single bunch resolution within train

## Slide 19: Beam Position Monitor Hardware
Cavities can be designed with same technology as cold accelerator structures.
  Option to integrate BPM cavities into structure if desired.
Need high digitizing rate (>1.6 Gs/s) to cleanly separate bunches.
  Beyond capabilities of existing SLAC LLRF readout (~10MHz bandwidth)
Can use existing “SMuRF” electronics with some modification and new firmware
Good application for RFSOC based readout (even for DEMO)
  Single RFSoC card has 8X 5Gs/s ADCS, sufficient for 2X cavity BPMs.
  Option of 16X 2.5Gs/s ADCs (5X BPMS) if higher density needed
  Can use commercial RFSoC hardware – multiple options exist
  Serves as demonstration of RFSoC technology in an application where firmware is not too complex. (can do processing in software).
SMuRF readout (for cryogenic detectors)
Each card is 8X 2.4Gs/s ADCs with signal processing

## Slide 20: Beam Profile Monitors
OTR (Optical Transition Radiation) profile monitors for low longitudinal brightness beams (post damping ring)
~2um resolution OTR at ATF2 Japan
Coherent emission prevents OTR monitor use for high longitudinal brightness beams
Shop of horrors of OTR distorted beam images from LCLS

## Slide 21: Wire Scanners
Provide integrated beam profiles even for very high brightness beams
Slow, integrated only, but no other demonstrated Technology when beam has optical micro-bunching
Will be destroyed by very high intensity beams.
SLAC LCLS
Injector
Laser wire scanners can operate with arbitrarily high-density beams, but are very complex
Saki et Al . Laser wire scan

## Slide 22: Longitudinal Profile
Transverse deflection cavity: The ultimate longitudinal measurement
Few femtosecond resolution
Spectrometer limited energy resolution
Operated like standard RF station, but with transverse cavity
But $$$$
LCLS
Coherent emission spectrometers and power detectors provide lower cost and non-invasive qualitative measurements that can be used for feedback

## Slide 23: Profile monitoring overall
Best technique depends on specific application
Low brightness, low density: (after damping ring)
  Optical transition radiation
  Possibly fluorescent screens in injector
High brightness, low density: Before damping ring
  Wire scanners
High density: Laser wires (hope to avoid)
Longitudinal
  Calibrated: Transverse deflection cavities
  Uncalibrated, non-invasive for feedback: Coherent emission power / spectrometers

## Slide 24: Beam Feedbacks
Linac
gun
Linac
Linac
X
DL1
BC1
BC2
DL2
Linac
sz1
d1
1
V1
sz2
d2
2
V2
d3
V3
d0
V0
1 to 10 Beam Position Monitors (BPMs)
2 or 4 corrector magnets
LTU Feedback : stabilizes beam for jitter frequencies < 10Hz @ 120Hz rep-rate
Injector
L2
L3
LTU
Undulator
gun
example
LCLS Longitudinal Feedbacks
LCLS Transverse Feedbacks
Beam based feedback greatly reduces drift requirements, especially for phase / timing
Low beam rate (120) Hz for C3 allows use of conventional networks
Train to train waveform corrections also possible – similar to Common Platform LLRF correction system

## Slide 25: Vibration Feedbacks
Structure and magnet stabilization will require local feedback.
Work done on this for decades around the world
Measurement:
  Capacitive position sensors
  Compact interferometers
Algorithm
  Control theory well understood for multi-DOF systems
  Easily fits in modern FPGA
Actuators
  For RF structures need high force
  Probably Piezo actuators, but needs careful study

## Slide 26: Miscellaneous Systems
Radiation Safety
  Beam is high power (Lower than ESS) but otherwise conventional.
  No new technology needed
Machine protection
  No practical way to interrupt within a train, so this is a conventional 120Hz MPS system.
  Beams similar to those run at SLAC during high power (E-158) experiments.
Magnet controls
  Conventional
Temperature Controls
  Operation temperature between typical “industrial” systems and low temperature cryogenics. Needs cost optimization but no new technology
Laser controls
  Similar requirements to LCLS laser systems.

## Slide 27: Network and Computation
Roughly 100Hz, X 100 Bunches X 10,000 fast readout devices = 108Hz, or ~1Gbit total data rate
8 millisecond latency train to train
Needs good architecture, but not beyond normal state of the art.

## Slide 28: Overall Controls / Instrumentation: Demo System
LLRF: Straightforward modification to SLAC mission readiness” system
Precision timing distribution:
  Commercial stabilized links + LCLS / LCLS2 style timing will work
  Existing beam arrival time monitors
Beam position:
  Cavity BPMS will meet requirements but need new readout electronics: Either modify SMuRF or new RFSoC based
Beam Profile
  Existing technology OTR, Wire scanners, laser wires, Transverse deflection cavities, depending on beam parameters in different parts of the accelerator.
Beam feedbacks - conventional
Safety Systems – conventional
Vibration feedback to stabilize structures and magnets
  Needs development based on detailed requirements but considerable related work has been done at labs around the work
Controls / network infrastructure: Conventional

## Slide 29: Overall Controls / Instrumentation: C3
With a TDR ~2030, there will likely be significant advances in ADC / DAC / signal processing hardware
If designed today, LLRF, BPMs, femtosecond timing would consist of:
  RF front end, amplifiers, mixers LO generation
  ADC/DAC/FPGA/CPU back end (like Xilinx RFSoC)
  ADC / DAC can operate directly at 6GHz, but noise is too high fro accelerator applications.
Xilinx has announced it will integrate RF front ends into its “Versal” line of parts – with higher performance than RFSoC
  No device specifications released.
  Need to wait / see if the RF performance of the integrated parts meets accelerator level noise requirements without an external RF system.
The hardware proposed for the DEMO system would work for the full C3 and meet all performance requirements. Any changes are only for cost reduction