## Slide 1: The power of gaining and sharing
N. Cartiglia, R. Arcidiacono
INFN Torino
Silicon sensors with internal gain and built-in charge sharing

## Slide 2
Outline
Requirements of future HEP experiments
First design innovation: low-gain avalanche diode
Second design innovation: resistive read-out
Resistive Silicon Detectors
  Experimental results
Conclusions and outlook

## Slide 3: Requirements of future HEP trackers
Spatial resolution ~ 5 mm
Temporal resolution ~ 10 ps
Very low material budget (sensor + elect. < 100 mm of silicon)
Very low power consumption (air cooling < 0.2 W/cm2)
Need very small pixels: about 50k pixels/cm2
Each pixel requires a lot of power
The signal in thin sensors is very small
Good temporal resolution requires a lot of power per pixel

## Slide 4: First design innovation: low gain avalanche diode (LGAD)
In LGAD, a moderately p-doped implant creates a volume of high field, where charge multiplication happens.
The low gain allows segmenting and keeping the shot noise below the electronic noise since the leakage current is low.
The gain layer:
a parallel plate capacitor with high field
zoom
Drift area with gain
0.5 – 2 mm long
Low gain is the key ingredient to excellent temporal resolution
30-50 mm
Traditional Silicon Detector
Low-gain avalanche diode

## Slide 5
LGAD temporal resolution vs sensor thickness
Resolution without gain
Both CMS and ATLAS have opted for 50 mm thick LGAD,
(intrinsic time resolution of about 30 ps)
Note: LGADs have an intrinsic resolution that depends on the thickness
LGAD
LGAD
Intrinsic LGAD
LGAD
LGAD
Intrinsic LGAD

## Slide 6
Chart: Comparison WF2 Simulation (gain = 20, Cdet = 3 pF) - Data Band bars show variation with temperature (T = -20 C -> 20 C), and gain (G = 20 -> 30)
| 25 | 50 | 100 | 200 | 300 | 35 | 80 | 45
Measured | 35 | 110 | 25 | 58 | 30 | 30
WF2: total resolution | 20.3148 | 21.9317 | 23.4307 | 27.933 | 29.7321 | 39.8246 | 69.7782 | 126.4911
WF2: Jitter | 13.7 | 16 | 18 | 19.5 | 22 | 31 | 63 | 120
WF2: Non-unif. Ionization | 15 | 15 | 15 | 20 | 20 | 25 | 30 | 40

## Slide 7: Intrinsic LGAD time resolution
Why LGAD have an “intrinsic” time resolution?
It is a combinatorial problem: how many different ways are there to produce a given amplitude summing up individual ionization clusters (imagine there is 1 cluster every 1 micron) ?
50 micron thick ==> 50! Permutations…
10 micron thick ==> 10! Permutation
1 micron thick ==> 1 permutation, no temporal spread!
+ + … =
+
Intrinsic time spread
Ionization clusters
Permutations
Drift into gain region

## Slide 8
Interplay of power, pixel size, and electronics
power
The LGAD mechanism provides large signals, a fundamental component for achieving high temporal resolution.
However: when using small pixels, the power requirement/cm2 is too high
Power will determine:
  The architecture of 4D tracking detectors
    how many layers will be 4D and how many will be 3D
  The pixel size and the temporal precisions.
Power

## Slide 9: Second design innovation: resistive read-out
-------------
+++++++++
-------------
+++++++++
In resistive read-out, instead of many p-n diodes, there is a single diode.
The n-doped implant is resistive and acts as a signal divider
Very uniform Electric and Weighing fields
p-bulk
n++
p++
n+
Signal sharing is the key ingredient to excellent spatial resolution
Silicon detector with standard read-out
Silicon detector with resistive read-out

## Slide 10: Some of the detectors containing resistive elements
A incomplete list of resistive detectors:
Multi-gap Resistive Plate Chambers (MRPC)
surface Resistive Plate Counter (sRPC)
MicroCAT’s two-dimensional interpolating readout
μ-Resistive-WELL
Small-pad resistive MicroMegas
Resistive-strip bulk MicroMegas
Resistive PICOSEC MicroMegas Detector
4D Diamond Detector
Resistive Silicon Detectors (RSD)
We are working on extending the list of resistive detectors geometries that can be modelled. Some of the detector types will be used to benchmark the model.
Image taken from G. Bencivenni et al., Nucl.Instrum.Meth.A 958 (2020) 162050.
  Fast grounding μ-Resistive-WELL

## Slide 11: Resistive Silicon Detector (RSD)
Resistive Silicon Detectors
combine low-gain && resistive read-out
p-bulk
n+
p++
Gain implant
30-50 mm
Note: RSD are also called AC-LGAD

## Slide 12: Why RSDs are well suited for future experiments?
Internal gain
Resistive read-out
Innovation
Thin
Large signals
Continuous gain layer
Signal sharing
Large pixels
Continuous cathode
Sensor property
Low material budget
100% efficiency
Excellent temporal precision
100% fill factor
Excellent spatial precision
Reduced power consumption
Space for electronics
Uniform weighting field
Uniform carriers drift velocity
Experimental feature

## Slide 13: RSD principle of operation in motion

## Slide 14: Example of signal sharing
Pad 1
Pad 2
Pad 4
Pad 3
0 2 4 6 8
Time [ns]
0 2 4 6 8 10
Time [ns]
0 2 4 6 8 10
0 2 4 6 8 10
60
40
20
0
-20
Amplitude [mV]
60
40
20
0
-20
60
40
20
0
-20
Amplitude [mV]
60
40
20
0
-20
1
2
4
3
P 1
Pad 1
The laser is shot at the position of the red dot: the signal is seen in 4 pads
50-mm thick RSD,
Gain ~ 20

## Slide 15: Present RSD research paths
RSD (AC-LGAD)
-+
-+
-+
-+
-+
-+
DC-RSD
-+
-+
-+
-+
-+
-+
E Field
E Field
Cathode
Anode
This design has been manufactured in several productions by FBK, BNL, and HPK
This design is presently under development by FBK
The main advantage of the DC-RSD design is the ability to control the signal spread

## Slide 16
FBK RSD productions
We have produced two RSD productions at FBK
RSD1 proved that the resistive read-out approach works
  Tune of production parameters such as n+ resistivity and AC-coupling parameters
RSD2:
  Optimize the fabrication parameters (resistivity, oxide, gain layer)
  Reduce as much as possible the metal area of the pads
  Design electrodes shape that would maximize the response uniformity obtained with the collected charge
    Use cross-shape electrodes

## Slide 17: RSD2 sensors with cross-shaped electrodes
Pitch = 1300 mm
Pitch = 450 mm
200 x 340 mm2
Several geometries are exploded in RSD2, for example cross with different pitch and arm length: 200, 340, 450, and 1300 mm
Pitch = 0.45 mm

## Slide 18: Position reconstruction using charge imbalance
The position is reconstructed using the charge imbalance among the electrodes positioned at the 4 corners
3
4
1
2

## Slide 19: Evaluate the spatial resolution using laser TCT
Shoot the laser in a grid of points
Reconstruct the hit position with charge imbalance
First take-home result: even without any additional correction, the cross-shaped electrodes provide a fairly accurate position reconstruction
Second take-home result: near the pads, the reconstructed positions are systematically shifted with respect to true positions

## Slide 20: Correct the reconstructed position
Laser Position
Reconstructed position
Compute the migration map:
For each laser position, connect the true and reconstructed positions.

## Slide 21: RSD2 spatial resolution
RSDs at gain = 30 achieve a spatial resolution of about 2-3% of the pitch size:
RSD:
1300 x 1300 mm2: sx ~ 40 mm
450 x 450 mm2: sx ~ 15 mm
Traditional standard pixel
1300 x 1300 mm2: sx ~ 920 mm
450 x 450 mm2: sx ~ 320 mm
Chart: RSD2 crosses: spatial resolution when the total AC amplitude = 60 mV
| 1300 | 450 | 340 | 200
1300 um | 40 | 15 | 13 | 10
 | 9.6519


Chart: RSD2 crosses: spatial resolution for 4 different pitch sizes
| 29 | 53 | 69 | 154
1300 um | 95 | 50 | 33 | 15.4
450 um | 34 | 25.3 | 19.9 | 15.5 | 10.6 | 10.1 | 8.4 | 7.9 | 10.6
340 um | 44.8 | 34.1 | 21.87 | 19.9 | 13.85 | 12.8 | 10.6 | 7.4 | 6.33
200 um | 45.9 | 26 | 24.13 | 18.5 | 15.9 | 10.5 | 8.5 | 7.8 | 5.2 | 4.4
gain = 30

## Slide 22: RSD2 temporal resolution
Chart: RSD2 Crosses: time jitter for 3 different pixel sizes
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 75 | 85 | 95 | 105 | 115 | 125 | 135 | 145 | 155 | 165 | 175 | 185
Calculated Jitter | 240 | 120 | 80 | 60 | 48 | 40 | 34.2857 | 30 | 26.6667 | 24 | 21.8182 | 20 | 18.4615 | 16 | 14.1176 | 12.6316 | 11.4286 | 10.4348 | 9.6 | 8.8889 | 8.2759 | 7.7419 | 7.2727 | 6.8571 | 6.4865
1300 x 1300 um^2 | 56.745 | 32.8786 | 23.4028
450 x 450 um^2 | 36.3716 | 28.9083 | 22.7264 | 17.598 | 16.4973 | 15.3704 | 14.2113
200 x 340 um^2 | 54.8016 | 56.5406 | 39.4137 | 30.3111 | 18.6773 | 15.7493 | 12.0416 | 8.6626 | 7.7775
gain = 30
The resolution depends mostly upon the signal size and weakly on the pixel size
RSDs at gain = 30 achieve a temporal jitter of about 20 ps

## Slide 23: RSD2 performance summary

## Slide 24
Final goal of RSD R&D: a completely new tracker
The design of a tracker based on RSD is truly innovative:
It delivers ~ 20 -30 ps temporal resolution
For the same spatial resolution, the number of pixel is reduced by 50-100
The electronic circuitry can be easily accomodated
The power consumption is much lower, it might even be air cooled (~ 0.1-0.2 W/cm2)
The sensors can be really thin
Standard Tracker
LGAD-RSD-based tracker
Resistive implant
~ 50 mm
---
- --
++
+++
Pixel size
~ 250 x 250 mm2
Silicon bulk
Contacts
Electronics
~ 150 mm
Gain implant
--
---
- --
+
++
+++
Pixel size
~ 25 x 25 mm2

## Slide 25: Conclusions
The combination of internal multiplication and built-in charge sharing leads to the design of a new type of silicon tracker.
Resistive read-out && LGAD can be used both in hybrid and monolithic sensors
The pixel size can be quite large given the very good spatial resolution.
Limitations might be introduced by occupancy.
Spatial resolution depends upon ~ 1/gain, ~ 1/pitch, and ~noise
The temporal resolution is weakly dependent on the pixel size
Our laboratory measurements yield to (at gain = 30)
  a spatial resolution of about 3% of the pixel size
  a temporal resolution similar (but marginally worse) than that of standard LGADs

## Slide 26
Acknowledgement
We kindly acknowledge the following funding agencies, collaborations:
RD50 collaboration
INFN - Gruppo V 4DShare project
INFN – FBK agreement on sensor production (convenzione INFN-FBK)
Horizon 2020, grant UFSD669529

## Slide 27
Backup

## Slide 28: State-of-the art
Physicist
No gain area ~ 50 um
JTE + p-stop design Trench-isolated design RSD -- AC-LGAD
JTE/p-stop UFSD
CMS && ATLAS choice
Signal in a single pixel
Not 100% fill factor
Very well tested
High Occupancy OK
Rate ~ 50-100 MHz
Rad hardness ~ 2-3E15 n/cm2
UFSD evolution: use trenches
Signal in a single pixel
Almost 100% fill factor
Temporal resolution (50 mm) : 35-40 ps
High Occupancy OK
Rate ~ 50-100 MHz
Rad hardness: to be studied
No gain area ~ 5 um
RSD evolution: resistive readout
Signal in many pixels
100% fill factor
Excellent position resolution:
  ~ 5 mm with large pixels
Temporal resolution (50 mm) : 35-40 ps
Rate ~ 10-50 MHz
Rad hardness: to be studied
HPK2
16x16 array
2.1 cm

## Slide 29: Reduced material budget
The active thickness of RSD sensor is rather small ~ 50 um.
There is a clear path leading to < 100 mm material:
50 um
25 um
Present design: no material budget optimization
ASIC
~200 mm
50 mm
~150 mm
Thinned handle wafer:
  500 um  10-20 um
50 mm
ASIC
~50 mm
Silicon beam
Thinned handle wafer:
500 um  10-20 um
Thinned active area:
50 um  25 um
50 ps  25 ps
~1 mm glue
25 mm
ASIC
~50 mm

## Slide 30
p-stop
VBias
p bulk
oxide
Gain layer
JTE
No gain
50-80 mm
JTE
Towards 100% fill factor: Trench Isolated LGAD
No-gain region ~ 50-80 mm
 cannot use UFSDs for small pixels
trench
VBias
p bulk
oxide
Gain layer
JTE
trench
Solution: use trenches for pad isolation
 No-gain region ~ 5 – 10 mm
No gain
5-10 mm

## Slide 31
p-stop
VBias
Epi p-bulk
oxide
Gain layer
JTE
No gain
50-80 mm
JTE
HPK2
16x16 array
2.1 cm
Handle wafer
Prototype of the final CMS sensor
The ATLAS and CMS timing layers will use about 25 m2 of UFSD sensors
Very well tested
Will be used up to ~ 2 E15 neq/cm2
Gain ~ up to 40 when new ==> up to 20 fC
Signal duration ~ 1 ns
Low noise
Rate ~ 50-100 MHz
Excellent production uniformity
State-of-the-art: sensors for ATLAS and CMS

## Slide 32: Hit position resolution
: contribution due to the electronic noise. This term determines the measurement precision. See next slide
: systematic error in the reconstruction of the signal amplitude. For example, the amplitude, due to the fitting method to determine the maximum of the gaussian, has a 1% systematic error.
: Possible systematic errors in the reconstruction program, the position is always shifted in x or y. This determines the measurement accuracy.
: this term groups all sensor imperfections. For example, uneven n+ resistivity

## Slide 33: Spatial resolution: the role of jitter
The main component of the position resolution is the position jitter, defined as:
100 mV
0 mV
Read-out pad
Imagine a system with a single read-out pad where a hit generates:
A signal of 100 mV when shot near a pad
A signal of 0 mV when shot at the opposite corner
Noise ~1 mV (as in our lab)
500 1000 1500
distance [mm]
Amplitude [mV]
inter-pad: 1300 mm
pitch: 450 mm
100
50
0
0
0.15
0.05
In this simplified system, the signal decreases by:
Pitch 1300 mm: 0.05 mV/mm
Pitch 450 mm: 0.15 mV/mm
So, the jitter is:
Pitch 1300 mm: 1 mV/(0.05 mV/mm) = 20 mm
Pitch 450 mm: 2 mV/(0.15 mV/mm) = 7 mm

## Slide 34
Irradiation effects
Irradiation causes 3 main effects:
Decrease of charge collection efficiency due to trapping
Doping creation/removal
Increased leakage current, shot noise
The main effect in LGAD is “acceptor removal”, i.e., the reduction of the gain implant doping
The electric field due to the gain implant decreases  Compensated with higher bias
Main technique to decrease acceptor removal: carbon implantation in the gain layer
Carbon spoils the properties of silicon sensors.
However, in the right amount and only on the gain implant, it increases the sensor rad. resistance by a factor of 3
carbon implantation

## Slide 35
RSD (AC-LGAD)
DC-RSD
p bulk
p++
gain implant
AC pad
oxide
p bulk
p++
resistive n+
DC pad
n+ contact
inter-pad resistor
Top view
Crosscut
---
--
++
+++
---
--
++
+++
Limiting the signal spread to a single cell

## Slide 36: UFSD temporal resolution in thinner sensors
Non uniform ionization:
Physical limit of UFSD sensors
UFSD temporal resolution improves in thinner sensors:
==> reasonable to expect 10-20 ps for 10-20 mm thick sensors.
Be aware: very difficult to do timing with small signals… power consumption increases
FBK UFSD32 production