## Slide 1: FACET-II 2-Bunch Simulated Performance
Glen White

## Slide 2: Overview
Accelerator configuration and 2-bunch start-to-end simulations
  Using Lucretia FACET-II electron beam model
BC20 “W” chicane
  Same as FACET (with XTCAV moved into FFS)
2-bunch tracking:
  Reminder of performance with double-pulsed configuration from gun shown previously
  Compare capability with “OG” FACET configuration: single pulse with ”notch” and “jaw” collimation inside BC20

## Slide 3: Linac Bunch Compression Double-Gun-Pulse Configuration
Φ=-19.2o
Φ=-38.35o
335 MeV
4.5 GeV
10.0 GeV
125 MeV

## Slide 4: Sector 20 Beamline & Optics
Current FACET-II Sector 20 layout, matched for R56=+7mm, β*=50cm
3 families of sextupoles matched to minimize T566, & εx
FFS quads (5 families of magnet) matched for round beams at IP
R56 matching range = [-10:+10] mm
  significant operations time required ~1 shift
β* matching range = [2,100+] cm
  Tool available for online matching
  For smaller β* values (<50cm), need to also re-optimize sextupoles for smallest beam size
BC20
FFS
SPECTROMETER
IP

## Slide 5: Start-to-end Tracking (2-bunch from photocathode) Longitudinal Phase Space at IP
Δt = 600 fs
Drive
Bunch
Witness
Bunch

## Slide 6: Start-to-end Tracking (2-bunch case) Transverse Phase Space at IP (PENT element)
γε (Drive Beam)= 73 x 35 μm-rad
γε (Witness Beam)= 4.5 x 2.6 μm-rad
Drive Bunch
Witness Bunch

## Slide 7: IP Waist Locations for Drive and Witness Bunch
“PENT”
ΔW
L*=2.58m
Witness Bunch
Drive Bunch
βIP,αIP
βD,αD
Drive Bunch Waist Location
Q0FF
βQ,αQ
 | αQ [x,y] | βQ [x,y] | αIP [x,y] | βIP [x,y] | αD [x,y] | βD [x,y]
Witness | 25, 13 | 67, 31 m | 0.13, -1.1 | 11, 41 cm | -2.3, 0.17 | 66, 20 cm
Drive | 5.1, 9.8 | 15, 28 m | 0.4, 0.6 | 65, 65 cm | 0.0, 0.0 | 56, 29 cm
ΔWx,y = 22.8, 17.3 cm
(Sketch – NOT TO SCALE)

## Slide 8: Linac Bunch Compression 2 Bunch Notch Configuration
Φ=-19.8o
Φ=-39.8o
335 MeV
4.5 GeV
10.0 GeV
125 MeV
Q = 2 nC
Φs = 30o

## Slide 9: BC20 Re-Match for Jaw+Notch 2-Bunch Config
Compared with FACET-I, smaller head-tail energy spread, need to re-configure for larger R56 in BC20
  Optics re-matched for R56=+10 mm
  Adjust L1 & L2 rf phases to fine-tune 2-bunch results
Use notch & jaw collimators as indicated to generate 2-bunch profile
BC20
FFS
SPECTROMETER
IP
CN2069 & CX2085
σδ / σβ ~ 30 / % (γε=10μm-rad)

## Slide 10: Start-to-end Tracking (2-bunch notch config) Longitudinal Phase Space at IP (PENT element)
Δt = 500 fs , Ipk ~5/15 kA, Q ~330/820 pC
Φ(L1) = -19.8 deg ; Φ(L2) = -39.8 deg
Can trade: >Ipk for < Δt by adjusting Φ (L1&L2)
Drive
Bunch
Witness
Bunch
Δx=1.1mm
Δx=1.1mm
Δx=0.65mm
Δx @ CN2069

## Slide 11: Start-to-end Tracking (2-bunch notch config) Longitudinal Phase Space at IP (PENT element)
Example of closer dz separation (collimation of standard single bunch, fully compressed pulse) BC20 R56=7mm
Simulation by C. Emma

## Slide 12: Summary and Outstanding Simulation Work
Solution for double-pulsed beam from gun
  Δt=600fs, Q=500/1400pC, Ipk=8/16kA
Solution for BC20 notch configuration
  Δt=500fs, Q=330/820pC, Ipk=5/15kA
    Requires increasing BC20 R56 match = 10mm
  Δt=130fs, Q=260/830pC, Ipk=3/30kA
In all cases, need to re-optimize configuration after injector is commissioned @ 2nC and injector performance is known
Also, need to calculate FFS & BC20 sextupole re-match for witness bunch to optimize witness emittance & Twiss @ IP
Notch configuration possibly benefit from longer pulse from injector?
  Longer laser pulse
  Increase charge, tradeoff for larger transverse emittance?