## Slide 1: What have we learned from E300 experiments so far:
Chaojie Zhang, Zan Nie, Ken A. Marsh, Chan Joshi
Oct 5, 2022
E300 collaboration meeting at UCLA
High-efficiency wake excitation in beam-ionized H2 plasma at FACET-II

## Slide 2: E300 goals
Main goals of E300:
A net energy transfer efficiency of 40% (drive to trailing bunch)
  pump energy depletion
  beam-to-wake efficiency >80%
Minimize the energy spread growth of the trailing bunch
Minimize the emittance growth
Conserve the charge of the trailing bunch

## Slide 3: Outline
Several experimental shifts had been finished using static-fill hydrogen and helium;
What have we learned from the data regarding the beam-plasma interaction?
plasma length
energy deposited into the plasma
beam-to-wake energy transfer efficiency
pump energy depletion
constraints on driver current profile

## Slide 4: Experimental layout
~4 m between Be windows
Beam direction
beam waist
beta = 0.5 m
beam focusing geometry (not to scale)

## Slide 5: Experimental layout
viewport 1
(SideView)
TopView
viewport 2 (SideView)
Dump table diag.
DTOTR1/2
LFOV (large field of view spectrometer)
Gamma
Beam direction

## Slide 6: Constraints on plasma length given by plasma emission
Dataset: 20220817 E300_02789, H2, 0.3 Torr
Plasma light was observed at three locations separated by ~1.7 m with good correlation
Plasma length is likely to be 2 m
TopView
SideView 1
(IPOTR1)
SideView 2
(IPOTR2)
shot #34
shot #34

## Slide 7: Energy loss of the drive bunch
Dataset: 20220817 E300_02781, H2, 0.08 Torr
shot #15
10 GeV peak
decelerated
Separate the unaffected (remains at 10 GeV) and the decelerated part:
shot #15
shot #22
shot #22
10 GeV peak
linearized energy spectrum

## Slide 8: Separate the unaffected (remains at 10 GeV) and the decelerated part
Dataset: 20220817 E300_02781, H2, 0.08 Torr
unaffected part
decelerated part gives energy loss:
No charge loss in transport
The energy lost by the drive bunch is deposited into plasma via wake excitation

## Slide 9: No charge loss in the transport
Dataset: 20220817 E300_02781, H2, 0.08 Torr

## Slide 10: Plasma light vs. energy deposited into the plasma
Dataset: 20220817 E300_02781, H2, 0.08 Torr
Deposited energy is calculated using the LFOV data (energy loss)
The plasma light collected at the IPOTR1 port scales linearly with the deposited energy
Maximum deposited energy ~1 J
Assume plasma length ~2 m, diameter ~200 µm
Ionization energy of H2 molecule: 15.4 eV
Plasma density (singly ionized): 2.8e15 cm-3
Requires ~ 0.4 mJ to ionize such a plasma
Significant energy loss due to wake excitation
linear fit:
p1=28.7, p2=3.9e3
TopView
IPOTR1
IPOTR2

## Slide 11: Energy loss doubled in 4x higher density plasmas
Dataset: 20220817 E300_02789, H2, 0.3 Torr
linear fit:
p1=39.6, p2=3.2e4
TopView
IPOTR1
IPOTR2
Maximum deposited energy ~2.5 J

## Slide 12: Significant energy loss in high density plasmas
Dataset: 20220817 E300_02805, H2, 1.5 Torr
In this dataset, the spectrometer only captures electrons with E>5 GeV
~73% of the total charge
~90% of the total energy in the transmitted beam (not the initial beam)
 | 10 GeV | 5-10 GeV | <5 GeV
charge [nC] | 0.65 | 0.38 | 0.38
avg. energy [GeV] | 10 | 7.5 | 2.5
energy [J] | 6.5 | 2.85 | 0.95
percentage | 90% |  | 10%
transmitted energy ~ 10 J
charge and energy partition:

## Slide 13: Deposited energy approaching to 8 J
Dataset: 20220817 E300_02805, H2, 1.5 Torr
brighter plasma light means more energy deposited into the plasma:
~6 J energy deposited into the plasma
~15 J energy in the drive beam
Calculate the energy in the transmitted drive beam using the LFOV data
Calculate the energy deposited in the plasma using the plasma emission data:

## Slide 14: Beam-to-wake energy transfer efficiency vs. backing pressure
~8 J energy was deposited into the plasma for the highest pressure 2.0 Torr
This corresponds to a beam-to-wake efficiency of ~80% (corrected: 8J/(15J*0.7), or ~50% uncorrected: 8J/15J)
Data agrees with the fit: implies that
  same plasma length
  deposited energy , therefore same ionization fraction for these pressures
  same ionization fraction for different pressure —> most likely 100% ionization? (Zan will talk about the ionization physics)

## Slide 15: Maximum energy loss
Dataset: 20220817 E300_02781, H2, 0.08 Torr
Max. energy loss

## Slide 16: Max energy loss vs. plasma light
Dataset: 20220817 E300_02781, H2, 0.08 Torr
Dataset: 20220817 E300_02789, H2, 0.30 Torr
Plasma emission scales linearly with maximum energy
(IPOTR1)
(IPOTR1)
0.08 Torr
0.3 Torr
Notes: p(1)=3.4724e-5
p(2)=0.873

## Slide 17: Pump energy depletion
Dataset: 20220817 E300_02805, H2, 1.5 Torr
(IPOTR1)
spectrometer (LFOV) limit
Plasma light proportional to max. energy loss (see Eloss<5GeV)
Spectrometer limit is ~5 GeV
Maximum plasma light indicates 10 GeV energy loss (pump depletion)
some electrons start losing all their 10 GeV energy
more electrons deplete 10 GeV

## Slide 18: Plasma light as a measure of the energy deposited into plasma
Recent experimental results published by FLASHForward
L. Boulton et al., Longitudinally resolved measurement of energy-transfer efficiency in a plasma-wakefield accelerator, arXiv:2209.06690v1, 14 Sep 2022

## Slide 19: Plasma light as a measure of the energy deposited into plasma
L. Boulton et al., arXiv:2209.06690v1, 14 Sep 2022

## Slide 20: Longitudinally-resolved measurement of the energy transfer efficiency
L. Boulton et al., arXiv:2209.06690v1, 14 Sep 2022
two shots with “same” input parameters
driver charge loss reduces efficiency

## Slide 21: Outline
Several experimental shifts had been finished using static-fill hydrogen and helium;
What have we learned from the data regarding the beam-plasma interaction?
plasma length
energy deposited into the plasma
beam-to-wake energy transfer efficiency
pump energy depletion
constraints on driver current profile

## Slide 22: How much charge are decelerated?
#6
#61
decelerated
10 GeV peak
10 GeV
10 GeV peak
shot number #6
shot number #61
Fit the 10 GeV peak with a Lorentzian distribution to separate the portion of the beam that is not affected by the plasma
Dataset: 20220817 E300_02789, H2, 0.3 Torr

## Slide 23: How much charge are decelerated?
Dataset: 20220817 E300_02789, H2, 0.3 Torr

## Slide 24: In this dataset, ~45% of the charge remains at 10 GeV
~45% of the charge remains at 10 GeV
NO interaction with plasma
Dataset: 20220817 E300_02789, H2, 0.3 Torr

## Slide 25: Unaffected fraction distribution (1.0 Torr)
In most shots, 34% of the drive beam electrons does no lose energy
Dataset: 20220817 E300_02817, H2, 1.0 Torr

## Slide 26: Unaffected fraction distribution (2.0 Torr)
Dataset: 20220817 E300_02810, H2, 2.0 Torr
In most shots, 39% of the drive beam electrons does no lose energy

## Slide 27: 10 GeV fraction vs. backing pressure
~35% of the drive beam electrons remains at 10 GeV
No energy change means that ~35% of the driver electrons did not interact with the plasma
Note that ionization of hydrogen molecule (15.4 eV) needs ~55 kA peak current for bunches

## Slide 28: A possible current profile for explaining the experimental observations
driver
current spike for ionization (I~56 kA) for
~34% remains at 10 GeV
energy loss
H2 plasma
Q = 1.5 nC;
Q_spike 0.2 nC; I=50 kA
Q_main 1.3 nC; I=6 kA
I_peak 56 kA
20 µm

## Slide 29: The location of the current spike
28% unaffected
34% unaffected
40% unaffected
In most shots, 34% of the drive beam electrons does no lose energy
Dataset: 20220817 E300_02817, H2, 1.0 Torr
80% unaffected
H2 plasma
H2 plasma
H2 plasma
H2 plasma
driver

## Slide 30: Glen’s latest simulation
https://www.slac.stanford.edu/~whitegr/F2_S2E/
Parameters: (not exactly this summer’s configuration)
single e- bunch, Q=1.5nC, beta*=10cm
E(BC11,BC14,Sector 20)=0.29, 4.5, 9.3 GeV
@IP: emit (90%) = 15 x 5 um-rad
core bunch size = 6 x 5 x 10 um
Ipk = 15 kA
drive beam
2D CSR model included in the simulation
but…”centripetal CSR terms are important…there is some theoretical debate still about whether this treatment is correct…” - Glen White
drive beam
~41%

## Slide 31: Summary
What have we learned from E300 experiments so far:
plasma length > 2 m
energy deposited into the plasma up to 8 J
beam-to-wake energy transfer efficiency approaching ~80%
pump energy depletion: some electrons has lost all their 10 GeV energy
constraints on driver current profile: narrow high-current spikes in the front of the driver
Zan will present QPAD simulations to support these hypotheses

## Slide 32: Backup slides
constraints on plasma length and density using betatron analysis
maximum decelerating field (in the short-driver regime)
spiky current profile due to CSR (measured using DTOTR)
charge throughput
energy gain

## Slide 33: Constraints on plasma length given by betatron oscillation
8.09 GeV
Dataset: 20220817 E300_02813, H2, 1.8 Torr

## Slide 34: Betatron oscillation
two slices in the bunch gain different energy
they also accumulate different betatron cycles

## Slide 35: Constraints on plasma the density-length product
uniform density over Leff
means: constant
linearly changing
Constraints on plasma density and length:
6.4e16 cm-3
6.4e15 cm-3
100% ionization
6.4e16 cm-3
~1.8 m
Dataset: 20220817 E300_02813, H2, 1.8 Torr

## Slide 36: Maximum decelerating field
Dataset: 20220817 E300_02799, H2, 0.5 Torr
In most shots, the maximum decelerating field is Edec ~ 2 GeV/m
(assume 2 m plasma)

## Slide 37: Constraint on the plasma density?
0.5 Torr E300_02799
driver
Ez
No energy loss
Max energy loss
double-value region
max energy loss
double-value region
E

## Slide 38: Micro bunching observed on DTOTR1 (20220725 E300_01846)
vacuum
DTOTR1 measures energy spectrum of the electron beam

## Slide 39: Correlation between DTOTR1 and SYAG
Good correlation between DTOTR1 (e- energy spectrum) and SYAG (X-ray from dispersed beam)

## Slide 40: Correlation between DTOTR1 and SYAG
SYAG signal charge
DTOTR signal [charge to charge2] depending on the coherence (micro-bunch length wavelength)
Enhanced peak in DTOTR indicates current spike 1 µm
comind=2
comind=60
comind=180

## Slide 41: Charge throughput
0.07 Torr
1.0 Torr

## Slide 42: Acceleration
Dataset E300_02837: 1.8 Torr H2. Quads re-image beam vacuum waist (at FILS) at 10 GeV. Dipole at 10 GeV.
Dataset: 20220817 E300_02837, H2, 1.8 Torr
x20
max. gain ~4 GeV

## Slide 43: Emittance of the accelerated beam
Dataset E300_02837: 1.8 Torr H2. Quads re-image beam vacuum waist (at FILS) at 10 GeV. Dipole at 10 GeV.
Dataset: 20220817 E300_02837, H2, 1.8 Torr