## Slide 1: C-band two-cell high-gradient RF cavity for high power HOM absorber testing
Haoran Xu, Dongsung Kim, and Evgenya I. Simakov
05/17/2023
LA-UR-23-25215

## Slide 2
Higher-order modes damping
Accelerator cell profile provided by SLAC and UCLA.
Goal: reduction of quality factor and transverse kick-factor of monopole and dipole modes from 5 to 40 GHz.
TM110 first dipole mode at 9.245 GHz
TM010 fundamental mode at 5.712 GHz

## Slide 3
Higher-order modes damping
Approach: HOM damping waveguides.
Damping load: NiCr or SiC coating layer.
20-cell studies in CST and Omega3P.
Length variation: 30-50 mm
Design 1 – straight waveguide slot
tin
tout
L_wg
Design 2 – one-section taper waveguide slot
t1
t2
L_wg1
L_wg2
t3
Design 3 – two-section taper waveguide slot
copper background

## Slide 4
Higher-order modes damping study workflow
Single cell with periodic boundary
20-cell structure
Find all monopole and dipole modes over 5 - 40 GHz.
Compute ohmic Q-factor, shunt impedance, kick-factor.
Add waveguide slots with lossy material coating layers.
Compute ohmic Q-factor, shunt impedance, kick-factor, for modes identified in STEP 1.
Compute Q-factor × kick-factor.
Setup waveguide slot with impedance boundary.
Compute ohmic Q-factor with damping, for modes identified in STEP 1.
Compute Q-factor × kick-factor.
STEP 1
CST
STEP 2
CST
STEP 3
CST / Omega3P

## Slide 5
Example: TM110 mode damping
Undamped TM110 mode (9.2 GHz).
  Q factor: 18150
  Q × transverse kick factor: 5.72×104 V/pC/m/mm
Damped TM110 mode in the individual cells of a 20-cell cavity.
  With Design 1: straight waveguide slot.
  SiC coating (1.0×102 S/m).
Chart: 9.2 GHz (TM110)
| 9223870000 | 9224870000 | 9227890000 | 9232270000 | 9238670000 | 9246530000 | 9255690000 | 9265450000 | 9276390000 | 9287350000 | 9298730000 | 9310100000 | 9320720000 | 9331060000 | 9340120000 | 9348440000 | 9355500000 | 9361260000 | 9365070000 | 9367650000
30 mm | 10280.7 | 10397.1 | 10737.7 | 11119.6 | 11246.8 | 10796.7 | 9758.64 | 8511.9 | 7344.13 | 6453.79 | 5855.35 | 5338.96 | 5045.76 | 4799.82 | 4634.03 | 4528.67 | 4445.92 | 4393.19 | 4311.9 | 4290.33
32 mm | 8352.67 | 8403.66 | 8554.61 | 8618.87 | 8415.82 | 7908.07 | 7185.85 | 6478.92 | 5749.46 | 5180.71 | 4708.5 | 4303.2 | 3984.49 | 3736.13 | 3509.84 | 3356.51 | 3221.11 | 3108.06 | 3026.46 | 2998.33
34 mm | 8144.03 | 8133.45 | 8041.8 | 7757.23 | 7315.58 | 6756.44 | 6096.63 | 5421.28 | 4714 | 4212.86 | 3824.12 | 3353.32 | 3026.17 | 2802.05 | 2599.62 | 2418.16 | 2279.28 | 2166.2 | 2108.48 | 2077.16
36 mm | 8664.16 | 8628.65 | 8513.72 | 8206.83 | 7761.88 | 7113.88 | 6388.21 | 5662.9 | 4977.03 | 4331.77 | 3828.55 | 3363.53 | 3027.29 | 2723.41 | 2500.34 | 2306.98 | 2179.5 | 2060.02 | 1996.65 | 1944.03
40 mm | 9534.78 | 9509.87 | 9408.22 | 9179.32 | 8771.1 | 8142.64 | 7351.99 | 6563.34 | 5704.52 | 5000.96 | 4423.84 | 3921.45 | 3563.17 | 3275.15 | 3048.64 | 2877.79 | 2773.27 | 2668.97 | 2603.94 | 2580.88
44 mm | 9532.47 | 9491.61 | 9308.32 | 8955.51 | 8385.25 | 7640.3 | 6805.87 | 5973.19 | 5219.97 | 4611.99 | 4134.84 | 3681.04 | 3349.38 | 3089.86 | 2901.58 | 2726.94 | 2620.48 | 2552.08 | 2461.41 | 2433.95
50 mm | 9330.34 | 9317.91 | 9231.03 | 8985.3 | 8575.39 | 7861.51 | 7149.69 | 6318.73 | 5504.93 | 4899.19 | 4283.73 | 3844.84 | 3438.79 | 3157.52 | 2939.86 | 2720.77 | 2636.28 | 2508.9 | 2435.62 | 2434
Chart: 9.2 GHz (TM110)
| 9223870000 | 9224870000 | 9227890000 | 9232270000 | 9238670000 | 9246530000 | 9255690000 | 9265450000 | 9276390000 | 9287350000 | 9298730000 | 9310100000 | 9320720000 | 9331060000 | 9340120000 | 9348440000 | 9355500000 | 9361260000 | 9365070000 | 9367650000
30 mm | 45.0061 | 393.0604 | 124.3496 | 513.7322 | 250.2923 | 788.3658 | 796.4328 | 6869.3357 | 4453.2345 | 245.8189 | 67.3321 | 10.4329 | 8.9974 | 2.8819 | 2.3211 | 0.077208 | 0.14953 | 0.04707 | 0.055227 | 0.047625
32 mm | 42.1272 | 290.7271 | 96.6109 | 392.2326 | 193.6319 | 603.2103 | 575.8103 | 5236.2324 | 3509.5037 | 194.2675 | 49.527 | 8.7696 | 8.4192 | 2.157 | 1.9333 | 0.067092 | 0.17271 | 0.016595 | 0.051787 | 0.0096534
34 mm | 75.2531 | 292.1881 | 89.5398 | 347.2948 | 157.596 | 514.6816 | 422.1651 | 4286.7333 | 2925.5229 | 193.1678 | 47.7983 | 8.2768 | 7.5576 | 1.6169 | 1.2918 | 0.010638 | 0.14536 | 0.037604 | 0.10854 | 0.021959
36 mm | 49.8611 | 340.5355 | 95.631 | 359.0017 | 171.5125 | 503.0352 | 522.1661 | 4522.6405 | 2994.4627 | 176.0247 | 44.5304 | 6.8263 | 6.5178 | 0.97258 | 0.803 | 0.0016541 | 0.070666 | 0.022775 | 0.0011869 | 0.0099152
40 mm | 45.596 | 344.6537 | 108.5565 | 409.7592 | 198.1831 | 610.3032 | 602.7432 | 5297.77 | 3441.77 | 183.7892 | 52.2865 | 7.1464 | 6.5329 | 1.8449 | 1.3394 | 0.065234 | 0.12645 | 0.035926 | 0.04598 | 0.021112
44 mm | 62.6255 | 342.8743 | 98.9121 | 420.4831 | 194.261 | 590.8763 | 535.9309 | 4767.413 | 3167.9898 | 192.5952 | 43.059 | 7.5509 | 7.6722 | 0.78221 | 1.5812 | 0.056049 | 0.25537 | 0.040028 | 0.039326 | 0.016528
50 mm | 42.8635 | 326.2758 | 117.1153 | 409.6377 | 175.1772 | 604.798 | 610.6252 | 5047.4023 | 3298.5259 | 192.6918 | 53.5414 | 8.321 | 9.1237 | 1.3304 | 1.6982 | 0.047669 | 0.040899 | 0.032556 | 0.044597 | 0.026598

## Slide 6
Current best-performing design
Design 3 – two-section taper waveguide slot
  NiCr coating (1.0×106 S/m).
Optimization setup.
t1 = 250 μm
t2 = 60 μm
L_wg1 = 4 mm
L_wg2 = 8 mm
t1 = 0.5 μm
Parameter | Value
Length of first w/g slot (L_wg1) | 2 to 8 mm
Length of second w/g slot (L_wg2) | 4 to 10 mm
Thickness of initial w/g (t1) | 0.25 mm (constant)
Thickness of 1st tapered (t2) | 20, 40, 60, 80 and 100 μm
Thickness of 2nd tapered (t3) | 0.5 μm
x1 = 22 mm
x2 = 26 mm
x3 = 34 mm

## Slide 7
HOM absorber high power test
NiCr (1.0×106 S/m) coating layers.
RF design verification at high accelerating gradient (~100 MV/m)
  Breakdown test
  Multipactor detection
Absorber performance vs. breakdowns.
  Damage examination
|E| plot
peak field
field in gap
0
1
(arb. units)

## Slide 8
Two-cell cavity design
π-mode operation, critical coupling.
HOM damping: straight waveguide slot.
HOM damping optimization.
  Waveguide longitudinal extension length
  Waveguide transverse sizes
    Eigenmode optimization result: 34 mm & 50 mm
    Finalized dimension: 45 mm
NiCr coating

## Slide 9
HOM damping waveguide transverse dimension
Providing maximal damping of HOM.
Rejecting additional parasitic modes introduced by the HOM damping waveguides.
22.0 mm
34.0 mm
unwanted waveguide mode
Q0, NiCr-coated = 10721
Q0, uncoated = 13152
Two-cell HOM simulation results
0
1
(arb. units)

## Slide 10
Two-cell cavity RF analysis
100-MV/m accelerating gradient.
Design parameters | 
Operating frequency f0 | 5.712 GHz
unit cell shunt impedance rsh | 118 MΩ/m
unloaded quality factor Q0 | 13500
unloaded quality factor, no absorber Q0, uncoated | 13525
Cavity coupling factor β | 1.00
RF power for 100-MV/m gradient | 4.4 MW
NiCr loss for 100-MV/m gradient | 2.5 kW
NiCr average loss for 100-MV/m gradient, 1-μs pluse length, 100 Hz repetition rate | 0.25 W
NiCr electrical conductivity | 1.0×106 S/m

## Slide 11
Two-cell cavity RF analysis
Local peak E-field normalized to Em.
Local peak H-field normalized to (Em/Z0).
  Z0 = 377 Ω.
Electric field local peak values | 
Cavity overall | 1.48
Coupling slot | 0.28
Waveguide | 0.086
Magnetic field local peak values | 
Coupling slot | 0.70
Waveguide | 0.075

## Slide 12
Two-cell cavity HOM damping
NiCr (1.0×106 S/m) coating layers
HOM E-field magnitude distributions –

## Slide 13
Fabrication and challenges
OFHC copper cavity fabricated in quadrants, coated with NiCr layers, and then brazed together.
Tuner design for quadrants.
Machining tolerance sensitivity.
  0.001-inch increase of the elliptical cell profile minor radius results in 5-MHz reduction in the cell resonant frequency.

## Slide 14
Acknowledgments
Work supported by the U.S. Department of Energy, under Contract No. 89233218CNA000001