## Slide 1: C-Band Distributed Coupling Structure Design and Wakefield Damping
Zenghai Li, Sami Tantawi, Emilio Nani, Muhammad Shumail (SLAC)
Dongsung Kim, Evgenya I. Simakov (LANL)
LCWS2023 May 15-19 SLAC

## Slide 2: Outline
Parallel feed scheme for linac structure design
High efficiency cell shapes for parallel feed linac
Parallel feed waveguide system design
Long-range wakefield damping
High efficiency, larger aperture 135 deg/cell parallel feed structure
Outlook

## Slide 3: Parallel Feed Scheme Extends Parameter Space for Linc Structure Design
Parallel Feed Structure
  Cells fed individually
  Feed waveguide distribute power equally to each cell at180 deg phase difference
  Scheme also apply to other phase advances to take advantage of higher shunt impedance
Advantages
  Iris radius not dictated by cell-to-cell RF coupling
  Cell shape can be optimized to achieve higher efficiency
  Structure can be machine in two halves or quadrants
  Structure tuning straight forward

## Slide 4: Flexible Cell Optimization to Achieve Higher Shunt Impedance
C-Band Cell at Cryo-T shunt impedance (77K): 298 MΩ/m
180 deg/cell. Iris radius: 2.62 mm
NLC X-Band structures shunt impedance (300K) : 98 MΩ/m
(iris radius: 4.75 mm)

## Slide 5: Short-range Wake Field Analysis – iris aperture for LC
https://arxiv.org/pdf/1807.10195.pdf
Karl Bane
Transverse Wakes
Longitudinal Wakes
C-band, 𝑎⁄𝜆 = 0.05, 2𝜋/3 cavity, 1% BNS correlated energy spread, 𝛽x0 = 4 m: 𝜎z = 150 μm (left) and 𝜎z = 100 μm (right).
The projected emittance growth factors are 4.5 (left) and 0.76 (right).
Preliminary studies on single-bunch short range wakefields indicate that for the nominal charge of 1 nC and an operating gradient at or above 100 MeV/m, an iris aperture radius as small as 2.62 mm is tolerable
Assume an injection energy of 10 GeV with a 𝛽x0 = 4 m, and a final energy of 1 TeV with an increase in 𝛽~E1⁄2 , 100 𝜇m bunch length.
Larger iris aperture possible with 135 deg/cell to achieve the same shunt impedance
Glen White, “C3 Main Linac Beam Dynamics”, May 17, 2023

## Slide 6: Parallel Feed Uniform Power Distribution
Phases
(180 phase alternation masked by port polarization vector definitions)
(Chris Nantista)
simulated scattering matrix
E field at mid-plane
TW
Input match better than -60 dB.
Normalized field amplitudes
(ohmic losses not included)
A waveguide with equal power tap-offs to feed each individual cell
All input power goes to the feeds, no reflection back to input port
All tap-off junctions identical. Can be designed to power any number of cells

## Slide 7: Modular Design Approach of Parallel Feed Structure
Two repeating elements
  The T-junction
  The cell and coupler

## Slide 8: The Manifold Circuit
3-port
S-matrix condition:
Each ½ manifold represents a shorted transmission line loaded with periodic ports.
We need to satisfy the following 3 conditions:
matched at input
power equally divided
p (180) phase advance/port
The 3-port junction need to satisfy the following scattering matrix
input
3-port
n=9
(Chris Nantista)

## Slide 9: Novel Fabrication Approach with Reduced Cost
Machined in two halves

## Slide 10: Field Quality - 3D Field Symmetrization to Minimize Coupler Effect
Dipole
with symmetrization
with symm-stub
Single side coupling induce significant dipole and quad fields
3D coupler symmetrized
  Minimizes side effects of 3D acceleration fields
  Minimizes electric center offset of HOMs
Dipole
Quad
Quad
w/o symmetrization
dipole, quad calculated at 50MV/m

## Slide 11: Long-range Wakefield Modeling and Suppression
Wakefield of 1-m structure of 40 identical cells
Dipole kickfactor of the CBand cell
Due to a smaller aperture, dipole modes up to ~40 GHz need to be included for long-range wakefield modeling
Both damping and detuning needed to suppress long-range wakefield
wakefield envelope without detuning
wakefield envelope with detuning

## Slide 12: HOM Damping Using Radial Slots Cutting Through Cell Iris
Structure machined in two halves, or in quadrants with other more optimal phase advance
Naturally can use a gap between the two halves to extract HOM power
Additionally, add lossy surface in slot to absorb HOM power (sigma=5.8e4)

## Slide 13: HOM Damping with Tapered Lossy Slot -
Slot surface conductivity (Ni-Cr) 1.0E+6 S/m
Tapered slot
Linear taper: slot height: from 300 micron to 100 micron
Non-linear taper
Optimization in progress
Need more studies in
  Lossy materials at cold temperature (77K)
  Coating or thin layers brazing on to structure

## Slide 14
135 degree/cell design
Higher efficiency
Larger iris opening

## Slide 15: C-Band 135 deg/cell Structure
Cell-to-cell phase advance: 135 deg
  Cell length: 19.682 mm
  Total number of cells: 104
  Parallel feed waveguides: 4, feed at middle of structure
4 135-deg cells form a 360+180 deg section
each cell fed by a respective waveguide
2m 104 cell Structure

## Slide 16: C-Band 135-deg Cell
Optimized to obtain the same shunt impedance as the 180 deg design
  Iris aperture can be enlarged to 7.11 mm, as compared with the iris aperture of 5.25 mm for the 180 deg design
  Relaxes structure alignment tolerance requirements
135-deg cell shape
single cell with parallel feed waveguide
E field
B field

## Slide 17: 135 deg/cell Parallel Feed
RF power fed at the middle of the structure
RF phase between the cells is 180 degrees
Parallel waveguide feed 13 cells on either side of upstream and down stream
RF phase: 180 deg between the cells
amplitude

## Slide 18: 180 degree/cell vs 135 degree/cell
180 deg/cell, TWO parallel feeding waveguides, 40cell/meter
135 deg/cell, FOUR parallel feeding waveguides, 52cell/meter

## Slide 19: 135/cell Structure – Possible Damping Scheme
Parallel feed waveguide acting as damping manifold
  similar to NLC DDS structure
Narrow slot cutting through the iris couples the cells to waveguide
HOM calculation in progress
HOM power extraction
(illustration of damping)
NLC RDDS

## Slide 20: Outlook
Structure optimization
  180 deg/cell parallel feed
  135 deg/cell parallel feed
Wakefield damping optimization, in collaboration with LANL (Evgenya I. Simakov, Dongsung Kim)
  Damping slot optimization
  Damping material studies