## Slide 1: Development of a Compact Periodic Permanent Magnet Focused C-Band Klystron
LCWS 2023
Presenter: Brad Shirley
Gonzalez, Haase, Herbst, Hernandez, Hong, Kemp, Krasnykh,
Le Sage, Li, Liu, Merrick, Nanni, Shumail, Tantawi, Weatherford
Date: May 17th, 2023
Notes: Key difficulties related to klystrons are much higher current / need to cram strong B-fields into tiny tunnel for high efficiency interaction

## Slide 2
This research was developed with funding from the Defense Advanced Research Projects Agency (DARPA). The views, opinions and/or findings expressed are those of the author and should not be interpreted as representing the official views or policies of the Department of Defense or the U.S. Government.

## Slide 3: High Level System
Develop a compact, light weight, and portable accelerator system for a variety applications
Array of 26 klystrons that are pulsed by a 35 MW modulator to deliver ~550 kW per klystron of power to two cells of a linac
Linac will accelerate beam to a maximum energy of 20 MeV with 0.5 A of current
High Level System Mockup
Ideally want to fit inside of a 40 cm radius cylinder 1 m long

## Slide 4: Two Cell System Block Diagram
SSA
RF Load
RF Source
Pulsed Power System
200W
5.712GHz
550kW
5.712GHz
60kV,1.5us
Phase 2: “Beam”
Reflected Power
Feedback
Accelerator Cavities
LLRF

## Slide 5: Two Cell Test High Level Mockup
RF Source
RF Window
RF Load
Linac
‘Two Cell Section’
Solid State Amplifier
Pump Out and Instrumentation
HV Power Supply
Modulator
mm

## Slide 6: Klystron Design

## Slide 7: Top Level Requirement
Metric | Threshold
Output Power | 540 kW (peak)
Frequency | 5.712 GHz
Efficiency | 50%
Beam Voltage | 60 kV
Beam Current | 17.2 A
Repetition Rate | 60 Hz
Pulse Length | 1 µs
Perveance | 1 µK
Beam Tunnel Radius | 3.8 mm
Brillouin Field | 1.3 kG
Circuit Length | 300 mm (as short as possible)
Mass | 1.5 kg

## Slide 8: Initial Design Tradeoffs
Tradeoffs were conducted to understand what operating parameters were needed to achieve efficiencies and output power
Lower frequencies allow for smaller magnetic field strengths, but larger beam tunnels
  Advantageous for weight constraints
  5.712 GHz was used
Higher perveance allows for higher beam power, but less efficient
  1 micro-perveance was used
  Setting the perveance and the voltage sets the current

## Slide 9: Preliminary Simulations
Preliminary simulations in KlyC, a 1.5-D large signal klystron code developed by CERN
Optimize a variety of cases to analyze performance
  3 cavities vs. 4 cavities
  Varying perveance
  Varying drive power
  Cavity frequencies and external Q factors
Four cavity geometry allows for higher efficiencies
This dictates an upper bound for further simulations
Bunching Current vs. Position
Optimization Process with > 1000 runs

## Slide 10: Electron Gun
EGUN was used to design electron gun and electrostatic focusing
Knowing the target power, operating voltage, and perveance sets the gun current
Cathode, heater, and focus electrode is currently on order
High voltage gun insulator and weld flange assembly on hand
Cathode
Focus Electrode
Anode
Beam Waist
Electron Beam
Electrostatic Potentials
Parameter | Value
Current | 17.2 A
Perveance | 1.178 uK
Beam Waist | 2.8 mm
Throw Distance | 29.6 mm
Fill Factor | 73%
Notes: The beam fill factor of 73% is very high (mitigation = very low duty operation. As long as beam losses don't impact efficiency, it should be OK)

## Slide 11: High Voltage Standoff for Electron Gun
High voltage electrostatic simulations completed to allow for sufficient standoff in and around the gun
Gun is biased to -60 kV
Utilizes existing ceramic design
  Reduces lead time and tooling development
Remaining assemblies ready for further mechanical design
Reduction in peak E-field is possible with an increase in size
Location | Peak E-Field
Air | 2.2 MV/m
Ceramic | 1.8 MV/m
Vacuum | 22.8 MV/m

## Slide 12: Cavity Design
Klystron cavities were designed in HFSS
Optimized for gap coupling factor (M) and shunt impedance (R/Q)
  M: 0.747
  R/Q: 117
  Qext Input – 250 , Qext Output – 45
Same geometry used for all four cavities with slight changes in outer radius for final RF design
Design of IP and OP coupled cavities complete
  Side coupling compensates for location of inlet on magnet stack
Full RF Circuit
Input and Output Coupled Cavities
Notes: Did you check ohmic losses and field strength in penultimate and output cavities? I originally designed with pretty small nose radii with the expectation that I would check and increase rounding if needed

## Slide 13: Magnetic Focusing Circuit
NdFeB periodic permanent magnets are used to focus the beam
  Allows for lighter weight magnetic focusing than electromagnets
Full nominal design complete which includes:
  Gaps in magnets for waveguide routing
  Correct field strength and period to focus beam

## Slide 14: Magnetic Focusing Circuit
Initial prototype klystron will use larger magnets
Preliminary designs show reduction in weight is possible with more complex magnet design
Weight reduction from 3.25 kg to 1.35 kg -> ~60% weight decrease
  Magnets hug beam pipe, reducing the inner diameter

## Slide 15: TESLA Simulations
TESLA, a 2.5D large-signal code, is used in the optimization process of the klystron
  Optimization of cavity positions, frequencies, and external Q factors
Current optimized design produces 619 kW at 57% efficiency -- gain of 36 dB
R vs. Z
RF Bandwidth at Fixed Drive
Transfer curve at 5.712 GHz
Maintain output power goal over ~ 40 MHz
Input SSA can be nominally operated at 350 W
  Nominal klystron design was optimized at 150 W

## Slide 16: Mechanical Design, Test, and Next Steps
Full mechanical package is nearly finished
  Many pieces are being manufactured
Next steps:
  Cold test of individual cavities
  System is brazed, leaked checked, and baked-out
  High power tests using pre-established modulator at SLAC
Modulator to be used in high power testing

## Slide 17: Thank you!

## Slide 18: Reference slides follow

## Slide 19: High-Level Block Diagram Overview
C49
C50
C51
C52
Magic Tee
Klystron 26
Mod
Klystron 25
Mod
Load
Load
LLRF
Magic Tee
LLRF
Vacuum Pipe
Gun
C0
Power Supply
SSA
C1
C2
C3
C4
Magic Tee
Klystron 2
Mod
Klystron 1
Mod
Load
Load
LLRF
Magic Tee
LLRF

## Slide 20: Cold Test – Clamped Test Cells
Preliminary clamped cold test of SST test cells
All cavities within ~1 MHz of each other
Next steps:
  Understand tuning behavior
  Post-braze cold test
  Copper plated test and tune
Cell | Resonant Frequency (GHz)
Design | 5.6740
1 | 5.7206
2 | 5.7213
3 | 5.7218
Test Setup

## Slide 21: Sensitivity Test Cont.
Perturbation in tuning of first two cavities
  Fixed drive power and frequency
All cavities copper (Q ~ 7000)
  Can maintain peak power goal over wide bandwidth
Cavity 1 & 2 SST (Q ~ 1000) , cavity 3 & 4 copper
  Greater wall losses, less overall gain