Status Report on the
Magnetohydrodynamic Simulations
of a Tapered Plasma Lens
for Optical Matching at the ILC e+ Source
M. Formela1, G. Moortgat-Pick1, N. Hamann1, G. Loisch2, M. Mewes2,
M. Thévenet2, J. Osterhoff2
1University of Hamburg, Hamburg, Germany
2Deutsches Elektronen Synchrotron DESY, Hamburg, Germany
LCWS2023

---
Motivation
- Need to collimate divergent e+
  - Optical Matching Device
Principle of Plasma Lens:
  1. Inlets fill capillary with gas (e.g. H2, Ar)
  2. Voltage on electrodes ignites plasma
  3. Electrons are accelerated (Electric current)
  4. Current induces azimuthal magnetic field Bφ
  5. Magnetic field focuses incoming charged particle beam
Source:	Adolphsen, Chris, et al. “The International Linear Collider Technical Design Report-Volume 3. II:	Accelerator Baseline Design.“, No. arXiv: 1306.6328. CERN, 2013.
ILC e+ source
Optical
matching
Device

---
Optmization of PL Design
Simulations
with ASTRA
Particle Tracking Simulations
    - Goal: find optimized PL design
    - Conditions:
        1. ILC e+ distribution
        2. No Beam self-interaction
        3. Idealised plasma lens:
            - No Plasma dynamics
            - Ideal magnetic field (from j(x,y,z,t) = jz(z))
    - Result: ~43% captured e+ with Tapered capillary profile!
Large dimensions!
	Electric Current	Taper Type	Opening Radius	Exit Radius	Capillary Length
Full Scale:	9000 A	linear	4.30 mm	25.5 mm	60 mm
Prototype:	350 A		0.85 mm	5.0 mm	12 mm
Downscaled
by factor ~5

---
Preliminary (M)HD Results
Model by
M. Mewes
- Simulations in COMSOL
- Effective 3D Model (2D with axial sym.)
Simulated Field underperformes!
  - Probably no problem
    1. Large overhead
    2. More realistic simulation needed

---
Outlook
Implementations needed:
  1. Argon reactions (instead of H2)
  2. More realistic electrode geometry
  3. Angled Inlets
  4. Realistic materials of components
  5. Rotating target
To study:
  1. Plasma response to multi-pulse discharges
    - Demanding e+ beam time structure
  1. Gas flow into downstream accelerator
    - Discharges in cavity possible (no acceleration)
  1. Heat load on geometries
Compare with prototype experiments by Niclas Hamann (next talk)

---
Thank you
for listening!