## Slide 1: Hybrid Asymmetric Linear Higgs Factory (HALHF)
https://arxiv.org/2303.10150

## Slide 2: Plasma Wave Acceleration

## Slide 3: Hybrid Asymmetric Linear Higgs Factory (HALHF)
The basic idea is – there are enough problems with a PWFA e- accelerator; e+ is even more difficult. Bypass this for e+e- collider by using conventional linac for e+.
For this to be attractive financially, conventional linac must be low energy => asymmetric energy machine.
This requirement led to (at least for us) unexpected directions – the more asymmetric the machine became, the better!

## Slide 4: Relativistic Refresher
It turns out that the optimum (see below) for Ecm = 250 GeV is to pick Ee = 500 GeV, Ep= 31 GeV, which gives a boost in the electron direction of g ~ 2.13.

## Slide 5: HALHF Layout
Overall facility length ~ 3.3 km – which will fit on ~ any of the major (or even ex-major) pp labs. (NB. There is a service tunnel a la ILC (not shown))
e-
e+
e+ BDS
e- BDS

## Slide 6: Energy Efficiency
Asymmetric machines less energy efficient than symmetric – energy lost “in accelerating the C.o.M.” For equal bunch charges => 2.5 times more energy required for same C.o.M. energy.
Can be reduced by introducing asymmetry into beam charges – increase charge of low-energy beam and decrease high-energy s.t. N2 = NeNp constant => L conserved.
P/P0 = (NeEe+NpEp)/(N*sqrt(s))
Optimum is to scale e+ charge by sqrt(s)/(2Ep), i.e. factor ~ 4.
Producing so many e+ problematic – compromise by scaling by factor 2 (2*e+, ½* e-).
Reduces energy increase to 1.25. Also reduces bunch charge in PWFA arm.

## Slide 7: Emittance reduction
Geometric emittance of bunch scales with 1/E .
Lower-energy e+ beam must have smaller b function at I.P. – use bx /by = 3.3/0.1 mm c.f. CLIC 8.0/0.1 mm.
In contrast, high-energy e- beam - b function can be increased, which could reduce complexity of BDS.
More interesting is to increase the e- emittance AND reduce the b function => normalized emittance can be 16 times higher for the same L => increased tolerances in PWFA arm.
Beam-beam focusing effect on L must be simulated with Guinea Pig.

## Slide 8: Beam-beam Effects
Guinea-Pig results:
ILC
HALHF
HALHF with reduced emittance for PWFA

## Slide 9: Positron Source
“Conventional” e+ sources are not trivial – that for ILC, which has relaxed requirements wrt HAHLF, still under development.
e- accelerated to 5 GeV and then collide with target to produce e+ which are accumulated, bunched and accelerated to 3 GeV and then damped in 2 rings (~identical to CLIC but bigger e+ bunch charge (4*1010 e+).
May be possible to use spent e+ bunch after collision rather than dedicated e- bunch, with cost savings.

## Slide 10: Main RF Linac
Split in 2, to accelerate e- PWFA drive beams from 1 – 5 GeV & then both e+ and e- from 5 GeV to 31.3 GeV.
Assume gradient of 25 MV => 1.25 km long.
Delivers total average power of 21.4 MW => including e+ power and e ~ 50%, wall-plug 47 MW.
Assume warm L-band linac – if necessary CW SRF could be used but would increase cost and change bunch pattern.
Before drivers, e+ bunch accelerated with 180o phase offset.

## Slide 11: PWFA Linac
Drivers go through turn-around and then distributed to plasma cells via undulating delay chicane.
Assuming TR ~ 1, e- bunch accelerated by 31 GeV/5m stage => 16 stages with r ~ 1.5*1016 => 6.2 GV/m.
Interstage optics needs ~ <26.5m> but scales with sqrt(E).
Total length of PWFA linac = 410m.

## Slide 12: PWFA Linac
Assuming PWFA e~37%, 75% driver energy into wake, 50% of which is extracted => 25% of driver energy dumped into 16 beam dumps, 37.5% goes into plasma cell => 100 kW/m.
Utilising emittance asymmetry eases emittance preservation problem & mitigates effects of ion motion – e- beam density reduced cf symmetric machine by factor 32 => ions Df ~ 0.17 (<<p/2) [J. Rosenzweig et al., PRL 95, 195002 (2005)] [W. An et al., PRL 118, 244801 (2017)

## Slide 13: Bunch-train pattern.
Assuming L-band linac:

## Slide 14: HALHF Parameter Table

## Slide 15: HALHF Parameters cf ILC & CLIC

## Slide 16: Cost Estimate
Scale from existing costed projects wherever possible – mostly ILC – very rough – not better than 25% accurate.

## Slide 17: Cost Estimate
Snowmass study ITF of various accelerator costs gives ILC Higgs Factory Total Project Cost (TPC) (= US accounting) of $7 – 12B (2021 $). Scaling this by the value estimate (~European accounting) of HALHF/ILC@Snowmass gives HAHLF TPC ~ $2.3 – 3.9B: c.f. EIC TPC = ~< $2.8B.

## Slide 18: Running Costs
Dominated by power to produce drive beams.
(100*16*4.3nC + 6.4nC)*100 => 47.5 MW@50% eff.
Damping rings: 2*10 MW.
Cooling – assume similar to CLIC => 50% of RF power (corresponds to 20 kW/m).
For magnets and other conventional sources assume ~9 MW.
Gives total power requirement ~ 100 MW – similar to other proposals.

## Slide 19: Experimentation at HALHF
Boost is smaller than HERA - HERA detectors very similar to those at symmetric machines.
Preliminary study (M. Berggren) with long ILD barrel shows ~ similar Higgs resolution.
Measurement of L via Bhabha (e+e- -> e+e-) - rate reduced by 1/(qg)2 & e+ scattered into barrel – but not a problem. Singles rate good for machine optimisation

## Slide 20: Project Staging
Any project of this size and scope needs a ~10% prototype. A few cells producing useful currents of e- at few 100 GeV would be very interesting for SFQED.
Once satisfactory performance demonstrated, remaining elements can be constructed and then running at Z can be used to tune up machine and detector.

## Slide 21: Upgrades
Energy upgrade: keep e+ energy same increases g as E increases – experiments more and more difficult; increasing e+ energy to keep g ~ constant gives expensive linac.
However, getting to ttbar threshold with same e+ energy => E(e-) ~ 1 TeV and g ~ 2.9, still less than at HERA and ttbar final state even more spherical. Keeping g constant by lengthening conventional linac needs E(e+) ~ 44 GeV and E(e-) ~ 700 GeV. (space allocated and tunnel already built both for linac &BDS).
Produce e+ polarization via ILC-like scheme - ideas exist for E(e-) 500 GeV.

## Slide 22: Summary & Conclusion
HALHF benefits from maximal asymmetry.
Even if e+ acceleration not a problem, HALHF could still be best way forward – but requires > a decade of significant R&D.
Conventional design work needed: DR with high bunch charge; heavily loaded linac; BDS…
PWFA R&D: higher accelerated charge (x ~10), higher repetition rate (x ~1000), plasma-cell power dissipation (x ~1000), beam jitter reduction (x ~10-100).
BUT – if R&D successful, HALHF would be the first e+e- Higgs Factory proposal that costs ~ same as a “national” project.