## Slide 1
C3 Alignment with Rasnik
…the alignment of the C3 accellerator structures…
Harry van der Graaf, Joris van Heijningen, Anoop Nagesh Koushik
LCWS 2023, SLAC, Stanford, CA

## Slide 2
Muon chambers in L3
First Rasnik design: 4QD
Red Alignment System NIKhef
1983: Alignment of the Muon Spectrometer of the L3 experiment at CERN
…..original idea was from Draper Lab/MIT, Cambridge, Mass

## Slide 3: 1993: CCD-Rasnik Three Point Alignment system for ATLAS
M. Beker et al., “The Rasnik 3-point alignment system”, JINST 14 P08010 (2019)
Coded mask is projected via lens on pixel sensor;;
In principle, all 6 DoFs of mask & pixel sensor + x,y,z of lens can be determined;
x,y,z and rotZ (qz, not for lens) are measured
z

## Slide 4: ATLAS experiment: 8000 Rasniks, none fails since start
In order to properly reconstruct vertices…
… we need to know where our detectors are!

## Slide 5: Long distance Rasniks: RasDif

## Slide 6
Alignment over long distance ( > 100 m): RasClic, later RasDif:
replace lens by zone plate
replace coded mask by monochromatic spherical-wave light source (1 $ laser diode)
140 m
Pioneered by A. Seryi, SLAC:
Investigation of slow motions of the SLAC linac tunnel, SLAC-PUB-8597 8597 (1) (2000) P06034, arXiv:physics/0008195.

## Slide 7: RasCLIC: 4 m set-up at Nikhef
2 Rasniks and 2 Rasdifs in parallel operation
2 masks and 2 lasers on actuator
2 lenses and 2 diffraction plates
4 pixel image sensors of a Logitech C300
JvH, “Precision Improvement in Optical Alignment Systems of Linear Colliders ”, M.Sc. Thesis, Delft University of Technology (2012)

## Slide 8
RasChain: interconnected “leapfrog” Rasnik systems for basic CLIC units of 2010 mm

## Slide 9: 140 m test set-up (TT1 @ CERN)
JvH, “Precision Improvement in Optical Alignment Systems of Linear Colliders ”, M.Sc. Thesis, Delft University of Technology (2012)
in vacuum: 100 nm RMS over 140 m

## Slide 10: Limits and sources of noise
Quantum noise =
√(electronic noise2 + photon noise2)
constant # photons
Blurring by diffraction
Image wobble by varying refractive index along optical path
H. van der Graaf et al., “The ultimate performance of the Rasnik 3-point alignment system”, Nuclear Inst. and Methods in Physics Research, A 1050 (2023) 168160

## Slide 11: Future Rasnik developments
Particle colliders and gravitational-wave detectors are going cryogenic
C3 cool copper collider
Einstein Telescope
77 K
Need for cryogenic CMOS pixel sensors and diode laser (e.g. VCSEL)
10 K

## Slide 12
From 3-point alignment system to n-point alignment system:
chainplates
image pixel sensor
zone plate
VCSEL laser diode

## Slide 13
accelerator structure
stick
C3: alignment of ~2100 accelerator structures
Stick

## Slide 14
Front view into accelerator structure
Alignment fits in two optical paths, adjascent and along to accelerator structures,
of 5 mm x 18 mm.

## Slide 15
acc structure
raft unit
cryo module n+1
cryo module n
8x RasDif chainplates
Structure can rotate around Y axis left unnoticed by Rasnik!
Each structure is 6D defined in space, with redundancy
↺

## Slide 16
The Stick
A Stick includes 4 items:
a CMOS image sensor chip
a transparent pattern forming a zone lens
a laser diode
a mounting interface
image sensor mount
zone lens
laser diode mount
YZ ref fixation
X ref fixation

## Slide 17
Rasnik for Quarter Cryogenic Module QCM
Sticks: fully submerged in LN2:
 Laser diode and cam (image sensor on pcb) should be able to operate in LN2 (77 K)!
Laser diode: tested 4 different types, worked allright simply submerged 😊
our favorite cam (Daheng VEN-134) fails at 90 K 🙁

## Slide 18
CCDs operating at 4 K exist (Webb telescope)
Commercially available: Teledyne CCD201-20. Too sophisticated, need to develop readout system
N. McConkey (Univ of Sheffield): tested, in 2016, many simple webcams at 77 K and found the Floureon Car Rear View cam working at 77 K. This cam is not anymore available.
Alternatives:
  1 place cam in mini-cryostat: complicated, expensive
  2 place Rasnik in gaseous N2 space: very unpractical
Nicola McConkey, Neil Spooner, Matthew Thiesse, Michael Wallbank, Thomas Karl Warburton:
Cryogenic CMOS Cameras for High Voltage Monitoring in Liquid Argon arXiv:1612.06124

## Slide 19
mirror
cam in dewar
Alternative 1: place cam in insulating container (dewar)

## Slide 20
LN2
gaseous N2
Alternative 2: bring Rasnik into gaseous volume

## Slide 21
Conclusions & plans
The continues alignment of all accelerator structures using Rasnik seems feasable
Priority 1: find 77 K-proof cam [including (warm) readout & control system]
Design Stick (and possible aux mechanics): produce 8 sticks for QCM, ready end 2023
Set up 3-stick calibration station: QCM is to be equipped with pre-calibrated Sticks.
QCM: Quarter Cryogenic Module