## Slide 1: C3 Structure Development Updates
Ankur Dhar
02/07/2023

## Slide 2: Main Linac Structure Update
Next iteration of main linac module is undergoing design
Main goals are to address poor surface bonding along the irises and post-machining warping
This is being addressed through the addition of an additional strongback along the center of the structure
  Braze alloy will also be applied inside the structure close to the irises, with copper spacer to ensure braze material flow
Point of Contact: Valery Borzenets valeryv@slac.stanford.edu

## Slide 3: NiCr Deposition Method
NiCr is typically sputtered for thin film applications
This is not viable for coating large damping slits
Potential solution is to electroplate layers of Ni and Cr and then use a hydrogen furnace to form NiCr
The RF loss of this fired sample was verified through S11 measurements of a resonant cavity
Point of Contact: Valery Borzenets valeryv@slac.stanford.edu

## Slide 4: NiCr Application to Main Linac
This electroplating method provides a scalable solution for depositing NiCr on damping slits
Linac cavities would be rough machined along with slits, waveguides, etc
Electroplating would cover entire linac
Final machining removes NiCr layer from unwanted areas, leaving coated slits
Point of Contact: Valery Borzenets valeryv@slac.stanford.edu

## Slide 5: Additive Manufactured C-Band Load: Escargload
Inspired by CERN’s efforts on designing an additively manufactured load for X-band
General design was to create a spiral load formed from a taper lossy waveguide with a pump-out port at the center
Point of Contact: Julian Merrick julianm@slac.stanford.edu

## Slide 6: Additive Manufactured C-Band Load: Escargload
Initial designs were iterated within HFSS, before being sent to Protolabs for manufacturing
Target loss was -20dB at 5.712 GHz
Simulations estimated -28dB
Point of Contact: Julian Merrick julianm@slac.stanford.edu

## Slide 7: Testing the Escargload
Cold tests were conducted at SLAC before being sent to Radiabeam for high power tests
Measured loss at 5.712 GHz was -22.8dB in vacuum
High power testing at Radiabeam was conducted with 8 MW max power
Tests were paused for reasons unrelated to load performance
In Air
In Vacuum
Point of Contact: Julian Merrick julianm@slac.stanford.edu

## Slide 8: Characterizing Large Aperture Injector Linac
Large apertures introduce coupling between cavities
This cross coupling means tuning needs to account for collective behavior within the structure
These adjustments were verified with extensive simulation in HFSS and ACE3P
Bead pulls were conducted to measure field flatness as tuning was conducted
Point of Contact: Ankur Dhar adhar@slac.stanford.edu

## Slide 9: Bead Pull Characterization
In order to better characterize the contribution of each cavity on the collective π mode, a second larger bead was used as a static perturbation
Second Line
First Line
Second Line
First Line
Crank
Point of Contact: Ankur Dhar adhar@slac.stanford.edu

## Slide 10: Measuring Perturbation Effects on Bead Pull
Cavities 5 and 16 are mirrored across the structure, and have reciprocal effects on the overall field structure
Tuning cavities based on these differential measurements allows us to tune the cavities relative to each other to restore field flatness
Point of Contact: Ankur Dhar adhar@slac.stanford.edu

## Slide 11: Modeling Perturbation using ACE3P
ϵ1
ϵ2
ϵ3
ϵ10
Each cavity has a dielectric bead with a relative permittivity to induce tuning
Each bead can be turned ON or OFF in simulation
ϵi=1,2,,..20,i≠10 =1, ϵ 10 = 3.5 → Overall pi mode shift of -15 kHz
No perturbation
Only Cell 10 perturbed
Frequency [GHz]
S11 [dB]
Point of Contact: Mohamed Othman mothman@slac.stanford.edu

## Slide 12: Perturbation Approach
First, calculate derivatives of π mode frequency of each cell versus change in dielectric constant εi
Calculate derivatives of field amplitude of each cell versus change in dielectric constant εi
Calculate derivatives of field amplitude of each cell versus against frequency shift
Symmetric matrix
Point of Contact: Mohamed Othman mothman@slac.stanford.edu

## Slide 13: π mode Frequency Perturbation
ϵ10
ϵ1
ϵ2
ϵ3
ϵ4
ϵ5
ϵ6
ϵ7
ϵ8
ϵ9
ϵ10
Frequency Shift [kHz]
End cells affect the π mode more strongly than inner cells
This allows for tuning each cavity by tracking π mode only
Point of Contact: Mohamed Othman mothman@slac.stanford.edu

## Slide 14: Field Profile Perturbation: Varying ϵ1
only changing ϵ1
z [m]
E Field [V/m]
ϵ1 =0.5
ϵ1 =0.9
ϵ1 =1.8
ϵ1 =2.2
ϵ1 =3.5
This is repeated for all other cells and values of ϵ1
Point of Contact: Mohamed Othman mothman@slac.stanford.edu

## Slide 15: Field Profile Perturbation : Varying ϵ1
ϵ1
% E Field change
This is repeated for all other cells
Point of Contact: Mohamed Othman mothman@slac.stanford.edu

## Slide 16: Preliminary Tuning Results
With this information, the first pass of tuning has been successful in improving field flatness
Structure will be brazed one more time to fix leaks before final tuning to 2.856 GHz

## Slide 17: Questions?

## Slide 18: Future Test Plans
Once tuned, various proposals to testing the structure are in preparation:
High power test measuring breakdown rate with 35 MW klystron at Station S-band at NLCTA
ASSET-style wakefield measurement without high power at FACET-II
  Also potentially at XTA within NLCTA
Full power + beam tests at CLEAR and/or APS
Open to further suggestions for test sites

## Slide 19: Comparison of Technologies for EIC pre-injector e- linac
 | SLAC Linac 3 m structure | PSI Linac 4 m structure | Distributed Coupling 1 m structure | Cryo-Distributed Coupling [77 K] 1 m structure
Shunt Impedance [M/m] a/ [radius/wavelength] | 51* 0.15-0.11 | 45-56+ 0.135-0.095 | 58 0.125 | 210 0.125
Power / Length @ 16 MeV/m [MW/m] / Power for 400 MeV [MW] in 25 m Min. 65 MW 5045 Klystron | 8.3 / 210 4 klystrons | 6.2 / 156 3 klystrons | 4.4 / 110 2 klystrons | 1.8 / 44 1 klystron
Achievable Gradient [MeV/m] Constant BDR Scaled from Pulsed Heating | 50 | 60 | 74 | 118
Power for 400 MeV in 8 m [MW] Corresponds to 50 MeV/m Min. 65 MW 5045 Klystron | 645 10 klystrons | 488 8 klystrons | 344 6 klystrons | 138 3 klystrons