## Slide 1
NAPA-p1: Nanosecond Timing Pixel for Large Area Sensors
November 8, 2023
Alexandre Habib1, Christos Bakalis1, James E. Brau2, Martin Breidenbach1, Lorenzo Rota1, Caterina Vernieri1 and Angelo Dragone1
1 SLAC National Accelerator Laboratory, 2575 Sand Hill Road, Menlo Park, CA 94025, USA
2 Department of Physics, University of Oregon, Eugene, OR 97403, USA
*Correspondence: alexhab@slac.stanford.edu
CPAD 2023

## Slide 2: Presentation Outline
Application: Future e+e- Colliders
Target Specifications Vs State of the Art
SLAC Development: NAPA_p1
Going Towards a Large Area Sensor
Conclusion & Perspectives

## Slide 3: Future Linear e+e- Colliders
ILC Timing Structure
C3 Timing Structure
Duty Cycle = 0.48%
Duty Cycle = 0.03 %
~1 ns time resolution is needed
3
Designed to work ad Higgs Factory driving the requiring for detectors:
Material budget <0.3% X0
Gas cooling  Very low average power consumption
Spatial resolution: 5 µm
Time-tagging in the order of O(1ns)

## Slide 4: Specifications from Physics to Pixel
Specification | Physics | Pixel
Input charge | Minimum Ionizing Particle (MIP) | Assuming epitaxial layer of ~ 10 µm MIP goes through pixel center generates ~ 600 e- MIP shared between 4 pixels  ~ 150 e-
Noise | Negligeable fake hits | Noise <  ENC < 30 e-rms
Time resolution | Identity bunches within a train (C3) | Time resolution < 1 ns-rms for whole chain considering : sensor, front-end, time walk, TDC
Average Power Consumption | Gas cooling | Depends on detector total area, used gas, and allowed increased in temperature. Initial estimation to be confirmed 20 mW/cm2
Spatial resolution | ~ 5 µm | Pixel pitch 25 µm
Specification | Physics | Pixel
Input charge | Minimum Ionizing Particle (MIP) | Assuming epitaxial layer of ~ 10 µm MIP goes through pixel center generates ~ 600 e- MIP shared between 4 pixels  ~ 150 e-
Noise | Negligeable fake hits | 
Time resolution | Identity bunches within a train (C3) | Time resolution < 1 ns-rms for whole chain considering : sensor, front-end, time walk, TDC
Average Power Consumption | Gas cooling | Depends on detector total area, used gas, and allowed increased in temperature. Initial estimation to be confirmed 20 mW/cm2
Spatial resolution | ~ 5 µm | Pixel pitch 25 µm
These initial specifications serve as a baseline for the first prototype developed at SLAC : NAPA-p1

## Slide 5: Presentation Outline
Application: Future e+e- Colliders
Target Specifications Vs State of the Art
SLAC Development: NAPA_p1
Going Towards a Large Area Sensor
Conclusion & Perspectives

## Slide 6: Target Specs Vs State of the Art
Chip name | Technology | Pixel pitch [µm] | Pixel shape | Time resolution [ns] | Power Density [mW/cm2]
Target Specification | ? | 25 x 100 | Sq / rect | 1 | < 20
ALPIDE [2][3] | Tower 180 nm | 28 | Square | < 2000 | 5
FastPix [4][5] | Tower 180 nm | 10 - 20 | Hexagonal | 0.122 – 0.135 | >1500
DPTS[6] | Tower 65 nm | 15 | Square | 6.3 | 112
Cactus [7] | LF 150 nm | 1000 | Square | 0.1-0.5 | 145
MiniCactus [8] | LF 150 nm | 1000 | Square | 0.088 | 300
Monolith [9][10] | IHP SiGe 130 nm | 100 | Hexagonal | 0.077 – 0.02 | 40 - 2700
Chip name | Technology | Pixel pitch [µm] | Pixel shape | Time resolution [ns] | Power Density [mW/cm2]
Target Specification | ? |  | Sq / rect | 1 | < 20
ALPIDE [2][3] | Tower 180 nm | 28 | Square | < 2000 | 5
FastPix [4][5] | Tower 180 nm | 10 - 20 | Hexagonal | 0.122 – 0.135 | >1500
DPTS[6] | Tower 65 nm | 15 | Square | 6.3 | 112
Cactus [7] | LF 150 nm | 1000 | Square | 0.1-0.5 | 145
MiniCactus [8] | LF 150 nm | 1000 | Square | 0.088 | 300
Monolith [9][10] | IHP SiGe 130 nm | 100 | Hexagonal | 0.077 – 0.02 | 40 - 2700
We decided to go with the Tower 65nm technology, which has been optimized by CERN WP1.2 to have low sensor capacitance allowing very good performance with low power consumption.
+ it has the possibility of a wafer-scale stitched sensor
+ it has been proven to be radiation tolerant
No design fulfills all target specification  The need to develop a custom design

## Slide 7: Tower Semiconductor 65 nm Imaging technology
  Thanks to CERN WP1.2 effort on sensor optimization in TowerSemi 180 nm and 65 nm technologies [12] [13]
     Csensor of 2-3 fF is achievable while maintaining high collection efficiency.
  This is very useful from a pixel performance point of view as:
  For a constant SNR and Qin as shown in [11]
Sensor optimization in TowerSemi 180 nm process from [12] and [13]

## Slide 8: Presentation Outline
Application: Future e+e- Colliders
Target Specifications Vs State of the Art
SLAC Development: NAPA_p1
Going Towards a Large Area Sensor
Conclusion & Perspectives

## Slide 9: NAPA_p1: NAnosecond Pixel for large Area sensors – Prototype 1
The prototype design submitted with a total area 5 mm x 5 mm and a pixel of 25 µm 25 µm, to serve as a baseline for sensor and pixel performance.
Design motivation  Synchronous architecture (known beam time structure), Correlated Double Sampling, eliminating low frequency noise, allowing use of minimum size transistors
Power pulsing  reduce average power consumption by more than 100
Layout of MAPS SLAC prototype for WP1.2 shared submission
Global threshold

## Slide 10: Simulation of Jitter and ENC as a Function of Csensor
ENC = 13 e-rms for Csensor_typ 2 fF
Chart: Csensor [fF]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.2768 | 0.3442 | 0.4171 | 0.491 | 0.5725 | 0.6541 | 0.7363 | 0.8175 | 0.8961 | 0.9716 | 1.047 | 1.122 | 1.199 | 1.275 | 1.351 | 1.427 | 1.503 | 1.579 | 1.654 | 1.73
jitter = 400 ps for Csensor_typ 2 fF
These simulations are with a nominal pixel current of 600 nA  <Power density> = 115 mW/cm2 x duty cycle
For e+e- machines such as ILC and C3, duty cycle is expected < 1%
Ok for Specs
Chart: Csensor [fF]
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 10.1811 | 12.0524 | 13.8368 | 15.5661 | 17.2572 | 18.9138 | 20.5502 | 22.1628 | 23.7613 | 25.3445 | 26.9231 | 28.5007 | 30.0445 | 31.608 | 33.1517 | 34.6987 | 36.2416 | 37.7893 | 39.3339 | 40.895
Csensor_max
Csensor_typ
Csensor_max
Csensor_typ

## Slide 11: Simulation Results : Jitter and Time Walk
Time Walk
Chart: Input Charge [eletrons]
| 82.857140000000001 | 95.714290000000005 | 108.5714 | 121.4286 | 134.28569999999999 | 147.1429 | 160 | 172.8571 | 185.71430000000001 | 198.57140000000001 | 211.42859999999999 | 224.28569999999999 | 237.1429 | 250 | 262.8571 | 275.71429999999998 | 288.57139999999998 | 301.42860000000002 | 314.28570000000002 | 327.1429 | 340 | 352.8571 | 365.71429999999998 | 378.57139999999998 | 391.42860000000002 | 404.28570000000002 | 417.1429 | 430 | 442.8571 | 455.71429999999998 | 468.57139999999998 | 481.42860000000002 | 494.28570000000002 | 507.1429 | 520 | 532.85709999999904 | 545.71429999999998 | 558.57140000000004 | 571.42859999999996 | 584.28570000000002 | 597.14290000000005 | 610 | 622.85709999999904 | 635.71429999999998 | 648.57140000000004 | 661.42859999999996 | 674.28570000000002 | 687.14290000000005 | 700
Pixel | 6.1135e-06 | 6.0547e-06 | 6.043e-06 | 6.0367e-06 | 6.0333e-06 | 6.0309e-06 | 6.0292e-06 | 6.0279e-06 | 6.0269e-06 | 6.026e-06 | 6.0253e-06 | 6.0247e-06 | 6.0242e-06 | 6.0238e-06 | 6.0234e-06 | 6.023e-06 | 6.0227e-06 | 6.0224e-06 | 6.0222e-06 | 6.0219e-06 | 6.0217e-06 | 6.0215e-06 | 6.0213e-06 | 6.0212e-06 | 6.021e-06 | 6.0209e-06 | 6.0207e-06 | 6.0206e-06 | 6.0205e-06 | 6.0204e-06 | 6.0203e-06 | 6.0202e-06 | 6.0201e-06 | 6.02e-06 | 6.0199e-06 | 6.0217e-06 | 6.0216e-06 | 6.0215e-06 | 6.0214e-06 | 6.0213e-06 | 6.0213e-06 | 6.0212e-06 | 6.0211e-06 | 6.021e-06 | 6.0209e-06 | 6.0209e-06 | 6.0208e-06 | 6.0207e-06 | 6.0207e-06
MIP
MIP/4
16 ns
Jitter
I_bias = 200 nA pixel current = 600 nA
From theory we expect :
Time walk for MIP  MIP/4 = 16 ns
Not negligeable and must be corrected
(in pixel? In balcony? Offline? TBD)
Chart: I_bias [nA]
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500
Simulation | 1.16 | 0.61 | 0.44 | 0.34 | 0.29 | 0.24 | 0.2 | 0.18 | 0.16 | 0.15
Fitting | 1.3 | 0.65 | 0.43333 | 0.325 | 0.26 | 0.21667 | 0.18571 | 0.1625 | 0.14444 | 0.13
Csensor = 2 fF
nominal

## Slide 12: Timing Limits for a Complete Detection Chain
< 150 ps-rms
For small optimized pixels
based on literature
< 400 ps-rms for < 1 µW/pixel
Can be corrected if we measure the ToT inside the pixel
< 150 ps-rms
Limited by quantization noise
Assuming time walk is fully corrected ps-rms with reasonable pixel power consumption, going lower will cost increasingly more power, not compatible with large area sensors
Accounting for residual time Walk after correction, and other non-idealities, it is reasonable to aim for ~1 ns-rms time resolution

## Slide 13: Summary of NAPA-p1 Performance
 | Specification | Simulated NAPA-p1
Time resolution | 1 ns-rms | 0.4 ns-rms
Spatial Resolution | 7 µm | 7 um
Noise | < 30 e-rms | 13 e-rms
Minimum Threshold | 200 e- | ~ 80 e-
Average Power density | < 20 mW/cm2 | 0.1 mW/cm2 for 1% duty cucle
The chip was received at SLAC in September 2023
Microscope photo of NAPA-p1
Acknowledgement: to CERN WP 1.2 for the excellent cooperation: NAPA-p1 uses the pixel masked developed and optimized by CERN, and was fabricated in a shared run led by CERN

## Slide 14: Test Setup for NAPA-p1
A custom carrier was designed at SLAC for the NAPA-p1 chip providing all analog references
The chip was wire-bonded at SLAC
The carrier board connects to a digital board containing an FPGA and several DAC’s
Digital Board
Carrier Board
Carrier Board
NAPA_p1

## Slide 15: Preliminary Characterization Results
V_pwell = 0
V_substrate = 0
No calibration
No fine tuning
Preliminary
Columns Scan
Functional Testing
Injection charge scan across different threshold configuration

## Slide 16: ENC measurement
Pwell = 0
Psub = -3V
Injection cap not calibrated yet. A Laser setup is needed for that. Design value is used for Cinj
ENC value is close to simulation ~ 13 e-rms for Csensor = 2 fF
ENC value satisfies the specification < 30 e-rms
More measurements to be available soon
Preliminary

## Slide 17: Presentation Outline
Application: Future e+e- Colliders
Target Specifications Vs State of the Art
SLAC Development: NAPA_p1
Going Towards a Large Area Sensor
Conclusion & Perspectives

## Slide 18: Going Towards a Large Sensor  Challenge
Assuming :Ipix = 600 nA and Rpix = 300 mΩ
Assuming pixel of 25 m x 25 m
A column of 10 cm would have 4000 pixels
Double sided powering
 max drop length = 2000 pixels
After 103 pixels (reticle, 2.5 cm), Vdrop 0.1 V
After 4 x 103 pixels (sensor, 10cm), Vdrop = 1.5V !
The main limitation comes from large scale power distribution rather than cooling constraints
Chart: Number of Pixels
VDD-GND goes from 1.2 V near the power pads down to around 480 mV after 2000 pixels
1.2V
0.48V
Local VDD
Local GND

## Slide 19: Going Towards a Large Sensor  Solutions
Potential solutions to address the power distribution over a large scale:
Decrease power density Physics requirement are for a pixel of 25 µm x 100 µm. Our initial study shows that a pixel of 25 µm x 50 µm gives the best optimization for
Reduce Rpix  Redesign of power grid
Keep power constant  Switch from a single ended to a differential comparator
Reduce the column length  Target sensor of 5 cm x 20 cm instead of 10 cm x 10 cm
Backup plan: develop capless LDO regulator  ongoing shared effort with CERN WP1.2
 NAPA-p2 design has started to tackle these challenges
Chart: Pixel Pitch vs. Performance
| 1 | 2 | 3 | 4
ENC | 14 | 18 | 19 | 21
Jitter | 750 | 650 | 710 | 810
Simulation by Jacob Sillman
19
Power = constant
Potential Configuration of NAPA-p2

## Slide 20: Presentation Outline
Application: Future e+e- Colliders
Target Specifications Vs State of the Art
SLAC Development: NAPA_p1
Going Towards a Large Area Sensor
Conclusion & Perspectives

## Slide 21: Conclusion & Perspectives
MAPS has great a potential to fit the future e+e- colliders requirements (tracker, calorimeter)
Simulations of NAPA_p1 show that it is possible to achieve a time resolution 1 ns-rms with reasonably low power consumption of ~100 mW/cm2 Duty Cycle. For e+e- machines duty cycles are typically < 1%
We’ve just received the NAPA-p1 chip and the first characterization results are promising. NAPA-p1 will serve as a pixel proof of concept.
Design of NAPA-p2 has started to tackle large sensor challenges. NAPA-p2 will serve as a system proof of concept.
These prototypes are customized for linear lepton colliders with low duty cycle, however, many of the developed technical solutions can be of value to other applications (large area stitched sensor with increased yield, power distribution, IP blocks (capless LDO regulator, TDC,…)
Thank You For Your Attention!
Microscope photo of NAPA-p1

## Slide 22: References
[1] Brau JE, Breidenbach M, Habib A, Rota L, Vernieri C. The SiD Digital ECal Based on Monolithic Active Pixel Sensors. Instruments. 2022; 6(4):51. https://doi.org/10.3390/instruments6040051
[2] Gianluca Aglieri Rinella, “The ALPIDE pixel sensor chip for the upgrade of the ALICE Inner Tracking System, Nuclear Instruments and Methods in Physics Research, Volume 845,2017, https://doi.org/10.1016/j.nima.2016.05.016
[3] M. Mager, “ALPIDE, the Monolithic Active Pixel Sensor for the ALICE ITS upgrade”, Nuclear Instruments and Methods in Physics Research, Volume 824, 2016, https://doi.org/10.1016/j.nima.2015.09.057
[4] T. Kugathasan et al., “Monolithic CMOS sensors for sub-nanosecond timing”, Nuclear Instruments and Methods in Physics Research, Volume 979, 2020, https://doi.org/10.1016/j.nima.2020.164461.
[5] J. Braach et al., “Performance of the FASTPIX Sub-Nanosecond CMOS Pixel Sensor Demonstrator”, Instruments 2022, 6(1), 13; https://doi.org/10.3390/instruments6010013
[6] G.A. Rinella et al. “Digital Pixel Test Structures implemented in a 65 nm CMOS process” https://doi.org/10.48550/arXiv.2212.08621
[7] Y. Degerli et al 2020 JINST 15 P06011 DOI 10.1088/1748-0221/15/06/P06011
[8] Y. Degerli et al., “MiniCACTUS: Sub-100 ps timing with depleted MAPS”, Nuclear Instruments and Methods in Physics Research, Volume 1039, 2022, https://doi.org/10.1016/j.nima.2022.167022.
[9] S. Zambito et al 2023 JINST 18 P03047 DOI 10.1088/1748-0221/18/03/P03047
[10] L. Paolozzi “A Picosecond Avalanche Detector in SiGe BiCMOS’ ULITIMA Conference 2023
[11] W. Snoeys, Monolithic Pixel Detectors for High Energy Physics, Nuclear Instruments and Methods in Physics Research A 731 (2013) 125–130
[12] M. van Rijnbach et al., Radiation hardness and timing performance in MALTA monolithic pixel sensors in TowerJazz 180 nm, 2022 JINST C04034
[13] M. Munker et al., Simulations of CMOS pixel sensors with a small collection electrode, improved for a faster charge collection and increased radiation tolerance,2019 JINST 14C05013