## Slide 1: GAMPix
Electron Track Detection with a Dual Scale LArTPC System
Bahrudin Trbalic
Stanford
11/10/2023

## Slide 2: GAMPix detector
Electron Track Detection with a Dual Scale System in TPCs
Low
Noise
Threshold
Power
Diffusion Independent
(Can use diffusion to estimate drift length)

## Slide 3: GAMPix detector
Electron Track Detection with a Dual Scale System in TPCs
Low
Noise
Threshold
Power
Diffusion Independent
(Can use diffusion to estimate drift length)

## Slide 4: GammaTPC
3m
Notes: A new Compton telescope concept for gamma rays. Large area/mass 10m^2, 4 tons, 2π FOV
Compton Scatters in LAr
Incoming Gamma Ray Compton Scatters and Produces:
- Electrons Tracks [this talk]
- Light (Scintillation)
To reconstruct the energy/direction we need:
- Positions of the Tracks
- Energies of the Tracks [part of it is in light signal]

## Slide 5: GammaTPC
1 MeV, 21K e-/ion pairs
3m
Technical Requirements
1. Submillimeter Track Imaging (3D)
2. Percent level Energy Resolution
3. Low Power Consumption
Notes: A new Compton telescope concept for gamma rays. Large area/mass 10m^2, 4 tons, 2π FOV
Compton Scatters in LAr
Incoming Gamma Ray Compton Scatters and Produces:
- Electrons Tracks [this talk]
- Light (Scintillation)
To reconstruct the energy/direction we need:
- Positions of the Tracks
- Energies of the Tracks [part of it is in light signal]

## Slide 6: Possible Application in DUNE FD Phase 2
Low-energy “blips” produced by neutrons and electrons in DUNE events.
- Many of those are below threshold in current readout schemes
Proposed GAMPix detector enables the detection of low energy scatters
- Greatly improves the Supernova neutrino (MeV scale) detection.
A. Friedland and S. W. Li, “Understanding the energy resolution of liquid argon neutrino
detectors,” Phys. Rev. D 99, no.3, 036009 (2019) [arXiv:1811.06159 [hep-ph]]

## Slide 7: How to Image the Electron Tracks?
Challenges:
- Charge loss when diffusion is on the scale of sensors

## Slide 8: How to Image the Electron Tracks?
Challenges:
- Charge loss when diffusion is on the scale of sensors

## Slide 9: Example of Pixels Only Readout
*threshold of 80 e
Lost Charge
> 10ms lifetime
Lost charge due to threshold

## Slide 10: How to Image the Electron Tracks?
Challenges:
- Charge loss when diffusion is on the scale of sensors
- Low noise needs high power
Noise sets the
- energy resolution
- threshold
noise power

## Slide 11: Grid Activated Multi-scale Pixel readout: GAMPix
TPC cell
Cathode
Anode
Coarse (cm-pitch) induction grids followed by fine grained pixels [individually ]
Coarse grids:
  Measure charge integral, with ~ 15 e-
  Provide trigger signal (address) to pixel chips
Pixel chips:
  Image track
  Power-up in < 1 µsec following coarse trigger
  Power, reduced by 103–104, to ~1 W/m2
1 cm
pixels
pixel chip

## Slide 12: Grid Activated Multi-scale Pixel readout: GAMPix
TPC cell
Cathode
Anode
Coarse (cm-pitch) induction grids followed by fine grained pixels
Coarse grids:
  Measure charge integral, with ~ 15 e-
  Provide trigger signal (address) to pixel chips
Pixel chips:
  Image track
  Power-up in < 1 µsec following coarse trigger
  Power, reduced by 103–104, to ~1 W/m2
1 cm
coarse electrode
wires
pixels
pixel chip

## Slide 13: Grid Activated Multi-scale Pixel readout: GAMPix
TPC cell
Cathode
Anode
electron track
1 cm
v
coarse electrode
wires
pixels
pixel chip
Coarse (cm-pitch) induction grids followed by fine grained pixels
Coarse grids:
  Measure charge integral, with ~ 15 e-
  Provide trigger signal (address) to pixel chips
Pixel chips:
  Image track
  Power-up in < 1 µsec following coarse trigger
  Power, reduced by 103–104, to ~1 W/m2

## Slide 14: Grid Activated Multi-scale Pixel readout: GAMPix
TPC cell
Cathode
Anode
1 cm
v
coarse electrode
wires
pixels
pixel chip
Electric Fields in GAMPix Unit

## Slide 15: GAMPix | Simulated Signal Chain

## Slide 16: GAMPix | Simulated Signal Chain Issue: Non-uniform response from the wire grid

## Slide 17: GAMPix | Simulation Results
Submillimeter (0.25mm) Resolution Pixelated Track Imaging
Energy Resolution of < 1%
for electron tracks >100 keV (2k e-) with an ENC of 20e- on pixels and 30e- on wires.
Low Power Consumption ~ 1 W/m2
Due to the triggering capability and fast pixel power cycling, the pixel plane has a low duty-cycle.
Energy saving by a factor of 10
Drift Length Estimation via Diffusion with ~5% accuracy
Outcomes
Electronic noise reduction from ~500e- to ~50e- lowers threshold for “blip” detection from >1MeV to much less
Power cycling the pixels’ front-end reduces the average power to acceptable levels
Drift Length Estimation via Diffusion with ~5% accuracy (Helps with background rejection for SN)
Geometry:
~ 5mm pitch pixels
~ 5 cm pitch grid
GammaTPC
DUNE

## Slide 18: GAMPix fast power cycle ASIC
Builds on pixelated ASICs from SLAC TID-ID, cryogenic SoC ASIC development for nEXO/DUNE and quantum instrumentation
130nm CMOS process (foundry + SLAC custom cryo models)
Preliminary transistor-level modeling of power switching CSA: ∆Ton ~500 ns,

## Slide 19: I would like to continue talking about…
Other possible applications of GAMPix
GAMPix hardware test
GammaTPC
- Machine learning for GAMPix
+ Depth estimation via diffusion
+ Initial electron direction estimation
Upcoming test with CRYO (~100e-) readout

## Slide 20: BACKUP Slides

## Slide 21: Track reconstruction promising
Initial direction
Powerful measurement of initial direction
Also: ~5% estimate of drift distance
(mm)
Track head location
CNN study: M. Buuck, B. Khek, A. Mishra, ArXiv/2207.07805
0.25 mm !!!
Notes: Dune Applications – neutrino : gamma rays

## Slide 22: GAMPix for DUNE
Pixel Based [1000 ENC]
Geometry:
~ 5mm pitch pixels
~ 5 cm pitch of unified grid
Outcomes
- A pixel-based readout system that reduces that electronic noise from ~500e- to ~50e- lowers threshold for “blip” detection from >1MeV to much less
- An “activation” signal from a coarse electrode “grid” to power the pixels’ front-end and reduce the average power to acceptable levels
- Drift length estimation via diffusion measure (with ~ 5% accuracy)
Wire/Strip [800 ENC]
Energy Threshold Improvement