## Slide 1: Machine learning based developments for LHC / CMS Level-1 triggers
CICADA & AXOL1TL for LHC Run-3
Possibilities for HL-LHC
https://fastmachinelearning.org/hls4ml/
JINST 13 P07027 (2018)

## Slide 2: Why Machine Learning Based Triggers?
Physics searches at LHC demand low thresholds
  No new physics at TeV scale has been discovered
  Hopes for new physics hiding in profusely produced SM backgrounds remain
Has new physics escaped our object-threshold-based triggers?
  Can one exploit complex correlations escaping simple triggers?
  Can we use machine learning, say, anomaly detection technique, to search for any rare/new physics in a model-independent way?
  Unknown correlations in interesting physics are unearthed by the ML model which is trained on many minimum-bias events.
With ~200 piled-up events every crossing will look like this at the HL-LHC

## Slide 3: Why ML at Level-1?
Traditional event selection at L1 based on object thresholds
  High-level and Data analysis selections limited to use those objects
ML decisions based on level-1 inputs themselves
  Reduce potential bias for later detailed analysis

## Slide 4: Level 1 Trigger Input Data & Traditional Algos

## Slide 5: Opportunities & Challenges at Level-1
Level-1 trigger system features
  Massively parallel processors (FPGAs)
  Very fast IO based on multi-gigabit transceivers
  Modern high level synthesis tools to implement complex models
Level-1 trigger system constraints
  Extremely low latency < O(1) 𝜇s
  Extremely tight resources from a single FPGA board
  Extremely low background rate < O(10–4)
CMS is trying improvements in Run-3 systems before getting to HL-LHC!

## Slide 6: CMS L1 Trigger System for LHC Operations
CICADA
AXOL1TL
ML-Based Improvements for Run-3

## Slide 7: Xilinx FPGAs In Use LHC Run-2/3 : V7 690T ; At HL-LHC: VU13P
Currently Deployed at LHC
Planned for HL-LHC

## Slide 8: Key element - Multi-gigabit Opto-electronics

## Slide 9: CMS Level-1 Trigger Electronics Boards
Calorimeter Trigger Processor(CTP7 – left), and Master Processor (MP7 - right)
  CTP7 (Layer-1) – mTCA Single Virtex 7 FPGA, 67 optical inputs, 48 outputs, 12 RX/TX backplane
    Virtex 7 allows 10 Gb/s link speed on 3 CXP(36 TX & 36 RX) and 4 MiniPODs (31 RX & 12 TX)
    ZYNQ processor running Xilinx PetaLinux for service tasks, including virtual JTAG cable
  MP7 (Layer-2) – mTCA Single Virtex 7 FPGA, up to 72 input & output links
    Virtex 7 has 72 input and output links at 10 Gb/s
    Dual 72 or 144MB QDR RAM clocked at 500 MHz
MMC
Power Supplies
ZYNQ
FPGA
JTAG
USB
Interface
Rx
Tx
Rx
Tx
FPGA
1V0
2xQDR
(Bottom)
2V5
3V3
1V5
1V8
mSD
USB
mC
(Bottom)
MiniPODs
3 CXP modules
MiniPod modules
Notes: oRSC – optical Receiver Summary Card
CTP7 – Calorimter Trigger Processor
MP7 ?

## Slide 10: CMS Calorimeter Trigger Run-2/3
Layer-1 CTP7
Layer-2 MP7
MOLEX
FlexPlane
Layer-1 to Layer-2 Patch Panel

## Slide 11: Firmware / Software: Decoupling with Modern Tools
A new paradigm for firmware development
  Core firmware written in VHDL by engineers
  Gigabit link support
  Data exchange between SLRs within chip
  Test buffers
  Clock and control
Physics
  Algorithmic firmware in high-level languages like C++ written by physicists
Linux / ZYNQ:
Control endpoint,
providing complete
board overhead
functionality
Processing FPGA:
I/O
data processor
DAQ
Algorithm Sandbox HLS-built RTL
Originally deployed on CTP7 with ZYNQ + Virtex-7

## Slide 12: CICADA Team
Calorimeter Image Convolutional Anomaly Detection Algorithm (CICADA)
Model/Implementation/Emulator/Firmware/Software/Hardware/Operations
  University of Wisconsin-Madison
    Kiran Das, Sridhara Dasu, Tom Gorski, Alexander Savin, Varun Sharma, Ales Svetek, Jesra Tikalsky, Ho Fung Tsoi
  Princeton University
    Pallabi Das, Kiley Kennedy, Andrew Loeliger, Luis Moreno, Isobel Ojalvo, Adrian Alan Pol

## Slide 13: Calorimeter Input to CICADA
One ZeroBias event
Calo region map
One region = 4x4 trigger towers
CICADA input from CaloLayer1
18 f x 14 h regions 252 regions in total
Each region contains energy deposits from both ECAL and HCAL
Summary of the energy distribution profile within the region
Low-level information not dependent on jet reconstruction etc.

## Slide 14: Auto-encoder Model
Autoencoder-based anomaly detection
Input is a 2D tensor from the Calo region energy information
Encoder and decoder are Convolutional Neural Networks
Unsupervised learning : train only on ZeroBias data to learn input reconstruction

## Slide 15: Event Reconstruction
Input
Reconstruction
Input
Reconstruction
ZeroBias data
BSM MC signal
Expectation:
Good reconstruction on normal events (ZeroBias used for training)
Bad reconstruction on anything else such as BSM signals (never seen during training)
Goal:
Use metric like MSE(input, output) as anomaly score to trigger on anomalous events

## Slide 16: Naïve Auto-encoder Model
324 K parameters model size cannot fit L1 constraints…
Encoder (compressor)
Latent space (compressed input)
Decoder (decompressor)

## Slide 17: Knowledge Distillation + Quantization
Anomaly score
Teacher
Student
Score regression
Compare with teacher’s score
Compute score
(e.g. MSE)
e.g.,quantized ReLu
Knowledge Distillation
Train a smaller model (student) under the guidance of a bigger model (teacher)
The student learns to regress MSE from teacher outputs
Quantization-aware training (QKeras)
Model weights quantized to fixed precision (e.g., 2 bits for integer, 4 bits for fraction)
Train a quantized model rather than quantize a trained model
x10 reduction
in resources/latency

## Slide 18: Teacher  Student
Student
324K parameters go down to 3.8K parameters

## Slide 19
Physics Performance (MC signals)
Model trained on 2023 ZB, evaluated on 2023 MC signals
Able to pick up a wide range of signals

## Slide 20: CICADA Rate Stability over the Run
Flexible trigger: tunable threshold for different rates, stable over the run

## Slide 21: AXOL1TL Team
Anomaly eXtraction Online Level-1 Trigger Lightweight (AXOL1TL)
Model/Implementation/Emulator/Firmware/Software/Operations
  Fermilab
    Abhijith Gandrakota, Jennifer Ngadiuba
  University of California – San Diego
    Javier Duarte, Melissa Quinnan, Andrew Skivington
  University of Colorado
    Jannicke Pearkes, Reece Rupp, Noah Zipper, Keith Ulmer
  ETH-Zurich
    Chang Sun, Patrick Odagiu, Thea Arrestad

## Slide 22: AXOL1TL is also Auto-encoder Based

## Slide 23: Inputs: Same as Traditional Global Trigger
Unlike CICADA, AXOL1TL also includes muons

## Slide 24: Anomaly Score Distribution : Good Rate Control

## Slide 25: Firmware Implementation & Results
Fits comfortably in the existing CMS Global Trigger running on MP7
Example performance improvement for BSM decay

## Slide 26: Rate for various AXOL1TL scores
Rates monitored on the mGT test crate

## Slide 27: Highest anomaly AXOL1TL event

## Slide 28: CMS HLLHC Level-1 Trigger 2029+
New for HLLHC
Many opportunities with tracking included at Level-1

## Slide 29: HL-LHC L1 Trigger Challenge Xilinx – Ultrascale+ Processors
Times 2
Many times
Times 3
Times 2.5

## Slide 30: Advanced Processor Prototype for HL-LHC
Wisconsin APxF Board
Xilinx VU13P or VU9P FPGA
ZYNQ-IPMC (ATCA IPMI controller)
ELM (ZYNQ-based embedded Linux)
ESM (GbE switch)
High efficiency heatsinks
Front-panel inputs
25G Samtec Firefly optics – 10x12 + 1x4 (124 25 Gbps links)

## Slide 31: Summary
Run-3 will see machine learning based triggers
  Improved technologies for easy high-level synthesis
  Improved auto-encoder model implementations
  Potential opportunity for hitherto unattainable physics reach
HL-LHC
  Increased resources in new boards
  Availability of tracker data at level-1
  Opportunities for ML-based discoveries are opening up.