## Slide 1: Ren-yuan
Minfang: scale-up calorimeter
Inorganic scintillators with different parameter optimization
Cost-effective scale-up calorimeter using liquid scintillators (<1$/Kg)
Water-based liquid scintillator with direct Cherenkov and scintillation detection capabilities. Capability of loading heavy metal at ~10%.
LiquidO: photon random walk (self-confinement)

## Slide 2: Bob Hirosky
Signal collection/active volume/granularity:
  direct integration with (in)organic scintillator block fabrication
  Effectively large area seensors
  Thin film electronics. OLED displays
Dynamic range for ecal: 10MeV-100GeV, readout and sensor integration
Fight tyranny of FPGA resource limits: fast, controlled-latency interfaces to CPU/GPU for L1 trigger.
Calibration: embedding calibration hardware at cell level
Synergies: choose optimization for a specific application, exploiting specific capabilities

## Slide 3: R&D drivers:
New materials for calorimetry, and how they can be tailored to a specific application (including prospects from nanotechnology); develop industrial partners
  Scale-up material (liquid scintillators)
  Inorganic scintillators
    Bright, fast, rad hard
    Ultrafast inorganic (quantum dots may help to break the ps timing barrier) [also medical industry]LuO:Yb can be o
    Dense-UV transparent, cost-effective heavy inorganic scintillator [water-based liquid scintillator] (HHCAL)
  Maps for cost-effective large scale structures
Wavelength shifters to match scintillator (quantum dots, pTP, flavenols)
Photon detectors: SiPM

## Slide 4: R&D drivers:
Front-end electronics needs for high energy resolution:
  High dynamic range [14 bits]
Front-end electronics needs for picosecond timing calorimetry:
  Waveform sampling and feature extraction
System aspects (mechanical): low mass support & cooling
System aspects (electronics): powering scheme & interconnections
System aspects (data processing): “intelligent calorimeter”
Concepts from the above lines of investigation that can be adapted to hadron identification (time-of-flight, RICH…)
Simulation: speed improvement with respect to GEANT

## Slide 5: RaDiCal (Ruchti/Wetzel)
Radical: point specific aspects of readout at the front and back

## Slide 6: Maps for calorimetry (Brau)
Overall detector performance with low-cost material
MAPS for tracking and calorimetry are feasible and can be cost effective (standard CMOS foundry, low resistivity, no bump bonding)

## Slide 7: Andy White
Use of AI