## Slide 1: H4RG analyses for Roman and PFS
Jahmour Givans
ISPA 2024 workshop
Image credit: Teledyne Imaging

## Slide 3: Wide-field instrument specifications
Surveys the sky 1,000 times faster than Hubble!
Imaging and spectroscopy available
0.281 deg^2 field of view
0.11 arcsec/pix, 288 Mpix focal plane
Detector array consisting of 18 H4RG-10s
4096 x 4096 pixels with border of 4 reference pixels per side
32 readout channels, taking 3.04 seconds to read
Bandpass of 0.48-2.3 microns

## Slide 4
Roman's Roadmap
Spergel et al. 2015

## Slide 5
Gravitational lensing
Image credit: NASA, ESA, CSA, STScI, A. Galan
Percent-level shape/size distortions
Dramatic distortions and multiple images
Correlations used to probe !

## Slide 6
Will Roman help resolve a tension?
Late universe
Abdalla et al. 2022
(clumpiness)
Early universe

## Slide 7
Most weak lensing surveys use CCDs and operate in the visible spectrum
Roman will use HgCdTe detector arrays with 4096^2 pixels
  Access to near-infrared wavelengths
  First application to weak lensing, so we need to understand their features!
Detectors are the difference!
Mosby et al. 2020

## Slide 8
Detector effects
Credit: Jenna Freudenburg

## Slide 9
All five effects can throw off our estimated galaxy shapes!
Correlations of signal across the detector used to quantify effects
  Use both spatial and temporal correlations to disentangle different effects
Built the first mathematical model to describe correlations including all effects
  J. Freudenburg, JG+ 2020 (2003.05978); JG+ 2022 (2110.08155)
Created simulated detector images with relevant physics included
  GitHub package: solid-waffle
Quantifying the impact

## Slide 10
Updated model (BFE+IPC+CNL) resolved lingering 12% bias on BFE parameters from earlier work
Full model recovered input parameters well within a standard deviation!
Performance against simulations
Quantum yield
Charge diffusion (2x2 matrix elements)

## Slide 11: Roman detector maps

## Slide 12
Pioneering analysis: charge diffusion "shear" signal
Black points are an order of magnitude above acceptable limits! Must be corrected for by Roman team.

## Slide 13
Joint endeavor between Roman and Rubin groups to build a synthetic survey
  M. Troxel+ (incl. JG) 2023 (2209.06829)
Incorporated my detector findings in the simulation pipeline
Testing ground for development and validation of joint pixel-level analysis techniques
Important for maximizing science yield from these two surveys
  Highest-priority missions outlined in the 2010 Decadal Survey!
From pixels to pictures

## Slide 14: Prime Focus Spectrograph
*Subaru Telescope building shown

## Slide 15
Credit: SubaruTelescope.org

## Slide 16: PFS science cases

## Slide 17: Example dark data
JHU lab data from June 2022
300 frame UTR darks for approximately 24 hours after illumination
IRP1:1 (one interleaved reference pixel read between each data pixel)
  Frame times of about 11 seconds
Raw dark frame 100
Raw dark frame 100 - dark frame 1

## Slide 18: Persistence tests
All persistence runs were carried out and analyzed by Eddie Bergeron
Two-part illumination frame followed by a series of long darks
Charge "soaked" into the detector for one frame time plus time for reset frame to reach a given pixel during the pixel-by-pixel reset
Gain factor for detector is 3.2 electrons/ADU, ASIC preamp gain factor 2.83

## Slide 21: Analyzing noise
We are interested in total noise, not disentangling noise sources
Build 3D array of signal in pixels across dark frames
  Do this using the difference of two (median subtracted) FITS files
Apply bad pixel mask based on hot pixel analysis
Fit signal across frame number and calculate rms noise
Get best-fit coefficients to describe the noise curve
  Noise = sqrt(a/N + b*N)

## Slide 22: Noise curves (current analysis)
Consistent shape from darks of different FITS files

## Slide 23: Noise curves (previous analysis)
Initial work in this area carried out by Erin Kado-Fong
IRP1 (left) and IRP2 (right)
Shape is overall discrepant with most recent analysis

## Slide 24: Basic nonlinearity characterization

## Slide 25: Going forward
Continued work studying effects of different IRP value choices on noise properties
  Thought from this conference: maybe reference pixels aren't the best strategy?
How to translate noise and parameters (BFE, IPC, etc.) to errors on science
  Developed/developing for Roman but PFS lags behind
  Perhaps Pyxel would be useful?
How will our findings affect the survey strategy?
What can Roman learn from Euclid (and later, SPHEREx) in-flight data?