## Slide 1: Integration of 120 kW Target into e+ Source
Andriy Ushakov (Ce+BAF WG)
New e+ Injector at LERF
123 MeV e+ Beam Injected to NL
New Transport Line along SL and West Arc
CEBAF Polarized Electron Injector
New Beamline to CEBAF Tunnel

## Slide 2: LERF Polarized Positron Injector Concept
  High current polarized electron injector (10 MeV, 1 mA, 1/4 C50 CM)
  High current 1-3 mA LINAC (two C75 CM)
  Positron conversion target (~120 kW)
  Positron capture linac (~60 MeV and ~20 MeV e+, 100 µA; 1497 MHz, nc, 1 MV/m) and momentum selection
  Positron bunch compression and acceleration to 123 MeV (C100 CM)

## Slide 3: Spinning High Power Target R&D
We expect a 4 mm thick tungsten target with 120 kW of beam power (120 MeV x 1 mA)
~17 kW will be deposited in the target
Target concept is a rotating cooled W disc of with diameter ~35 cm and 2 Hz rot. frequency
Computational fluid dynamics calculations predicts the equilibrium temperature rise will be < 1000 K
We anticipate this will be a major design effort of the project

## Slide 4: Capture of e+ with Energy of ~60 MeV in QWT (Polarized Mode) - S. Habet
QWT consists from 2 solenoids: 1st high-field solenoid with a short length and 2nd low-field solenoid with a long length around warm RF cavities
Efficiency of <10-4 requires a high-current polarized e- drive beam (>1 mA)
Ne+ [a.u.]
Parameters used for capture of 60 MeV e+
Length of 2.5 T solenoid: 25 cm
Length of 0.05 T solenoid: 6 m
1497 MHz cavities
E = 1 MV/m
30 mm aperture of cavities
QWT
QWT Exit
Target Exit

## Slide 5: High Field Solenoid
1.29 T Solenoid
Absorbers
e+
Target
Solenoids with and without Steel (calculated by Jay Benesch)
Field Map (imported in FLUKA)

## Slide 6: Deposition of Power in Capture Solenoid. Energy Spectra at “End” of Solenoid
 | Power [kW]
Target | 17.0
Cu Coils and Steel | 0.3
W10Cu Absorber inside Solenoid | 17.2
TZM Absorber | 22.7
W10Cu Absorber (downstream Solenoid) | 31.6
Cu Cavities | 6.5
Total Absorbed Power | 105.8
Power of All Beams at z = 125 cm | 13.1
Cu Coils (Bmax=1.29 T)
W10Cu
W10Cu
TZM
Target
 | Photons | Electrons | Positrons
Yield [N/( GeV)] | 0.50 | 0.17 | 0.03
Mean Energy [MeV] | 10.6 | 42.0 | 24.2
Power [kW] | 5.3 | 7.1 | 0.75
 | Photons | Electrons | Positrons
 | 0.50 | 0.17 | 0.03
Mean Energy [MeV] | 10.6 | 42.0 | 24.2
Power [kW] | 5.3 | 7.1 | 0.75
Cu Cavities
Steel

## Slide 7: Spatial Distributions of γ, e-, e+, n. Neutron Energy and Yield
Yn = n/
Electrons
Photons
Positrons
Neutrons
Energy Distribution of Neutrons
Neutron Yield:

## Slide 8: CST Model of KEK/ILC e+ Source (Y. Enomoto)
Many thanks to Enomoto-san for providing CST models of all parts of the ILC Positron Source!
Expertise of KEK group in modeling of positron source can help us in development of JLab e+ source

## Slide 9: Summary and Outlook
Calculations for integration of high power target into positron capture system have been started
For positron focusing downstream target sc and nc solenoids are considered
Solenoid with steel
  Helps to reduce field in target
  Reduces required current and makes magnet cooling much easier
  Removes more low energetic (low polarized) positrons
Beam dynamics and energy deposition calculations in progress

## Slide 10
Backup Slides

## Slide 11: Distributions of Electrons and Positrons at Target (FLUKA/Geant4)
105 primary electrons

## Slide 12: Distributions of Photons and Neutrons (FLUKA/Geant4)
n Yield = 4.7·10-3 n/e-

## Slide 13: Yield, Energy and Power of Particles at 4 mm Tungsten Target (Geant4)
Forward Direction |  | 
Photon Yield | 7.5 | ph/e-
Average Energy of Photons | 7.9 | MeV
Average Power of Photons | 59.2 | kW
Electron Yield | 1.12 | e-/e-
Average Energy of Electrons | 35.2 | MeV
Average Power of Electrons | 39.3 | kW
Positron Yield | 0.24 | e+/e-
Average Energy of Positrons | 16.9 | MeV
Average Power of Positrons | 4.0 | kW
Total Power | 102.5 | kW
Backward Direction |  | 
Photon Yield | 0.39 | ph/e-
Average Energy of Photons | 1.03 | MeV
Average Power of Photons | 0.40 | kW
Electron Yield | 0.014 | e-/e-
Average Energy of Electrons | 2.18 | MeV
Average Power of Electrons | 0.03 | kW
Positron Yield | 0.001 | e+/e-
Average Energy of Positrons | 4.21 | MeV
Average Power of Positrons | 0.005 | kW
Total Power | 0.44 | kW
Power Deposition in Target | 16.84 | kW

## Slide 14: Capture of e+ with Energy of ~19 MeV in QWT (Unpolarized Mode) - S. Habet
QWT consists from 2 solenoids: 1st high-field solenoid with a short length and 2nd low-field solenoid with a long length around warm RF cavities
Ne+ [a.u.]
Parameters used for capture of 19 MeV e+
Length of 1.3 T solenoid: 25 cm
Length of 0.05 T solenoid: 6 m
1497 MHz cavities
E = 1 MV/m
30 mm aperture of cavities
QWT
QWT Exit
Target Exit

## Slide 15: Momentum Collimation and Bunch Length Compression (S. Habet)
Long. positron phase space before and after compression
Momentum collimation