## Slide 1
FACET-II Long-term planning meeting:
E-320
Alexander Knetsch
01/10/24

## Slide 2: High-level response
What are the high-level scientific goals of this experiment?
Measure non-linear Compton scattering
Measure shift in Compton as function of a0
Measure qualitative change from discrete edges to continuum.
What will be the first high impact result/publication?
  Measurement of dressed electronic mass
  Transition from perturbative to non-perturbative
Lower impact publications:
    Characterization of synchronization method with YAG
    Laser wire measurements
What do we need to do to get from here to there?
  Improve electron diagnostics
  Increase a0

## Slide 3: Status as of E-320 retreat in May 2023
Electron beam:
  same beam parameters as Summer 2022, but smaller is better.
Laser:
  2 um FWHM, 50 fs fwhm, target: a0 ~ 4
  Get the goose trigger going
  Open window between compressor and picnic basket. Perform RGA measurements
  Get the EOS working for E320
  Electron Spectrometer:
  EDC is not necessary at the moment.
  Beam-based alignment the spectrometer quads
  Special quad settings for better E320 imaging
  Improve LFOV with for better light collection
  Test ePIX
Simulations:
  Build a model for compton scattering to understand what to expect under ideal circumstances on the spectrometer

## Slide 4: Progress in 2023
~30 fC signal on low-background LFOV
Scattering simulation implemented in Lucretia
Linear Compton scattering observed with pencil beam
Small laser spot size
Progress from previous year (2022)
  Improvement on laser wavefront
  New low background LFOV diagnostic
  RGA measurements done.
  Start-2-end modeling developed
  EOS works again and can be timed in with E320
  Goose trigger en route
  Specialized E-320 imaging optics calculated
  Gamma-ray profile, Cherenkov detector, PDC tracker

## Slide 5: Encountered issues and mitigation strategies
Out of 3 beamtimes only 1 led to observed scattering !
Issues encountered last year (2023)
  YAG damage
  Spatial drifts in electron beam in IP
Resources/plans to address issues
Strategies to avoid YAG damage:
  Use long pencil beam and beam off waist initially
  Use YAG only in periphery of beam
  Develop plasma-glow like synchronization
  Use different references for coarse timing e.g. EOS or gas jet
Strategies to reduce drift risk:
  Dispersion monitoring with BPMs
  x,y drift measurement with BPMs or DTOTR similar to E332
Beam request:
  First priority: Stability and repeatability
  Second priority: High charge density in IP
  Two configurations under discussion: Pencil beam, compressed beam