## Slide 1: TMS at DUNE Near Detector
SLAC Neutrino Group Summer Retreat
Tom Markiewicz /SLAC
15 July 2024

## Slide 2: Outline
Description of scope of activities (and its context within the overall DUNE ND) along with SLAC roles/responsibilities.
Issues, challenges in design, prototyping, and physics studies
Upcoming major activities, milestones, decision points
Needs/opportunities of more SLAC (or other) engagement

## Slide 3: NDLAr and TMS
TMS measures muon momentum via range and muon charge by bending in a 1-Tesla field
40 planes 15mm
60 planes 40mm
100 40mm slots for detectors
Detectors are 35mm x 3m x 17mm scintillator arranged in 6 32bar panels per plane
Readout is via WSF, SiPM and CAEN 5202 system

## Slide 4: TMS Magnet Based on Pre-Assembled Coils

## Slide 5: Detector Planes
Steel height 5066mm->4200mm
  Height above/below coil = 300mm
  Feature of the Flux Return Insert
Middle plate split for transport
Detector “cassettes” of 6 panels (was 4)
  ±3° stereo 32 x 35mm 3m long bars
  90° 32 x 35mm 3.5m long bars
    Number horizontal panels TBD
Cassettes installed after magnet assembled and tested
  Removable for servicing
Details of scintillator-fiber-SiPM-Connector interface, location of Front-End Readout and cable plant not final
Cassette Mechanics and required space between coils not final

## Slide 6: Scope of activities and SLAC roles/responsibilities
TMS Consortium
  Design, document, defend, prototype, procure, build, install, run, analyze TMS
SLAC
  Management: L2 (Tom), Lead Engineer (Marco Oriunno)
  Engineering design and procurement of support structure, steel plates and coil
    Marco, Wes Craddock, Scott Newbry
University of Minnesota
  Individual Detector Panels and packaging into “cassettes” of 6 panels
LSU and U. Pittsburg
  SiPMs, cabling, front end electronics, power, digital data concentration
Analysis: Various: U. Mississippi lead, Wichita State University, Rochester
Installation and Integration: TBD but U. Rochester included

## Slide 7: Issues, challenges in design, prototyping, and physics studies
Issues
Cost constraints
Old technology may not attract new collaborators
Design Challenges
Design iteration difficult
  FEA for fields & forces has many elements and requires long run times
  No physics analysis to support design choices
Prototyping
Coil corner & copper bar samples to test weld
Mini-scintillator panels (1/2 width, 1/3 length), full size first example
Tests of commercial CAEN SiPM readout
Physics Studies
Team led and populated with junior members
Simple reconstruction and basic performance plots not available

## Slide 8: Upcoming major activities, milestones, decision points
Major activities
  Convert CDR Design to PDR and document
    All sub-elements of TMS have changed
Milestones
January 2025 PDR presentations supported by PDR document and updated BOE
June 2025 CD2 of Full Near Detector
Decision Points
Final width & thickness of scintillator bars and Final size of panels
Independent evaluation of changes to magnet and coil design

## Slide 9: Needs/opportunities of more SLAC (or other) engagement
Analysis support from the ML group
  Track reconstruction would seem to me to be an easy project

## Slide 10: TMS Coils Based on MINOS Plank Design Vendor fabricated and pre-tested
For long legs, 1.5” x 1.0” Copper Bars, 8 planks high

## Slide 11: Coil Corner Details
Current Input/Output Corner Detail
Current Corner Detail
(opposite from Current In/Out)
Notice double sided machining on plank end and G-10 step mismatch

## Slide 12: Flux Return Bridged by “Lap Joints”
Will also act as plate stiffeners

## Slide 13: Fiber to Fiber-Plug Design

## Slide 14: Module End Concept: Tom Chase UMN 5/30/24

## Slide 15: PPT Detail View of Fiber-SiPM Interface

## Slide 16: Front End Readout: Commercial
3 A5202 64-channel boards per layer
3 DT5215 Concentrator Boards Total

## Slide 17: Examples of Cables and Connectors