## Slide 1: 1K Plate Design
Tori Ankel
8/5/2024

## Slide 2: What is fixed?
1K plate
20mK plate
4K ring
1K shield
1K standoffs
Inverted top hat
66 cm

## Slide 3: What are the open questions?
Materials
Interfaces
Attocubes!
Snorkel
SC connection
Flexible 1K cold finger
connection

## Slide 4: Materials
  Needs to be cooled through the 1K flexible connection (with acceptable thermal gradients)
  Inside of the shield and plate need to be superconducting
  Needs to be mechanically stable
First ideas?
Notes: (insides of 1k shield, plate and tophat? – maybe flat parts are more important bc of inductor)
Some ideas? What is first step + copper ring maybe

## Slide 5: Calculations Required
For a given design/ set of materials
  Do we have sufficient cooling power?
  Will it support the weight we need?
  How can we get it made?
What is the total heat load on the 1K plate?
What is the temperature at the end of the flexible 1K cold finger connection?
Given the temperature at the end of the cold finger connection and using known heat loads on the 1K plate what are the thermal gradients across the 1K plate and shield?

## Slide 6: Heat Load on the 1K Plate
Radiation
Sheath
Magnet structural legs & skirts
4K shield
4K ring
1K ring standoffs
4K thermal shield onto 1K cold finger
4K  1K
Conduction
1K standoffs
DC Phosphor Bronze wiring from 4 K intercept
DC Copper (low resistance) wiring from 4K intercept
RF wiring from 4 K intercept (NbTi)

## Slide 7: Heat Load on the 1K Plate
Radiation
Sheath
Magnet structural legs & skirts
4K shield
4K ring
1K ring standoffs
4K thermal shield onto 1K cold finger
4K  1K
Conduction
1K standoffs
DC Phosphor Bronze wiring from 4 K intercept
DC Copper (low resistance) wiring from 4K intercept
RF wiring from 4 K intercept (NbTi)

## Slide 8
Sheath walls + sheath top lid
Magnet structural legs & skirts
4K shield walls + shield top lid
4K ring
1K standoffs
4K thermal shield onto 1K cold finger
Radiation
 Set emissivity to 0.3 for all undesigned parts
 Use Stefan-Boltzmann law to estimate an upper bound
Total = 8.5 μW
https://arxiv.org/pdf/1501.07153

## Slide 9
1K standoffs
  400 μW; from four-nine
DC Phosphor Bronze wiring from 4 K intercept
DC Copper (low resistance) wiring from 4K intercept
RF wiring from 4 K intercept (NbTi)
Conduction
From Joe’s wire conductivity spreadsheet + Nicholas’s heat load calculations
Total = 405.4 μW
G10 is for the standoff

## Slide 10: Effect on the Still Temperature
Total Heat Load ~ 413.9 μW
This corresponds to a still temperature of
~841 mK!
841
.413 mW

## Slide 11: 1K Plate Interfaces
Thermal and structural legs
Wiring
Attocubes
20 mK struts
Skirts + SC wire connection on thermal legs
Inverted top hat
Flexible connection to 1K cold finger
Design of the stand-offs?

## Slide 12: 1K Shield Interfaces
  Snorkel
    4K to 1K connection
    May interface with both the 1K plate and the 1K shield
  Connection between 1K shield and 1K plate
    Requires an analysis of screening currents
  Permanent thermometer on the top of the shield

## Slide 13: Timeline
Sep. 3
Decide on materials for plate and shield
Sep.17
Finish snorkel interface
Sep. 10
Determine the cold finger 1K connection
Sep. 17
Finalize attocube positioning on the 1K plate
Nov
1K plate delivered
Oct
1K plate and shield ordered
Aug. 14
Model temperature gradients for a pure Al plate and shield as a baseline
Aug. 20
Finalize 1K interfaces to structural legs and standoffs, make decisions about adding a SC wire to thermal legs
Sep. 20
Finalize interfaces to the 20mK plate, including wiring
Aug. 27
Discuss and determine how the 1K shield will be attached to the 1K plate
Sep. 26
Finalize all interfaces from the 1K plate and shield