## Slide 1: Accelerator Structure Design and Optimization for the FCC-ee Pre-injector Complex
A. Kurtulus, A. Grudiev, A. Latina :: CERN
S. Bettoni, P. Craievich, J.-Y. Raguin :: PSI
Acknowledgment: P. Wang

## Slide 2: Introduction

## Slide 3: FCCee injector linacs layout (new baseline)

## Slide 4: Methodology
Initially, lookup tables were created as functions of aperture and iris thickness of convex cell geometry for the first 20 HOMs to be used to calculate RF parameters of the structure.
This method allows us to compute many structures rapidly.
Motivation of the study:
  Increase the effective shunt impedance of the structure compared to the previous S-band structure.
  As a result of a good compromise between beam dynamics and RF constraints, we studied accelerator structure with an average aperture of 0.12λ.
Structure parameters and requirements:
  f = 2.8 GHz, Length = 3m, Phase advance = 2π/3.
  <a> = 0.12λ, tapered aperture, tapered iris thickness.
  |Wx| from 17.5 to 30 ns < 0.1 V/pC/mm/m
  Emax < 100 MV/m and Sc < 2300 mW/μm²
Rc
L = βλψ/(2π)
a
d_iris
e_iris = (radial size)/d_iris

## Slide 5
RF Pulse Compression and Accelerating Structure
For rectangular klystron pulse, gradient at injection can also be derived analytically:
where
We define an effective shunt impedance: Reff = Vmax2/Pklystron/Lstructure [MΩ/m]
The SLED-type RF pulse compressor has been analytically designed and realized.
Pulse compressor increases peak pulse amplitude and reduces pulse length by charging storage cavity.
The electric field strength within the accelerator cavities depends on the peak power of the RF signal.

## Slide 6: Parameter Sweeps
Damping long-range wakes by HOM detuning.
Aperture and Iris thickness sweeps to get highest effective shunt impedance which satisfies the wake condition.
a = <a> = 0.12λ= 12.8483 mm
= a
= a
Constant aperture structure
Down tapering structure
delta
delta
Delta values = 0.2 to 4mm by step of 0.2mm
Up tapering structure
delta
delta
= a+delta
= a-delta
= a+delta
= a-delta
Delta values = -4 mm to -0.2 by step of 0.2mm
a = <a> = 0.12λ= 12.8483 mm
a = <a> = 0.12λ= 12.8483 mm

## Slide 7: Parameter Sweeps
For each delta we find entrance (firstl cell) and exit (last cell) iris thicknesses for the highest effective shunt impedance.
Scanning iris thickness from 2.04 mm to 6.2 mm by step of 0.2mm (These numbers are the limits of Lookup table).
Q0,SLED = 2e5, Tklystron = 3 us.
delta= 0 mm
delta= 2 mm
delta= -2 mm
Constant aperture
Down tapering
Up tapering
Highest shunt imp.
Highest shunt imp.
Highest shunt imp.
(Delta from 0.2 mm to 4mm)
(Delta from -4mm to -0.2 mm)

## Slide 8: Parameter Sweeps
Checking for Transverse wake condition: |Wx| from 17.5 to 30 ns < 0.1 V/pC/mm/m
Long-range wake from frequency-domain parameters: R/Q, Q and ω.
Where
delta= 2 mm
Highlighting the areas that satisfy the wake requirment for every delta.
Updating maximum effective shunt impedance for < 0.1 V/pC/mm/m.
Calculating structure parameters with the corresponding aperture and
iris thickness.

## Slide 9: Parameters Sweep Results
 | Delta = -3 mm | Delta = -2 mm | Delta = 2 mm | Delta = 3mm
Aperture | 9.85 mm → 15.85 mm | 10.85 mm → 14.85 mm | 14.85 mm, → 10.85 mm | 15.85 mm → 9.85 mm
Iris thickness | 3.44 mm → 2.84 mm | 4.04 mm → 2.84 mm | 2.84 mm → 4.04 mm | 2.84 mm → 3.44 mm
Vg (% c) | 0.97 → 4.65 | 1.25 → 3.87 | 3.87 → 1.25 | 4.65 → 0.97
r/Q (kOhm/m) | 4.65 → 3.44 | 4.38 → 3.64 | 3.64 → 4.38 | 3.44 → 4.65
Q | 16340 → 16685 | 16178 → 16642 | 16642 → 16178 | 16685 → 16340
Filling time | 479 ns | 462 ns | 462 ns | 479 ns
SLED coupling | 17 | 17 | 15 | 15
Eff. shunt impedance | 108 MΩ/m | 107 MΩ/m | 103 MΩ/m | 102 MΩ/m
 | 25 MV/m | 25 MV/m | 25 MV/m | 25 MV/m
Emax (instant.) | 133 MV/m | 106 MV/m | 83 MV/m | 102 MV/m
Sc,max (instant.) | 1226 mW/μm² | 911 mW/μm² | 643 mW/μm² | 732 mW/μm²
 | Delta = -3 mm | Delta = -2 mm | Delta = 2 mm | Delta = 3mm
Aperture | 9.85 mm → 15.85 mm | 10.85 mm → 14.85 mm | 14.85 mm, → 10.85 mm | 15.85 mm → 9.85 mm
Iris thickness | 3.44 mm → 2.84 mm | 4.04 mm → 2.84 mm | 2.84 mm → 4.04 mm | 2.84 mm → 3.44 mm
Vg (% c) | 0.97 → 4.65 | 1.25 → 3.87 | 3.87 → 1.25 | 4.65 → 0.97
r/Q (kOhm/m) | 4.65 → 3.44 | 4.38 → 3.64 | 3.64 → 4.38 | 3.44 → 4.65
Q | 16340 → 16685 | 16178 → 16642 | 16642 → 16178 | 16685 → 16340
Filling time | 479 ns | 462 ns | 462 ns | 479 ns
SLED coupling | 17 | 17 | 15 | 15
Eff. shunt impedance | 108 MΩ/m | 107 MΩ/m | 103 MΩ/m | 102 MΩ/m
 | 25 MV/m | 25 MV/m | 25 MV/m | 25 MV/m
Emax (instant.) | 133 MV/m | 106 MV/m | 83 MV/m | 102 MV/m
Sc,max (instant.) | 1226 mW/μm² | 911 mW/μm² | 643 mW/μm² | 732 mW/μm²
  Emax < 100 MV/m and Sc < 2300 mW/μm²
  Based on requirements delta=2mm is the best candidate.

## Slide 10: Wakefield Studies

## Slide 11: Wakefield Studies
Wakefields are calculated both with lookup table and ECHO2D time-domain wakefield solver by I. Zagorodnov.
Long-range wake damping by dipole mode detuning is effective by tapering both aperture and iris thickness.
25 ns of bunch spacing with 4 bunches.

## Slide 12: CST benchmarking

## Slide 13: Benchmarking with CST Model
After we decided aperture and iris thickness parameters, we benchmarked our lookup table results with the 3D model in CST for the first, middle and last cells.
Less surface fields observed with the 3D model in CST.
Delta = 2 mm | CST
Entr., exit aperture | 14.85 mm → 10.85 mm
Iris thickness | 2.84 mm → 4.04 mm
Vg (% c) | 3.92 → 1.25
r/Q (kOhm/m) | 3.63 → 4.38
Q | 16571 → 16039
Filling time | 460 ns
SLED coupling | 15
Eff. shunt impedance | 102 MΩ/m
 | 25 MV/m
Emax (instant.) | 79 MV/m
Sc,max (instant.) | 638 mW/μm²
Delta = 2 mm | CST
Entr., exit aperture | 14.85 mm → 10.85 mm
Iris thickness | 2.84 mm → 4.04 mm
Vg (% c) | 3.92 → 1.25
r/Q (kOhm/m) | 3.63 → 4.38
Q | 16571 → 16039
Filling time | 460 ns
SLED coupling | 15
Eff. shunt impedance | 102 MΩ/m
 | 25 MV/m
Emax (instant.) | 79 MV/m
Sc,max (instant.) | 638 mW/μm²
 | f (GHz) | Q | Rz/Q (kOhm/m) | Vg/c (%)
First Cell | 2.8 | 16571 | 3.63 | 3.92
Middle Cell | 2.8 | 16293 | 4.02 | 2.34
Last Cell | 2.8 | 16039 | 4.38 | 1.25
 | Esmax/G | Sc/G^2
First Cell | 2.8669 | 9.105e-4
Middle Cell | 2.4254 | 5.876e-4
Last Cell | 2.0923 | 3.614e-4
E-fields
Sc-fields

## Slide 14: High Energy Linac
Delta = 2 mm | HE-linac
Entr., exit aperture | 14.85 mm, 10.85 mm
Iris thickness | 2.84 mm → 4.04 mm
Vg (% c) | 3.92 → 1.25
r/Q (kOhm/m) | 3.63 → 4.38
Q | 16571 → 16039
Filling time | 460 ns
SLED coupling | 15
Eff. shunt impedance | 102 MΩ/m
Repetition rate [Hz] | 100
Klystron power per structure | 15 MW
Average Structure Input Power | 4.95 kW
 | 22.5 MV/m
Emax (instant.) | 56 MV/m
Sc,max (instant.) | 328 mW/μm²
Delta = 2 mm | HE-linac
Entr., exit aperture | 14.85 mm, 10.85 mm
Iris thickness | 2.84 mm → 4.04 mm
Vg (% c) | 3.92 → 1.25
r/Q (kOhm/m) | 3.63 → 4.38
Q | 16571 → 16039
Filling time | 460 ns
SLED coupling | 15
Eff. shunt impedance | 102 MΩ/m
Repetition rate [Hz] | 100
Klystron power per structure | 15 MW
Average Structure Input Power | 4.95 kW
 | 22.5 MV/m
Emax (instant.) | 56 MV/m
Sc,max (instant.) | 328 mW/μm²

## Slide 15: Thermomechanical Studies

## Slide 16
Thermal Studies
…….
…….
3m long structure (84 cells)
Pin
Pout=0.607xPin
Common Linac structure
Thermal load parameters of first cell | 
frep , Tklystron | 100 Hz, 3 µs
αpulse_compressor | 0.872
Pin (Klystron power per structure) | 18.9 MW
<Pin> (Avg. structure input power) | 4.95 kW
Ufirst_cell | 1.5e-5 J
Ploss (Avg. wall losses first cell) | 16.11 W
Thermal load parameters of last cell | 
αstruture | 0.607
<Pin_last> (Avg. Last cell input power) | 3 kW
Ulast_cell | 1.4e-5 J
Ploss (Avg. wall losses first cell) | 15.36 W
Cooling channel diameter | 16 mm
Convection to water channel | 4 kW/m²/K
ΔT = 0.41 ͦC increase
ΔT = 0.35 ͦC increase

## Slide 17
Max deformation ≈ 0.1 μm which is negligible
Mechanical Studies
Based on thermal studies we simulated total deformation on the first cell with mechanical solver of ANSYS.

## Slide 18: Beam-loading effect

## Slide 19: Beam-loading effect
Parameters for the structure:
f = 2.8 GHz, Length = 3m, Phase advance = 2π/3, <a> = 0.12λ, Q0,SLED = 2e5, Tklystron = 3 us, .
4 bunches with Qbunch = 5 nC, Tbunch_seperation = 25 ns, Ibeam = 0.2 A.
Max energy spread is 2.45%

## Slide 20: Minimization of bunch-to-bunch energy variation
By modulating the input pulse shape of the klystron, we can optimize the energy variation between the bunches.
After modifying the input pulse shape of the klystron, we successfully achieved a flattening of the unloaded (also loaded) voltage, with the total bunch-to-bunch energy variation observed to be less than 0.1%.

## Slide 21: Conclusion
Design and Optimization :
  Conducted design studies of accelerating structures for the <a> = 0.12λ.
  Optimized aperture size and iris thickness to determine optimal configurations for highest shunt impedance and minimal long-range wakefield impact.
RF Pulse Compression Design:
  Designed and implemented a SLED-type RF pulse compressor to enhance RF performance.
Benchmarking:
  Benchmarked design parameters using CST’s eigenmode solver, ensuring accuracy of lookup table predictions.
Beam-Loading and Energy Spread Reduction for 4 bunches of 5nC:
  Studied the effect of beam-loading.
  Minimized bunch-to-bunch energy variation less than 0.1% by optimizing klystron input pulse shape.
Thermal and Mechanical Robustness for the Common Linac operating at 22.5 MV/m and :
  Conducted thermal and mechanical studies to ensure structural integrity and performance stability.
  Thermal studies are done with CST’s Thermal solver.
  Negligible deformation (0.1 μm) observed.

## Slide 22: Thanks for your attention!

## Slide 23: Spare Slides

## Slide 24
SLED-type RF pulse compressor
Farkas et al., A method of doubling SLAC‘s energy, Proc. HEACC 1974
Increase peak pulse amplitude and reduce pulse length by charging storage cavity
Output pulse AL given by where AK: klystron pulse, β, Q0, τ: coupling, Q-factor, filling time of storage cavity.

## Slide 25
@2.8 GHz, 0.12λ = 12.8483 mm
a_entr = 12.8483 + delta, a_exit = 12.8483 – delta, where delta = -4 to 4 mm by step of 0.2mm
a_entr = 14.2483, a_ext=11.4483
delta=1.4 mm
delta=1.6mm
delta=1.8mm
delta=2mm
a_entr = 14.4483, a_ext=11.2483
a_entr = 14.6483, a_ext=11.0483
a_entr = 14.8483, a_ext=10.8483
delta=2.4 mm
delta=2.6 mm
a_entr = 15.2483, a_ext=10.4483
a_entr = 15.4483, a_ext=10.2483
delta=2.8 mm
a_entr = 15.6483, a_ext=10.0483
delta=2.2 mm
a_entr = 15.0483, a_ext=10.6483
DOWN TAPERING

## Slide 26
DOWN TAPERING
@2.8 GHz, 0.12λ = 12.8483 mm
a_entr = 12.8483 + delta, a_exit = 12.8483 – delta, where delta = -4 to 4 mm by step of 0.2mm
delta=3 mm
a_entr = 15.8483, a_ext=9.8483
delta=3.2 mm
a_entr = 16.0483, a_ext=9.6483
delta=3.4 mm
a_entr = 16.2483, a_ext=9.4483
delta=3.6 mm
a_entr = 16.4483, a_ext=9.2483
delta=3.8 mm
a_entr = 16.6483, a_ext=9.0483
delta=4 mm
a_entr = 16.8483, a_ext=8.8483

## Slide 27
@2.8 GHz, 0.12λ = 12.8483 mm
a_entr = 12.8483 + delta, a_exit = 12.8483 – delta, where delta = -4 to 4 mm by step of 0.2mm
a_entr = 11.4483, a_ext= 14.2483
delta= -1.4 mm
delta= -1.8mm
delta= -1.6 mm
delta= -2mm
a_entr = 11.2483, a_ext= 14.4483
a_entr = 11.0483, a_ext= 14.6483
a_entr = 10.8483, a_ext= 14.8483
delta= -2.2 mm
delta= -2.4 mm
delta= -2.8 mm
a_entr = 10.4483, a_ext= 15.2483
delta= -2.6 mm
a_entr = 10.2483, a_ext= 15.4483
a_entr = 10.0483, a_ext= 15.6483
a_entr = 10.6483, a_ext= 15.0483
UP TAPERING

## Slide 28
@2.8 GHz, 0.12λ = 12.8483 mm
a_entr = 12.8483 + delta, a_exit = 12.8483 – delta, where delta = -4 to 4 mm by step of 0.2mm
UP TAPERING
delta= -3 mm
a_entr = 9.8483, a_ext= 15.8483
delta= -3.2 mm
a_entr = 9.6483, a_ext= 16.0483
delta= -3.4 mm
a_entr = 9.4483, a_ext= 16.2483
delta= -3.6 mm
a_entr = 9.2483, a_ext= 16.4483
delta= -3.8 mm
a_entr = 9.0483, a_ext= 16.6483
delta= -4 mm
a_entr = 8.8483, a_ext= 16.8483

## Slide 29
Other parameter scans
Different Q0,SLED, Tklystron , Length of the structure, Phase advance scanned .
Q0,SLED from 2e5 to 2.5e5.
≈ 1% of increase

## Slide 30
Other parameter scans
Different Q0,SLED, Tklystron , Length of the structure, Phase advance scanned .
Tklystron from 3 us to 4 us.
≈ 14% of increase

## Slide 31
Other parameter scans
Different Q0,SLED, Tklystron , Length of the structure, Phase advance scanned .
Length of the structure from 3 m to 4 m.

## Slide 32
Other parameter scans
Different Q0,SLED, Tklystron , Length of the structure, Phase advance scanned .
Phase advance from 2π/3 to 5π/6.