## Slide 1: Positron Source
Yoshinori Enomoto (KEK)

## Slide 2: contents
Recent progress of positron source for ILC
Electron driven positron source LINAC (EDPL)
  Layout
  Parameters
  Possibility of a C3 application

## Slide 3: contents
Recent progress of positron source for ILC
Electron driven positron source LINAC (EDPL)
  Layout
  Parameters
  Possibility of a C3 application

## Slide 4: Prototype to be built by JFY2027
target
Flux concentrator
Acc. structure
solenoid

## Slide 5: What we did in JFY2023
Vacuum system
FC
Design and manufacture parts
Target
rotation mechanism
ACC structure
RF design, 3D model
Solenoid
Design and procurement of material

## Slide 6: What we plan to do in JFY2024
FC
assemble
solenoid
ACC structure
Manufacturing test
Target disk
Collimator with pillow seal

## Slide 7: Target
 | Technical design | Engineering design | 3D model | Drawings | Manufacturing | Evaluation
Rotation mechanism | Done | Done | Done | Done | Done | Done
Target disk | Done | Done | Done | Done | Done | In progress
Design and manufacturing of rotation mechanism done in FY2023
Design and manufacturing of target disk finished
Assembled into the chamber
  Vacuum test OK
  Rotation test OK
  run-out evaluation by laser displacement sensor is in progress
  Thermal contact evaluation between W and Cu is planned
Narrow gap1 for differential pumping 30um
Narrow gap2 for differential pumping 100um
Mechanical face seal
<10-5 Pa
~10-2 Pa
~101 Pa

## Slide 8: FC
FY2023
FY2024
Machining
done
EBW
done
Secondary working
Milling & EDM
done
Black plating
done
Welding & assembly
Parts(delivered)
feedthrough
flange, support
piping
electrode
bolt, pin, bush
coil

## Slide 9: FC
FY2023
FY2024
Machining
done
EBW
done
Secondary working
Milling & EDM
done
Black plating
done
Welding & assembly
Done
Parts(delivered)
feedthrough
flange, support
piping
electrode
bolt, pin, bush
coil

## Slide 11: Acc. structure
Machining and bonding of test cell is in progress
Drawing preparation is almost finished
Clean hut for RF test and assemble work was built
Precise cost estimation for all the prototype manufacturing process completed
 | Technical design | Mechanical design | 3D model | Drawings | Material | Manufacturing
Acc. Structure | Done（RF） | Done | Done | Ongoing | Delivered 2024/3 + additional 2025/3 | FY2024-FY2025
Test cell | Done（RF） | Done | Done | Done | Delivered 2024/3 | In progress

## Slide 12: Hot pressing cells
C plate
□445×40t
C plate
□445×40t
C sheet 0.5t
coupling-cell rp
accelerating-cell rp
294 kN@900℃

## Slide 13: 3D model
Updated largely including many peripheral devices,
such as piping and cable connections
These peripheral devices will be manufactured and integrated by the end of FY2024

## Slide 14: contents
Recent progress of positron source for ILC
Electron driven positron source LINAC (EDPL)
  Layout
  Parameters
  Possibility of a C3 application

## Slide 15: Layout of ILC
Additional linac for electron driven positron source

## Slide 16: Present layout of EDPL

## Slide 17: Candidate site
H. Hayano

## Slide 18: Candidate site
H. Hayano

## Slide 19
H. Hayano

## Slide 21: Conditions
The candidate site is mountainous
It’s difficult to prepare long flat area to build Linac on surface
Dumping Ring and Main Linac are both deep under ground
EDPL (2 km) will be also in the same level
Long and wide tunnel for EDPL deep under ground is not cost effective
Compact (< 300 m) high gradient Linac on surface might be a promising alternative

## Slide 22: Parameters
Primary electron energy | 3 GeV
Primary electron bunch charge | ～4 nC
No. of bunches / pulse | 66
repetition | 300 Hz / 100 pps
Positron energy | 5 GeV
Positron bunch charge | 4.2 nC

## Slide 23: Possible layout
To DR
Electron gun
target
Large aperture capture linac
(0 → 1 GeV)
Electron 3 GeV Driver
(high gradient)
< 300 m
ECS
Positron booster
(high gradient 1 → 5 GeV)
Pre-dumping ring
Use a pre-dumping ring to reduce emittance of positron beam.
Small aperture high shunt impedance Acc. Structure is applicable for positron booster section

## Slide 24: Summary
Prototyping of a positron source for the ILC is ongoing
Target disk and FC delivered and assembled
EDPL design and cost estimation is in progress
High gradient compact linac will be a promising option

## Slide 26: Bunch structure
H. Hayano

## Slide 27: Bunch structure
Create positron for 66 ms
Store them in the DR for 199.3 ms
Extract them to main linac for 0.7 ms
20 pulse / train
66 bunch / pulse
1312 bunch / train (8 bunch subtracted)
Repetition 5 Hz
EDPL operated 100 pps / 300 Hz
M. Kuriki, OHO seminar 2021
…….
3.3 ms✕20 = 66 ms
66
train
pulse