## Slide 1: Preliminary Damping Ring Design for the Cool Copper Collider
Matthew Andorf

## Slide 2: Motivation for Damping Rings
Spin Polarized Electron Production:
  GaAs photocathode operated in a DC electron gun
  Round beam, ~2-3 μm normalized emittance
Positron production:
  Tungsten target
  2-3 orders of magnitude larger beam emittance than electron beam
Damping Rings optimize beam luminosity!
  Can produce ~100 nm horizontal emittances
  Produce flat beams, ~1 nm emittance
Beamstrahlung:
  Use of a flat beam reduces beam collision induced radiative losses

## Slide 3: Ring Layout
Most damping designs use a race-track layout:
  Arcs consist of periodic cells designed for low emittance
  Straight sections provide room for damping wigglers, RF cavities and injection/extraction lines
Periodic arc-cells
Periodic arc-cells
Damping wigglers, RF
injection/extraction lines/wigglers
From Booster Linac
(or pre-damping ring)
To Main Linac

## Slide 4: Synchrotron Radiation Damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Longitudinal damping is straightforward
  Particles with more energy radiate more, particles with less energy radiate less
  RF cavities restore energy loss
  Results in reduction of particle beam energy spread

## Slide 5: Synchrotron Radiation Damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Longitudinal damping is straightforward:
  Particles with more energy radiate more, particles with less energy radiate less
  Results in reduction of particle beam energy spread
Damping in the transverse planes is more complicated:

## Slide 6: Synchrotron Radiation damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Longitudinal damping is straightforward:
  Particles with more energy radiate more, particles with less energy radiate less
  Results in reduction of particle beam energy spread
Damping in the transverse planes is more complicated:
  A photon is emitted tangential to particle path

## Slide 7: Synchrotron Radiation damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Longitudinal damping is straightforward:
  Particles with more energy radiate more, particles with less energy radiate less
  Results in reduction of particle beam energy spread
Damping in the transverse planes is more complicated:
  A photon is emitted tangential to particle path, resulting in a change in momentum in both Px and Pz
  RF cavities restore energy in the longitudinal plane only

## Slide 8: Synchrotron Radiation damping
Synchrotron radiation damps particle motion in all three planes (horizontal, vertical and longitudinal)
Longitudinal damping is straightforward:
  Particles with more energy radiate more, particles with less energy radiate less
  Results in reduction of particle beam energy spread
Damping in the transverse planes is more complicated:
  A photon is emitted tangential to particle path, resulting in a change in momentum in both Px and Pz
  RF cavities restore energy in the longitudinal plane only
  Total cycle results in a reduction of Px only, and consequently beam emittance

## Slide 9: Damping Ring Basic Considerations
Train 1
Train 2
Givens:
  Collider repetition rate
  Bunch structure (e.g. bunch spacing, number of bunches per train)
  Injected beam emittance
Choices:
  Number of stored bunch trains (Ntrain)—determines min. circumference
  Stored number of damping times(Nτ )—constrains value of damping time
  Lattice design, wiggler parameters
Consequences of those choices:
  Beam energy
  Extracted beam emittance

## Slide 10: Periodic Focusing and Lattice Function
Circular accelerators are necessarily periodic
  For any periodic lattice, the Twiss parameters (α, β, γ) can be found
  Together (α, β, γ) can describe the particles “action”, which is an invariant of motion in the lattice
  The emittance can be defined by an ellipse which encloses the beam.

## Slide 11: Periodic Focusing and Lattice Function
A particle with an energy deviation from the machine design will be displaced horizontally in a bending magnet
The dispersion function and its derivative describe the displacement:
Dispersion is generated from bend magnets and controlled with quadrupoles
  Outside of dipoles, a dispersion invariant (“Curly H”) exists.

## Slide 12: Natural Equilibrium Emittance
SR damping is countered by quantum excitation leading to a ‘natural’ or zero-charge beam emittance
The emission of a photon in a dispersive region results in an increase in betatron motion.
fixed by ring geometry
Optimized by layout of quads/bend magnets
In vertical plane, ultimate emittance set by opening angle of radiation emission
Magnet misalignments and IBS will additionally grow emittance.

## Slide 13: Arc Cell design
Double Bend and Multibend Achromats (DBA, MBA)
  Produce low emittance while also providing dispersion free straight sections outside dipole pairs
  All diffraction limited light sources use MBA’s
Bending magnets
DBA

## Slide 14: Arc cell design
Optimal values at dipole center
Bend magnet
Theoretical Minimum Emittance (TME) cells:
  Produce lowest achievable emittance
  Twiss parameters chosen to minimize I5 integral while accounting propagation through dipole
  Does not produce dispersion free section…not a problem for damping rings!

## Slide 15: Arc Lattice design
Emittance scales as θ3. Therefore, more cells results in a lower emittance
Some limitations to consider:
  The minimum cell length needs to be achievable from magnet/vacuum design considerations
  TME cells require strong focusing resulting in high chromaticity. Operating at optimum emittance may not be achievable.
  Higher number of cells will result in a tighter alignment requirement (vertical emittance)
  The cost and complexity of building the ring goes up with number of cells

## Slide 16: Damping Wigglers
Damping Wigglers can be used to both lower the equilibrium emittance
  Damping rate is proportional to radiative losses around the ring
  I2 is increased due to extra bending (independent of ring circumference) directly lowering eq. emittance
  Faster damping allows reduction in design energy, indirectly lowering eq. emittance
  Wigglers are installed in dispersion free region
  Wiggler ‘self-dispersion’ modifies I5. Wiggler B-field can not be increases arbitrarily.

## Slide 17: C3 design parameters
Parameter | Value
Energy (GeV) | 4.6
Rep-rate (Hz) | 60
Stored bunch trains | 2
Bunches per train | 266
Bunch train length (m) | 423
Circumference (m) | 1190
# TME cells | 248
#FODO cells | 30
Horizontal tune | 120.44
Vertical tune | 52.28
Damping time (ms) | 4.2
Nt | 7.9
Hor. Normalized natural emittance (nm) | 170
TME section
FODO section

## Slide 18: TME cell
Parameter | Value
Bend angle (degree) | 1.43
Bend B field (T) | 0.55
Bend Length (m) | 0.7
Bend gradient | +22.9
QF1 gradient (T/m) | -60
QF1 length (m) | 0.20
QF2 gradient (T/m) | -17.6
QF2 length (m) | 0.20
ξx/Qx (Normalized natural chromaticity) | -2.79
ξx/Qx (Normalized natural chromaticity) | -2.56
ε/εopt | 2.6

## Slide 19: FODO/Wiggler section
Parameter | Value
QF1 gradient (T/m) | -15.4
QF1 length (m) | 0.25
QF2 gradient (T/m) | 15.2
QF1 length (m) | 0.25
Wiggler peak field (T) | 1.0
Wiggler period (m) | 0.11
Filling factor (%) | 90

## Slide 20: Intrabeam Scattering
As particles undergo betatron/synchrotron oscillations, collisions occur
Large angle scattering results in particle loss
  Touschek lifetime
  Needs to be reasonably long for machine tuning but not relevant during collider runs
Multiple small angle scattering results in emittance growth in all three planes
  IBS
Theory simplifies at high energy (“CIMP”), allowing fast computation of IBS effect
  Rates are a function of lattice and beam parameters
  IBS program available in BMAD

## Slide 21: IBS in C3 Damping Rings
Zero-charge bunch length can be varied by RF voltage
IBS rates depend strongly on bunch length
  Long bunch reduces IBS effect
  Shorter bunch simplifies bunch compression after extraction
  Trade-off to be analyzed in future work
IBS looks very manageable for C3!

## Slide 22: Summary
Damping rings are critical for achieving high luminosity in electron-positron linear colliders
  Reduce by several orders of magnitude the source emittances of both electrons and positrons
  Naturally produces a flat-beam which minimizes beamstrahlung effect
Theoretical Minimum Emittance (TME) cells used in arc’s produce lowest achievable emittances
Damping wigglers improve performance by:
  Decreasing damping time, allowing operation at lower energy
  Decreasing horizontal beam emittance with correct B-field choice
C3 damping ring design in progress!
  Ultimately focused on achieving highest possible beam luminosity