## Slide 1: Ce+BAF: Simulations of CW Positron Beam Generation, Capture and Acceleration
Main Solenoid
Absorbers
Target
Cavity
Bucking Solenoid
Target and Capture Magnets
Cu Coil
W10Cu
W10Cu
TZM
Target
Cu Cavity*
Steel
Cu Coil
Compensation
Solenoid
Power Deposited by 1 mA e‒ Beam @ 120 MeV
e+ Energy Spectrum at Target Exit and Captured e+
Simplified Scheme of Positron Generation, Capture, Selection of e+ Energy Band and Acceleration to 123 MeV
1 mA 120 MeV

## Slide 2: Conceptual Development and Design of CW NC Capture Cavity
Conceptual Development
Improve design of e+ injector
Develop pCDR
Address Critical Risk Areas
mA polarized e- source
High power target
CW capture cavity
Year 1: Define solenoid and cavity specifications, generate preliminary cavity fields, integrate with target geometry, perform radiation simulations, thermal analysis, preliminary e+ and e- beam tracking
Year 2: Iterate and optimize magnet and cavity design, explore beam loading and magnetization effects, find optimal parameters of capture system with an adjustable energy selection band
At the early design stage, the goal is not to produce a single design but to provide a range of options
Capture Cavity Design Strategy
Balance and Tradeoff
Large cavity iris radius is expected, >15mm, to accommodate more e+ transversely → lowers the shunt impedance
As high as possible E field gradient is desired to manipulate the incoming e+ beam longitudinally → requires high shunt impedance
Type A: simpler structure, larger cell-to-cell coupling
Type B: typically higher shunt impedance
Capture cavity set for CW Ce+BAF was obtained for further capture section design
Studied influence of solenoid magnetic field to the e+ transportation before entering cavity
Performed initial studies of the action of cavity field on 20, 60 MeV positrons