## Slide 1
Analog Front-end for HEP
HEPIC Summer Week
Angelo Dragone
23 June 2025

## Slide 2: Outline
From Particle to Detected Charge
  Sensors
  Signal Formation and characteristics
  Source model
From Charge to Amplified Analog Signal
  Typical Front-End Channel
  Charge Sensitive Amplifier
  Shaper
Noise and Design Optimization
  Thermal, Shot, Flicker
  Series vs. Parallel noise
  Noise calculation and optimization

## Slide 3: The aims of particle detectors
Discover the identity of the particles that pass through the detector after an event (collision or decay)
To achieve this goal, we need to reconstruct the momenta of the particles, thus tracking their trajectory and measuring their energy.
A detector needs to have:
  Enough layers - to recognize trajectories easily and reconstruct them reliably
  Large numbers of sensor channels to easily distinguish tracks and achieve the required spatial resolution
    Best spatial precision near the interaction point
  Material - enough to generate signals but minimize scattering, secondary interactions, and conversions…
  Magnetic field to bend trajectories

## Slide 4: Sensors
Particles passing through a detector lose energy by ionization (charged particles) or by absorption (photons)
Many kind particle detectors exist, built with several kind of sensors. Details are beyond the scope of this lecture, but typically detectors are:
  Gaseous detectors
    TPC, large volume drift chambers
    planar wire chambers, MSGC, GEM,…
    straw tubes
  Silicon detectors
    Pixels, MAPS and CCDs
    Silicon strips
    Silicon drift detectors
  Sensor parameters are not identical but often similar
    Signal size ~ 25,000 electrons (~2000 - 100,000e)
    Collection time ~few x10ns, but may have slow components
    Electrical parameters: capacitance, resistance, leakage currents
Hybrid Detector

## Slide 5: Operation principle
The basic principle is the one used in Ionization Chambers
A
+
-
Gas
Particles deposit energy in the sensor
Ionize a gas molecule
Charges drift due to the electric field
Current pulse can be measured
We always want signals to be large and collected fast
Most semiconductor sensors work in a similar way
HV
X-ray
+
e-
+
e-

## Slide 6: Signal size
The basic principle of all tracking devices is to detect the free charges resulting from the interaction of a medium with a passing charged particle.
The Bethe-Bloch formula is used to estimate the average energy loss of a charged particle in a medium:
Where:
z is the charge of the incident particle,
Tmax is the maximum kinetic energy that can be imparted to a free electron in a single collision,
I is the mean excitation energy,
Z is the atomic number
A is the atomic mass of the considered material,
NA Avogadro’s number,
me is the electron mass,
c is the speed of light,
re is the classical electron radius,
β is the relative particle velocity ν/c,
γ is the relativistic factor 1/sqrt(1- β2)
βγ=p/Mc where p is the relativistic momentum, and M is the particle mass
δ is the density effect correction

## Slide 7: Signal size
The most important region of the Bethe-Bloch plot is the minimum present at βγ~3, which expresses the minimum energy deposited in the medium.
Particles providing such energy loss are called Minimum Ionizing Particles (MIPs)
Each detector system must have an intrinsic noise lower enough to detect these "worst-case" particles.
In silicon, a MIP loses an average energy of about 288eV/um

## Slide 8: Signal generation depends on the band gap
Klein’s empirical formula relates energy, E, to create electron-hole pair to the band gap: E = 2.67 EGap +0.87
 | Egap [eV] | E [eV] | ni [300K, cm3] | Z
Si | 1.12 | 3.6 | 1.45x1010 | 14
Ge | 0.67 | 2.9 | 2.4x1013 | 32
GaAs | 1.42 | 4.3 | 1.8x106 | 31-33
CdTe / CZT | 1.4 | 4.6 | 2.6x105 | 48-52
Diamond | 5.45 | 13.2 | <103 | 6
E for semiconductors is relatively low compared to other media (Gas ~30eV, Scintillators ~20eV) → Large signals
In Si a MIP produces ~80 e/h pairs per um. For a 300μm thick sensor, the signal is thus ~24000 e/h pairs or 4fC/MIP
Issue: at room temperature, intrinsic semiconductors have too many free electrons

## Slide 9: Fully depleted diodes
Solution: create a reverse biased p-n junction to fully deplete the sensor made on a high resistivity substrate
Fast collection time
For Si 350um thick fully depleted with 100V μ = 1350 cm2/Vs:
The electron’s collection time is
~10ns
Segmentation in pixels enables position resolution

## Slide 10: Source model
The signal that we want to detect is a charge Q0, which is, created by an ionizing particle or a photon. Normally charge creation is much faster than the amplifier bandwidth so we can model it by a current spike
The input impedance is generally the detector capacitance Cin
Ileak is a DC leakage current of the detector
=+ Ileak
Cin
Detector
=
V+
0

## Slide 11: Outline
From Particle to Detected Charge
  Sensors
  Signal Formation and characteristics
  Source model
From Charge to Amplified Analog Signal
  Typical Front-End Channel
  Charge Sensitive Amplifier
  Shaper
Noise and Design Optimization
  Thermal, Shot, Flicker
  Series vs. Parallel noise
  Noise calculation and optimization

## Slide 12: Typical Front-End Channel
Iin
Cf
CS
CSA
Detector
Vth
Shaper
Comp
S/H
Charge Sensitive Amplifier
Integrates the incoming charge on a feedback capacitor. The output is a voltage step. Has a large signal gain
such that the noise of the subsequent stage (shaper) is negligible.
Shaper
Shapes (Filters) the signal to give a predefined
output signal shape, and rejection of noise frequency components that are outside of the signal frequency range and provides an optimal Signal to Noise Ratio
Comparator to detect an event above a certain threshold (event detection)
and/or a TDC to detect the time of arrival/time over threshold (timing detection)
and/or a Sample and Hold circuit for an ADC further in the channel (energy detection)
TDC
ADC
Reset

## Slide 13: Charge Sensitive Amplifier (CSA)
Cascode Architecutre
Folded-Cascode Architecutre
LF Monopix chip
AC coupling, current feedback, Source Follower stage

## Slide 14: Charge Sensitive Amplifier (CSA)
ePixM for LCLSII
Krummenacher Architecture
Synchronous reset, 2 gain modes
Leakage current compensation
There are many other architectures: differential, inverter based, …. with different reset mechanisms and leakage current compensation

## Slide 15: During this week we will examine 3 CSA configurations
VDD
In
Out
Vcc
Vld1
VDD
In
Vcc1
Vgb
Vcc2
Out
Vld
VDD
In
Vcs
Vld
Out
Vcc
VDD
Vld2

## Slide 16: How to model a simple CSA?
How to calculate the transfer function?
How to derive frequency behavior?
How to derive temporal behavior?
How to choose design parameters?
How to minimize noise?
How to gain design intuition?
Iin
RL
Vout
Cin
CL
-gm
If
I1
Cf
Rf

## Slide 17: Understanding CSAs from the Ground Up
Begin by analyzing the basic atomic units of an CSA
Use the gained insights to understand more complex realizations
…
Intrinsic gain stage
(open loop)
Adding capacitive feedback
Adding a cascode (for higher gain)

## Slide 18: Intrinsic Gain Stage (IGS)
Initially neglect extrinsic capacitances
  Feedforward due to at frequencies beyond range of interest
  Loading due to can be lumped into
Specifications of interest
  Low-frequency gain
  Gain-bandwidth product
Small-signal model

## Slide 19: IGS Frequency Response
is irrelevant for the high-frequency behavior (around )
Gain-bandwidth product (GBW) of intrinsic gain stage

## Slide 20: Basic gm/Id Design Flow
Design choices

## Slide 21: Closing the Feedback Loop
Questions
  What is the phase margin?
  How fast does this circuit settle (in response to the input step)?
  What is the total integrated output noise?
Iin

## Slide 22: Feedback Loop Analysis
Feedback factor
Loop gain Return Ratio
Total load capacitance

## Slide 23: Loop Unity Gain Frequency and Phase Margin

## Slide 24: Impulse Response of the Closed-Loop Circuit
Need ACl(s) to make further progress
We could perform a nodal analysis on the closed loop circuit, but it is more insightful to work with a loop gain-based approach
Closed-loop transfer function
Time domain response follows from inverse Laplace transform
Impulse response

## Slide 25: Finding A(s) using Return Ratio Framework
Models feedforward effects (due to CF in our example)
[Gray & Meyer, Chapter 8]
Asymptotic Gain =
gain for L approaching
i.e. the control variable is a virtual ground
Dead Net Gain =
gain the passive net
i.e. gain of the net with the controlled source generator removed

## Slide 26: First-Order Analysis (Neglecting Feedforward)
Ideal closed-loop gain
Iin

## Slide 27
Ideal
Static Error
Dynamic Error

## Slide 28: Graphical Illustration
Dynamic Error
Static Error

## Slide 29: Design Considerations
Need large low-frequency loop gain () for small static error ()
Need small (large ) for fast settling
Define settling time () based on specified dynamic error

## Slide 30: Required Number of Time Constants
Going from 1% dynamic settling error to 10-6 requires only a ~3x increase in settling time
1% | 4.6
0.1% | 6.9
0.01% | 9.2
10-6 | 13.8
1% | 4.6
0.1% | 6.9
0.01% | 9.2
10-6 | 13.8

## Slide 31: CSA: example ideal case
Cin = 100fF Cf= 10fF CL = 20fF
= 100k Q = 10 000 e- over 1 ns
Vout = Q/Cf = 160 mV
Qin = 10 000 e-

## Slide 32: What’s a high open loop gain?
Sweep from 1 to 105
For very low gains, Vout is dependent on and Cin
In order for the output to be only dependent on Cf, the gain must be high so that:
Iin
Cf
Vout
Cs
ZL
-gm
I1
Iin
Cs
)
We could intuitively understand this using Miller
(This approach assumes an ideal amplifier)

## Slide 33: CSA: Returning to baseline – Continuous Reset (ideal amp)
If 
Iin
Rf
Vout
Zin
ZL
-gm
I1
Cf
T domain
S domain
Instantaneous rise time (ideal amp), and discharge with a time constant RfCf

## Slide 34: CSA: Returning to baseline – Continuous Reset (ideal amp)
Rf = 500k
RxC = 5 ns
Pole = 1/(2*pi*RC) = 31.8 MHz

## Slide 35: The effect of Rf : sweep 10 kΩ - 5 MΩ

## Slide 36: CSA: Returning to baseline – Continuous Reset (real amp)
Iin
RL
Vout
Zin
CL
-gm
If
I1
Cf
Rf
If the system has a dominant pole () then the TF can be written as:
Feedback pole
Output pole
Rising time constant
Falling time constant

## Slide 37: CSA: Returning to baseline – Continuous Reset (real amp)
In time domain:
It is already assumed that then the TF approximates to :
Iin
RL
Vout
Cin
CL
-gm
I1
Cf
Rf

## Slide 38: CSA: Returning to baseline – Continuous Reset (real amp)
NB: The signal reaches max amplitude only if

## Slide 39: Case of complex conjugate poles
P1 = -82 + j 97 MHz
P2 = -82 – j97 MHz
Damped oscillation

## Slide 40: Stability Study by Simulation
Simulate open loop response, and check for phase margin. Good practice PM ~ 7

## Slide 41: What have learned so far?
We get:
=+ Ileak
Cs
Ileak
We know:
i
w

## Slide 42: Outline
From Particle to Detected Charge
  Sensors
  Signal Formation and characteristics
  Source model
From Charge to Amplified Analog Signal
  Typical Front-End Channel
  Charge Sensitive Amplifier
  Shaper
Noise and Design Optimization
  Thermal, Shot, Flicker
  Series Vs Parallel noise
  Noise calculation and optimization

## Slide 43: Typical Front-End Channel: 2- Shaper
Iin
Cf
Cin
CSA
Detector
Vth
Shaper
Comp
S/H
Chare Sensitive Amplifier
Integrates the incoming charge on a feedback capacitor
Shaper
Shapes (Filters) the signal for an optimal Signal to Noise Ratio
Comparator to detect an event above a certain threshold
And/Or
a Sample and Hold circuit for an ADC further in the channel
Counter
ADC

## Slide 44: Shaper: CR-RC filter
Differentiator
= High pass filter
Integrator
= Low pass filter
Shaper = Band pass filter

## Slide 45: Qualitative Approach
CSA output
(assuming
Effect of while = constante
Effect of while = constante
Normally the choice = is the best compromise for signal amplitude within a fixed duration, and for filtering of high and low noise frequencies

## Slide 46: CR-RC Shaper Modeling
It can be demonstrated that for :
Taking inverse Laplace Transform yields:
The peaking time is Tpeak =
And the maximum amplitude is:
NB: The ratio of resistors and capacitors can introduce gain in addition to filtering

## Slide 47: CR-RCN shaper
Introducing ‘N’ number of integrator stages yields a higher the order of the shaper
Higher order filters give faster return to baseline, useful for high-rate applications, at the expense of power and circuit surface

## Slide 48: Optimum Filter for Amplitude Measurement

## Slide 49: Complex Conjugate Shapers
The Gaussian shape approaches the optimal filter’s response.
This response can better be approximated using complex conjugate poles in the transfer function.
The math can be complex, so there are tables that give the poles positions as a function of the shaper order. (Poles are normalized to  )
Theoretical Gaussian pulse shape

## Slide 50: Outline
From Particle to Detected Charge
  Sensors
  Signal Formation and characteristics
  Source model
From Charge to Amplified Analog Signal
  Typical Front-End Chain
  Charge Sensitive Amplifier
  Shaper
Noise and Design Optimization
  Thermal, shot, Flicker
  Series Vs Parallel noise
  Noise calculation and optimization

## Slide 51
Noise
Practically, the signal fluctuates around a mean value for baseline and amplitude due to noise. This limits the capability of the CSA to detect small charges, which must be distinguishable from the noise.
In order to optimize our circuit, we need to understand the origin of noise sources.
Noise ca be represented by a voltage source whose power spectral density is noted measured in . The average output power obtained after integration over the BW is then noted
Noise can also be represented as current sources.

## Slide 52: Types of Electronic Noise
Thermal noise
  Associated with the thermal agitation of charge carriers in conductors (Brownian motion)
  Occurs in resistive components regardless of DC current
  Relevant for resistors, MOSFETs in moderate and strong inversion
  Power spectral density is proportional to temperature
Resistor: In a resistor of value R, the thermal noise:
  or
MOS transistor: In a transistor, thermal noise is given by
  or
  for strong inversion and for weak inversion
noiseless
noiseless

## Slide 53: Types of Electronic Noise
Shot noise
  Associated with the flow of DC current across a barrier (PN junction, impurities, defects)
  It stops when the current stops
  Power spectral density is not directly dependent on temperature ()
  If the leakage current through a diode is 𝐼_𝑙𝑒𝑎𝑘 then the shot noise is:
Both thermal noise and shot noise are considered White Noise, that is, their power spectral density is constant for all frequencies

## Slide 54: Types of Electronic Noise
Flicker (1/f) noise
  Non-fundamental, technology related
  Attributed to material defects and "roughness“ (dangling bonds) creating traps near interfaces
  The traps randomly capture and release carriers, leading to fluctuations in the number of carriers and their mobility
Equivalent

## Slide 55: Noise calculation
Considering a noise spectral density of at circuit input, whose unit is
is the system’s transfer function
The average output noise is:
  [V2]
H(f)
Vin
Vout

## Slide 56: Series Vs Parallel noise
Normally the resolution of the front-end is limited by the noise from the input MOSFET
We see that, when referred to the input, the noise can be represented either by voltage sources connected in series with the input or by current sources connected in parallel as they are different in nature.
Voltage sources e.g. input MOS thermal noise, 1/f noise. They are directly applied to input of amplifier and are generally reduced as you reduce the amplifier bandwidth (i.e. increase peaking time).
Current sources e.g. : leakage current, feedback circuitry noise current. These currents are integrated on Cin (like input charge) and increase as the integration window increases (increase with slow peaking time).
Noise optimization consists in reducing the overall noise of the system
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 57: Series vs Parallel noise: calculation
Since the transfer function is already calculated for an input current, we can directly use it to calculate the output noise due to current noise sources.
The voltage noise sources can be treated as current using the Norton equivalent
By assuming a total series and parallel unilateral noise spectral densities of Svn and Sin, respectfully, then the total output noise N is:
Cs
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 58: Equivalent Noise Charge
The Equivalent Noise Charge is the input charge that generates a S/N ratio at the output equal to 1
Assuming that the front-end implements a time invariant filter with overall impulse response h(t). If the input charge is Then the output response is Vout (t) = which admits a maximum at t=t0
We have calculated that the output noise is:
Thus, the SNR is:
(in Coulombs)
The charge that would make SNR = 1 is:
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 59: Equivalent Noise Charge – with Shapers
Using a classical model (only approximation in deep technologies )
In this case, one could note that:
Series and parallel noise are weighted inversely WRT
MOS thermal noise is reduced by increasing gm
Parallel noise is reduced by increasing Rf
Flicker is reduced by increasing the transistor area WL
Overall noise is reduced by decreasing Cin , Cf
While optimizing for noise, one must keep an eye on other specifications, like gain, speed, count rate, maximum area, power, etc
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 60: Series Vs Parallel noise: Example
By calculations or simulations, we can optimize the peaking time in order to have a minimum ENC for the system
Peaking time = 50 ns
ENC =275 e-rms
Peaking time = 1.8 us
ENC = 67 e-rms
Considering an amplifier whose ENC changes with peaking time as in the above figure
Non-optimized design
Optimized design
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 61: References
Angelo Rivetti «CMOS Front-end Electronics for Radiation Sensors .» CRC Press. 2015
Boris Murmann / Angelo Dragone – Stanford EE214B 2024
Francis Aghinolfi - Analog Signal Processing of Particle Detector Signals, CERN 2005
Veljko Radeka - Detector Signal Processing, NSS 2009
Gianluigi De Geronimo - MOSFET Optimization in Deep Submicron Technology for Charge Amplifiers, TNS 2004
Acknowledgment: Alexandre Habib

## Slide 62: Conclusion

## Slide 63: Pole zero cancellation
Rf
Rf
Rz

## Slide 64: Equivalent Noise Charge – Shaperless case
Using a classical model (only approximation in deep technologies)
And knowing that
We’ve already seen that the transfer function of a CSA with RC feedback can be modeled as:
By integrating the different noise sources’ spectral densities over all frequencies, we can demonstrate that:
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 65: Equivalent Noise Charge – Shaperless case
The ENC is thus expressed as:
In this case, one could note that:
MOS thermal noise is not reduced by increasing gm
Parallel noise is not reduced by increasing Rf
Flicker is reduced by increasing the transistor area WL
Overall noise is reduced by decreasing Cin , Cf
Thermal noise
Flicker noise
Parallel noise
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 66: ENC dependencies
HEPIC 2025 – Analog Signal Processing for Radiation Detectors

## Slide 67: Stability of a closed loop system
The transfer function can be written under this form:
is called the natural frequency, and the quality factor. The denominator admits the following roots:
If then the poles are real, and the system is over-damped (stable)
If =0.5 then the poles are real and coincident, and the system is critically-damped (stable)
If then the poles are complex conjugate, and the system exhibits damped oscillations
X
X
X
X
X
X