## Slide 1: Custom ICs for Physics Research
Carl Grace 6/23/2025
Lawrence Berkeley National Laboratory
HEPIC Summer School @ SLAC Seminar

## Slide 2: Lawrence Berkeley National Laboratory
MOST DIVERSE
US NATIONAL LABORATORY
Key Strengths
Physical Sciences, Computing, Biosciences, Earth and Energy Sciences, Materials, and Nanotechnology
NATIONAL
USER FACILITIES
Advanced Light Source
National Energy Research Scientific Computing Center
Energy Sciences Network
Joint Genome Institute
Molecular Foundry (including National Center for Electron Microscopy)
16
NOBEL PRIZES
Most recent: 2020 Nobel Prize in Chemistry for co-discovery of CRISPR gene editing (Prof. Jennifer Doudna)
EXCELLENCE IN SCIENCE
3800 employees
1000 students
16,350 users and visiting researchers
3018 publications in CY24

## Slide 3
Fun Fact
At LBNL you can write your address in elements!
All discovered by LBNL along with 12 other elements!
Plutonium discovered in 1940 at LBNL
Radiation hazard trefoil invented in 1946 at LBNL

## Slide 4: Introduction
Custom Integrated Circuits – also called Application-Specific Integrated Circuits (ASICs) - are an increasingly important technology for experimental physics
ASICs are an enabling technology. Without ASICs, many modern detector systems would not be feasible
The goal of an ASIC in HEP is to generate data that physicists can turn into papers

## Slide 5: How do we study the Universe?
Probably the best way, is to look at it!
Basic fact in science: Rayleigh Criterion. To see features of something, the probe (light in many cases) must be smaller than the features you wish to see

## Slide 6: Biology – 10-6 m (eV). Probe = visible light

## Slide 7: Chemistry / Mat. Sci. – 10-9 m (keV) Probe: electrons

## Slide 8: Particle Physics – 10-18 m (TeV) Probe: hadrons

## Slide 9
LHC+ATLAS is a microscope
Typical microscope = light source + camera
Best microscope = brightest light source + highest res. camera
Our kind of Microscope = collider + detector
Best Microscope there is = LHC + ATLAS
White circle is 300ft underground
Detector is 300ft under here

## Slide 10
What does it do?

## Slide 11
Takes multi-media snapshots of collision events

## Slide 12: Detector Readout
Rutherford’s discovery of the atomic nucleus (1909)
Detector: Fluorescent Screen
Readout Technology: Eyeball
Worked great! But not exactly scalable…
Detector: Silicon Strip (1970s)
Readout Technology: Electronics
Major advance in particle tracking. Is it scalable?
H. SPIELER

## Slide 13: Silicon Strip Readout
State of the art ~ 1980
256 channel strip detector
Readout is implemented using rack of discrete amplifiers and line drivers.
Clearly this is not scalable.
C. HABER

## Slide 14: Silicon Strip Readout
NA11 experiment at CERN (1984) measured charm lifetimes.
NA11 deployed community’s first silicon vertex detector using a 128-channel strip detector module.
Strip detector had 20 µm pitch, but state of the art for discrete readout channels (on PCBs now) was 60 µm.
Strips read out using 32 individual 4-channel boards requiring a LIMO connector per channel.
Better, but this is still not scalable. Great for 1000s of channels. Not so great for millions. End of the road?
C. HABER
128 channel Si Strip
4-channel readout cards
Individual readout card
~ 15 mW/channel

## Slide 15: In the dark ages*…
*1960s – 1970s
Paul Gray
Paul McCreary
Hodges Flip-Flop (1963)
William Black
David Hodges
Mask Camera
Ion Implanter
Stephen Lewis – First Pipelined ADC (1986)
IC Development at UC Berkeley
First all-MOS ADC (1975)!

## Slide 16: The rise of the Custom ASIC
1960s : Only a few Universities made chips
Late 70s : Technology for Multi-Project Wafers (Mead and Conway)
1981 : Founding of MOSIS with DARPA support
1987 : MOSIS commercialized (first large-scale eCommerce application on the Internet)
Also 1987 : TSMC founded (and Fabless Semi industry was born!)
Trivia alert! The same DARPA program led to the development of the first hardware description language, VHDL.

## Slide 17: The decline of the “internal fab”
BEFORE
AFTER

## Slide 18: First Physics ASICs
NMOS process (no P-channel devices) - SLAC - 1984
Microplex – first custom ASIC for Physics Research
Walker, Parker, Hyams, Shapiro, “Development of High Density Readout for Silicon Strip Detectors,” NIM 226 (1984)
SVX – First CMOS ASIC for Physics Research
CMOS process (with P-channel devices) - LBNL - 1987
128 channels
3 mW / channel
Kleinfelder, et al.; “A Flexible 128-Channel Silicon Strip Detector Instrumentation Integrated Circuit with Sparse Data Readout”, TNS 35 (1988)
128 channels
1.25 mW / channel
6.3 mm
6.3 mm
11,000 transistors
CDF experiment used 240 SVX chips  30720 channels
Already at discrete limit

## Slide 19: Challenges for Custom ASICs
Physics experiments often create extreme environments for their readout ASICs
High Radiation
ATLAS Detector
Cold Temperature
ProtoDUNE LAr TPC
Liquid Argon

## Slide 20: Challenges for Custom ASICs - Radiation
Two main types of radiation damage to integrated circuits that concern us (Single Event Latchup and Single Event Transients of less importance in HEP experiments)
Total Integrated Dose – structural damage to silicon structure that leads to failures
Single Event Upset – transient effects that could modify data or lead to incorrect data

## Slide 21: Radiation -- Total Integrated Dose (TID)
Requirements for TID radiation tolerance for physics far exceed any commercial application
F. Faccio

## Slide 22: Radiation – Single Event Effects (SEE)
C. Zamantzas
Scaling devices makes ASICs more resilient to TID, but less resilient to SEE
R. Gaillard

## Slide 23: Radiation – Single Event Effects (SEE)
Key mitigations: Triple Modular Redundancy (TMR), Hamming encoding, continuous reconfiguration
K. Berg
Triple Modular Redundancy (TMR)
- Device level? Circuit? Module?
Hamming encoding
Continuous Reconfiguration

## Slide 24: Cryogenic Operation
Functionality, Threshold Shifts
Negative resistance and hysteresis. Carrier freeze out also an issue.
Reliability and biasing drift
“Hot” carriers cause early device aging
180 nm

## Slide 25: Typical ASICs for HEP
Typical large physics experiments use capacitive detectors:
    For example, reverse-biased diodes for charged particles, microchannel plates, wires (e.g. in drift chambers), pixels or silicon photomultipliers (SiPMs) for photons (also can be used with scintillators)
Trend is towards lower noise, improved time and energy resolution, operation in extreme environments, reduced power, and increased number of channels
Importance of ASICs in physics research is increasing
Rivetti “CMOS Front End Electronics for Radiation Detectors”
Typical multi-channel physics ASIC
Typical timing ASIC

## Slide 26: ASIC for Physics Example: ATLAS Inner Tracker (ITk)
Large Hadron Collider – Switzerland and France
ATLAS Detector
ATLAS Inner Tracking Detector (ITk)

## Slide 27: ASIC for Physics Example: ATLAS Inner Tracker (ITk)

## Slide 28: ASIC for Physics Example: ATLAS Inner Tracker (ITk)
Analog island in a sea of synthesized digital logic.
More of a “commercial” design methodology than previous HEP chips.
RD53A – test chip prior to ITk chip
ITk will have 13 m2 active area or 1.4 Billion pixels!

## Slide 29
On 8 October 2013 the Nobel prize in physics was awarded jointly to François Englert and Peter Higgs "for the theoretical discovery of a mechanism that contributes to our understanding of the origin of mass of subatomic particles, and which recently was confirmed …
by the ATLAS and CMS experiments at CERN's Large Hadron Collider."
Actual Event showing the creation of a Higgs Boson, 10/19/2017 @ 11:30 PM, Geneva time

## Slide 30: Silicon Tracker Summary
Name | Microplex | SVX | D-OMEGA | LHC1 | FE-I3 | FE-14 | RD53A | ITkPixv1
Year | 1984 | 1987 | 1991 | 1996 | 2005 | 2011 | 2017 | 2021
Node [µm] | 5 | 3 | 3 | 1 | 0.25 | 0.13 | 0.065 | 0.065
Chip Size [mm] | 4.4 x 6.4 | 6.3x6.3 | 8.3x6.6 | 6.6x3.5 | 10.8x7.6 | 10.2x19 | 20x10 | 20x20
Pixel Size [µm] | 47.5 (pitch) | 50 (pitch) | 70x500 | 50x500 | 50x400 | 50x250 | 50x50 | 50x50
Number of Pixels | 128 (strips) | 128 (strips) | 1008 | 2032 | 20k | 26.9k | 79.2k | 158.4k
Transistor Count | ? | 11000 | ? | 800k | 3.5M | 80M | 311M | 600M

## Slide 31: ASIC for Physics Example: The DUNE Experiment
The Deep Underground Neutrino Experiment (DUNE) is an international science collaboration focused on neutrinos
Key Purpose:
Enable the search for CP Violation
Help us understand the matter/antimatter
imbalance of the universe.
LBNL is leading the development of the Near Detector (ND) and has an important role in the cold electronics for both the ND and Far Detector (FD).
Neutrinos have a mean-free-path of 60 light years in water so extremely intense beam and dense detector material (Liquid Argon) needed
Illustration courtesy LBNF

## Slide 32: What is the ND key technical challenge?
The DUNE ND will experience ~10M neutrino events per year. Below is a simulation of neutrino pileup in the ND from a single beam pulse (each color indicates a separate neutrino interaction) not including neutrino background.
Approximately 50 neutrino interactions per beam spill

## Slide 33: What is the ND key technical challenge?
The much larger Far Detector (FD) uses a conventional wire-based liquid Argon (LAr) Time Projection Chamber. Electrons generated by neutrino collisions are drifted in an electric field to wire planes in the cold volume.
Ambiguity could be a showstopper!
Solution: True 3D readout with a pixelated detector immersed in LAr for the DUNE Near Detector.
3 GeV electron neutrino charge-current interaction in LAr.

## Slide 34: LArPix – Liquid Argon Pixel ASIC
Approach: Integrating Amplifier with Self-triggered Digitization and Readout
Front-end amplifier
Self-triggering Discriminator
Standard SAR Digitizer
Digital Control
Achieve low power: avoid digitization and readout of mostly quiescent data.
64 channels per ASIC
  Charge Sensitive Amplifier
  Discriminator (self trigger)
  ADC (per channel)
  Digital Control logic
Global control logic
2k FIFO
On chip references and bias currents
Only decoupling capacitors needed
Immersed in Liquid Argon (-184° C)

## Slide 35
May 2018:
832-pixel system @ LBNL
Apr 2018:
512-pixel system @ Bern
60 cm drift, 1 kV/cm
Feb 2018:
128-pixel system @ LBNL
10 cm drift, 200 V/cm
Demonstration of cosmic ray detection at increasing scales
JINST 13 (2018) P10007

## Slide 36: Quick Design Iteration  Continuous Improvement
5.28 mm
6.25 mm
5.0 mm
5.0 mm
LArPix-v1
LArPix-v2
32 channels, 33 mm2
64 channels, 25 mm2

## Slide 37: LArPix Pixel Tile
Tile with 100 LArPix-v2 ASICs (6400 channels)
Closeup of tile
Prototype tiles have 100 LArPix ASICs
(30 cm by 30 cm)
ND Tiles will scale to 160 ASICs/tile
Front of tile with sensor array
Need O(10 Million) pixels for ND

## Slide 38
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
System successfully operated.
Demonstrator for DUNE Near Detector
4 modular LArTPCs
Total active mass: ~3 ton
Readout area: 6.4 m2
400k pixels, 6.3k ASICs

## Slide 39
Demonstrate system scalability in large LArTPC: ArgonCube 2x2 Demonstrator
Raw data (no filtering) of cosmics in ArgonCube module0 demonstrator.
Detector delivers unprecedented track fidelity and would be impossible to implement without custom ASICs
The final DUNE Near Detector will require approximately 350k ASICs to instrument a 100m2 pixel plane (22.4 Mpix)

## Slide 40
First Neutrino Events (DUNE ND 2X2 Demonstrator)
First-ever neutrino events measured using pixelated LArTPC at FNAL (July 7, 2024)!

## Slide 41: Final Thought (Courtesy M. Garcia-Sciveres)
1980s
1990s
2000s
2010s – 2020s
2030s?
M Garcia-Sciveres
(EEs)

## Slide 42: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231