## Slide 1: Introduction to Analog-to-Digital Converters
Katerina Papadopoulou 6/24/2025
Lawrence Berkeley National Laboratory
HEPIC Summer School

## Slide 2: Lawrence Berkeley National Laboratory
MOST DIVERSE
US NATIONAL LABORATORY
Key Strengths
Physical Sciences, Computing, Biosciences, Earth and Energy Sciences, Materials, and Nanotechnology
NATIONAL
USER FACILITIES
Advanced Light Source
National Energy Research Scientific Computing Center
Energy Sciences Network
Joint Genome Institute
Molecular Foundry (including National Center for Electron Microscopy)
16
NOBEL PRIZES
Most recent: 2022 Nobel Prize in Chemistry (Carolyn Bertozzi) and Physics (John Clauser)
EXCELLENCE
& DIVERSITY
3500 employees
1000 students
1750 visiting researchers

## Slide 3: Agenda
ADC Overview
ADC Performance metrics
ADC Architectures
ADC requirements for High-Energy Physics
Extra: Design Study - Oversampling ADC

## Slide 4
ADC Overview

## Slide 5: What are ADCs?
Analog-to-Digital Converters (ADCs) provide the link between the analog world and digital processing
In HEP, detector outputs are usually analog (e.g. charge pulses) and ADCs pace experimental improvements

## Slide 6: ADC Applications
Paul Gray (UCB)
CT, CA: Continuous time, continuous amplitude
DT, DA: Discrete time, discrete amplitude

## Slide 7: ADC Applications
B. Murmann (Stanford)
Huge application space  many complementary ADC techniques
Resolution:
log2 of quantization levels
Sampling Rate: number of conversions/sec
Bandwidth: Sampling Rate / 2 (stay tuned!)

## Slide 8: ADC Applications (cellular phone example)
Y. Chui (UTD)
CMOS? or
something else?
Ericsson CH388
(Hybrid, 1995)
Ericsson Bluetooth
(CMOS, 2001)
Berkäna GSM/GPRS
(CMOS, 2005)
Past
Future
Present
A
D

## Slide 9: What exactly is Analog-to-Digital Conversion?
Analog-to-Digital conversion is essentially a ruler that can be used to measure an unknown quantity to some level of accuracy
This is an ancient algorithm to determine weights (for example in a metal assay). Today this algorithm is called Successive Approximation (and the leading ADC technique uses this algorithm still).
Analog Devices

## Slide 10: Steps of Analog-to-Digital Conversion
Monolithic Power Inc.
Sampling
“discrete-time analog”
“continuous-time analog”
“digital”

## Slide 11: Sampling & Aliasing
How fast do you need to sample?
Shannon-Nyquist Theorem:
If a system uniformly samples an analog signal at a rate that exceeds the signal’s highest frequency by at least a factor of two, the original analog signal can be perfectly recovered from the discrete values produced by sampling.
Did you sample the red curve? Or the blue curve?
Aliasing
The frequencies fx and nfs ± fx, n integer, are indistinguishable in the discrete time domain
If aliasing occurs, no signal processing operation downstream of the sampling process can recover the original continuous time signal!
No aliasing if fsample > 2 fmax where fmax is the maximum frequency in your input signal.

## Slide 12: Sampling & Aliasing in the frequency domain
What can you do?
Important! Use anti-aliasing filter!
H. Khorramabadi (UCB)

## Slide 13: Quantization and Encoding
Y. Chui (UTD)
Important! Every ADC has three inputs. The analog input, the reference, and the power supply.

## Slide 14
ADC Performance metrics

## Slide 15: Key ADC Specifications (there are many others…)
Static:
  Linearity
  Noise
  Offset (Typically don’t care, sometimes you do…)
  Gain Error (Typically don’t care)
Dynamic:
  Signal-to-Noise-Plus Distortion (SNDR)
  Spurious-Free Dynamic Range (SFDR)
  Total Harmonic Distortion (THD)
  Effective Number of Bits (ENOB)
Performance Parameters:
  Sampling Rate
  Resolution
  Analog Bandwidth: Different from sampling rate! Can be more or less (e.g. subsampling applications)
  Power Dissipation
  Die Area
First commercial ADC. 11b, 50 kS/s
$8500 in 1954 ($96,000 today!)

## Slide 16: ADC Noise - Quantization
Quantization noise or quantization error or residue:
Difference between ideal output and real digital output
H. Khorramabadi (UCB)
rms quantization noise =
Ideal converter (infinite number of bits)
Real converter (finite number of bits)
Error has a max peak-to-peak of
+
-
-
+

## Slide 17: ADC Noise - Thermal
Thermal noise generated by resistances in the circuit (rms level determined by capacitors when sampled)
Thermal noise depends on sampling capacitance. Fundamental tradeoff between noise, speed, and power
Total rms noise =

## Slide 18: ADC Static Linearity
Often a key specification, and defines the accuracy of the ADC (as opposed to raw resolution)
Two main static linearity measurements: Differential Nonlinearity and Integral Nonlinearity
Simpler in practice than they seem.
DNL: deviation of code width from Δ
ΙNL: deviation of code transition from its ideal location

## Slide 19: Testing ADC Static Linearity
General approach:
1. Apply test signal with known probability density function (PDF)
2. Create histogram of measured ADC codes
3. Map measured probability mass function to expected PDF
4. Interpret per-code deviations as DNL and sum DNL to get INL
Example:
Ramp Based Testing: Apply a ramp to ADC input. PDF is uniform (simple!)
DNL for each code is simply count for that code minus average count (simple!)
Don’t need many codes - for 0.01 LSB resolution  100 samples/code
- for N bit ADC  2N*100 total samples
Create histogram – remove over-range bins – calculate average count/bin and normalize
Catch: difficult to generate a linear ramp, and typically you want your test signal to be 10X more linear than ADC. Most commercial ramp generators are linear to only 8-10 bits.
Knowing how to test an ADC is critical, because it:
1. informs your design choices
2. testing techniques can often be adapted to simulation
H. Khorramabadi (UCB)
Raw
histogram
Normalized
histogram

## Slide 20: Testing ADC Static Linearity
Solution sine-wave-based testing
It is much easier to generate a linear sine than ramp  can heavily filter
PDF of sine is more complicated than ramp
“bathtub”
For details:
[1] EE247 Lectures UCB (Matlab code available)
[2] M. V. Bossche, J. Schoukens, and J. Renneboog,
“Dynamic Testing and Diagnostics of A/D Converters,” IEEE
Transactions on Circuits and Systems, vol. CAS-33, no. 8,
Aug. 1986
[3] IEEE Standard 1057

## Slide 21: ADC Dynamic Performance
SNDR: Captures both noise and nonlinearity into a single measure.
Assuming a full-scale sine wave input, SNDR is:
SFDR: Difference between input tone and highest harmonic.
Rule of thumb for estimating SFDR:
THD: Ratio of power of fundamental to sum of powers of all harmonics
ENOB: Number of bits of ideal ADC that gives same SNDR as ADC under test.
When quantization = thermal, ENOB = N-1

## Slide 22: ADC Dynamic Performance – example plot
Here, ENOB = (55.54 – 1.76)/6.02 = 8.9 bits

## Slide 23: ADC Dynamic Performance – Coherent Sampling
General technique: apply pure sine wave to ADC and take FFT of resulting output codes
Vitally important that all power of input tone is in single FFT bin  Coherent Sampling
Tip: pick prime # of cycles
VERY useful for top-level simulation (and testing!) of ADCs

## Slide 24: ADC Testing Takeaways
Make sure your reference & power are significantly more stable than your ADC
Make sure your test signal is significantly more linear than your ADC
Make sure your board and input have extremely low noise during noise tests
Make sure you use coherent sampling for dynamic testing
Make sure you lock both the signal generator and the ADC clock to the same time base

## Slide 25: ADC Performance Space
S. Chen, R. Brodersen, “A 6-bit 600-MS/s 5.3-mW Asynchronous ADC in 0.13-μm
CMOS: IEEE J. of Solid-State Circuits, Vol. 41, No. 12, December 2006.
Golden reference for ADC performance space:
B. Murmann, "ADC Performance Survey 1997-2024," [Online]. Available: https://github.com/bmurmann/ADC-survey.

## Slide 26: Impact of ADCs (Digital Audio example)
Fairlight CMI
1979: $32000
($132k in 2024)
Genesis, Stevie Wonder,
Duran-Duran
E-mu Emulator II
1984: $8000
($23k in 2024)
Front 242, Depeche Mode,
New Order, Bowie, Vangelis
Akai S-1000
1988: $2500
($6350 in 2024)
Boards of Canada, Cabaret Voltaire,
Portishead, and Everyone!
Akai MPC-One
2024: $599

## Slide 27
ADC Architectures

## Slide 28: ADC Architectures
Integrating (“Wilkinson”)
Sigma-Delta
Successive Approximation
Pipelined
Flash
HEP Relevant ADC architectures from slowest to fastest. Note: Everything was invented by 1970.

## Slide 29: Integrating ADC (and single-slope)
Dual-Slope ADC:
- Vin integrated for a fixed amount of time
- Then de-integrated with Vref until Vo=0
- Remove R (direct charge readout) to make a Wilkinson
Single-slope ADC:
- T1 proportional to Vin
- Counter output proportional to T1-n*Tclk

## Slide 30: Oversampling
Spread constant noise power over a larger bandwidth and then digitally filter  reduced quantization noise
Extend this by shaping the noise (pushing more of it to higher frequencies where it can be filtered)
When fs>>2fm, filtering is easier!

## Slide 31: Sigma-Delta ADC
Key Idea: signal sees low-pass filter,
quantization noise sees high-pass filter.
Loop order is defined as number of poles in H(z)
- Oversampling ratio M = fs/2fsignal
- Average of Y approximates X (digital filtering!)=
- 2X increase in M -> 9db (1.5bit) increase in dynamic range
Idea: Don’t just oversample, modulate the input to put more of the quantization noise power at higher frequencies
For more details:
S. Pavan, R. Schreier, G. C. Temes, and R. Schreier, Understanding delta-sigma data converters, IEEE Press/Wiley, 2017.

## Slide 32: Successive Approximation (SAR) ADC
- Directly implements binary search algorithm in hardware
- High accuracy possible (>16bits)
- Requires N clock cycles for N-bit conversion -> moderate speeds
- Most common type: charge redistribution SAR ADC
Simple 6-bit example

## Slide 33: Pipelined ADC
Combining the bits
- Cascade several low resolution stages to obtain high overall resolution
- Each stage processes the (amplified) quantization error of previous stage
- Stages can operate concurrently! -> higher speeds
- Latency function of number of stages
H. Khorramabadi (UCB)
- Example: Three 2-bit stages
- The gains between stages are 2Bieff
- Then to combine bits:

## Slide 34: Flash ADC
- Very fast.
- Very power Hungry.
- Limited to about 8 bits.
-Used as sub-ADCs in multi-stage ADCs
Sources of error:
- DC offset
- Non-linear input capacitance
- Signal feedthrough
- Signal kickback

## Slide 35: Flash ADC
TRW TDC1007 8-bit, 20 MS/s Flash ADC enabled new field of “digital video”
Won technical Emmy for analog/digital video conversion technology in 1989!
ADC designers are creative.

## Slide 36
ADC requirements for
High-Energy Physics

## Slide 37: In the dark ages*…
*1960s – 1970s
Paul Gray
Paul McCreary
Hodges Flip-Flop (1963)
William Black
David Hodges
Mask Camera
Ion Implanter
Stephen Lewis – First CMOS Pipelined ADC (1986)
IC Development at UC Berkeley
First all-MOS ADC (1975)!

## Slide 38: The rise of the Custom ASIC
1960s : Only a few Universities made chips
Late 70s : Technology for Multi-Project Wafers (Mead and Conway)
1981 : Founding of MOSIS with DARPA support
1987 : MOSIS commercialized (first large-scale eCommerce application on the Internet)
Also 1987 : TSMC founded (and Fabless Semi industry was born!)
Trivia alert! The same DARPA program led to the development of the first hardware description language, VHDL.

## Slide 39: First Physics ASICs
NMOS process (no P-channel devices) - SLAC - 1984
Microplex – first custom ASIC for Physics Research
Walker, Parker, Hyams, Shapiro, “Development of High Density Readout for Silicon Strip Detectors,” NIM 226 (1984)
SVX – First CMOS ASIC for Physics Research
CMOS process (with P-channel devices) - LBNL - 1987
128 channels
3 mW / channel
Kleinfelder, et al.; “A Flexible 128-Channel Silicon Strip Detector Instrumentation Integrated Circuit with Sparse Data Readout”, TNS 35 (1988)
128 channels
1.25 mW / channel
6.3 mm
6.3 mm
11,000 transistors
CDF experiment used 240 SVX chips  30720 channels
Already at discrete limit
Technology soon advanced to make on-chip ADCs practical

## Slide 40: Unique Challenges for HEP ADCs
Physics experiments often create extreme environments for their readout ASICs
High Radiation
ATLAS Detector
Cold Temperature
ProtoDUNE LAr TPC
Liquid Argon

## Slide 41: Unique Challenges for HEP Custom ADCs - Radiation
Two main types of radiation damage to integrated circuits that concern us:
Total Ionizing Dose: structural damage to silicon structure that leads to failures:
- threshold shifts, leakage currents, oxide degradation etc
Single Event Upsets: transient effects that could modify data or lead to incorrect data
- affect memory and logic circuits

## Slide 42: Radiation -- Total Ionizing Dose (TID)
Requirements for TID radiation tolerance for physics far exceed any commercial application
F. Faccio

## Slide 43: Radiation -- Total Ionizing Dose (TID)
F. Faccio
Key mitigations:
  use scaled technologies -> reduced charge collection volume (Microplex and SVX only radiation tolerant to 10s of krad)
  “Hardness-By-Design” techniques (enclosed layout / guard rings / shielding)

## Slide 44: Radiation – Single Event Upsets (SEUs)
Key mitigations: Triple Modular Redundancy (TMR), Hamming encoding, continuous reconfiguration
K. Berg
Triple Modular Redundancy (TMR)
Hamming encoding
Continuous Reconfiguration

## Slide 45: Cryogenic Operation
Functionality, Threshold Shifts
Negative resistance and hysteresis. Carrier freeze out also an issue.
Reliability and biasing drift
“Hot” carriers cause early device aging
180 nm

## Slide 46: What’s Next?
Architectures that harness the unique capabilities of scaled CMOS to improve efficiency
Pipelined SAR
Asynchronous SAR
Examples

## Slide 47: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231

## Slide 48
Extra: Design Example

## Slide 49: Design Example – Sigma-Delta ADC
Doubling OSR improves
SQNR by (6L+3) dB
or L + 0.5 bits
Choose 2nd order modulator
Synthesize ADC transfer function in MATLAB or Python
Goal: 12b – 100 kHz ADC for power monitoring

## Slide 50: Design Example – Sigma-Delta ADC
Synthesized modulator close to ideal

## Slide 51: Design Example – Sigma-Delta ADC
Modulator Schematic
Implement transfer function coefficients as capacitor ratios

## Slide 52: Design Example – Sigma-Delta ADC
1st int
2nd int
Vinput
Filter out

## Slide 53: Design Example – Sigma-Delta Digital Filter
For sinc3 filter:
Structure called Cascaded Integrator Comb (CIC) filter
Filter implemented with Verilog HDL

## Slide 54: Design Example – Sigma-Delta ADC

## Slide 55: Design Example – Sigma-Delta ADC filter layout