## Slide 1: Beam-Beam Interaction Point
Alexander Pukhov & Tom Wilson
Heinrich-Heine-University Dusseldorf
John Farmer
CERN & MPI Physics

## Slide 2: Particle colliders
Particle beams cross each other, and events will occur. The rate is proportional to the cross section of the event. The constant of proportionality is called luminosity
Mathematically, luminosity is a measure of the overlap between the colliding species. The final figure of merit for a collider is the integrated luminosity, which relates to the total number of events expected per second
e-
e+

## Slide 3: Pinch & disruption
The most relevant IP physics for us at the moment is beam pinch
e-e+ colliders exhibit pinching at the IP, the reason for this is easy to see
Disruption parameter , where is the betatron frequency
Ey
Bz
e-
e+
e-
e+

## Slide 4: Beamstrahlung-enhanced disruption
Collision of two cylindrical beams (Movie)
QED off
QED on
A. Samsonov et al., NJP 23, 103040 (2021)

## Slide 5: Beamstrahlung-enhanced disruption
For : high yield of electron-positron pairs
  Formation of a QED cascade
Simulations with QED exhibit kink instability
  QED effects are probabilistic changes in symmetric particle distribution
Requirement „“ poses restrictions on beam length and diameter
  Considering RR changes restrictions
Estimate for disruption parameter in QED regime ():
Results
A. Samsonov et al., NJP 23, 103040 (2021)

## Slide 6: Virtual Laser Plasma Lab
Plasma or neutral gas
Gas of an arbitrary element can be used.
Advanced physics & numerics
Inelastic processes
Radiation damping
QED effects
hybrid hydro model
quasi-static approximation
Galilean boost
Fields
Particles
A. Pukhov, J. Plasma Phys. 61, 425 (1999); CERN Yellow Reports (2016)

## Slide 7: Quantum electrodynamics (QED)
Quantify importance of QED with parameter
  (“Schwinger field“)
: hard-photon emission, electron-positron pair creation, … become important
: fully non-perturbative QED
  no experiments
  only preliminary analytical studies
Photon emission
Pair production
V. Ritus, Ann. Phys. 69, 555 (1972)
V. Yakimenko et al., PRL 122, 190404 (2019)

## Slide 8: Modeling QED effects
1. Randomized photon energy
2. Calculate probability rate
3. Probability of decay process
4. Second random number for photon emission
(Similar procedure for electron-positron pair creation)
Monte-Carlo QED loop (Photon emission)
N. Elkina, PRAB 14, 054401 (2011)

## Slide 9: Modeling QED effects in VLPL
Modified PIC cycle

## Slide 10: Maxwell Solvers in VLPL
Full EM solvers
Yee
Universal
Isotropic Overdense plasmas
RIP
No numerical Cerenkov LWFA
iRIP
Implicit RIP high transverse resolution
GEM
Galilean boost for LWFA
Quasi-static
Beam-driven PWFA
Special solvers
Static
Beam-beam IP

## Slide 11: Removing Numerical Cherenkov Instability
novel „rhombi-in-plane“ (RIP) solver removes numerical dispersion along one direction
Co-located positions of transverse field pairs this excludes interpolation errors
Numerical Cherenkov is eliminated
Allows to accurately simulate bunch propagation
A. Pukhov, J. Comp. Phys. 418, 109622 (2020)

## Slide 12: VLPL vs Yee solvers
Ultra-relativistic electron bunch moving in vacuum
Yee solver: full NCI
VLPL solver:
stable
M. Filipovic et al., PRAB 25, 054405 (2022)

## Slide 13: VLPL vs Yee solver
Radiative losses using the Yee solver
NCI effectively suppressed for the RIP solver
Fourier transform
Radiative energy loss
M. Filipovic et al., PRAB 25, 054405 (2022)
Yee solver: full NCI
VLPL solver:
stable

## Slide 14: Typical CLIC and PWFA bunches
CLIC: long flat bunches with high aspect ratio
PWFA: long narrow pencil bunches
It is extremely challenging to simulate these bunch with full EM PIC codes
Phys. Rev. Accel. Beams 24, 071001

## Slide 15: Beam-Beam IP Simulations
Simple static solver:
Valid for highly relativistic bunches,
At the moment, only coherent photon and pair production implemented via the QED module

## Slide 16: Beam-Beam IP Simulations
Explicit full EM RIP solver:
Explicit RIP is dispersionless in one direction, but uses Yee in the transverse plane This limits the transverse grid step
In addition, limited transverse box size causes significant in full EM codes

## Slide 17: Beam-Beam IP Simulations
Implicit full EM RIP (iRIP) solver solves full set of Maxwell equations:
Like eRIP, iRIP is dispersionless in one direction, the time step is fixed to However, the transverse grid step is unlimited, is possible
The uniform can be easily eliminated by transverse 2D FFT

## Slide 18: CLIC-like parameters
  x-size σx = 2.9 nm
  y-size σy = 144 nm
  Longitudinal size σz = 70 μm
  Population 4.4x109 (0.7 nC)
  x-emittance εx = 30 nm
  y-emittance εy = 950 nm
  Energy 190 GeV (γ ~ 370000)
The same problem was simulated by GuineaPig++ and static VLPL

## Slide 19: CLIC-like parameters
  x-size σx = 2.9 nm
  y-size σy = 144 nm
  Longitudinal size σz = 70 μm
  Population 4.4x109 (0.7 nC)
  x-emittance εx = 30 nm
  y-emittance εy = 950 nm
  Energy 190 GeV (γ ~ 370000)
The same problem was simulated by GuineaPig++ and static VLPL

## Slide 20: Test case with a short bunch
  x-size σx = 20 nm
  y-size σy = 20 nm
  Longitudinal size σz = 1 μm
  Population 2x109 (0.3 nC)
  x-emittance εx = 100 nm
  y-emittance εy = 100 nm
  Energy 8 GeV (γ ~ 15000)
The same problem was simulated by GuineaPig++ and VLPL using two different Maxwell solvers

## Slide 21: Test case with a short bunch
All 3 results compare very well
Question: when do we need full electromagnetic simulations?

## Slide 22: Full EM vs Static Simulations
Bunch self-fields
Assume sharp transverse bunch displacement Static code: instantaneous field response
Bunch self-fields
Full EM code: retarded self-fields

## Slide 23: Offset short bunches
  x-size σx = 20 nm
  y-size σy = 20 nm
  Longitudinal size σz = 1 μm
  Population 2x109 (0.3 nC)
  x-emittance εx = 100 nm
  y-emittance εy = 100 nm
  Energy 8 GeV (γ ~ 15000)
  Offset Δx = 2.5 σx
The same problem was simulated by GuineaPig++ and VLPL using two different Maxwell solvers

## Slide 24: Offset short bunches
All 3 results compare well. Small differences can be seen between them, especially in the Breit-Wheeler pair spectra
Coherent pair-production seems especially sensitive to proper representation of the fields at the IP and the initial space-charge field distribution

## Slide 25: Luminosity test case
We have difference roughly factor 2 between GuineaPIG++ and VLPL Looking for the cause

## Slide 26: Conclusion
GuineaPIG++ and VLPL were compared and a good agreement achieved
In most relevant cases static approximation works good
VLPL has a new implicit RIP Maxwell solver It allows to simulate beam-beam IP in full electromagnetic approximation
Samsonov & Pukhov arXiv:2409.09131 (2024)