## Slide 1: Lifetime of 10Hz, 10 GeV Beam Driven Wakes in H2, Ar and Li at the FACET-II Facility
Jason Brooks, Rafal Zgadzaj, Timothy Araujo, Robert Ariniello, Michael Downer
Experiment Goal: observe, analyze, understand post-wake plasma recovery and its potential bearing on accelerator repetition rates
E-224 publications: Zgadzaj et al., “Dissipation of electron-beam-driven plasma wakes,” Nature Commun. 11, 4753 (2020).
Khudyakov et al., "Ion dynamics driven by strongly nonlinear plasma wake," PPCF 64, 045003 (2022).
Chang et al., "Faraday rotation study of plasma bubbles in GeV wakefield accelerators," PoP 28, 123105 (2021).
Silva et al., “Stable positron acceleration in thin, warm, hollow plasma channels,“ PRL 127, 104801 (2021)

## Slide 2
A recent DESY experiment reported
~60 ns plasma recovery time (lower limit)
D’Arcy et al. “Recovery time of a plasma-wakefield accelerator.” Nature 603, 58 (2022).
FlashForward parameters:
• drive bunch: 1 GeV, 0.5 nC
• plasma: 1.75 x 1016 cm-3 Ar
• probe: secondary PWFA driver
at 1 ns < ∆t ≤ 150 ns + trailing
witness bunch
FACET-II parameters:
• drive bunch: 10 GeV, 2 nC
• plasma: 5 x 1016 cm-3 Li
• optical probe at
1 ns < ∆t < ms
FACET-II is uniquely positioned to resolve current
orders-of-magnitude uncertainty in plasma recovery time
“Hail Mary” E-224 result (Zgadaj, 2020):
0.3 ns
10 µs
• Previous experiment observations:
• “recovery” measured after
single shots only. No account
of cumulative plasma heating.
10 Hz heated Li oven tens ˚C within minutes
Notes: Plasma based accelerators and light sources - need to know rep rate for operation comparable to match conventional equivalents (luminosity and brilliance)
Meter scale beam driven plasma targets are more sensitive than e.g. gas jets because there’s no rapid laminar flow
  Gas jets also carry complications/limitations at high rep rate
How rapidly does a stationary, meter scale plasma recover, and is recovery time dependent on rep rate, beam energy and/or charge?
  J/m heating; developing probes to measure [R. Zgadzaj et al., Nat Commun 11, 4753 (2020)]
  Similar study in H2 performed in R.Pompili et al., Commun Phys 7, 241(2024).

## Slide 3
Another recent experiment reported ~0.7 ns plasma recovery time in H2
SPARC_LAB parameters:
• Drive bunch: 0.084 GeV, 0.5 nC, 167 fs duration
• Gas species: H2 in 3 cm capillary
• Probe: trailing 0.084 GeV bunch
R.Pompili et al., “Recovery of hydrogen plasma at the sub-nanosecond timescale in a plasma-wakefield accelerator” Commun Phys 7, 241(2024).
• Stated findings: Pump probe recovery at <0.7ns
Notes: Plasma based accelerators and light sources - need to know rep rate for operation comparable to match conventional equivalents (luminosity and brilliance)
Meter scale beam driven plasma targets are more sensitive than e.g. gas jets because there’s no rapid laminar flow
  Gas jets also carry complications/limitations at high rep rate
How rapidly does a stationary, meter scale plasma recover, and is recovery time dependent on rep rate, beam energy and/or charge?
  J/m heating; developing probes to measure [R. Zgadzaj et al., Nat Commun 11, 4753 (2020)]
  Similar study in H2 performed in R.Pompili et al., Commun Phys 7, 241(2024).

## Slide 4: Shallow angle shadowgraph results in 1 Torr Ar plasma
• expanding plasma observed out to ∆t ~ 300 ns (~4x longer than DESY results)
10 ns
∆t < 0
1 ns
5 ns
25 ns
50 ns
70 ns
150 ns
200 ns
250 ns
300 ns
400 ns
2
-2
r [mm]
0
2
-2
r [mm]
0
-- similar results obtained in 3 Torr Ar
250 ns
background-subtracted,
spatially-filtered
In-focus slice
Expanding plasma
-Z
+Z
CCD
f=750 mm
1:1 imaging
Θ=17 mrad
Ar plasma
+Z
Obj plane
P1
P1
• drive bunch: 1 GeV, 0.5 nC -> 10 GeV, 1 nC
• plasma: 1.75 x 1016 cm-3 Ar -> 3x10^16 Ar
DESY accelerator parameters:
Notes: Repeating every 60 ns can lead to cumulative heating

## Slide 5
3 Torr H2 plasma, e-beam-ionized (June 16-17, 2024 run)
We observed 5-6x faster ion wake evolution in H2 plasma
2
-2
r [mm]
0
∆t < 0
1 ns
2 ns
4 ns
5 ns
10 ns
2
-2
r [mm]
0
15 ns
25 ns
50 ns
70 ns
100 ns
35 ns
• Plasma structures no longer discernible for ∆t ≥ 70 ns
• Faster evolution consistent with ion motion governing plasma dynamics for ∆t ≳ 0.3 ns *
original probe profile
* Zgadzaj et al., Nature Commun. 11, 4753 (2020).

## Slide 6: Ion wake radius vs time
1 Torr Ar fit
3 Torr Ar fit
3 Torr H2 fit
time delay ∆t after e-bunch (ns)
102
101
Cylindrical blast wave:
  = energy per unit length
  = mass density
  = dimensionless; function of the specific heat ratio
Average wake radius (mm)
0.2
0.6
0.8
0.4
1.0
3
Notes: .

## Slide 7: Scattered light from probe persists up to ~1us in Li oven
10-1
100
101
102
103
time delay ∆t after e-bunch (ns)
CCD
f=750 mm
1:1 imaging
Θ5 mrad
Obj plane
Notes: Plot in red shows sum of all pixels measured by scattered light from 6 mrad probe in Li with blue showing relative size of trailing e bunch measured in [D’Arcy et al. 2022]
Different beam energies, charge, gas species ( blue line Ar plasma with e density ~1017 cm-3; red line Li density ~5 x 1016 cm-3)

## Slide 8: Bessel interferometry
Interferometry used to improve sensitivity to us+ effects
New approach: repurpose Bessel beam as an interferometer
  Longitudinal variations -> shift in Bessel rings
angle
ΔOPD
angle
ΔOPD
Obj plane
Thin lens
Ar plasma
Head erosion
Plasma
Vacuum
Transverse Bessel probe intensity asymptotic form

## Slide 9: Bessel Interferometry reveals slow signal decay out to ∆t > 10 µs in 1 Torr Ar
Δt<0ns
Δt10μs
averaging
cone
10 deg averaging cone
Δt<0 average phase shift
Slow decay out to 10’s of µs
1 Torr Ar, ~10 µs max time delay
∆t (µs)
9
2
3
4
5
6
7
8
Phase shift (waves)
0.06
0.07
0.25
0.35

## Slide 10
Summary of main results
plasma
species
Probe method
...1 µs
Li
near-forward light scatter
...0.3 µs
Ar
grazing-incidence shadowgraphy
...0.07 µs
H2
“
2D’Arcy et al. “Recovery time of a plasma-wakefield accelerator.” Nature 603, 58 (2022).
Wake excitation conditions
...>10 µs
Ar
Bessel-beam interferometry
...0.06 µs
Ar
recovery of wake-accelerated e- properties
1 GeV, 0.5 nC drive bunch2
10 GeV, 2 nC drive bunch3
“
“
“
3This work
• Calibrate optical methods for conditions of Ref. 1,2: e.g. 10 GeV, sub-nC excitation of Ar, H2
Requirements for an impactful study
This will require laser pre-ionization of Ar
⇒
independent probe laser needed for ∆t ~ µs
• Address cumulative plasma heating question
⇒
measure vessel heating at 10 and 30 Hz
... µs
H2
recovery of probe e- properties
0.084 GeV, 0.5 nC drive bunch1
1R.Pompili et al., “Recovery of hydrogen plasma at the sub-nanosecond timescale in a plasma-wakefield accelerator” Commun Phys 7, 241(2024).

## Slide 11: Thank you!
Thanks to Mark Hogan, Brendan O’Shea, Robert Ariniello and all of the FACET-II staff for their help with this experiment
Thanks to NSF for supporting this project (award number 2308921)

## Slide 12: Backups

## Slide 13
$1,986.71
$2,998.80
$2,168.78
$1,874.25
$1,820.70
45% Light transmission
THORLABS - Nanosecond Pulsed Laser Diode System, 6 - 129 ns Adjustable Pulse Width
Laser can be interlocked
Goggles that could function for 450nm and 800nm

## Slide 14: Diode intensity and phase
Profile at laser output (zL)
zL + 1.75m

## Slide 15: Beam expander design
Y/Z view
X/Z view
L1:Thorlabs LJ1277L1-A (250 mm fl in y)
L2: LA1484-A-ML (spherical; 300 mm fl)
L3: LJ1144L2-A (500 mm fl in y)
L4: LJ1516L1-A(1000 mm fl in x)
d1: 273.6432 mm (0mm defined to be laser output)
d2: 215.1291 mm
d3: 489.4393 mm
d4: 491.9747 mm
Total distance: ~1500 mm
d1
d2
d3
d4
L1, L2
L3
L4
Pinhole
Pinhole

## Slide 16: Output shape
wx(e-2) radius: 3.77 mm
wy(e-2) radius: 1.85 mm
<=lambda/10 variation in phase across 1/e^2 area

## Slide 17
Thorlabs
6 ns-pulsed laser diode
Proposed E-324 interferometric probe setup
Ar gas
< $2 K
450 nm
0.2 µJ/pulse
e-beam
ionizing
laser
• dedicated E-324 probe
• high-beam quality & stability
+ independent wavelength
for improved bkgd. subtraction
• enables study of laser-preionized
Ar, H2 plasmas
• interferometric shadowgraphy
enables sensitive plasma probing
at multi-µs ∆t.

## Slide 18
(1) Chang et al., “Faraday rotation study of plasma bubbles in GeV wakefield accelerators,” Phys. Plasmas 28, 123105 (2021)
ne > 1019 cm-3:
ne ≈ 1017 cm-3:
(2) Kaluza et al., Phys. Rev. Lett. 105, 115002 (2010);
(3) Buck et al., Nat. Phys. 7, 453 (2011).
Faraday “streaks” of magnetized plasma bubble walls
in ne ≈ 1017 cm-3 plasma
𝜏pr = 1-2 ps
Texas PW
drive pulse
ne ≈ 1017 cm-3
plasma
large B𝜑 and l
compensate
small ne/ncr(pr)
𝜏pr = 1 ps
𝜏pr = 2 ps
𝜏pr = 2 ps
𝜆pr = 1 µm
Texas Petawatt
2026: Faraday rotation to image plasma bubbles in low-ne plasma
At FACET-II, the drive bunch will magnetize the front end of the bubble.

## Slide 19
(right) Comparison with flat plasma, plasma with 1mrad tilt and no plasma (Code V simulation)
(below) FACET-II Bessel data

## Slide 20: Probing Ar wakes at 3 Torr with 17 mrad probe
Probe from 0 ns to 400 ns
Probe fully recovered at ~T0 + 200 ns

## Slide 21: Multiple object plane shallow angle probing
In focus element
Simulated probe beam passing through plasma using Code V
P1
P2
P3
P1
P2
P3
Reconstructed plasma profile via Gerchberg-saxton [Optics Letters 38, 5157 (2013).]
Probe
plasma

## Slide 22: Phase shift: off axis
Plano-convex lens;
f=500mm
Object plane
Plasma offset: X0=250μm, Y0=500μm
Image plane phase at X=0

## Slide 23: Ax pointing throughout data collection